STATEMENT OF WORK

USDA, Natural Resources Conservation Service

Wisconsin

Tree/Shrub Establishment (612)

DESIGN (911)

Deliverables:

1.	Design documents that demonstrate criteria in NRCS practice standard have been met and are compatible with planned and applied practices.  Practice standard criteria-related computations and analyses to develop plans and specifications including but not limited to:

a.	Determination of adapted species of woody plants to be planted and/or naturally reestablished.

b.	Protective measures for planted stock including supplemental water, cultural treatments to enhance survival and health, and use exclusion.

c.	Additional provisions, as required, for improving or restoring natural diversity and increasing carbon storage in biomass and soils.

2.	Written plans and specifications including sketches, location maps and drawings shall be provided to the client that adequately describes the requirements to install the practice and obtain necessary permits.

3.	Documentation of needed operation and maintenance.

4.	Certification that the design meets practice standard criteria and comply with applicable laws and regulations.

5.	Documentation requirements for design modifications during practice installation.

6.	Itemized cost estimate.

CERTIFICATION OF COMPLETION

Tree/Shrub Establishment (612)

Design (911)

Program Participant Information

Name (print):

Contract Number: _______________________________     Contract Item #(s):

Technical Service Provider Information

Name (print):

TSP ID Number: _______________________________________     Expiration Date:

I hereby certify that the technical services I provided as a Technical Service Provider for this component(s) checked above: (1) comply with all applicable Federal, State, Tribal, and Local laws and requirements, (2) meet applicable USDA NRCS conservation practice standards, specifications, and program requirements, (3) are consistent with and meet the particular conservation program goals and objectives, (4) that I have provided the above named Program Participant the Deliverables in this Statement of Work for this component, and (5) comply with all “Certification Terms” as identified in the Technical Service Provider Certification Agreement.

________________________________________________________	__________________

Technical Service Provider Signature	Date

________________________________________________________	__________________

Received By (NRCS staff)	Date

STATEMENT OF WORK

USDA, Natural Resources Conservation Service

Wisconsin

Tree/Shrub Establishment (612)

INSTALLATION (912)

Deliverables

1.	Documentation of pre-application conference with client.

2.	Verification that client has obtained required permits.

3.	Staking and layout according to plans and specifications including applicable layout notes.

4.	Application guidance as needed.

5.	Facilitate, implement and document required design modifications with client, original designer permitting and funding agencies.

6.	Advise client/NRCS on compliance issues with all federal, state, tribal, and local laws, regulations and NRCS policies during installation.

7.	Certification that the application process and materials meet design and permit requirements.

CERTIFICATION OF COMPLETION

Tree/Shrub Establishment (612)

Installation (912)

Program Participant Information

Name (print):

Contract Number: _______________________________     Contract Item #(s):

Technical Service Provider Information

Name (print):

TSP ID Number: _______________________________________     Expiration Date:

I hereby certify that the technical services I provided as a Technical Service Provider for this component(s) checked above: (1) comply with all applicable Federal, State, Tribal, and Local laws and requirements, (2) meet applicable USDA NRCS conservation practice standards, specifications, and program requirements, (3) are consistent with and meet the particular conservation program goals and objectives, (4) that I have provided the above named Program Participant the Deliverables in this Statement of Work for this component, and (5) comply with all “Certification Terms” as identified in the Technical Service Provider Certification Agreement.

________________________________________________________	__________________

Technical Service Provider Signature	Date

________________________________________________________	__________________

Received By (NRCS staff)	Date

STATEMENT OF WORK

USDA, Natural Resources Conservation Service

Wisconsin

Tree/Shrub Establishment (612)

CHECKOUT (913)

Deliverables

1.	Records of application.

a.	Extent of practice units applied with location identified on a plan map.

b.	Actual plant materials used and protective measures.

2.	Certification that the application meets NRCS standards and specifications and is in compliance with permits.

3.	Provide the following information to the NRCS field office servicing the relevant land unit for entry into the Performance Results System (PRS):

a.	Technical Service Provider Name

b.	Customer name

c.	USDA program funding the practice (if known)

d.	Location of work (state, county, conservation district, land tract identifier)

e.	Land use of field where the practice was installed (cropland, etc.)

f.	NRCS practice name and quantity of practice installed in appropriate units

4.	Documentation of exit conference with client and contractor.

CERTIFICATION OF COMPLETION

Tree/Shrub Establishment (612)

Checkout (913)

Program Participant Information

Name (print):

Contract Number: _______________________________     Contract Item #(s):

Technical Service Provider Information

Name (print):

TSP ID Number: _______________________________________     Expiration Date:

I hereby certify that the technical services I provided as a Technical Service Provider for this component(s) checked above: (1) comply with all applicable Federal, State, Tribal, and Local laws and requirements, (2) meet applicable USDA NRCS conservation practice standards, specifications, and program requirements, (3) are consistent with and meet the particular conservation program goals and objectives, (4) that I have provided the above named Program Participant the Deliverables in this Statement of Work for this component, and (5) comply with all “Certification Terms” as identified in the Technical Service Provider Certification Agreement.

________________________________________________________	__________________

Technical Service Provider Signature	Date

________________________________________________________	__________________

Received By (NRCS staff)	Date

STATEMENT OF WORK

USDA, Natural Resources Conservation Service

Wisconsin

Tree/Shrub Establishment (612)

REFERENCES

- WI NRCS Field Office Technical Guide (eFOTG), Section IV, Conservation Practice Standard 612, Tree/Shrub Establishment

- NRCS National Forestry Handbook (NFH), Part 636.4

- NRCS National Environmental Compliance Handbook

- NRCS Cultural Resources Handbook