96E03/29/06

S617-96E.doc

Use on all projects with guardrail work.

Section 617. - GUARDRAIL

Description

Include subsection 617.01(a) when CRG guardrail is used.

617.01

(a) Delete the CRT designator and substitute the following:

CRG		Curved W-beam guardrail and no blockout

Include subsection 617.01(d) when guardrail terminals are required.

617.01

(d) Delete the text and substitute the following:

Terminal section types are designated as follows:

CRT		Cable releasing terminal

G4-BAT	Back slope anchor terminal

FAT-30	Flared anchor terminal, 30 feet long

FAT-20	Flared anchor terminal, 20 feet long

SBT-BAT	Back slope anchor terminal

Flared		Straight or parabolic flared W beam terminal

Tangent	Tangent W beam terminal

Construction Requirements

Include the following when FLH metric standard M617-10, G4 W beam guardrail wood posts, M617-18, G4 W beam guardrail steel posts, or M617-60, steel-backed timber guardrail, type A & type B, is included in the plans.

617.03  Posts.  Delete the text and substitute the following:

Where pavement is within 3 feet of the guardrail, set posts before placing the pavement.

Where it is not possible to maintain a 24-inch minimum distance between the back of the guardrail post and the top of a slope 2:1 or steeper, increase the post length to 8 feet.

Where an impenetrable object is encountered, use a short post.  Treat field cuts for wood posts with two coats of preservative treatment applied with a brush or a sprayer.  Do not place field cuts in contact with the ground.  Anchor short posts in concrete.  Backfill and compact the remaining hole with acceptable material.

Use only standard length posts in terminal sections.

Drive posts into pilot holes that are punched or drilled.  The dimensions of the pilot hole shall not exceed the dimensions of the post by more than ½ inch.  Set posts plumb, backfill, and compact.

When steel-backed timber rail is required, include the following:

617.04  Rail Elements.

(b) Timber rail.  Add the following after the second paragraph:

Field drill holes in the steel backing on curved sections or where required to correspond to the field cut wood rails at joints.  Do not use a torch to cut holes.

Include the following subsection for all projects with guardrail terminals. Check with the maintaining agency to determine whether a specific terminal type (e.g., ET-2000, Best 350 or others) is required. If so, insert the specific terminal type/name in the blank. Write a justification in the project file for use of a proprietary terminal. If the maintaining agency does not have a preference, insert either FLARED or TANGENT in the blank. Determine the test level for the terminal type chosen and insert it in the blank (e.g., 2 or 3). Also include the appropriate drawings in the plans.

617.05  Terminal Sections.  Delete the third paragraph and substitute the following:

Use ________ terminals that meet Test Level __.  Submit drawings from the manufacturer for the terminals according to Subsection 104.03.