$$619.00A

Section 619.—FENCES, GATES, AND CATTLE GUARDS

Revised 8 May 2005

INCLUDE THE FOLLOWING FOR TEMPORARY FENCE

$$619.06A

619.06.  Delete the first paragraph and substitute the following:

When necessary, construct temporary fence to keep livestock, pedestrians and traffic off the road being constructed or away from trees requiring protection.  Temporary fence is intended to remain in place only during the construction of the project or until the fence is directed to be removed.  At the completion of the project, remove fence and dispose of legally off Government property.

619.06.  Add the following after the first paragraph:

Install fence as shown on the drawings or as directed by the CO.  Use a conventional metal "T" or "U" post spaced every 7 to 10 feet (2 to 3 meters).  Drive posts 12 to 18 inches (30 to 45 centimeters) into the ground.  Secure the fence to the post using 3 wire ties.