# UNDERGROUND OUTLET

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 620

### UNDERGROUND OUTLET

An underground outlet is a conduit installed beneath the surface of the ground to collect surface water and convey it to a suitable outlet.

### PRACTICE INFORMATION

The purpose of the practice is to dispose of excess water from structures such as terraces, diversions, and surface drains without causing damage by erosion or flooding. An underground outlet can be installed when a buried outlet is needed or when surface outlets are impractical because of stability problems, climatic conditions, land use, farmability, or equipment traffic.

The outlet must be sufficiently stable for all anticipated flow conditions and designed for the maximum anticipated water surface. Outlets should not be placed in areas of active erosion.

### COMMON ASSOCIATED PRACTICES

Underground Outlet is commonly used in a Conservation Management System with:

Filter Strip (393)

Diversion (362)

Surface Drainage, Field Ditch (607)

Surface Drainage, Main or Lateral (608)

Roof Runoff Structure (558)

Terrace (600)

Nutrient Management (590)

Pest Management (595)

For further information, refer to the practice standard in the local Field Office Technical Guide and associated practice specifications and job sheets.

# Text boxes

Roof Runoff Structure (558)

I.7 (+) Growing conditions for desired crop

Note: Effects are qualified with a plus (+) or minus (-).  These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

Surface Drainage, Field Ditch (607)

Terrace (600)

Diversion (362)

I.3 (+/-) Recreational opportunities

C.1 (+/-) Health of aquatic habitats;     (+/-) swimmable, fishable waters

I.10 (+/-) Net return to producer

Underground Outlet 4/2007

D.1 (+)

Water volume at outlet

Pest Management (595)

Nutrient Management (590)

Associated practice

Mitigating practice or measure

(+) increase; (-) decrease

I.9 (+) Potential income

Pathway

Start

I.4 (-) Runoff

(inlet site)

D.2 (-) Surplus

water at inlet

1. Dig trench and install conduit

C.  Cumulative effect

I.  Indirect effect

Underground Outlet

(620)

Critical Area Planting (342)

I.2 (+/-) Water quality

D.  Direct effect

#.  Created by practice

LEGEND

I.6 (-) Sediment

deposited offsite

2. Seed area, if necessary, to minimize erosion

Initial setting: Cropland or animal feeding operation where disposal of excess surface water from terraces, diversions, surface drains or other similar practices is needed and a surface outlet is impractical

C.2 (+/-) Income and income stability (individuals and community)

I.3 (+) Transport water-borne

contaminants

I.8 (+) Plant productivity

I.5 (-) Soil erosion

(inlet site)

D.3 (+) Cost for installation and maintenance

Stable outlet

Streambank and Shoreline Protection (580)

Critical Area Planting (342)

I.1 (+) Erosion potential downstream

I.6 (-) Maintenance of drainage ditches and other structures