96E03/29/06

S626-96E.doc

When plants, trees, shrubs, vines or groundcovers are required, include the following:

Section 626. - PLANTS, TREES, SHRUBS, VINES, AND GROUNDCOVERS

Construction Requirements

626.05  Protection and Temporary Storage.  Delete the text and substitute the following:

Package plants to provide protection against climate and breakage during transit.  When shipment is made by open vehicle, tie and cover plant materials to prevent wind damage and dehydration.  Spray evergreen and deciduous trees in leaf with an anti-transparent, according to the manufacturer's instructions.  When shipment is made by closed vehicle, carefully pack and adequately ventilate plants to prevent “sweating.”

Keep all plant material moist and exercise care to prevent damage to bark, branches, and root systems.  Replace all damaged plants including plants with cracked or crushed root balls.

Tag each plant delivered to the project with a weatherproof tag showing the plant name and date of delivery.

Protect plants delivered, but not scheduled for immediate planting, as follows:

- Open the bundles of bare root material, separate plants, and cover the roots in moist trenches.

- Cover the earth balls of balled and burlapped material with mulch or other suitable material and keep moist.

Install all plant material received on the project within 30 days.

626.06  Excavation for Plant Pits and Beds.  Delete the text of the first paragraph and substitute the following:

Submit planting locations and methods of planting to the CO for approval.  Mark planting locations with stakes or flagging.  Remove all sod, weeds, roots, and other unsuitable material from the planting site.  Excavate plant pits as follows:

Add the following after the last paragraph:

Do not leave any planting holes open overnight.

When vines and groundcovers are include in the contract, included the following:

(b) Depth of excavation.  Add the following:

(4) Vines and groundcovers.  Twice the depth of the pot.

When balled and burlapped stock may be provided, included the following: When vines and groundcovers are included in the contract, include the following:

626.07  Setting Plants.

(b) Balled and burlapped stock.  Add the following after the second sentence:

Score the root ball to a depth of 1 inch along the entire side equally on 4 sides.

When trees and shrubs with staking are required, include the following:

626.13  Plant Establishment Period.  Add the following:

At the end of the plant establishment period, remove all guys and stakes.