$$627.00A

Section 627.—SOD

Revised 8 May 2005

INCLUDE THE FOLLOWING.  SELECT ONE SOD TYPE OR INSERT TYPE REQUIRED.  ALSO $$713.10A OR B

$$627.03A

627.03.  Add the following:

$$627.03B

Furnish Bermuda grass or Tall Fescue, Kentucky 31 sod.

# INCLUDE THE FOLLOWING.  REVISE SOD SEASONS

$$627.03C

Lay sod between April 1 and September 30.

INCLUDE THE FOLLOWING

$$627.05A

627.05.  Delete the last sentence of the first paragraph and substitute the following:

Grade the finished surface of the sod bed to a smoothness comparable to results obtained by hand raking, leaving it clean and free of stones over 1 inch (2.5 centimeters)  in size, sticks, stumps, other debris and depressions that might interfere with proper placement or subsequent growth.

Apply fertilizer and agricultural limestone at the same rates specified in Section 625.

$$627.06A

627.06.  Add the following:

Thoroughly water the sod, immediately after installation, to a depth of 4 inches (10 centimeters).