##### Hazard Analysis

Work Plan Title: CDF / B0 LOW BETA SURVEY  (Collision Hall & Tunnel)

Date:  30 July, 2007

Prepared By:	 Gary W. Crutcher x3652 or pager (630) 218-4562) and

Craig A. Bradford x3653 or pager (630) 218-4702

Reviewed By:(optional)  Virgil Bocean x6297 or pager (630) 722-1374

Approved By (Supervisor/Task Manager):  Gary Coppola (Assistant AMG Group Leader)  x4687  or cell (630) 388-9869

Description of work:

As-found / As-set alignment surveys of low beta magnets and separators either side of CDF Collision Hall

Personal Protective Equipment:  (Check protective equipment required for the job.)

□ Safety glasses     □ Side shields	□ Chemical splash goggles

“X” Hearing Protection	“X” Hard Hats

□ 3.0 Braising goggles	□ Impact goggles

□ Face shield	□ Rubber apron

□ Leather gloves	□ Hot/Cold thermal protective gloves

□ Chemical resistant gloves (specify type):	□ Respirators

“X” Other required PPE (specify): 	“X” Fall protection equipment (specify):

###### Shipping blankets                                                        Harnesses, retractable lanyards

Equipment required for the job:

2ea. Brunson 76 Alignment scopes, 1ea. N3 Precision Level, 1ea. Stick-Mic Kit, 1ea. Dijak Bolt Kit, 6 foot starrett scale, Trivets / short tripods, 2ea. 8-10 Brunson Instrument Stands, 1ea. Lap-top computer w/ excel spreadsheets for (Q1>Q5 low beta quads and Separators, Lighting (i.e. 4 foot fluorescent light, and small hand lanterns.

Work Plan History Information:

Prior to starting any work Radiation Safety must have the survey ports unlocked the poly-bead bags removed, the fiducials uncovered on the Q3 and Q4 low beta quads, and the steel shielding stacked out of the way for the instrumentation.

# HAZARD ANALYSIS

| Step | Description | Hazards | Precautions / Safety Procedures |
| --- | --- | --- | --- |
| 1 | General | Multiple documents | This document ADDS to the work rules described in the “CDF Supervised Access Work Rules” regarding General Hazards in the CDF Collision Hall. See attached document. |
| 2 | Lift operation while maneuvering the lift inside of CDF | Collisions hazards (horizontal and vertical) | Be aware of your surroundings (i.e. fans, electrical cabling, walls, magnet cradles, waterlines, and people). Must have had lift training to operate all lifts in CDF. |
| 3 | Falling from lift, ladders, or the upper alcoves located on either side of the Collision Hall | Fall hazards | Harness and retractable lanyards are required for operation of lifts. Do not tie-off to points below you. Inspect the ladder before use to ensure there are no defects. Do not climb on the top 2 steps of step ladder (3 steps of extension ladder). Stabilize and hold the ladder in place (tie-off ladder or use a buddy to secure as necessary) while the Surveyor is measuring the point. All personnel must use a body harness and retractable lanyards when accessing the survey points from the ladder from higher than 6 feet. Must ware a harness while accessing the magnets suspended in the cradles, tie-offs are in place and mounted in the ceiling. If removing the alcove guardrails use harness and retractable lanyards. Make sure that all guardrails are replaced after equipment is set onto alcoves. |
| 4 | Trip over equipment, extension cords, or materials stored on floor | Tripping hazards | Walk cautiously and be aware of your surroundings. Clear work area of unnecessary items as needed. |
| 5 | Hearing damage caused by excessive noise, from machinery, water lines, and fans | Loud Noises hazard | Carry ear protection with you and use as needed. |
| 6 | Head Injuries | Material Falls hazard | Hard Hats must be worn on the floor level. |
| 7 | Back or muscle injury caused by lifting too much weight or improper lifting technique (carry survey equipment, move the ladder) | Back / Body Injury hazard | Use proper lifting technique, do not place your body in awkward positions while lifting. Utilize a buddy while lifting excessive weight moving ladders or heavy equipment. Keep the load close to your body, pivot your feet do not twist. Communicate with your partner so you are lifting and moving together |
| 8 | Exposure to hot or cold environments | Temperature Extremes hazard | Use shipping blankets to cover up exposed cryogenic piping to prevent freeze burn. “B” side of CDF (tunnel) requires ones body to be in very close proximity to the cryo-pipes. |
| 8 |  |  |  |
| 9 |  |  |  |
| 10 |  |  |  |

(Use additional pages as needed.)

My supervisor has reviewed this hazard analysis with me and I understand the hazards and required precautionary actions.  I will follow the requirements of this hazard analysis or notify my supervisor if I am unable to do so.  I understand that there are Environmental, Safety and Health Professionals on staff if I need further assistance or clarification.

| Name and ID (please print) | Signature | Date |
| --- | --- | --- |