$$633.00A

Section 633. — PERMANENT TRAFFIC CONTROL

Revised 10 December 2008

INCLUDE THE FOLLOWING FOR SIGN PANELS

$$633.01A

633.01.  Delete the second paragraph and substitute the following:

Sign panels are designated as plywood, aluminum, extruded aluminum, steel, plastic, or fiberglass reinforced plastic.

INCLUDE THE FOLLOWING FOR SIGNS ON NPS PROJECTS

$$633.03A

633.03.  Add the following after the first sentence:

Furnish signs also meeting the requirements of the National Park Service UniGuide Sign System Manual (see http://www.nps.gov/hfc/acquisition/uniguide.htm).

INCLUDE THE FOLLOWING FOR SIGNS AND/OR POSTS (AND INCLUDE $$633.03C AND/OR $$633.03D).  INCLUDE THE FOLLOWING IF $$633.03E IS USED.

$$633.03B

633.03.  Add the following:

INCLUDE THE FOLLOWING FOR SIGN PANELS IF A SPECIFIC SIGN PANEL MATERIAL IS REQUIRED — DELETE THE HIGHLIGHTED MATERIAL TYPES THAT ARE NOT ACCEPTABLE

$$633.03C

Furnish plywood, aluminum, extruded aluminum, steel, plastic, or fiberglass reinforced plastic sign panels.

INCLUDE THE FOLLOWING FOR POSTS IF A SPECIFIC POST MATERIAL IS REQUIRED — DELETE THE HIGHLIGHTED MATERIAL TYPES THAT ARE NOT ACCEPTABLE

$$633.03D

Furnish wood, aluminum, galvanized steel, or corrosion resistant steel posts.

INCLUDE THE FOLLOWING FOR SIGNS ON NPS PROJECTS

$$633.03E

Paint posts, sign supports, and sign panel backs and edges with Benjamin Moore, Moorgard, exterior latex low luster paint, Federal Standard 595B Color No. 20059 (brown), or approved equal.

INCLUDE THE FOLLOWING FOR SIGN PANELS

$$633.05A

633.05.  Add the following after the first sentence of the first paragraph:

For all legends on guide signs, use ASTM Type VIII, IX, X, or 3M DG3 retroreflective sheeting.