# JRG-41

## United Kingdom

ITU-R JRG 1A-1C-8B

Airborne radar systems.

##### Stephen Parry – NATS

23rd May 2005

### 1	Background

The work program of the JRG calls for specific studies to determine the characteristics of airborne radar systems. This document provides some information on the use of airborne weather radar and the annex contains characteristics of some 9 GHz airborne radar systems found in the UK. The information was collated for an earlier study published by the UK Radiocommunications Agency and which may be found at the following link (to a 6.5 MB file).

http://www.ofcom.org.uk/static/archive/ra/topics/research/topics/s-studies/civil-radio-systems.pdf

##### 2	Meteorological Radars Airborne (X-Band)

These types of radars are used in commercial and general aviation to detect weather phenomena such as storms and wind-sheer.  Some systems are also capable of interrogating Search And Rescue Transponders (SARTs) and RAdar beaCONs (RACONs).  General aviation pilots also use these systems for ground mapping to aid navigation.

The majority of installed systems are Magnetron based however solid state systems are now coming into service.  Of the Magnetron systems there are many system variants generally based on antenna size.

Airborne weather radar is intended to detect and display hazardous weather systems that present a potential danger to the aircraft. The types of weather systems that present the greatest potential danger are wind shear and microbursts, which frequently exist in thunderstorms.

Wind shear is a term given to two wind currents blowing at different speeds or directions close to each other. This can cause eddy currents and areas of extreme turbulence in the space between the two wind currents.

Microbursts are sudden violent downward air currents that occasionally exist beneath thunderstorms. They tend to exist close to the ground, where they pose maximum risk to aircraft on final approach. There have been many fatal accidents attributed to microbursts, one of the best documented being the Delta Airlines l-1011 that crashed at Dallas Fort Worth Airport in February 1985.

Figure 1 shows a typical display of an airborne weather radar, the weather targets are colour-coded by the intensity of the return. The display correlation to approximate rainfall is given in Table 1 below.

Table 1  Colour/rainfall correlation

| Colour | Echo strength | Rainfall rate |
| --- | --- | --- |
| Black | Very light or no returns | Less than 0.7 mm/hr. |
| Green | Light returns | 0.7 - 4 mm/hr |
| Yellow | Medium returns | 4 - 12 mm/hr. |
| Red | Strong returns | Greater than 12 mm/hr. |
| Magenta | Turbulence | N/a |

Figure 1  Airborne weather radar display

##### 3	Transmitter characteristics

Airborne weather radar transmitters operate at X-Band and may use either magnetron or solid state technology. Without exception airborne weather radar are forward looking systems. The antenna is usually of flat plate construction that is housed behind a radome on the nose of the aircraft. The antenna is fixed to a scanning mount that mechanically moves the antenna from side to side continuously.  The pilot also has the ability to adjust the elevation axis of the antenna.

Figure 2  Airborne weather radar antenna and mount.

##### 4	Interference considerations

An interfering RF source operating at a frequency close to the radar’s operating frequency can create unusual return displays on the cockpit display (see Figure 3.1.1-8 below). These returns will appear as a single wedge of radar return that extends from very close range (< 5 nm) out to maximum range for the selected range scale. The wedge will typically cover from 3 to 5 degrees in azimuth.

Figure 3  Airborne weather radar cockpit display in the presence of an interferer

These patterns are caused by CW sources of interference. Types of CW RF source that can cause this effect include:

military CW radar

radar jamming equipment

satellite uplink equipment

Adjusting the manual gain or the antenna tilt angle may help alleviate the effect of the interfering source but the effect will not completely disappear until the interfering source is no longer in the radar’s field of view.

Aircraft are more susceptible to bad weather during the approach phase of flight. This is the time when weather radar is needed most. In this phase of flight the aircraft has a nose-down pitch attitude and hence the weather radar antenna points towards the ground. Some systems automatically adjust the antenna pitch if ground clutter is detected.

The downward direction of the antenna makes the system most susceptible to ground based interference in the most critical phase of flight (i.e. during landing). Interference that degrades performance and hence masks potentially dangerous weather cannot be accepted.

5	Generic system characteristics

A survey was made of the radar models installed in the UK; the information from this survey was reduced to generic radar types based upon the radar role and operational frequency band. The parameters for these generic radar types/roles are discussed further in the source document.

The annex lists the parameters of airborne weather radar models/types identified as installed in the UK. The parameters listed have been derived from a variety of sources, each source having its own level of confidence. The main sources were:

Manufacturers published data;

Experience of similar Radar systems;

Assessment by experienced Radar Engineers.

Due to the varying levels of confidence that the data actually reflects the installed systems, the annex only identifies the systems by their role and a unique number.

Within the annex the following abbreviations are used:

N/A - (Not applicable) - means that the particular parameter is not applicable to this type of radar.

NDA (No data available) - means that no data is available for this particular parameter, although the parameter is thought to be applicable.

The characteristics are reproduced here for the use of the JRG in its work.

Annex

Key to tables

| Platform type (airborne, shipborne, ground) | Where the radar system is used; on land, at sea or in the air |
| --- | --- |
| Roles | The purpose for which the radar is installed |
| CHARACTERISTICS |  |
| Radar Band | The radar frequency band (L, S, C, Ku, or X) in which this type of radar operates |
| Tuning range (GHz) | The frequency range over which this radar can be used |
| Operational Frequencies | The number of discrete frequencies that any one radar uses |
| Specific operating frequency | The actual operational frequency(ies) where it is not installation specific |
| Modulation | The form of modulation applied to the radar transmitter pulses using the ITU Radio Regulation emission codes where applicable; most radars use an unmodulated pulse |
| Tx Power into Antenna (kW) | The peak power of the transmitter output pulse |
| Pulse width (µs) | The width of the pulse amplitude measured between the -3 dB points. Many radars use two or more pulse lengths |
| Pulse rise/Fall time (µs) | The rise and fall times of the transmitter output pulse measured between the 10% and 90% levels |
| Pulse repetition rate (Hz) | The pulse repetition rate of the radar. Some radars use a mixture of PRRs and others the PRR changes with the selected display range |
| Duty cycle (%) | The percentage of time that the transmitter is transmitting ( the mark/space ratio) |
| Chirp bandwidth (MHz) | The bandwidth of the FM modulation of the pulses used on some radar types |
| Phase-coded sub-pulse width | no radars of this type in civil use in the UK |
| Compression ratio | The ratio by which the receiver compresses the received pulses |
| RF emission bandwidth (-3 dB) (MHz) | The bandwidth of the transmitted pulses measured between the -3 dB points |
| RF emission bandwidth (-20 dB) (MHz) | The bandwidth of the transmitted pulses measured between the -20 dB points |
| RF emission bandwidth (-40 dB) (MHz) | The bandwidth of the transmitted pulses measured between the -40 dB points |
| Output device | The type of device used as the final output power amplifier in the transmitter |
| Antenna pattern type (pencil, fan, cosecant-squared, etc.) | The shape of the elevation beam produced by the radar antenna |
| Antenna type (reflector, phased array, slotted array, etc.) | The type of antenna fitted to the radar |
| Antenna horizontal beamwidth (degrees) | The azimuth beamwidth of the antenna measured between the -3 dB points |
| Antenna polarisation | Whether the antenna radiates horizontal, vertical or circularly polarised RF |
| Antenna mainbeam gain (dBi) | The gain of the antenna compared to an isotropic radiator measured on the peak of the beam |
| Antenna vertical beamwidth (degrees) | The elevation beamwidth of the antenna measured between the -3 dB points |
| Antenna horizontal scan rate (degrees/sec) | The rate at which the antenna beam rotates in the azimuth plane |
| Antenna horizontal scan type (continuous, random, 360 degrees, sector, etc.) | Whether the antenna rotates continuously or performs a scan pattern |
| Antenna vertical scan rate (degrees/sec) | The rate at which the antenna beam scans in the elevation plane |
| Antenna vertical scan type | Whether the antenna scans continuously or performs a scan pattern in the elevation plane (i.e. continuous, random, 360 degrees, sector, etc.) |
| Antenna sidelobe levels (1st SLs and remote SLs) (dB) | The level of the sidelobes with respect to the beam peak. Where only 1 figure is given, this can be taken to reflect both SLs. |
| Antenna height above ground or sea (m) | The height in metres that the electrical centre of the antenna is above ground (or sea) level |
| Receiver IF bandwidth (3 dB) (MHz) | The bandwidth of the radar receiver response measured at IF and between the -3 dB points |
| Receiver noise figure (dB) | The noise figure of the radar receiver |
| Minimum detectable signal (dBm) | The minimum signal that the radar receiver can detect in the presence of background noise and in a clutter free region |
| Receiver front-end 1 dB Gain Compression point. Power density at antenna (W/m2) | The power density into the radar antenna that causes the radar receiver to have a 1 dB gain compression |
| Receiver on-tune saturation level Power density at antenna (W/m2) | The power density into the radar antenna that causes the radar receiver to saturate |
| RF receiver 3 dB bandwidth (MHz) | The bandwidth of the radar front end receiver measured between the -3dB points |
| Proportion of time in use | The Proportion of time that the radar is normally in use |

|  | Airborne-1 | Airborne-2 | Airborne-3 |
| --- | --- | --- | --- |
| Platform type (airborne, shipborne, ground) | Airborne | Airborne | Airborne |
| Roles | Weather | Weather | Weather |
| CHARACTERISTICS |  |  |  |
| Radar Band | X | X | X |
| Tuning range (GHz) | 9.3 to 9.5 | 9.3 to 9.5 | 9.3 to 9.5 |
| Operational Frequencies | 1 | 1 | 1 |
| Specific operating frequency | 9.33 GHz | 9.33 GHz | 9.33 GHz |
| Modulation | P0N | P0N | P0N |
| Tx Power into Antenna (kW) | 0.145 | 0.035 | 0.035 |
| Pulse width (µs) | 1 to 20 | 1.8,2.4,4.8,9.6, 19.2,28.8 | 1.8,2.4,4.8,9.6, 19.2,28.8 |
| Pulse rise/Fall time (µs) | ( 0.02 | ( 0.02 | ( 0.02 |
| Pulse repetition rate (Hz) | 180 to 9000 | NDA | NDA |
| Duty cycle (%) | NDA | NDA | NDA |
| Chirp bandwidth (MHz) | N/A | N/A | N/A |
| Phase-coded sub-pulse width | N/A | N/A | N/A |
| Compression ratio | N/A | N/A | N/A |
| RF emission bandwidth (-3 dB) (MHz) | 0.05 to 1 | 0.035 to 0.55 1 | 0.035 to 0.55 1 |
| RF emission bandwidth (-20 dB) (MHz) | 0.32 to 6.4 1 | 0.30 to 6.4 1 | 0.30 to 6.4 1 |
| RF emission bandwidth (-40 dB) (MHz) | 3.2 to 53 1 | 3.2 to 54 1 | 3.2 to 54 1 |
| Output device | Solid state | Solid state | Solid state |
| Antenna pattern type (pencil, fan, cosecant-squared, etc.) | Pencil | Pencil | Pencil |
| Antenna type (reflector, phased array, slotted array, etc.) | Flat Plate | Flat Plate | Flat Plate |
| Antenna horizontal beamwidth (degrees) | 3.5 | 8 | 8 |
| Antenna polarisation | Pencil | Pencil | Pencil |
| Antenna mainbeam gain (dBi) | 34.4 | 26 | 26 |
| Antenna vertical beamwidth (degrees) | 3.5 | 8 | 8 |
| Antenna horizontal scan rate (degrees/sec) | NDA | 27 | 27 |
| Antenna horizontal scan type (continuous, random, 360 degrees, sector, etc.) | 60 degree Sector | 120 degree Sector | 120 or 60 degree Sector |
| Antenna vertical scan rate (degrees/sec) | N/A | N/A | N/A |
| Antenna vertical scan type | tilt range ± 15 degrees | tilt range ± 15 degrees | tilt range ± 15 degrees |
| Antenna sidelobe levels (1st SLs and remote SLs) (dB) | -31 dB | NDA | NDA |
| Antenna height above ground or sea (m) | N/A | N/A 2 | N/A 2 |
| Receiver IF bandwidth (3 dB) (MHz) | NDA | NDA | NDA |
| Receiver noise figure (dB) | 4dB | NDA | NDA |
| Minimum detectable signal (dBm) | -125 | NDA | NDA |
| Receiver front-end 1 dB Gain Compression point. Power density at antenna W/m2 | NDA | NDA | NDA |
| Receiver on-tune saturation level Power density at antenna W/m2 | NDA | NDA | NDA |
| RF receiver 3 dB bandwidth (MHz) | NDA | NDA | NDA |
| Proportion of time in use | NDA | NDA | NDA |

|  | Airborne-4 | Airborne-5 | Airborne-6 |
| --- | --- | --- | --- |
| Platform type (airborne, shipborne, ground) | Airborne | Airborne | Airborne |
| Roles | Weather | Weather | Weather |
| CHARACTERISTICS |  |  |  |
| Radar Band | X | X | X |
| Tuning range (GHz) | 9.3 to 9.5 | 9.3 to 9.5 | 9.3 to 9.5 |
| Operational Frequencies | 1 | 1 | 1 |
| Specific operating frequency | 9.33 GHz |  |  |
| Modulation | P0N | P0N | P0N |
| Tx Power into Antenna (kW) | 0.035 | 0.035 | 0.15 |
| Pulse width (µs) | 1.8,2.4,4.8,9.6, 19.2,28.8 | 1.8,2.4,4.8,9.6, 19.2,28.8 | 1 to 20 |
| Pulse rise/Fall time (µs) | ( 0.02 | ( 0.02 | ( 0.02 |
| Pulse repetition rate (Hz) | NDA | NDA | 180 to 9000 |
| Duty cycle (%) | NDA | NDA | 0.36 to 0.9 |
| Chirp bandwidth (MHz) | N/A | N/A | N/A |
| Phase-coded sub-pulse width | N/A | N/A | N/A |
| Compression ratio | N/A | N/A | N/A |
| RF emission bandwidth (-3 dB) (MHz) | 0.035 to 0.55 1 | 0.035 to 0.56 | 1 to 0.05 |
| RF emission bandwidth (-20 dB) (MHz) | 0.30 to 6.4 1 | 0.22 to 3.56 1 | 0.3 to 64 1 |
| RF emission bandwidth (-40 dB) (MHz) | 3.2 to 54 1 | 2.2 to 35.6 1 | 3.2 to 54 1 |
| Output device | Solid state | Solid state | Solid State |
| Antenna pattern type (pencil, fan, cosecant-squared, etc.) | Pencil | Pencil | Pencil |
| Antenna type (reflector, phased array, slotted array, etc.) | Flat Plate | Flat Plate, 18 inch | Flat Plate, 28 |
| Antenna horizontal beamwidth (degrees) | 7 | 6 | 3.5 |
| Antenna polarisation | Pencil | Pencil | Pencil |
| Antenna mainbeam gain (dBi) | 27 | 28 | 35 |
| Antenna vertical beamwidth (degrees) | 7 | 6 | 2.5 |
| Antenna horizontal scan rate (degrees/sec) | 27 | 27 | NDA |
| Antenna horizontal scan type (continuous, random, 360 degrees, sector, etc.) | 120 or 60 degree Sector | 120 or 60 degree Sector | NDA |
| Antenna vertical scan rate (degrees/sec) | N/A | N/A | N/A |
| Antenna vertical scan type | tilt range ± 15 degrees | tilt range ± 15 degrees | tilt range ± 15 degrees |
| Antenna sidelobe levels (1st SLs and remote SLs) (dB) | NDA | NDA | -30 dB |
| Antenna height above ground or sea (m) | N/A 2 | N/A 2 | N/A 2 |
| Receiver IF bandwidth (3 dB) (MHz) | NDA | NDA | NDA |
| Receiver noise figure (dB) | NDA | NDA | NDA |
| Minimum detectable signal (dBm) | NDA | NDA | NDA |
| Receiver front-end 1 dB Gain Compression point. Power density at antenna W/m2 | NDA | NDA | NDA |
| Receiver on-tune saturation level Power density at antenna W/m2 | NDA | NDA | NDA |
| RF receiver 3 dB bandwidth (MHz) | NDA | NDA | NDA |
| Proportion of time in use | NDA | NDA | NDA |

|  | Airborne-7 | Airborne-8 | Airborne-9 |
| --- | --- | --- | --- |
| Platform type (airborne, shipborne, ground) | Airborne | Airborne | Airborne |
| Roles | Weather | Weather | Weather |
| CHARACTERISTICS |  |  |  |
| Radar Band | X | X | X |
| Tuning range (GHz) | Fixed | Fixed | Fixed |
| Operational Frequencies | 1 | 1 | 1 |
| Specific operating frequency | 9.345 GHz | 9.345 GHz | 9.345 GHz |
| Modulation | P0N | P0N | P0N |
| Tx Power into Antenna (kW) | 10 nom, 12 max. | 12 max. | 3.5 |
| Pulse width (µs) | 1 or 2 | 1 or 2 | 1 or 2 |
| Pulse rise/Fall time (µs) | 0.015 | 0.015 | 0.015 |
| Pulse repetition rate (Hz) | NDA | NDA | NDA |
| Duty cycle (%) | NDA | NDA | NDA |
| Chirp bandwidth (MHz) | N/A | N/A | N/A |
| Phase-coded sub-pulse width | N/A | N/A | N/A |
| Compression ratio | N/A | N/A | N/A |
| RF emission bandwidth (-3 dB) (MHz) | 1 to 0.5 | 1 to 0.5 | 1 to 0.5 |
| RF emission bandwidth (-20 dB) (MHz) | ( 2.2 to 8 | ( 2 to 4 | ( 2.2 to 8 |
| RF emission bandwidth (-40 dB) (MHz) | ( 50 to 150 | ( 50 to 150 | ( 50 to 150 |
| Output device | Magnetron | Magnetron | Magnetron |
| Antenna pattern type (pencil, fan, cosecant-squared, etc.) | Pencil | Pencil | Pencil |
| Antenna type (reflector, phased array, slotted array, etc.) | Flat Plate Slotted array 12 inch dia. | Flat Plate Slotted array 12 or 18 inch dia. | Flat Plate slotted array 10 or 12 inch dia. |
| Antenna horizontal beamwidth (degrees) | NDA | NDA | NDA |
| Antenna polarisation | Horizontal | Horizontal | Horizontal |
| Antenna mainbeam gain (dBi) | NDA | NDA | NDA |
| Antenna vertical beamwidth (degrees) | NDA | NDA | NDA |
| Antenna horizontal scan rate (degrees/sec) | NDA | NDA | NDA |
| Antenna horizontal scan type (continuous, random, 360 degrees, sector, etc.) | 120 or 60 degree Sector | 120 or 60 degree Sector | 120 or 60 degree Sector |
| Antenna vertical scan rate (degrees/sec) | N/A | NDA | NDA |
| Antenna vertical scan type | tilt range ± 15 degrees | tilt range ± 15 degrees | tilt range ± 15 degrees |
| Antenna sidelobe levels (1st SLs and remote SLs) (dB) | -20, -25 | -20, -25 | -20, -25 |
| Antenna height above ground or sea (m) | N/A 2 | N/A 2 | N/A 2 |
| Receiver IF bandwidth (3 dB) (MHz) | NDA | NDA | NDA |
| Receiver noise figure (dB) | NDA | NDA | NDA |
| Minimum detectable signal (dBm) | NDA | NDA | NDA |
| Receiver front-end 1 dB Gain Compression point. Power density at antenna W/m2 | NDA | NDA | NDA |
| Receiver on-tune saturation level Power density at antenna W/m2 | NDA | NDA | NDA |
| RF receiver 3 dB bandwidth (MHz) | NDA | NDA | NDA |
| Proportion of time in use | NDA | NDA | NDA |

|  | Airborne-10 | Airborne-11 | Airborne-12 |
| --- | --- | --- | --- |
| Platform type (airborne, shipborne, ground) | Airborne | Airborne | Airborne |
| Roles | Surface mapping, Weather & Beacon | Weather & turbulence | Weather & turbulence |
| CHARACTERISTICS |  |  |  |
| Radar Band | X | X | X |
| Tuning range (GHz) | Fixed | Fixed | Fixed |
| Operational Frequencies | 1 | 1 | 1 |
| Specific operating frequency | 9.345 GHz | 9.345 GHz | 9.345 |
| Modulation | P0N | P0N | NDA |
| Tx Power into Antenna (kW) | 12 max. | 12 max. | 125 Watts |
| Pulse width (µs) | 1 or 2 | 1 or 2 | 1.5, 6, 18 |
| Pulse rise/Fall time (µs) | 0.015 | 0.015 | ( 0.02 |
| Pulse repetition rate (Hz) | NDA | NDA | 6000, 1600, 380 |
| Duty cycle (%) | NDA | NDA | 1 max |
| Chirp bandwidth (MHz) | N/A | N/A | NDA |
| Phase-coded sub-pulse width | N/A | N/A | N/A |
| Compression ratio | N/A | N/A | N/A |
| RF emission bandwidth (-3 dB) (MHz) | 1 to 0.5 | 1, 0.5 | 0.8, 0.17, 0.06 |
| RF emission bandwidth (-20 dB) (MHz) | ( 2.2 to 8 | ( 2.2 to 8 | 5.1, 1.1, 0.4 1 |
| RF emission bandwidth (-40 dB) (MHz) | ( 50 to 150 | ( 50 to 150 | 51.2, 10.7, 3.6 1 |
| Output device | Magnetron | Magnetron | Solid State |
| Antenna pattern type (pencil, fan, cosecant-squared, etc.) | Pencil | Pencil | Pencil |
| Antenna type (reflector, phased array, slotted array, etc.) | Flat Plate Slotted array 5 sizes, 10 to 24 inches | Flat Plate Slotted array 3 sizes 12, 18 & 24 inches | Flat Plate Slotted array 2 sizes 30 & 24 inches |
| Antenna horizontal beamwidth (degrees) | NDA | NDA | 2.9 & 3.6 |
| Antenna polarisation | Horizontal | Horizontal | Horizontal |
| Antenna mainbeam gain (dBi) | NDA | NDA | 35, 33 |
| Antenna vertical beamwidth (degrees) | NDA | NDA | 2.9, 3.6 |
| Antenna horizontal scan rate (degrees/sec) | NDA | NDA | 45, 38 |
| Antenna horizontal scan type (continuous, random, 360 degrees, sector, etc.) | NDA | NDA | Sector |
| Antenna vertical scan rate (degrees/sec) | NDA | NDA | 38 or 45 |
| Antenna vertical scan type | tilt range ± 15 degrees | tilt range ± 15 degrees | tilt range ± 15 degrees |
| Antenna sidelobe levels (1st SLs and remote SLs) (dB) | NDA | NDA | NDA |
| Antenna height above ground or sea (m) | N/A 2 | N/A 2 | N/A 2 |
| Receiver IF bandwidth (3 dB) (MHz) | NDA | NDA | NDA |
| Receiver noise figure (dB) | NDA | NDA | NDA |
| Minimum detectable signal (dBm) | NDA | NDA | NDA |
| Receiver front-end 1 dB Gain Compression point. Power density at antenna W/m2 | NDA | NDA | NDA |
| Receiver on-tune saturation level Power density at antenna W/m2 | NDA | NDA | NDA |
| RF receiver 3 dB bandwidth (MHz) | NDA | NDA | NDA |
| Proportion of time in use | NDA | NDA | NDA |

--------------------------------

# Footnotes

Estimated from pulse shape

Many aircraft use their weather radar on landing