| NRCS Natural Resources Conservation Service | MANURE TRANSFER Conservation Practice Job Sheet 634 |
| --- | --- |
| New Mexico February 2005 |
| Client: |  | Tract: |  | Farm No. |  | Field No.: |  |
| Farm/Ranch Location: |  | County: |  | Acre(s): |  | Date: |  |
| Program: |  | Contract No: |  | Planned Installation Date: |  |
| Drawing No.: |  | Item No.: |  |  |
| Definition: |

A manure conveyance system using structures, conduits, or equipment.

Purpose:

To transfer animal manure (bedding material, spilled seed, process and wash water, and other residue associated with animal production may be included) through a hopper or reception pit, a pump (if applicable) and a conduit.  This transfer could be from collection to storage, treatment, or utilization areas.

Requirements:

- CONSTRUCTION SHALL NOT COMMENCE PRIOR TO THE ISSUANCE OF A DESIGN ACCEPTANCE LETTER ISSUED BY THE NRCS.  (See §NM521.01 of the National Engineering Manual.)

- It shall be the responsibility of the owner / lessee to obtain all necessary permits and/or rights, and to comply with all ordinances and laws pertaining to this installation.

- On Federal, State, or Tribal lands, or when federal funding is involved on private land, the landowner / lessee must have archaeological clearance and approval / permit from the responsible permitting agency prior to any construction.  If during installation, any cultural resources, historical resources, threatened or endangered species are found, the landowner / lessee must cease operations and obtain archaeological clearance and approval / permit from the responsible permitting agency prior to continuing construction.

- In designing a manure transfer system, in addition to Conservation Practice Standard 634, refer to Conservation Practice Standards 313,  359, 382, 428A, 430, 442, 533, 590, and 633.  The National Engineering Handbook, Part 651, and the Agricultural Waste Management Field Handbook shall be used as needed.  In addition refer to §NM521 of the National Engineering Manual.

- Supporting data for this practice shall include a record of planning, design, installation, checking, and maintenance necessary to ensure an effective practice.

- Installation shall be in accordance with the drawings, specifications, and special requirements.

Practice Classification and Approval (NEM Section 501):

A Job Class for this practice has not been established.

Engineer Certification:

A registered professional engineer shall certify that the design has been prepared in accordance with Practice Standard 634, the Statement of Work for Practice Standard 634, and any other applicable practice standards necessary to complete the design.

For designs prepared by NRCS personnel:

Design Approved by SCE: 					  New Mexico PE License No.:  				  Date:

For designs prepared by other than NRCS personnel:

Designed by:  								  New Mexico PE License No.: 				  Date:

Accepted by SCE for NRCS: 							  Date:

Landowner/Operator Acknowledgement and Acceptance:

The landowner/operator acknowledges that:

- They have received a copy of the construction drawings and specifications, and understands the contents and requirements and,

- Maintenance of the installed work is necessary for proper performance for the life of the practice.  All federal cost shared practices must be maintained to these specifications for the expected life of the practice.

Accepted by: ____________________________________ Date: _____________________

Landowner/Operator

Practice Completion:

I have made an on-site inspection (or I am accepting owner/contractor documentation located in the case file), and have determined that the job, as installed, conforms to the drawings and specifications.

Accepted by: _____________________________ Job Title: ___________________ Date: ____________

Authorized NRCS Representative