03M09/22/06

S634-03M.doc

Use on projects as appropriate.

Section 634. - PERMANENT PAVEMENT MARKINGS

Construction Requirements

634.03 General.  Delete the last sentence of the first paragraph and substitute the following:

For all 4R projects add the following paragraph (also include detail CM634-50 and SCR for Section 401, 402, or 403):

For simple curve widening locations (widening only on one side) shift the centerline striping location such that the centerline stripe is midway between the normal edge of shoulders.  The shift from the staked centerline will be towards the widened lane one-half the total curve widening specified for the given station as shown in the plans.

OR For all 3R projects add the following paragraph to the above paragraph (make sure 152.03(n) is included or change reference and SCR for Section 401, 402, or 403):

Place the centerline stripe along the existing striped centerline, as recorded under Subsection 152.03(n).

Use on all projects, unless the maintaining agency has requested a specific material type.

Add the following:

The Contractor may use, upon approval, permanent pavement marking materials and layouts meeting current state approved standards that are practiced in the region of the project in lieu of contract requirements, if the state standards meet the requirements of the MUTCD.  The material substituted must be equivalent to that required in the specifications.  Obtain the CO’s approval before incorporating into the work.  When requesting approval, furnish to the CO the applicable state standards (specifications and drawings), manufacturer’s name and address, supplier’s certification indicating material is produced to state approved specifications, pricing data showing cost difference for labor and materials, and any other available information describing application and performance.  When directed, submit samples for approval at the Contractor’s expense.  Within 14 days, the CO will inform the Contractor as to the acceptance of the request.  The unit price for the contract item(s) will be reduced to reflect any cost savings.