96E03/29/06

S638-96E.doc

When rock bolts are required, include 722.03 and the following:

Section 638. - ROCK BOLTS

Description

638.01  This work consists of furnishing and installing rock bolts.

Material

638.02  Conform to the following Sections and Subsections:

Grout	725.22 (a)

Rock Bolts	722.03

Construction Requirements

638.03 Submittal.  At least 14 days before the installation of rock bolts, submit the following information:

(a) Evidence that the foreman has a minimum of 1500 hours and the drill operator has a minimum of 1000 hours of satisfactory work in similar installation of post-tensioned rock bolts.

(b) Construction sequence and schedule.

(c) Drilling methods and type of equipment.

(d) Proposed rock bolt, couplers, bearing plate, anchor unit, flat washer, and beveled washer specifications including manufacture's data sheets.

(e) If using resin adhesives, include manufacturer's data sheets and placement procedures.

(f) Proposed grout mix design.

(g) Calibration data for each torque wrench to be used.  Submit results of calibration tests performed by an independent testing laboratory within the last 60 days.

Allow 7 days for acceptance or rejection.  Do not begin work until submittals have been approved.

638.04  Rock Bolt.  Size the bolt so the design load does not exceed 60 percent of the minimum guaranteed ultimate tensile strength of the bolt.  Select and fabricate bolts to carry the specified loads.

638.05  Handling and Storage.  Protect bolts from dirt, mud, water, and other harmful substances  to avoid damage and corrosion.  Do not use rock bolts that are heavily corroded, pitted, damaged due to welding, or show signs of abrasions, cuts, or nicks.

638.06  Installation.  Drill holes at locations and depths shown in the plans or directed by the CO.  Drill rock bolt holes to the diameter specified by the bolt manufacturer and to a depth that will allow 12 inches of open hole beyond the end of the specified rock bolt.  Clean holes of all drill cuttings, sludge, and debris before the rock bolt is inserted or grout is injected into the hole.  Drill holes for rock bolts normal to the rock surface unless otherwise specified by the plans or the CO.

Couple only grouted bolts.  Couple sections together when standard, commercially available lengths are exceeded.  Provide a center stop for connecting sections so that an equal length of thread connects each section.  Provide couplings that equal the manufacturers guaranteed ultimate strength for the rock bolt.  Do not fabricate couplings in a manner that interferes with the flow of grout.

Insert bolt into the hole with the end of the bolt positioned approximately 12 inches from the bottom of the hole. Attach the bearing plate, washer, and nut to the bolt with the threaded outer end of the bolt projecting beyond the nut at least 2 inches.

For grout-anchored bolts, inject sufficient grout into the drill hole to fill the bond zone around the bolt. For mechanically anchored, hollow stem rock bolts, inject grout through the hollow core of the bolt or through a grout tube until the space between the bolt and drill hole wall is filled and grout is forced out of the de-airing tube at the face of the hole. Apply tension to bolt after the time specified in Table 638-1.

Table 638-1

Grout Curing Time

| Cement Type | Curing Time (Days) |
| --- | --- |
| I | 5 |
| II | 5 |
| III | 3 |

For bolts anchored with polyester resin, use fast setting polyester resin cartridges in the bond zone and slow setting polyester resin cartridges in the no load zone with gel times consistent with rapid installation. Select cartridge diameters in accordance with the manufacturer's recommendations to ensure complete encapsulation of the rock bolt and satisfactory in-hole mixing.  Break and mix resin cartridges by spinning the bolt as it is inserted into the drill hole according to the manufacturer's instructions.

638.07  Tensioning.  Apply tension to the bolt with a calibrated torque wrench to 100 percent of the design load.

Tension polyester resin anchored bolts immediately after the fast-set resin in the distal bond zone has set up and before the slow-set resin in the unbonded zone has set up.

Tension grouted bolts after the bonded length has been grouted and the grout has set up but before the unbonded length is grouted.

Tension mechanically anchored rock bolts immediately after insertion into the drill hole according to the manufacturer's recommendations and the approved rock bolting plan.  Upon tensioning, lock bolt off at the specified lock-off load.

Allow the bolt to remain in place if:

- The bolt can be tensioned to the design load.

- The design load is maintained after final grouting has been accomplished.

Replace any bolt that does not meet (a) or (b) in a manner and in a location approved by the CO.

638.08  Acceptance.  Material for rock bolts will be evaluated under Subsections 106.02 and 106.03.

Installation of rock bolts will be evaluated under Subsections 106.02 and 106.04.

Measurement

638.09  Measure rock bolts by the foot or by the each.

Payment

638.10  The accepted quantities, measured as provided above, will be paid at the contract price per unit of measurement for the pay item listed below that are shown in the bid schedule. Payment will be full compensation for the work prescribed in this Section. See Subsection 109.05.

Payment will be made under:

Pay Item	Pay Unit

63801	Rock bolt	Foot

63802	Rock bolt	Each