| NRCS Natural Resources Conservation Service | WATER & SEDIMENT CONTROL BASIN Conservation Practice Job Sheet 638 |
| --- | --- |
| April 2003 |
| Client: |  | Tract: |  | Farm No. |  | Field No.: |  |
| Farm/Ranch Location: |  | County: |  | Acre(s): |  | Date: | 4/9/03 |
| Program: |  | Contract Item #: |  | Planned Installation Date: |  |
| Drawing No.:NM-E- |  |
| Definition: |

An earth embankment or a combination ridge and channel generally constructed across the slope and minor water courses to form a sediment trap and water detention basin.

Purpose:

To improve farmability of sloping land; reduce watercourse and gully erosion; trap sediment; reduce and manage onsite and downstream runoff; and improve downstream water quality.

Requirements:

- CONSTRUCTION SHALL NOT COMMENCE UNTIL THE DESIGN IS APPROVED BY THE APPROPRIATE NRCS REPRESENTATIVE.

- It shall be the responsibility of the owner / leasee to obtain all necessary permits and/or rights, and to comply with all ordinances and laws pertaining to this installation.

- On Federal, State, or Tribal lands, or when Federal funding is involved on private land, the landowner / lessee must have archaeological clearance and approval / permit from the responsible permitting agency prior to any construction.  If during installation, any cultural resources, historical resources, or threatened / endangered species are found, the landowner / lessee must cease operations and obtain archaeological clearance and approval / permit from the responsible permitting agency prior to continuing construction.

- NRCS assumes no responsibility for interference with private or public utilities or facilities.

- Supporting data for this practice are to include a record of planning, design, installation, checking, and maintenance necessary to ensure an effective practice.  Location identification is required.

- Installation shall be in accordance with the drawings, specifications, and special requirements.

- The following additional data is required as applicable: Profile and cross sections of embankment and channel, yardage computations, clearing, adequacy of vegetation, and fencing.

- NM-ENG-121, 127, 143, 184, and 242 can be used to assist in system design.

Practice Classification and Approval (NEM Section 501):

Job Class is based upon the following limiting element from Practice Specification 638:

| Job Class |
| --- |
| Height of Fill | ______ Feet |  |
| Drainage Area | ______ Acres |  |

Design Approved By: ___________________________________ Date: ____________________________

Authorized Designer

Landowner/Operator Acknowledgement and Acceptance:

The landowner/operator acknowledges that:

- They have received a copy of the approved construction drawings and specifications, and understand the contents and requirements, and

- Maintenance of the installed work is necessary for proper performance for the life of the practice.  All federal cost shared practices must be maintained to these specifications for the expected life of the practice.

Accepted by: ____________________________________; Date: _____________________

Landowner/Operator

Practice Completion:

I have made an on-site inspection (or I am accepting owner/contractor documentation located in the case file).  	  I have determined that the job, as installed, conforms to the drawings and specifications, and that _______Each Water and Sediment Control Basin (s), was (were) installed according to Specification 638.

Accepted by: _____________________________; Job Title: ___________________; Date: ____________

Authorized NRCS Representative