Study Title

Percent Crop Treated Refinement and its Impact on the Acute Drinking Water

Dietary Assessment for Carbofuran

Data Requirement

Not Applicable

Author

Robert T. Morris, Ph.D.

Study Completion Date

November 10, 2005

Performing Laboratory/Testing Facility

FMC Corporation

Agricultural Products Group

P.O. Box 8

Princeton, NJ 08543

(609) 951-3000

Sponsor

FMC Corporation

Agricultural Products Group

1735 Market Street

Philadelphia, PA 19103

(215) 299-6436

Report Number

P-3790

© 2005 FMC Corporation

All rights reserved

# STATEMENT OF NO DATA CONFIDENTIALITY CLAIMS

No claim of confidentiality is made for any information contained in this study on the basis of its falling within the scope of FIFRA §10 (d) (1) (A), (B), or (C).

Company:	FMC Corporation

____________________________	__________________________

Donald Carlson, Ph.D.		Date

Manager, Product Registrations

COMPANY AGENT

# GOOD LABORATORY PRACTICE COMPLIANCE STATEMENT

The following risk assessment is not required to follow Good Laboratory Practice Standards (GLPS) set forth in Title 40, Part 160 of the Code of Federal Regulations (CFR) of the United States of America.  Multiple studies used as references for this document were conducted in accordance with the appropriate GLP standards as verified by the GLP compliance statements found in those study reports.

____________________________________	_________________________

Robert T. Morris, Ph.D.	Date

Research Risk Assessment Specialist

AUTHOR

____________________________________	__________________________

Donald B. Carlson, Ph.D.	Date

Manager, Product Registrations

SPONSOR/ SUBMITTER

# ABBREVIATIONS AND SYMBOLS

| Abbreviation | Definition |
| --- | --- |
| A | acre |
| ai | active ingredient |
| EFED | Environmental Fate and Effects Division |
| EXAMS | EXposure Analysis Modeling System |
| FIRST | FQPA Index Reservoir Screening Tool |
| HED | Health Effects Division |
| kg | kilogram(s) |
| L | liter(s) |
| lb | pound |
| MRID | Master Record Identification |
| n | number |
| NA | not applicable |
| ND | not detectable |
| OPPTS | Office of Prevention, Pesticides and Toxic Substances |
| PCA | Percent Cropped Area |
| PCT | Percent Crop Treated |
| ppb | parts per billion |
| ppm | parts per million |
| PRZM | Pesticide Root Zone Model |
| RED | Reregistration Eligibility Decision |
| USDA | United States Department of Agriculture |
| USEPA | United States Environmental Protection Agency |
| USGS | United States Geological Survey |
| WARP | Watershed Area Regressions for Pesticides |

# TABLE OF CONTENTS

STATEMENT OF NO DATA CONFIDENTIALITY CLAIMS	2

GOOD LABORATORY PRACTICE COMPLIANCE STATEMENT	3

ABBREVIATIONS AND SYMBOLS	4

TABLE OF CONTENTS	5

1.0	EXECUTIVE SUMMARY	6

2.0	INTRODUCTION	7

3.0	EXPOSURE ASSESSMENT AND REFINEMENTS	7

3.1	Estimation of Surface Water Exposure	8

3.2	Percent Crop Treated Refinement	8

4.0	RESULTS	9

4.1	Comparison to WARP Data	9

4.2	Comparison to USGS Reservoir Monitoring Data	10

6.0	REFERENCES	12

TABLES	13

Table 1 – Chemical Input Parameters for Carbofuran	13

Table 2 -  Estimated Peak Surface Drinking Water Concentrations for a Single 1 lb ai/A application of Carbofuran Using the FIRST Model	13

APPENDIX 1 - FIRST Output Files for a Single 1 lb ai/A application to Corn or PA Alfalfa	14

APPENDIX 2 - FIRST Ouput Files for a Single 1 lb ai/A application to CA alfalfa	16

APPENDIX 3 - FIRST Output Files for a Single 1 lb ai/A application to TX Sorghum	18

APPENDIX 4 - FIRST Output Files for a Single 1 lb ai/A application to Cotton Nationwide	20

APPENDIX 5 - FIRST Output Files for a Single 1 lb ai/A application to ME Potato	22

Aerial Application	22

APPENDIX 6 - FIRST Output Files for a Single 1 lb ai/A application to ID Potato	24

# 1.0	EXECUTIVE SUMMARY

FMC Corporation is providing additional information to the US EPA (United States Environmental Protection Agency) to outline a more realistic estimation of surface water concentrations resulting from agricultural uses of carbofuran.  Both the PCT (percent crop treated) approach in this assessment and the WARP (Watershed Area Regression for Pesticides) approach from a previous assessment incorporate usage data in modeling predictions.  In this report, the recent EPA dietary exposure data was used to closely match internal sales data used in the recent carbofuran WARP assessment.

The PCT approach using FIRST modeling was performed to reflect a single application at 1 lb ai/A (pound active ingredient per acre) using aerial, ground and in-furrow application techniques.  A single 1 lb treatment was simulated on corn, alfalfa, cotton, sorghum, and potatoes.  The purpose of this simulation was to allow comparison between existing WARP and PRZM (Pesticide Root Zone Model)/EXAMS (EXposure Analysis Modeling System) modeling estimates.  To facilitate this comparison, a uniform 1 lb ai/A rate was utilized, although carbofuran label rates below and above 1 lb ai/A exists.  The average PCT figures from the 2005 HED chapter for the five cropping scenarios were utilized.  Nationwide and regional PCA (percent crop area) adjustments from the current drinking water HED assessment were included in the evaluation.

Under the PCT approach, estimated carbofuran surface water concentrations from aerial, ground and in-furrow applications for the single 1 lb treatments were as follows (Table A):

Table A – Estimated Carbofuran Surface Water Concentrations from Aerial, Ground and In-furrow Applications for the Single 1 lb Treatments

| Crop | PCA Adjustment (%) | PCT Average (%) | Estimated Surface Water Concentration from Aerial/Ground Applications (ppb) | Estimated Surface Water Concentration from In-furrow Applications (ppb) |
| --- | --- | --- | --- | --- |
| corn | 46 | <1 | 0.5 | 0.3 |
| alfalfa | 46 to 56 | <1 | 0.5 to 0.6 | 0.3 to 0.4 |
| sorghum | 67 | <1 | 0.7 | 0.5 |
| cotton | 20 | 5 | 2.5 | 0.5 |
| potatoes | 14 to 63 | 10 | 5.0 | 1.0 to 4.0 |

The results of the PCT approach are conservative and protective when compared directly to the results from the USGS (United States Geological Survey)/USEPA Reservoir Monitoring Study performed in 1999-2000 and closely resemble the maximum 90th percent value of 0.37 ppb from a recent WARP assessment.

Incorporation of additional factors into PCT approach allows for a conservative yet more refined prediction of surface water concentrations in reservoirs used for drinking water.  Incorporating these factors into the PCT approach using FIRST modeling provided outputs comparable to those from WARP; a model that incorporates usage intensity.

This assessment provides additional evidence that the actual concentrations expected in drinking water reservoirs are far below the concentrations predicted by recent EPA modeling.  Hence, the results of this assessment are more suitable for use in a dietary assessment for carbofuran.

# INTRODUCTION

FMC Corporation has provided previous comments to EFED stating that the Tier II model PRZM/EXAMS over estimates potential carbofuran surface water concentrations when output values are compared to the wealth of monitoring data that is available (Reference 1).  Tier II surface water modeling outputs from Texas sorghum and Illinois corn scenarios were used by the EPA for the acute human dietary assessment (Reference 2).

In this current assessment, drinking water refinements are presented to the EPA as an alternative approach for the more realistic (but still conservative) estimation of surface water concentrations.  The PCT approach incorporates average usage data as an input to the Tier I screening level runoff prediction tool within the FIRST model, to estimate surface water concentrations.  Incorporation of usage data result in a more realistic and more refined exposure assessment.  The PCT approach is considered to be complementary to WARP since both approaches allow correction for the relatively small amount of carbofuran applied on an annual basis.

PCT type approaches have been discussed in previous scientific forums.  It was recommended by the majority of the members of the May 1999 FIFRA (Federal Insecticide Fungicide Rodenticide Act) SAP (Scientific Advisory Panel) meeting suggested that EPA incorporate PCT in future model refinements, especially for the assessment of lower market share compounds (e.g. carbofuran) (Reference 3).

# 3.0	EXPOSURE ASSESSMENT AND REFINEMENTS

The Tier I FIRST Model uses the following information for a screening level prediction:

- Basic chemical parameters consisting of Koc, water solubility, soil aerobic metabolism half-life, aerobic aquatic half-life, and photolysis half-life from the current HED Chapter.

- Average usage data and percent crop areas from the current carbofuran HED RED chapter.  The two parameters are simply multiplied together for input into the model.  In the case of less than <1% average, 0.9% or 0.009 as a decimal fraction was used as the value prior to multiplying by the PCA (Percent Cropped Area).  For example, a calculation for corn would be as follows:

0.009 (corn treated usage data) x  0.46 (national PCA) =  0.004

## 3.1	Estimation of Surface Water Exposure

FIRST Version 1.0 (May 16, 2001) (Reference 4) was used to predict untreated water concentrations.  Five different crops consisting of corn, alfalfa, cotton, sorghum, and potato were simulated using EPA chemical input values.  For modeling simulations, a single 1 lb ai/A treatment was applied by either aerial, ground, or in-furrow (2 inch depth incorporation) techniques.  The chemical input values are provided in Table 1.

The PCA assumption was included in the modeling (Reference 2).  A PCA is the largest percent of a watershed covered by a single crop either nationally, by region, or by a state.  National default factors used by the EPA are 46% for corn and 20% for cotton.  Regional default factors include 46% for PA alfalfa, 56% for CA alfalfa, 14% for ME potatoes, 63% for ID potatoes, and 67% for TX sorghum. The PCA adjustment applied is included in Table 2.

## Percent Crop Treated Refinement

The PCT approach used values that were selected from screening level usage data presented in the Dietary carbofuran RED Chapter (Reference 5).  An average value rather than a maximum value from EPA sources was selected for direct comparison to average FMC internal usage data for the state of IL previously included in a recent WARP assessment as a confidential business attachment (Reference 6).

# 4.0	RESULTS

Estimated carbofuran surface water concentrations arising from aerial or ground applications for single 1 lb treatments were as follows and included in Table 2.

Table B – Estimated Carbofuran Surface Water Concentrations from Aerial, Ground and In-furrow Applications for the Single 1 lb Treatments and Output File Locations.

| Crop | PCA Adjustment (%) | PCT Average (%) | Estimated Surface Water Concentration from Aerial/Ground Applications (ppb) | Estimated Surface Water Concentration from In-furrow Applications (ppb) | Location of Output/ Results In Appendix Number |
| --- | --- | --- | --- | --- | --- |
| corn | 46 | <1 | 0.5 | 0.3 | 1 |
| alfalfa | 46 to 56 | <1 | 0.5 to 0.6 | 0.3 to 0.4 | PA in 1 & CA in 2 |
| sorghum | 67 | <1 | 0.7 | 0.5 | 3 |
| cotton | 20 | 5 | 2.5 | 0.5 | 4 |
| potatoes | 14 to 63 | 10 | 5.0 | 1.0 to 4.0 | ME in 5 & ID in 6 |

Location of output files appear in the Table B above.

## 4.1	Comparison to WARP Data

The results of the PCT approach are similar to those from a recently completed FMC WARP assessment for IL (Reference 6).  The results from both assessments are considerably lower than those PRZM/EXAMS results in the 2005 EPA RED.

The modified FIRST outputs were compared to WARP as a validation of the technique. The maximum WARP 90th percentile value from IL is 0.37 ppb while the most refined PCT values with less than 1% average PCT range per corn from 0.3 ppb for an in-furrow application to 0.5 ppb for aerial and ground applications.

The comparison of techniques within the state of IL is reasonable since:

- The screening model FIRST was developed using data collected on the Shipman Reservoir in IL

- Predominant carbofuran usage is on corn in IL at the rates simulated

WARP model uses compound usage data and available monitoring data to predict the concentration of that compound within unmonitored streams.  The accuracy of the overall prediction is based upon the accuracy of usage data within a given watershed and the strength of the evidence that the monitoring data is reflective of the given stream that it represents.  For carbofuran, usage data at the county level is available through Doanes and FMC while extensive stream monitoring data is available through the USGS NAWQA program.

## Comparison to USGS Reservoir Monitoring Data

The results of this analysis and WARP are conservative and protective when compared directly to results from the USGS Reservoir Monitoring Study performed in 1999-2000 (Reference 7).

Twelve reservoirs and community water systems of various sizes in twelve different states (CA, IN, LA, MO, NY, NC, OH, OK, PA, SC, SD, and TX) were sampled to provide information on pesticide concentrations in drinking water and to assist in the implementation of the Food Quality Protection Act of 1996.

Samples of water were collected quarterly throughout the year and at weekly or bi-weekly intervals following the primary pesticide application periods.  According to the study abstract, drinking-water utilities that withdrew from reservoirs were sampled because reservoirs are vulnerable to pesticide contamination; integrate pesticide loading from their watersheds, and show smaller temporal variations than streams.

Only 5 carbofuran detections (< 1%) were reported out of 551 samples collected in the study.  The maximum concentration of carbofuran detected was only 0.050 ppb with the 95th percentile value below the reporting limit of 0.003 ppb.  In other words, single highest actual, monitored carbofuran concentration in surface water is one to two orders of magnitude lower than the concentrations modeled above, further demonstrating that the methodology employed above is amply conservative and unlikely to understate actual concentrations that might be observed in the environment.

5.0	CONCLUSIONS

The PCT modeling approach (i.e. corn) provides modeling estimates that are comparable to a WARP assessment previously performed by FMC for the state of IL.  Both PCT and WARP illustrate the importance of usage intensity and typical application patterns in estimating drinking water concentrations for surface water sources.

The surface water modeling results from both the PCT and WARP approaches are significantly lower than the results generated by the EPA using PRZM/EXAMS.  In addition, the results from PCT and WARP are conservative and protective when compared to results obtained in the USGS/EPA Reservoir Monitoring Study of 1999-2000.  A weight of evidence view of available information indicates that concentrations predicted in this assessment are more reflective of actual concentrations observed in the environment.  Hence, the results of this assessment (0.37 ppb) are more suitable for use in a dietary assessment for carbofuran.

# 6.0	REFERENCES

1.  	Morris, R., Nissen-Meyer S., Glazer- McCoy, E. and Mitchell, G.  “FMC Response Commments to OPP-2005-0162 the EPA June 3, 2005 RED” EPA Public Docket no. OPP-2005-0162-011 dated as June 3, 2005, FMC Corporation, Philadelphia, PA, August 23, 2005.

2.	Young, Dirk F.  “Drinking Water Estimated Concentrations” ,Located on EPA Public Docket as OPP-2005-0162-0033”, USEPA, Jan. 27, 2005

3.	EPA “THE AGENCY’S RESPONSES TO PUBLIC COMMENTS ON THE DRAFT FQPA SCIENCE POLICY DOCUMENT” on “Estimating the Drinking Water Component of a Dietary Exposure Assessment” October 19, 1999

4.	FQPA INDEX RESERVOIR SCREENING TOOL (FIRST) Version 1.0, Environmental Fates and Effects Division, Office of Pesticide Programs, U.S. Environmental Protection Agency, August 1, 2001.

5.	Stanton, S. “Revised Carbofuran Acute Probabilistic and Chronic Dietary Exposure Assessments for the Reregistration Eligibility Decision”, Office of Pesticide Programs, U.S. Environmental Protection Agency, September 1, 2005.

6. 	Trask J. and Amos, J. “Watershed Regressions for Pesticides (WARP) Model Estimates for Carbofuran in Illinois Watersheds” Located on EPA Public Docket as OPP-2005-0162-018 dated as August 15, 2005, FMC Corporation, Philadelphia, PA.

7.	Blomquist, J. (USGS) and Denis, J. (USGS) Cowles, J. (USEPA), Hetrick, J. (USEPA), Jones, R.(USEPA), and Birchfield, N. (USEPA) “Pesticides in Selected Water-Supply Reservoirs and Finished Drinking Water, 1999-2000:  Summary of Results from a Pilot Monitoring Program,”Open File Report 01-456, Baltimore, MD, 2001.

# TABLES

# Table 1 – Chemical Input Parameters for Carbofuran

| Parameter | Input Value | Reference |
| --- | --- | --- |
| Koc (mL/g) | 30 | 2 |
| Aerobic soil metabolism half-life (days) | 321 | 2 |
| Aerobic aquatic metabolism half-life (days) | 642 | 2 |
| Water solubility (mg/L) | 700 | 2 |
| Aqueous photolysis half-life (days) | 6 | 2 |

# Table 2 -  Estimated Peak Surface Drinking Water Concentrations for a Single 1 lb ai/A application of Carbofuran Using the FIRST Model

| Crop | Application Rate (lb ai/A) | Number of Applications | PCA Adjustment | PCT Adjustment | Application Pattern | Estimated Concentration (ppb) |
| --- | --- | --- | --- | --- | --- | --- |
| Corn1 | 1 | 1 | 0.46 | 0.009 | aerial | 0.4 |
| Corn | 1 | 1 | 0.46 | 0.009 | ground | 0.4 |
| Corn | 1 | 1 | 0.46 | 0.009 | in-furrow | 0.2 |
| Alfalfa2 | 1 | 1 | 0.46 to 0.56 | 0.009 | aerial | 0.4 to 0.5 |
| Alfala | 1 | 1 | 0.46 to 0.56 | 0.009 | ground | 0.4 to 0.5 |
| Alfalfa | 1 | 1 | 0.46 to 0.56 | 0.009 | in-furrow | 0.2 |
| Sorghum3 | 1 | 1 | 0.67 | 0.009 | aerial | 0.6 |
| Sorghum | 1 | 1 | 0.67 | 0.009 | ground | 0.6 |
| Sorghum | 1 | 1 | 0.67 | 0.009 | in-furrow | 0.3 |
| Cotton4 | 1 | 1 | 0.20 | 0.05 | aerial | 1.0 |
| Cotton | 1 | 1 | 0.20 | 0.05 | ground | 1.0 |
| Cotton | 1 | 1 | 0.20 | 0.05 | in-furrow | 0.5 |
| Potatoes5 | 1 | 1 | 0.14 to 0.63 | 0.10 | aerial | 1.0 to 6.0 |
| Potatoes | 1 | 1 | 0.14 to 0.63 | 0.10 | ground | 1.0 to 6.0 |
| Potatoes | 1 | 1 | 0.14 to 0.63 | 0.10 | in-furrow | 0.5 to 3.0 |

# APPENDIX 1 - FIRST Output Files for a Single 1 lb ai/A application to Corn or PA Alfalfa

Aerial Application

RUN No.   1 FOR carbofuran       ON   corn          * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   AERIAL(16.0)    .4    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

412.766                    200.252

Ground Application

RUN No.   2 FOR carbofuran       ON   corn          * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GROUND( 6.4)    .4    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

413.405                    200.391

In-Furrow Application

RUN No.   3 FOR carbofuran       ON   corn          * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GRANUL(  .0)    .4   2.0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

203.523                     98.599

# APPENDIX 2 - FIRST Ouput Files for a Single 1 lb ai/A application to CA alfalfa

Aerial Application

RUN No.   1 FOR carbofuran       ON   alfalfa       * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   AERIAL(16.0)    .5    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

503.373                    244.209

Ground Application

RUN No.   2 FOR carbofuran       ON   alfalfa       * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GROUND( 6.4)    .5    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

504.152                    244.379

In-Furrow Application

RUN No.   3 FOR carbofuran       ON   alfalfa       * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GRANUL(  .0)    .5   2.0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

248.199                    120.242

# APPENDIX 3 - FIRST Output Files for a Single 1 lb ai/A application to TX Sorghum

Aerial Application

RUN No.   1 FOR carbofuran       ON   sorghum       * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   AERIAL(16.0)    .6    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

604.047                    293.051

Ground Application

RUN No.   2 FOR carbofuran       ON   sorghum       * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GROUND( 6.4)    .6    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

604.982                    293.255

In-furrow Application

RUN No.   3 FOR carbofuran       ON   sorghum       * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GRANUL(  .0)    .6   2.0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

297.839                    144.291

# APPENDIX 4 - FIRST Output Files for a Single 1 lb ai/A application to Cotton Nationwide

Aerial Application

RUN No.   1 FOR carbofuran       ON   cotton        * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   AERIAL(16.0)   1.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

1.007                       .488

Ground Application

RUN No.   2 FOR carbofuran       ON   cotton        * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GROUND( 6.4)   1.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

1.008                       .489

In-Furrow Application

RUN No.   3 FOR carbofuran       ON   cotton        * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GRANUL(  .0)   1.0   2.0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

496.398                    	240.484

# APPENDIX 5 - FIRST Output Files for a Single 1 lb ai/A application to ME Potato

# Aerial Application

RUN No.   1 FOR carbofuran       ON   potato        * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   AERIAL(16.0)   1.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

1.007                       .488

Ground Application

RUN No.   2 FOR carbofuran       ON   potato        * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GROUND( 6.4)   1.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

1.008                       .489

In-Furrow Application

RUN No.   3 FOR carbofuran       ON   potato        * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GRANUL(  .0)   1.0   2.0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (NANOGRAMS/LITER (PPTr))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

496.398                    240.484

# APPENDIX 6 - FIRST Output Files for a Single 1 lb ai/A application to ID Potato

Aerial Application

RUN No.   1 FOR carbofuran       ON   potato        * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   AERIAL(16.0)   6.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

6.040                      2.931

Ground Application

RUN No.   2 FOR carbofuran       ON   potato        * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GROUND( 6.4)   6.0    .0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

6.050                      2.933

In-furrow Application

RUN No.   3 FOR carbofuran       ON   potato        * INPUT VALUES *

--------------------------------------------------------------------

RATE (#/AC)   No.APPS &   SOIL  SOLUBIL  APPL TYPE  %CROPPED INCORP

ONE(MULT)    INTERVAL    Koc   (PPM )   (%DRIFT)     AREA    (IN)

--------------------------------------------------------------------

1.000(  1.000)   1   1      30.0  700.0   GRANUL(  .0)   6.0   2.0

FIELD AND RESERVOIR HALFLIFE VALUES (DAYS)

--------------------------------------------------------------------

METABOLIC  DAYS UNTIL  HYDROLYSIS   PHOTOLYSIS   METABOLIC  COMBINED

(FIELD)  RAIN/RUNOFF  (RESERVOIR)  (RES.-EFF)   (RESER.)   (RESER.)

--------------------------------------------------------------------

321.00        2          N/A      6.00-  744.00   642.00    344.62

UNTREATED WATER CONC (MICROGRAMS/LITER (PPB))   Ver 1.0 MAY 16, 2001

--------------------------------------------------------------------

PEAK DAY  (ACUTE)      ANNUAL AVERAGE (CHRONIC)

CONCENTRATION             CONCENTRATION

--------------------------------------------------------------------

2.978                      1.443