# SHALLOW WATER DEVELOPMENT AND MANAGEMENT

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 646

### SHALLOW WATER DEVELOPMENT AND MANAGEMENT

Shallow water development and management is the inundation of lands to provide habitat for fish and/or wildlife.

### PRACTICE INFORMATION

This practice is applicable to lands where water can be impounded or regulated by diking, excavating, ditching, and/or flooding. It can also be used to provide refuge habitats for native fish during high flow periods.

The purpose is to provide habitat for wildlife such as shorebirds, waterfowl, wading birds, mammals, fish, reptiles, amphibians, and other species that require shallow water for at least a part of their life cycle.

Site selection is important to successfully carrying out this practice. Soils must have a low permeability or seasonal high water table. The site must be free of hazardous materials, and the water supply must be adequate to maintain water levels between 1 to 18 inches in depth over the majority of the area during the inundation period. Operation and maintenance is very important to ensure that this practice functions as intended throughout its expected life.

### COMMON ASSOCIATED PRACTICES

Shallow Water Development and Management is commonly used in a Conservation Management System with the following practices:

- Dike (356)

- Structure for Water Control (587)

- Irrigation Water Conveyance (428)

- Pipeline (516)

- Pond (378)

- Wetland Wildlife Habitat Management (644)

Refer to the practice standard in the local Field Office Technical Guide and associated Job Sheets for further information.

# Text boxes

Start

Note:  Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

I.16 (-) Potential income

Associated practice

Mitigating practice

(+) increase; (-) decrease

Pathway

C.  Cumulative effect

I.  Indirect effect

D.  Direct effect

#.  Created by practice

LEGEND

I.15

(+/-) Air quality

I.14 (+/-) Greenhouse gases

I.12 (-) Organic matter oxidation

I.13 (+) Temporary carbon storage

I.11 (+) Methane production

I.1 (-)

Habitat fragmentation

I.17 (-) Net return to producer

C.5 (+/-) Community health and safety

C.6 (+/-) Income and income stability (individuals and community)

I.2 (+) Use of habitat by target species

C.2 (+) Biodiversity

I.10 (+) Temporary flood storage

I.7 (-) Sediment-borne contaminants to receiving waters

D.2 (+) Ponded water (seasonal)

D.5 (+) Cost of installation and maintenance

D.3 (+) Anaerobic conditions (during inundation)

I.9 (+/-) Water-borne contaminants to receiving waters*

C.4 (+/-) Water quality

C1. (+) Health and population of fish and wildlife

D.4 (-) Land available for commercial agricultural production or development

I.3 (+) Use of habitat by non-target species

1. Inundation of lands to provide habitat and refuge for fish and/or wildlife species that require shallow water for at least a part of their life cycle

I.5 (+/-) Water temperature

I.6 (+) Sedimentation (onsite)

I.8 (+/-) Nutrients

Shallow Water Development and Management

7/2008

C.3 (+) Recreational opportunities

I.4 (-) Habitat for noxious/invasive species (with vegetation management)

D.1 (+) Habitat for target species

Shallow Water Development

and Management (646)

Initial setting: Where habitat is needed for wildlife that require shallow water:  (1) on lands where water can be impounded or regulated by diking excavating, ditching, and/or flooding; (2) on flood plains area that provide refuge habitats for native fish during high flow periods