# WETLAND CREATION

## PRACTICE INTRODUCTION

USDA, Natural Resources Conservation Service―Practice Code 658

### WETLAND CREATION

Wetland creation is the establishment of a wetland on a site that was historically nonwetland.

### PRACTICE INFORMATION

Wetland creation applies to sites where no natural wetland occurred historically. These sites contain soils that are not hydric.

This practice does not apply to:

a constructed wetland intended to treat point and nonpoint sources of water pollution

wetland enhancement intended to rehabilitate a degraded wetland

wetland restoration intended to return the soils, hydrology, vegetative community, and biological habitat to approximate original wetland conditions

The purpose of this practice is to create wetland functions and values.

The purposes, goals, and objectives of the creation must be clearly defined, including the appropriate criteria for the site and purposes. The soil, hydrology, and vegetative characteristics existing on the site and the contributing watershed must be documented. Native vegetative species should be used whenever possible. Water levels can be controlled to prevent oxidation of organic soils and for vegetation management.

### COMMON ASSOCIATED PRACTICES

Wetland Creation is commonly used in a Conservation Management System with the following practices: Dike (356), Structure for Water Control (587), Grade Stabilization Structure (410), Pond Sealing and Lining (521 A–D), and Use Exclusion (472).

For further information, refer to the practice standard in the local Field Office Technical Guide and associated practice specifications and job sheets.

# Text boxes

I.2 (-) Downstream flooding

C.4 (+/-) Income and income stability (individuals and communities)

C.3 (+/-) Water available for other uses

I.15 (+) Wetland wildlife habitat

1.  Create macro and microtopography to artificially provide wetland hydrology

Wetland Creation

7/2008

Mitigating practice or activity

(+) increase; (-) decrease

Pathway

C.2 (+) Water quality

D.3 (+) Cost of installation and maintenance

I.16 (+) Soil organic matter

C.1 (+/-) Health and safety for humans, domestic and wild animals

C.  Cumulative effect

D.4 (+) Vegetation

I.  Indirect effect

D.  Direct effect

#.  Created by practice

LEGEND

Wetland Creation (658)

I.9 (-) Downstream

sedimentation

I.12 (-/+) Land values

Initial setting: Land areas that are not natural wetland or were not formerly natural wetland, where wetland hydrology can be provided from external sources of water, and where deep-water habitat conditions do not exist

C.5 (+) Recreational

opportunities

I.14 (+/-) Consumptive use of water

I.6 (+/-) Air quality

I.17 (-) Greenhouse gases

I.1 (+) Temporary flood storage

I.13 (+/-) Net return to landowner

D.2 (-) Land available for agricultural production

I.8 (+) Sediment retention

I.11 (+) Sequestration of elements and compounds

D.1 (+) Water retention

Note: Effects are qualified with a plus (+) or minus (-). These symbols indicate only an increase (+) or a decrease (-) in the effect upon the resource, not whether the effect is beneficial or adverse.

Water level management/control

I.7 (-) Dissolved and suspended pollutants

2. Establish hydrophytic vegetation

I.3 (+) Habitat for undesirable insects

Start

I.5 (+) Greenhouse gases

I.4 (+) Methane produced

I.10 (+) Aquatic habitats