68-Er-167 Review

Drafted by J. Chang, KAERI, 2004.

Files:

ENDF/B-VI: Origin 1988, Res. Param. by Mughabghab[1984] .

JEF:	Copied ENDF/B-V of 1974, latest revision 1988 , Res. Param. by Mughabghab[1984] .

BROND:	Origin 1976, Revision 1989.

- Thermal cross section

The most reliable evaluation for capture cross section is

Mughabghab[1984]	 = 659±16 b, RI: 2970±70 b

s = 1.6±0.9 b, bcoh = 3.5±1.0 fm, R’ = 7.9±0.3 fm

Mughabghab[2003]	 = 659±16 b, RI: 2970±70 b

Holden[1998]	 = 700±200 b , RI: 2970±70 b, b = 3.0±0.3 fm

Knopf[1997]	 = 568±9 , b = 3.06±0.05, R'= 7.6±0.2 fm

Cap	RI	Fast Cap.	Scat.	b.	R	R’

ENDF	657.6	2992.	1508.	1.27	2.30	7.9	7.9

JEF	671.1	3027.	1713.	0.89	1.67	6.64	6.6433

BROND	653.8	3393.	1257.	26.76	3.56	9.89	9.89

- Resolved Resonance Parameter

ENDF is based on Mughabghab[1984], and upper limit is 0.5 keV.

JEF is based on Mughabghab[1984], and upper limit is 0.132 keV.

BROND upper limit is 0.5 keV.

- Unresolved Resonance Parameters

Mughabghab[1984]

D0=4±0.2 eV, 	S0 = 1.8±0.2,	<> = 88±2 meV

ENDF uses energy dependent URR parameters, up to 10 keV.

JEF has NO URR parameters.

BROND uses energy independent URR parameters up to 1 keV.

ENDF:	D0 = 4 eV, 	S0=2.28,		<> = 89 meV

D1 = 2 eV, 	S1=1.80, 		<> = 89 meV

BROND:	D0 = 5 eV, 	S0=2.13,		<> = 5.06 meV

- The small <> of BROND is apparently due to typo.

- Capture (high energy)

ENDF and JEF are same.

BROND is more smooth.

- Elastic

BROND is too high.

ENDF and JEF agree well with experimental data.

- Inelastic

ENDF and JEF are same and show rather flat shape.

BROND shows reasonable shape.

- (n,p) and (n,)

ENDF and JEF are missing.

BROND shows reasonable shape, but higher (n,p) than experimental data.

- (n,2n)

ENDF and JEF are missing.

BROND is reasonable.

Recommendation:

ENDF is recommendable for the reactor application.

# References

Mughabghab[1984], Neutron Cross Sections Vol. 1, Part B, Academic Press.

Holden[1998], CRC Handbook of Chemistry and Physics, 78th ed., CRC Press.

Mughabghab[2003], INDC(NDS)-440, 2003.