| Princeton Plasma Physics Laboratory NSTX Experimental Proposal |
| --- |
| Title: CHI into an ohmic discharge |
| OP-XP-533 | Revision: | Effective Date: (Ref. OP-AD-97) Expiration Date: (2 yrs. unless otherwise stipulated) |
| PROPOSAL APPROVALS |
| Author: D. Mueller | Date |
| ATI – ET Group Leader: R. Raman | Date |
| RLM - Run Coordinator: J. Menard, S. Sabbagh (Deputy) | Date |
| Responsible Division: Experimental Research Operations |
| Chit Review Board (designated by Run Coordinator) |
| MINOR MODIFICATIONS (Approved by Experimental Research Operations) |

NSTX EXPERIMENTAL PROPOSAL

CHI into an ohmic discharge 	OP-XP-533

# 1.	Overview of planned experiment

The aim of this experiment is to apply the CHI voltage after an ohmic discharge has been established and to observe changes in plasma parameters, especially the current, li or E.

# 2.	Theoretical/ empirical justification

Experiments on HIT-II have demonstrated that it is possible to increase the observed plasma current by adding CHI to an already established OH discharge and that this current persists after the CHI voltage is reduced to zero.  It is expected that the CHI current is added as a surface current and that this may effect the energy confinement time as well as provide current drive.  Of course, other effects may occur such as impurity generation or changes in the equilibrium that could affect plasma control.

A condition for driving current inside closed flux surfaces by CHI is that inj  > tok , where

tok = 0 Ip / T and inj =  0 Iinj /inj

= 0J/B.  Integrating J and B over a surface with current I and flux  gives  = 0I/.

For the injector, the flux is taken to be the flux penetrating the insulating gap.



tok ~ 1 for Ip = 500 kA and BT = 4.5 kG 
inj ~ 4 for Iinj = 10 kA and inj ~ 0.03 Wb  (from EFIT for shot 106447)

So this condition is easily satisfied.

# 3.	Experimental run plan

Establish ohmic targets (3 each):

500 kA, LSN, TF = 4.5 kG

500 kA, CS, TF =4.5 kG

500 kA, DN, TF = 4.5 kG

with > 100 ms flattop and well-controlled shapes.

5 min. He GDC between shots.

Starting with the LSN plasma, apply the CHI voltage for 20 ms (time between application of cap  bank voltage voltage and firing the crowbar) during the Ip flattop. Use a LDGIS branch 5 puff with fill of 1000 T with gas timed to arrive at the time CHI voltage is applied..

- Begin with VCHI = 400 V and increase VCHI in ~200 V increments to 1500 V. (8 shots)

- Binary search from 0 to 2000 Torr for the "best" pressure for LDGIS branch 5 puff . (5 shots)

- Try another gas puff location (outer midplane and/or top) if time permits (3 shots)

- Use beam blips before and after CHI to compare current distributions. (4 shots)

- Delay firing of crowbar as appropriate to allow longer current penetration time at best condition (3 shots)

"Best" is that which gives most Ip, low li or improved E without a large impurity influx or density increase.

Repeat A-E with the DN plasma

Repeat A-E with the CS plasma

Repeat LSN plasma at end to document changing wall conditions

# 4.	Required machine, NBI, RF, CHI and diagnostic capabilities

See above ohmic target requirements.  CHI must be ready; use 8 capacitors in the CHI circuit and use the crowbar to terminate injector current.

Required diagnostics:

Magnetics, EFIT (timed to get bins immediately before and after injector current pulse)

Filter scopes for C, H and O

Fast Camera with wide- angle view.

MPTS (at least some of the time)
	Dynamo Probe (desired, but not essential for first go-round)

Divertor Langmuir probes (desired)

Possible MSE with beam  blips before and after injector current pulse

# 5.	Planned analysis

EFIT,

# 6.	Planned publication of results

PPPL report, APS talk, and or journal publication, depending upon quality of results

PHYSICS OPERATIONS REQUEST

CHI into an ohmic discharge	OP-XP-533

Machine conditions (specify ranges as appropriate)

ITF (kA): 53.5	Flattop start/stop (s):  -.01/1.0

IP (MA): 0.5	Flattop start/stop (s):  ~.15 / .5

Configuration: LSN

Outer gap (m):	0.1,	Inner gap (m):	0.1

Elongation :	2,	Triangularity :	~0.4

Z position (m):	0.00

Gas Species:  D,	Injector:  Midplane / Inner wall / Lower Dome

NBI - Species: D,	Sources: A,	Voltage (kV): 90,	Duration (s): .01-.02

ICRF – Power (MW): ____,	Phasing: Heating / CD,	Duration (s): _____

CHI:  ON

Either:	List previous shot numbers for setup: 106447

Or:	Sketch the desired time profiles, including inner and outer gaps, , , heating, fuelling, etc. as appropriate. Accurately label the sketch with times and values.

DIAGNOSTIC CHECKLIST

CHI into an ohmic discharge	OP-XP-533

| Diagnostic | Need | Desire | Instructions |
| --- | --- | --- | --- |
| Bolometer – tangential array |  |  |  |
| Bolometer array - divertor |  |  |  |
| CHERS |  | ( | Beam Blips |
| Divertor fast camera |  | ( |  |
| Dust detector |  |  |  |
| EBW radiometers |  |  |  |
| Edge deposition monitor |  |  |  |
| Edge pressure gauges |  |  |  |
| Edge rotation spectroscopy |  | ( |  |
| Fast lost ion probes - IFLIP |  |  |  |
| Fast lost ion probes - SFLIP |  |  |  |
| Filtered 1D cameras |  |  |  |
| Filterscopes |  |  |  |
| FIReTIP |  |  |  |
| Gas puff imaging |  |  |  |
| Infrared cameras |  |  |  |
| Interferometer - 1 mm |  |  |  |
| Langmuir probe array |  | ( |  |
| Magnetics - Diamagnetism | ( |  |  |
| Magnetics - Flux loops | ( |  |  |
| Magnetics - Locked modes |  | ( |  |
| Magnetics - Pickup coils | ( |  |  |
| Magnetics - Rogowski coils | ( |  |  |
| Magnetics - RWM sensors |  |  |  |
| Mirnov coils – high frequency |  |  |  |
| Mirnov coils – poloidal array |  |  |  |
| Mirnov coils – toroidal array |  |  |  |
| MSE |  | ( | Beam Blips |
| Neutral particle analyzer |  |  |  |
| Neutron measurements |  |  |  |
| Plasma TV | ( |  |  |
| Reciprocating probe |  | ( | Dynamo Probe head |
| Reflectometer – core |  |  |  |
| Reflectometer - SOL |  |  |  |
| RF antenna camera |  |  |  |
| RF antenna probe |  |  |  |
| SPRED |  |  |  |
| Thomson scattering |  |  |  |
| Ultrasoft X-ray arrays |  |  |  |
| Visible bremsstrahlung det. |  |  |  |
| Visible spectrometers (VIPS) |  |  |  |
| X-ray crystal spectrometer - H |  |  |  |
| X-ray crystal spectrometer - V |  |  |  |
| X-ray PIXCS (GEM) camera |  |  |  |
| X-ray pinhole camera |  |  |  |
| X-ray TG spectrometer |  |  |  |