96E03/29/06

S710-96E.doc

Use with wood guardrail posts.

Section 710. - FENCE AND GUARDRAIL

When steel backed timber rail is specified, include the following:

710.08  Steel-Backed Timber Rail.  Delete the text and substitute the following:

Edit the following as necessary. See commentary for SCR 716.03 for discussion of preservative treatment alternatives. If CCA is not to be used, delete last sentence. If copper naphthenate is used, change minimum retention to 2lb/yd3.

Furnish timber conforming to AASHTO M 168.  Fabricate the 6 by 10 inch timber rail, the 4 by 9 inch blockouts, and the posts from dry, well seasoned, and dressed rough sawn coast Douglas fir, southern pine, or other species having a stress grade of at least 1500 psi.  Refractory species such as larch and Rocky Mountain Douglas fir are not acceptable.  Treat the timber rail, blockout elements, and posts according to AASHTO M 133.

Fabricate the steel backing elements from ⅜ inch structural steel conforming to ASTM A588.  For fastener hardware, conform to AASHTO M 164, type 3.

All timber members shall bear an approved ALSC (American Lumber Standards Committee) quality mark assuring treatment is in conformance with appropriate AWPA standards.

Use with guardrail posts.

710.09  Guardrail Posts.  Delete the text and substitute the following:

Conform to the AASHTO-AGC-ARTBA “Guide to Standardized Highway Barrier Hardware,” 1995 edition.

Do not use a wood guardrail post that has a through check, shake, or end split in the same plane as, or a plane parallel to the bolt hole and extending from the top of the post to within 3 inches of the bolt hole.

For steel-backed timber rail posts, furnish 10 by 12 inch posts conforming to Subsection 710.08.

When temporary crash cushions are required, include the following: NOTE TO DESIGNER: This subsection is being handled in subsection 635.19.

710.12  Crash Cushion Barrels.  Delete the text.

Use the following for UPS projects with log rails. Verify copper naphthenate preservative is acceptable.

Add the following subsection:

710.13  Log Rails.

Use logs that are seasoned, straight, and sound No. 1 Grade Western Hemlock, Western Red Cedar, or Pine of the dimensions shown on the drawings.  Logs that taper in excess of 1.2 inches will not be permitted.  Remove all bark and at least 80% of the inner bark.  Peeler marks or incision marks on visible portions of logs will not be allowed.  Utilize logs that do not have a season checks, singular or any 2 opposite each other that exceed 2 the thickness of the member.  Incorporate logs that are free of knot clusters, but may contain sound, tight, well-spaced knots.

Incise that portion of the log which will be below ground.  Make all dimensional cuts and holes in the timber members prior to pressure treatment.  Treat all timber members with Copper Naphthenate preservative treatment conforming to AWPA C14.  Preservative retention in the assay zone shall not be less than 2 pounds per cubic yard.  Assay only in the incised, below ground portion of the posts.

All timber members shall bear an approved ALSC (American Lumber Standards Committee) quality mark assuring treatment is in conformance with appropriate AWPA standards.