Subject:	Comments, Docket No. FAA–2008-0618; Directorate Identifier 2007–NM–355–AD, Model 777 Engine Suction Feed Test

References:	(a)	Boeing 777 MPD Section 2 Tasks 28-020-00 & 28-020-02

- Boeing 777 Task Card 28-020-00-01

- Boeing 777 Task Card 28-020-02-01

- Boeing 777 AMM task 28-22-00-710-802

- Boeing 777 AMM task 28-22-15-710-802-001 – GE 90

- Boeing 777 AMM task 28-22-15-710-803-002 - Trent

British Airways has reviewed the subject NPRM and provides the following comments.

- British Airways recognises the need to test the ability of the engine to suction feed regularly to ensure correct operation in the event of loss of pressurised engine fuel feed.

2.	The task required by the NPRM is already covered by the ref (a) Boeing777 MPD tasks at 7,500 hrs.

3.	The Boeing task card quoted in para (f) of the NPRM (ref (C)) only applies to the Trent powered Boeing 777. The ref (b) task card also covers this check for the GE90 powered aircraft.

4.	The ref (b) & (c) task cards allows for two checks. Either one fulfills the requirements of the MPD. Ref (d), (e) & (f) AMM tasks refer to this check.

5.	The NPRM sets the issue date for the manual to be used to 05 May 2007. BA does not hold previous issues of AMM or Boeing task cards for general use. BA engineers only use the latest revision of the instructions.

6.	British Airways request the following:-

- The NPRM references the Boeing MPD tasks associated with this check.

ii.	The NPRM quotes all the Boeing task cards applicable to different engine types.

iii.	The NPRM acknowledges and allows use of either procedure quoted in the Boeing task cards.

iv.	The NPRM allows for using AMM and Boeing task cards that have more recent issue dates than 05 May 2007.