$$721.00A

Section 721.—ELECTRICAL AND ILLUMINATION MATERIAL

Revised 25 January 2005

INCLUDE THE FOLLOWING FOR LIGHTING

$$721.01A

721.01(c).  Add the following:

Furnish either ozone resistant cross-linked polyethylene (XLP) or polyvinyl chloride (PVC) insulated cable, with or without a nylon jacket, as applicable, conforming to the following:

(1)  XLP.  IPCEA S-66-524 and NEMA WC-7 (code type XHHW);

(2)  PVC.  UL 83, ANSI C33.80-1971, and Federal Specification J-C-304 (code types THWN or THW).

INCLUDE THE FOLLOWING FOR ELECTRICAL WORK

$$721.01B

721.01(c).  Add the following:

Furnish soft drawn or annealed copper conductors conforming to ASTM B 3, and stranding conforming to ASTM B 8.  Furnish 7 strand for #10 AWG through #2 AWG, and 17 strand for #1 AWG through #4/0 AWG.  Furnish #6 AWG minimum solid copper ground wires.