About this resource:

EPA is providing this resource solely for informational purposes. The agency can not attest to the accuracy, effectiveness, legality or usefulness of the information provided, nor does the inclusion or reference of such language constitute an endorsement by EPA.

Document Name:

MHD Odor (Emissions) Control

Organization/Agency Responsible:

Massachusetts Highway Department (MHD)

Contact:  	Trygve Swift

Environmental Scientist

Massachusetts Turnpike Authority

Central Artery/Tunnel Project

617-342-1357

Tbswift@bigdig.com

Description:  	Central Artery Project (Big Dig)

This project reconstructs the central artery and extension of the Massachusetts Turnpike and is expected to be completed in the spring of 2007. All pieces of construction equipment must have a diesel oxidation catalyst (DOC) and cannot idle in excess of five minutes.

SECTION 721.562

CONSTRUCTION ODOR CONTROL

DESCRIPTION

1.01	GENERAL

A.	This Section specifies requirements for controlling odors generated during Work of this Contract.  It supplements the air pollution control requirements of Division I, Subsection 7.01B.

B.	The Contractor is responsible for controlling hazardous odors and nuisance odors encountered or created during Work of this Contract, including odors associated with site sanitation.

C.	The Contractor shall investigate odor complaints, ascertain the odor source, and promptly implement appropriate odor control measures.

1.02	TERMS USED

A.	Hazardous odor - Odor that is determined to be hazardous or toxic.

B.	Nuisance odor - Odor that is determined to be non-hazardous or non-toxic.

C.	Contractor personnel - Contractor employees and representatives, and Subcontractor employees and representatives.

1.03	RELATED WORK SPECIFIED ELSEWHERE

A.	Section 119.010 - Site Sanitation for Pest Control

B.	Section 120.020 - Transportation and Disposal of Clay and Till

C.	Section 120.080 - Contaminated Soil Excavation

D.	Section 140.141 - Erosion and Sedimentation Control

E.	Section 148.100 - Dredging

F.	Section 721.110 - Hazardous Materials Health and Safety Plan Requirements

G.	Section 721.120 - Emergency Response Plan Requirements

1.04	REGULATORY REQUIREMENTS

A.	The Contractor shall perform Work in compliance with the Massachusetts Department of Environmental Protection, Code of Massachusetts Regulations (CMR) 310 CMR 7.00, "Air Pollution Control Regulations" specifically 310 CMR 7.09, "Dust, Odor, Construction and Demolition" and 310 CMR 7.11, "Transportation Media."

B.	The Contractor shall also perform Work in compliance with the City of Boston's Air Pollution Control Commission "Regulations for the Control of Atmospheric Pollution" as adopted under the provisions of Section 31C, Chapter 3, "General Laws."

1.05	SUBMITTALS

A.	Submit materials data required by Division I Subsection 6.01.

B.	Prior to the use of an odor suppression agent, submit pertinent literature and Material Safety Data Sheet to the Resident Engineer for review.

C.	Submit odor control program required by Division I Subsection 7.01B.  The program shall outline in detail the measures to be implemented by the Contractor to comply with this Section.

D.	Furnish monitoring results and logs of complaints as specified under Construction Methods.

MATERIALS

2.01	ODOR SUPPRESSION AGENTS

A.	Odor suppression agents shall be water soluble, non-toxic, non-reactive, and non-volatile.

B.	The use of petroleum based products for odor suppression is strictly prohibited in this Contract.

2.02	COVERS

A.	Covers for excavated areas and stockpiled material shall be at least 10-mil thick polyethylene sheets.  Covers for contaminated soil or material shall comply with Section 120.080.  For material consisting of clay or till, coverings shall comply with Section 120.020.

CONSTRUCTION METHODS

3.01	NUISANCE ODOR CONTROL

A.	Methods that shall be used by the Contractor to control nuisance odors associated with earthwork include:

1.	Improving site drainage and preventing standing water from remaining in excavated areas.

2.	Covering stockpiles of excavated material with polyethylene sheeting and securing it with sandbags or an equivalent method to prevent the cover from being dislodged by the wind.  The Contractor shall repair or replace covers whenever damaged or dislodged, at no additional cost to the Department.

3.	Reducing the amount of time that excavated material is exposed to the open atmosphere.

4.	Chemically treating excavated areas and stockpiled material.  Permission of the Engineer must be obtained prior to the use of any chemical application for controlling odor.  This method shall be used only when other methods are impractical.

5.	Maintaining the construction site free of trash, garbage, and debris in accordance with Section 119.010.

6.	Fully covering and securing haul truck cargos during material transport on public roadways.

7.	Cleaning-up and properly disposing of excavated material that is deemed odorous.  If odorous material is located on public roadways or walkways, clean-up methods shall consist of wet spray sweeping or vacuuming only.

B.	Methods that shall be used by the Contractor to control nuisance odors associated with diesel emissions from construction equipment include:

1.	Turning off diesel combustion engines on construction equipment not in active use and on dump trucks that are idling while waiting to load or unload material for 5 minutes or more.

2.	Establishing a staging zone for trucks that are waiting to load or unload material at the contract area, in a location where the diesel emissions from the trucks will not be noticeable to the public.

3.	Locating combustion engines away from sensitive receptors such as fresh air intakes, air conditioners, and windows.

4.	In addition to the above diesel emission control measures, all off-road diesel powered equipment used for this contract shall contain oxidation catalyst emission control equipment on the exhaust system side of the equipment.

3.02	ODOR MONITORING

A.	Sensory Detection

1.	Sensory detection of odors (i.e., smelling) shall only be performed to determine a "boundary" of potential odor source(s).

B.	Instrumentation Monitoring

1.	As directed by the Engineer odor monitoring to determine potential hazards using instrumentation shall be used in accordance with Section 721.110.

2.	The Contractor shall document and submit to the Engineer all data on odor monitoring concentrations.

3.03	CONTRACTOR COMPLAINTS

A.	The Contractor shall notify the Engineer of all internal complaints originated from Contractor personnel regarding odors at the construction site.  The Engineer will notify the Contractor of all external complaints from regulatory agencies or the public.

B.	The Contractor shall document and maintain a log of all complaints originated from Contractor personnel and from the Engineer, regarding odors at the construction site.

C.	For odors that are being produced from materials that are determined to be hazardous, the Contractor shall comply with the requirements of the Hazardous Materials Health and Safety Plan Section 721.110 and the Emergency Response Plan Section 721.120.

D.	For odors that are determined to be non-hazardous, (i.e., nuisance odors), the Contractor shall implement appropriate control measures.

COMPENSATION

4.01	METHOD OF MEASUREMENT AND BASIS OF PAYMENT

A.	All odor control measures will be considered incidental to the Work and will not be measured or paid for separately.