Construction Specification 726—Topsoiling

1.	Scope

The work consists of salvaging topsoil from the locations shown on the drawings.  It also includes spreading the salvaged topsoil to specified depths at locations shown on the drawings.

2.	Quality of topsoil

Topsoil shall consist of friable surface soil reasonably free of grass, roots, weeds, sticks, rocks, or other unsuitable material.

3.	Salvaging

After the site has been cleared and grubbed, the topsoil shall be removed from the locations designated on the drawings.

4.	Stockpiling

Salvaged topsoil shall be stockpiled at locations approved by the Engineer.  Stockpiles of topsoil shall not conflict with the requirements of Construction Specification 5, Pollution Control.

5.	Spreading

Spreading shall not be performed when the ground or topsoil is frozen, excessively wet, or otherwise in a condition detrimental to uniform spreading operations.  Surfaces designated to receive a topsoil application shall be lightly scarified just before the spreading operation.  Where compacted earthfills are designated to be topsoiled, the topsoil shall be placed concurrently with the earthfill and shall be bonded to the compacted fill with the compacting equipment.

Following the spreading operation, the topsoil surface shall be left reasonably smooth and without ruts or surface irregularities that could contribute to concentrated waterflow downslope.

6.	Measurement and payment

Method 1—The total surface covered by topsoil is measured and the area(s) computed to the nearest square yard.  Payment for furnishing and placing topsoil is made at the contract unit price.

Method 2—The total surface covered by topsoil, except the surface area of embankments, levees, dikes, and other earthfills not included for payment, is measured and the area(s) computed to the nearest square yard.

Payment for topsoil spread on the surface of embankments, levees, dikes, and other earthfills is included in the measurement and payment for that item of earthfill where topsoil application occurred.

Method 3—For items of work for which specific unit prices are established in the contract, the volume of topsoil furnished and spread is computed to the nearest cubic yard by the method of average cross-sectional end areas from surveys of the excavated topsoil stockpile or, if not stockpiled, cross-sectional surveys of the borrow area(s).  Payment for furnishing and spreading topsoil is made at the contract unit price.

All methods—The following provisions apply to all methods of measurement and payment.  Compensation for any item of work described in the contract, but not listed in the bid schedule is included in the payment for the item of work to which it is made subsidiary.  Such items and the items to which they are made subsidiary are identified in section 7 of this specification.

All payment methods—Payment will constitute full compensation for all labor, equipment, material, and all other items necessary and incidental to the completion of the work.  This includes excavating, stockpiling, hauling, spreading, and the wasting of unsuitable excavated material.

7.	Items of work and construction details

Items of work to be performed in conformance with this specification and the construction details therefore are:

Bid Item 11, Topsoiling

- This item shall consist of salvaging and spreading topsoil in all borrow areas.

- The borrow areas shall be stripped to a depth of 8 in.  and stockpiled adjacent to the borrow areas.  After the required borrow material has been removed the stockpiled topsoil shall be spread uniformly over the borrow area from which it was removed.

- Measurement and payment shall be by Method 1.