# Large Transport Aircraft Engineering Packages

| Model | Service Bulletin | Operational Changes | Air Data Computer | Skin Check | Pitot Static Probe Life |
| --- | --- | --- | --- | --- | --- |
| 737-300/400/ 500 | 737-53-1180 (2/96) IN-03 | No Change | No Change | Visual | Unplated, no limit |
| 737-600/700/ 800/900/BBJ | N/R | Service letter: 737-SL-02-017 (1/98) |
| 737-600 | Service letter: 737-SL-02-017 (1/98) | Factory RVSM ready s/n 28259 and subsequent (delivered Sep 98) |
| 737-700 | Service letter: 737-SL-02-017 (1/98) | Factory RVSM ready s/n 27835 and subsequent (delivered Dec 97) |
| 737-800 | Service letter: 737-SL-02-017 (1/98) | Factory RVSM ready s/n 27977 and subsequent (delivered Apr 98) |
| 737-900 | Service letter: 737-SL-02-017 (1/98) | Factory RVSM ready s/n 29599 and subsequent (delivered Jun 00) |
| 737-BBJ | Service letter: 737-SL-02-017 (1/98) | Factory RVSM ready s/n 29102 and subsequent (delivered Dec 98) |
| 747-400 5” Probes | 747-53-2394 IN-03 (7/95) 747-53-2398 (11/95) | Mach < 0.90 in RVSM airspace | No Change | Detailed Measurement | Unplated: 3 years Plated: no limit |
| 747-400, 10” Probes | 747-53-2393 (11/95) | Mach < 0.90 in RVSM airspace | No Change | Visual | Plated: no limit |
| 757-200 | 757-34-0132 IN-02 (12/95) 757-53-0074 (10/95) | No Change | ADC Upgrade & new SSEC | Visual | N/A |
| 757-300 | Service letter 757-SL-02-016C (3/99) | Factory RVSM ready s/n 29012 and subsequent (delivered Mar 99) |
| 767-200/300 | 767-34-0237 IN-02 (1/95) 767-53-0068 (7/95) Rev 2 - 5/97 | No Change | Use 767-300 SSEC on all models | Visual | Unplated: 3 years Plated: no limit |
| 767-400 | Service Letter 767-02-011-B 8/2000 | Factory RVSM ready s/n 29446 and subsequent (delivered Aug 00) |
| 777-200/300 | 777-53-0007 (4/97) | No Change | No Change | Visual | N/A |
| 707 | STC group approval is under development by AeroMech, Inc. and is expected 2nd Quarter of 2003. |
| 727-100/200 | 727-53-0220 (Contact Boeing for AFM update) | No Change | New ADC and SSEC | Visual | N/A |
| 727-100/200 | ST01011SE (11/01) (Aeromech) | No Change | New ADC | Visual | N/A |
| 737-200 | 737-53-1191 IN-01 (7/96) | No Change | New ADC | Visual | Unplated: no limit |
| 737-200/200 Advanced | ST00894SE (3/01) (Aeromech) | No Change | New ADC | Visual | Unplated: no limit |
| 747-100/200/ 300/SP | 747-53-2405 (5/96) 747-53-2394 (7/95) 747-34-2135 (11/80) | Mach < 0.90 or 0.87 @ low weight in RVSM airspace | Specific SSEC | Detailed Measurement | Unplated: 4 years Plated: no limit |
| MD-81/82/83/ 87/88 | MD-80 34-289 (2/97) Rev 2 – 5/98 | No Change | No Change | Detailed Measurement (Static Plate) | N/A |
| MD-90-10/30/40 | MD-90 34-006 (5/97) | No Change | No Change | Detailed Measurement (Static Plate) | N/A |
| 717 | N/R | N/R |  |  |  |
| MD-11 Combi, Freighter, Passenger | MD-11 34-065 (3/96) Rev 2 – 2/97 | No Change | No Change | Detailed Measurement (Static Plate) | N/A |
| DC-10 | DC-10 34-134 (3/96) Rev 7 – 6/99 | No Change | No Change | Detailed Measurement (Static Plate) | N/A |
| DC-9 | ST01136LA (3/01) -30,-40,-50 series aircraft in conjunction with Boeing-Douglas Corporation (Aeromech) | No Change | New ADC | Detailed Measurement (Static Plate) | N/A |
| DC-8 | ST01073LA (9/00) -61,-62,-63,-71,-72,-73 series aircraft both passenger and freighter models (Aeromech) | No Change | New ADC | Detailed Measurement (Static Plate) | N/A |
| A319 | A320-34-1137 |  | No Change | Visual |  |
| A320 | A320-34-1137 |  | MSN <621 : Pitot 1 relocation A320-34-1122 | Visual |  |
|  | or A320-34-1115 | MMEL/FCOM restriction: ADR1 and 2 operative | No Change | Visual |  |
| A321 | A320-34-1137 |  | MSN < 621 Pitot 1 relocation A320-34-1122 ADIRU 3 modification A320-34-1129(Hwl) A320-34-1129(Lit) | Visual |  |
|  | or A320-34-1115 | MMEL/FCOM restriction: ADR1 and 2 operative | No Change | Visual |  |
| A340 | A340-34-4034 |  | No Change | Visual |  |
| A330 | A330-34-3031 |  | No Change | Visual |  |
| A300-600 | A300-34-6101 |  | No Change | Visual |  |
| A310 GE | A310-34-2112 |  | No Change | Visual |  |
| A310 PW | A310-34-2112 |  | MSN < 698 DADC-914 required A310-34-2114 | Visual |  |
| A300 B2/B4 | A300-34-0139 |  | No Change | Visual |  |
| L-1011 | L1011-093-34-204 | No Change | No Change | Detailed Measurement | 6 years or 10 years |
| F100 | FBF100-34-072 |  | Functional test | Visual |  |
| Non-Group RVSM Programs | Each STC is serial number specific (Aeromech) |  |  |  |  |
| 707-300 |  |  |  |  |  |
| 727-100 |  |  |  |  |  |
| DC-8-60/-70 |  |  |  |  |  |
| DC-9-10 |  |  |  |  |  |
| DC-9-30 |  |  |  |  |  |
| KC-135A (USAF) |  | J-57 engines |  |  |  |
| KC-135E (USAF) |  | Turbofans |  |  |  |