UNITED STATES

PRELIMINARY VIEWS ON WRC-07

Agenda Item 1.21:  to consider the results of studies, regarding the compatibility between the radio astronomy service and the active space services in accordance with Resolution 740 (WRC-03), in order to review and update, if appropriate, the tables of threshold levels used for consultation that appear in the Annex to Resolution 739 (WRC–03);

ISSUE:  Taking into account the results of the compatibility studies, including the impact on the active and passive services concerned, consider which band pairs (contained in the Table to Resolution 740) need to be added to the consultation provisions of Resolution 739 (WRC-03)?  If so, what are the appropriate threshold levels for consultation?

BACKGROUND: In preparation for WRC–03, Task Group 1/7 conducted studies that led to the adoption of Recommendation ITU–R SM.1633, which contains nine Annexes that, using the methodology contained in the Recommendation, assess the compatibility of various band pairs between the radio astronomy service and space services. Not all studies in the Annexes are complete.  On the basis of Recommendation SM.1633 and associated studies, WRC-03 adopted Resolutions 739 and 740.

Resolution 739 contains guidance to administrations operating space and radio astronomy stations in the band pairs contained in Tables 1-1 and 1-2, in order to come to acceptable solutions regarding space station unwanted emissions at a radio astronomy station. The Resolution includes a consultation process adopted at WRC-03 to assist administrations in reaching mutually acceptable solutions when unwanted emissions from space services exceed specified levels in certain radio astronomy bands.  The consultation process is included is included in Resolution 739 and it will not be considered at WRC-07.

Resolution 740 calls for the completion of studies for the band pairs indicated in its associated band-pair Table. Comprehensive studies are needed to determine whether any of the band pairs from the Table of Resolution 740 should be added to the tables in Resolution 739, and, if so, to determine the impact on all the concerned active and passive services and the appropriate threshold levels for consultation.  In accordance with the resolves 1 of the Resolution 740, only the band pairs listed in the Table of Resolution 740 are to be considered by WRC-07.

U.S. VIEW:

- Satisfactory studies in ITU-R TG 1/9 need to be completed before a determination is made regarding adding any of pairs contained in Resolution 740 to the Table in Resolution 739. The studies must identify the appropriate threshold levels for consultation and the impact on the concerned active and passive radio services.

- The scope of Agenda Item 1.21 is limited to consideration of the band pairs in the table of Resolution 740 (and the associated threshold levels for consultation), for purpose of making appropriate additions from this table to the existing tables in Resolution 739.  Any other proposals for modifications to Resolution 739 would be clearly outside the scope of this agenda item and would not be appropriate.