5022.1TA

BELOW-THE-HOOK LIFTING DEVICE

## Engineering Note Cover Page for MD-ENG-112

Lifting Device Numbers:

| FNAL Site No/ |  | Div. Specific No. | 160 | Asset No. |  |
| --- | --- | --- | --- | --- | --- |
|  | If applicable |  | If applicable |  | If applicable |

ASME B30.20 Group: 	[X ]  Group I	Structural and Mechanical Lifting Devices

(check one)	[ ]  Group II	Vacuum Lifting Devices
[ ]  Group III	Magnets, Close Proximity Operated
[ ]  Group IV	Magnets, Remote Operated

| Device Name or Description | 38 Ton Lifting Fixture For the SciBooNE Scibar & EC Detector |
| --- | --- |

| Device was | [ ] Purchased from a Commercial Lifting Device Manufacturer. Mfg Name |  |
| --- | --- | --- |
| (check all applicable) | [ X] Designed and Built at Fermilab | Eng. Drawing: ME - 444427 |
|  | [ ] Designed by Fermilab and Built by a Vendor. Assy drawing number |  |
|  | [ ] Provided by a User or other Laboratory |  |
|  | [ ] Other: Describe |  |

| Engineering Note Prepared by | Edward Chi | Date | January 22, 2007 |
| --- | --- | --- | --- |
| Engineering Note Reviewed by | Dave Pushka | Date | February 8, 2007 |

Lifting Device Data:

| Capacity | 76,000 lbs |
| --- | --- |
| Fixture Weight | 2,740 lbs. |

Service:		[ X]  normal	[ ]  heavy	 [ ]  severe  (refer to B30.20 for definitions)

| Duty Cycle | _______ 8, 16 or 24 hour rating (applicable to groups III, and IV) |
| --- | --- |
| Inspections Frequency |  |
| Rated Load Test by FNAL (if applicable) | Date |  | Load |  |
| [ ] Check if Load Test was by Vendor and attach the certificate |  |  |  |  |
| Satisfactory Load Test Witnessed by: |  |
| Signature (of Load Test Witness) |  |

Notes or Special Information:

The load test procedures and the load test also should make as part of the note.

|  | Fermilab |
| --- | --- |

Particle Physics Division

Mechanical Department Engineering Note

# Number:	MD-ENG- 112	Date: January 22, 2007

Project Internal Reference:

Project:  SciBooNE

Title:	   The 38 Ton Lifting Fixture for the SciBooNE Scibar & EC Detector

Author(s): Edward Chi

Reviewer(s): Dave Pushka    02/08/2007

Key Words: Beam, lifting fixture, bolt, allowable stress, weld, tensile, shear

Abstract Summary:  The 38 ton lifting fixture is specially designed for

lifting and moving the Scibar and Electron Catcher

detector of the SciBooNE experiment. The calculated

working stresses of some critical locations, the welding

sizes, the lifting pin and the connecting bolts subject to

the applying loads have been extensively studied and

discussed per the related applicable specifications and

codes.

Applicable Codes:

“Allowable Stress Design”, AISC, 9th edition

“Below-the-Hook Lifting Devices”, ASME B30.20

#5022, ES&H Manual, FermiLab.

“Structural Welding Code-Steel”, AWS D1.1-90

“Aluminum Design manual” by The Aluminum

Association, Inc. 6th edition.

Design the lifting fixture (38 tons) for moving the SciBooNE  Scibar and EC detectors

General:

The assembled Scibar and EC detector weights about 35 tons, and it will move from the CDF assembly hall to the SciBooNE enclosure as one piece.  All the materials used for the lifting fixture are recycled from the existing materials for the cost savings. Though some configurations of the fixture are awkward due to the availability of the materials, however, we never compromise the safety and applications of the fixture. The following calculations and analysis will approve our ultimate principles.

1. Design Criteria, Assumptions and References:

Total design load Py and the loading capacity of the fixture Pyc:

The fixture is designed to lift the SciBooNE Scibar and Electron Catcher detectors from the CDF assembly hall and move it to the SciBooNE experimental enclosure.

Figure 1.1 is showing the data of the total weight of the detector with the lifting fixture, it also indicates the coordinated location of the center of the gravity.

Figure 1.1, The data of the load and the location of the center of the gravity.

It found out that the total weight of the detector and fixture is ~70,279 lbs, where the fixture weight is about 2, 733 lbs, and the detector weight is about 67,546 lbs. We assume there is about 12% of the additional accessorial and miscellaneous item weight, that leads to the total applying capacity load of the lifting fixture  Pyc = 1.12 x 67,546 lbs  = 75,651 lbs → 76,000 lbs, so:

Pyc = 76,000 lbs = 38 tons  (lifting capacity)

Py = 76,000 lbs + 2,740 lbs = 78,740 lbs.

Where Py = 78,740 lbs is the total  load applying under the crane hook from

the lifting pin.

Allowable stresses:

All materials for the lifting fixture are: ASTM A36 ( or better, or unless it specified):

Fu = 58 ksi, Fy = 36 ksi

Fb =  Fy /3.0 =  12 ksi = Fv = Fp = Ft

(per section 20-1.2.2.2, ASME B30.20)

All bolt materials: ASTM A325, Fu = 105 ksi

Ft = 44 ksi, Pat = 34.6 kips (for 1” nominal dia.)

Fv = 21 ksi, Pav = 16.5 kips (for 1” nominal dia.)

(per page 4-3, part 4, ASD 9th edition)

All welding metals are E70, where Fu = 70 ksi

Fwv = 0.30 x 70 ksi = 21ksi

References:

Figure 1.2 of page 4 is an isometric view of the 38 tons lifting fixture.

From page 13, there is a listing for the reference drawings which related to this engineering note.

Figure 1.2, The isometric view of the 38 tons lifting fixture

2. Find out the working stresses when the lifting force Pv applying vertically.

Figure 2.1 is simulating the force distribution of the bracket when force applying

vertically through the middle lifting pin.

From figure 2.1 and the engineering drawing ME – 444427, it is found that:

L = 139.75”

Figure 2.1, Force distribution diagram of the lifting fixture as it applies vertically

Py = 76,000 lbs.

R1 = R2 = 38,000 lbs.

*. The distance between the lugs for the lifting pin.

So, Mmax = (Py L) / 4

= (78,740 lbs x 139.75 in) / 4

= 2,751,000 in-lbs. @ the center

Assuming R1 = R2 =  Py/2 = 39,370 lbs.

2.1 Calculate the working stress at several different locations

2.1a. The working stress in the center of the lifting fixture (x = L/2 = 70”):

Per figure 2.2, the sectional modulus Sxc  and the other geometrical properties in the center of the spreader bar of the strong axis x-x are calculated as following:

Ixx1 = (447 x 2) in4 = 894 in4    for two S15x42.9 I-beams

A1 = 12.6 in2 x 2 = 25.2 in2

y1 =   7.5 + 1 = 8.50 in

Ixx2 =[(14.50 – 6.50) x ( 2.03) /12] in4 = 5.333 in4

A2 =  (2.0 x (14.5 – 6.5)) in2 = 16 in2

y2 =   17.0 in

Ixx3 =[(14.50 x  1.03) /12] in4 = 1.208 in4

A3 =  1.0 x 14.5 in2 = 14.5 in2

y3 =   0.50 in

Ixx4  = (2 x 1.0 x 123) ÷ 12) in4 = 288 in4

A4 = ((12.0 x 1.00 x 2) in2 = 24 in2

y4 =   8.50 in

Ixx5  = (2 x 1.44 x 5.1253) ÷ 12) in4 = 32.3 in4

A5 = (5.125 x 1.44 x 2) in2 = 14.76 in2

y5 =   10.50 in

Since  y = ∑Aiyi ÷ ∑Ai

= ((25.2 x 8.5 + 16 x 17.0 + 14.50 x 0.5 + 24 x 8.50 –14.76 x 10.5) / 64.94) in

= (542.47 / 64.94) = 8.353 in

Figure 2.2, The cross section view of the lifting fixture in the center locatio

∆d1 = 0.147 in,  ∆d12 = 0.0216 in2

∆d12 A1= 0.544 in4

∆d2 = 8.647 in,  ∆d22 = 74.77 in2

∆d22 A2= 1,196 in4

∆d3 = 7.853 in,  ∆d32 = 61.67 in2

∆d32 A3= 894 in4

∆d4 = 0.147 in,  ∆d22 = 0.0216 in2

∆d22 A2= 0.518 in4

∆d5 = 2.147 in,  ∆d22 = 4.6096 in2

∆d22 A2= 68 in4

Also:

∑Ii = Ixx1 + Ixx2 + Ixx3 + Ixx4 - Ixx5

= (894 + 5.33 + 1.208 + 288 – 32.3) in4

= 1,156 in4

∑∆di2 Ai = (0.544 + 1,196 + 894 + 0.518 - 68) in4

= 2,023 in4

Itotal =∑Ii +∑∆di2 Ai

= 3,179 in4

Sxc1  = Itotal  ÷ 8.353 in = 380 in3

Sxc2  = Itotal  ÷ (18- 8.353) in = 329 in3

The max. calculated bending stress fb:

fbc =  Mmax / Sxc1 → compressive bending stress

= 2,751,000 lbs-in ÷ 380 in3

= 7.239 ksi < Fb = 12 ksi,

fbc =  Mmax / Sxc1 → tensional bending stress

= 2,751,000 lbs-in ÷ 329 in3

= 8.362 ksi < Fb = 12 ksi,

The calculated shear stress fv:

fv =  Fy / Atotal = 78,740 lbs / 64.94 in2  = 1.213 ksi < Fv = 12 ksi

2.2a. The working stress at the location where x=19.94” away from the end of the lifting

fixture (x =19.94”):

Per figure 2.3, as it indicating, there is no top connecting plate. However, an 8”x4”x1/4”  rectangular tube locates in the middle. The sectional modulus Sxc  and the other geometrical properties at the location of x = 19.94” of the lifting fixture with respect the strong axis x-x are calculated as following:

Figure 2.3, The cross section view of the lifting fixture at the x = 19.94” location

Ixx1 = (447 x 2) in4 = 894 in4    for two S15 x 42.9 I-beams

A1 = 12.6 in2 x 2 = 25.2 in2

y1 =   7.5 + 1 = 8.50 in

Ixx2 =(14.50 x 13) / 12  in4 = 1.2083 in4

A2 = 1.0 x 14.50 in2 = 14.50 in2

y2 =  0.50 in

Ixx3  = (10.56 x (8.03- 7.503) ÷ 12) in4 = 79.31 in4

A3 = 0.25 x 10.56 x 2 in2 = 5.28 in2

y3 =  (4.50 + 4.00) in = 8.50 in

Since  y = ∑Aiyi ÷ ∑Ai

= ((25.2 x 8.5 + 14.5 x 0.5 + 5.28 x 8.5) / 44.98 ) in

= 5.921 in

∆d1 = 2.579 in,  ∆d12 = 6.651 in2

∆d12 A1= 167.605 in4

∆d2 = 5.421 in,  ∆d22 = 29.387 in2

∆d22 A2= 426.111 in4

∆d3 = 2.579 in,  ∆d32 = 6.651 in2

∆d32 A3= 35.117 in4

Itotal =∑Ii +∑∆di2 Ai  = ((894 + 1.208 + 79.31) + (167.605 + 426.111 +35.117)) in4

= (974 + 628) in4

= 1,602 in4

Atotal = A1 + A2 + A3 =  44.98 in2

Sxc  = Itotal  ÷(16 – 5.921) in = 158.9 in3

The moment @ this location when the fixture is lifted:

M@ x=19.94”  = 19.94 in x 39,370 lbs = 785,038 lbs- in

The calculated bending stress fb:

fb =  M@ x=19.94” / Sxc

= 785,038 lbs-in ÷ 158.9 in3

= 4.94 ksi < Fb = 12 ksi,

The calculated shear stress fv:

fv =  Ri / Atotal = 39,370 lbs / 44.98 in2  = 0.876 ksi < Fv = 12 ksi

The working stresses of the lifting fixture are satisfactory when it is subjected 38 tons lifting force vertically.

I don’t think the deflection is an issue for this application regarding the values of the calculated working stresses. To this end, I omit the calculations of the fixture deflection.

3, The discussions of the lifting pin and the others:

3.1,  The size of the pin and the material:

As showing from figure 1.2, there is on lifting pin locates in the center (axial dir. of the fixture) of the fixture.  Per figures 2.1 and 2.2, it can assume the following force distribution data:

Load case: simple beam with concentrated load at the center

L = 10.0” (See figure 2.2)

Py = 78,740 lbs.

R1 = R2 = 39,370 lbs.

Mmax = (Py L) / 4  (@ the center of the span L)

= (78,740 lbs x 10 in) / 4

= 196,8500 in-lbs.

Assuming use a cold finished round steel (C1018, ASTM 108) with dia. 5.0 in,

where:

Fu = 64 ksi, Fy = 54 ksi

The allowable stresses:

Fb =  Fy /3.0 =  18 ksi = Fv = Ft

(per section 20-1.2.2.2, ASME B30.20)

then:

Ixx = Iyy = (π d4) / 64  = 30.68 in4

Sxx= I ÷ r = 12.272 in3

Apin = (π d2) / 4 = 19.63 in2

fb =  Mmax / Sxx = 196,850 in-lbs / 12.272 in3

= 16.041 ksi  < Fb =  18 ksi

fv =  Ri / Apin= 39,370 lbs / 19.63 in2

= 2.006 ksi < Fv =  18 ksi

3.2,  Bearing stresses of the pin hole area:

Abearing = (1.4375 x 5.00) in2

= 7.1875 in2  → the bearing area of the hole, see fig. 2.2 for more details

fp =  Ri / Abearing = 39,370 lbs / 7.1875 in2

= 5.478 ksi < Fp =  12 ksi

The design of the pin and the pin hole area are satisfactory.

4. The connecting bolt and the welds of the lifting fixture:

4.1,  The connecting bolts:

The lifting fixture is designed to use 8 bolts (4 bolts at each end of the fixture) to connect with the Scibar & EC detector or other connecting partner (see figures 1.1 & 1.2)

The spec. of the bolt:  ASTM A325, 1”- 8 UNC, 31/2” length

Ft = 44 ksi (allowable tensile stress)

Pt = 34.6 kip (allowable tensional load for nominal 1” dia. bolt)

(per page 4-3, part 4, ASD 9th edition)

Total allowable tensional load for eight 1” dia. A325 bolts:

8 x 34.6 kip = 276.8 kip > 78.74 kip.

The computed pull out force Pout from the base metal:

Per eq. 5.3.2.1-1, section 5.3.2.1, part I-A of “Aluminum Design Manual” 6th edition,

Pout = 0.85 tb D Ftb

= 0.85 x 1.25 in x 1.00 in x 58 ksi

= 61.62 kip (per bolt bearing area) > 78.74 kip/8 = 9.85 kip

Where: tb  the thread bearing length on base metal (see drawing ME - 435903)

D.the nominal dia. of the bolt

Ftb. The tensile strength of the base metal  (see drawing ME - 435903)

So the bolt selection is satisfactory subject to the applying loads.

4.2, The welding calculations:

The welds at the end bottom bearing plate area with subject to the lifting force:

Per figure 1.1, figure 1.2 and drawing of ME – 444427, it is found that all the welds do not subject any significant moments along the major axis. However, we still present some welding calculations to make sure that all welding sizes are satisfactory.

Figure 4.1,  The welds at the bottom bearing plate of the lifting fixture

Figure 4.1 is the welding configuration for the bottom bearing plate (omitting the gussets conservatively). Treating the welds as a line, then:

L = (5.5 x 4 + 8.5 x 2 + (8.5 -1.5) x 2) = 53 in  *

R1 = R2 = 39,370 lbs.

fv = R1 / L = 39,370 lbs / 53 in

= 743 lbs/in

*:  Where 1.50” is the free of weld zone for the bolt washer access.

C = working load per unit length ÷ (effective factor × allowable stress)

= (743 lbs/in) ÷ (0.707 x 21 ksi) (See page 4 for Fv value)

= 0.05 in < 0.375 in (designated weld size in the area)

Where: C is the size of the weld.

The welds subject to the minor axis (assuming the z axis of the lifting fixture) moment:

When the lifting fixture is lifting through the bottom bearing plate, we have discussed the primary and secondary stresses subject the major axis moment in section 2 of page 5 to page 9. Here are the discussions of the welds subject to the minor axis moment:

Per drawing of ME – 444427, there is an 8”x4”x1/4” tube to connect two beams together at each end of the fixture. Let’s conservatively assume that the tube will take all the loads and moment at this location as showing from figure 4.2. By referring to figure 2.1, it is found that:

L = 21.25 in,

R1 = R2 = 39,370 lbs/2 = 19,685 lbs.

The moment @ x = 5.34” (where the tube welds to the beam)

Mx=5.34 = 19,685 lbs x 5.34 in

=  105,118 lbs-in

Figure 4.2, The end connecting tube and the welds of the lifting fixture.

Per figure 4.2, treating the welds as a line, it is found that:

( per page 276, table 5.16.1, part 5, “Steel Structures” by C. Salmon & J.

Johnson, 3rd edition)

d = 8.0 inch, b = 4.0 inch

Lw = 2 ( 6+3)  = 18 in   length of the welds

Ixx = d2 (3b + d)/ 6

= 213.33 in3

Sxx = d (3b+d) / 3

= 53.33 in2

fv = R1 / Lw = 19,685 lbs / 18 in

= 1,094 lbs/in

fb =  Mx=5.34 / Ixx = 105,118 lbs-in / 53.33 in2

=  1,971 lbs/in

fr  =  ( fb2 + fv2 )½ = (1,0942 + 1,9712 )½

=  2,255 lbs/in

C = combined working load per unit length÷ (effective factor × allowable

stress)

= (2,255 lbs/in) ÷ (0.707 x 21 ksi)

= 0.152 in < 0.187 in (designated weld size in the area)

Where: C is the size of the weld

The designated weld sizes are satisfactory.

Conclusions:

The lifting fixture has been designed per the related engineering codes after the calculations and discussions from several the most critical areas, such discussions were

approached by computing the working structural stresses, bolt stresses and weld sizes in

terms of the different applications.

Reference drawings related to this engineering note:

3954.330- ME – 444427

MC – 444423

MC – 444425

MC – 444426

MC – 444449

MC – 444439

ME – 444071 -1

ME – 435903 -1

# Text boxes

x

a

L

R2

P

R1