Construction Specification 742—Concrete Pipe Conduits and Drains

1.	Scope

The work shall consist of furnishing and installing concrete pipe or concrete drain tile and the necessary fittings as shown on the drawings.

2.	Material

Concrete culvert pipe shall meet the requirements of Section 850.01, Concrete Pipe, of the latest edition of the Alabama Department of Transportation Standard Specifications for Highway Construction.  Pipe class shall be as specified in Section 8.

3.	Laying and bedding

Pipe and tile shall be laid to the line and grade shown on the drawings. Unless otherwise specified, belled pipe shall be laid with the bells or grooves facing upstream.

4.	Joints

Pipe joints shall conform to the details shown on the drawings and to the requirements of Sections 5 and 6 of this specification applicable to the type of joint specified. Except where unsealed joints are indicated, pipe joints shall be sound and watertight at the pressure specified.

5.	Joining tongue and groove pipe

Cement mortar sealed joint

Mortar shall be as specified for bell and spigot joints. The tongue end of the section being placed shall be covered with mortar and firmly pressed into the groove of the laid section so that the tongue fits snugly and truly in the groove and that mortar is squeezed out on both the interior and exterior of the joint. Care shall be taken that no mortar falls from the groove end during the abutting operation. Immediately after the pipe sections have been abutted, exposed external surface mortar shall be pressed into the joint and any excess mortar removed. After this is done, the interior surface of the joint shall be carefully pointed and brushed smooth and all surplus mortar removed.

6.  Curing Mortar Joints and Bands

The external surfaces of mortar joints shall be covered with moist earth, sand, canvas, burlap or other approved materials and shall be kept moist for 10 days or until the pipe is backfilled.

7.	Measurement and payment

Method 1—For items of work for which specific unit prices are established in the contract, the quantity of each kind, size, and class of pipe or tile is determined to the nearest 0.l foot by measurement of the laid length along the invert centerline of the conduit.  Payment for each kind, size, and class of pipe or tile is made at the contract unit price for that kind, size, and class.  Such payment constitutes full compensation for furnishing, transporting, and installing the pipe or tile complete in place.

Method 2—For items of work for which specific unit prices are established in the contract, the quantity of each kind, size, and class of pipe or tile is determined as the sum of the nominal laying lengths of the sections used. Payment for each kind, size, and class of pipe or tile is determined as the sum of the nominal laying lengths of the sections used. Payment for each kind, size, and class of pipe or tile is made at the contract unit price for that kind, size, and class. Such payment constitutes full compensation for furnishing, transporting, and installing the pipe or tile complete in place.

All methods—The following provisions apply to all methods of measurement and payment. Compensation for any item of work described in the contract, but not listed in the bid schedule, is included in the payment for the item of work to which it is made subsidiary. Such items and the items to which they are made subsidiary are identified in section 11 of this specification.

8.	Items of work and construction details

Items of work to be performed in conformance with this specification and the construction details therefore are:

Bid Item 17, Concrete Pipe, 24in. Diameter

- This item shall consist of furnishing and installing the reinforced concrete pipe conduit and appurtenances as shown on the drawings.

- The pipe shall be class III.

- A concrete collar shall be installed at the junction of the existing pipe and new pipe if the pipe joints are not compatible and a water tight joint cannot be achieved.  Use of the collar will be approved by the Contracting Officer's Representative. The concrete collar shall be constructed in accordance with the details shown on the drawings. Concrete shall be furnished in accordance with Construction Specification 732, Concrete.

- Measurement and payment shall be by Method