Subject:	Comments, Docket No. FAA–2008-0616; Directorate Identifier 2007–NM–353–AD, Model 767 Engine Suction Feed Test

References:	(a)	Boeing 767 MPD Section 6 Tasks 28-22-00-5G (MRB 28-040)

- Boeing 767 Task Card 28-018-02

- Boeing 767 AMM task 28-22-00-725-575

- Boeing 767 AMM task 28-22-07-796-001

British Airways has reviewed the subject NPRM and provides the following comments.

- British Airways recognises the need to test the ability of the engine to suction feed regularly to ensure correct operation in the event of loss of pressurised engine fuel feed.

2.	The task required by the NPRM is already covered by the ref (a) Boeing767 MPD tasks at 1C Check (6,000 hrs, 3,000 cyc, 18 mths).

3.	Although the Boeing task card for the ref (a) MPD item is ref (b) and links to ref (c) AMM procedure, the MPD item also offers an alternative procedure that covers the intent of it. Ref (d) AMM procedure covers the alternative procedure.

4.	The NPRM sets the issue date for the manual to be used to 22 August 2007. BA does not hold previous issues of AMM or Boeing task cards for general use. BA engineers only use the latest revision of the instructions.

5.	British Airways request the following:-

- The NPRM references the Boeing MPD task associated with this check.

ii.	The NPRM acknowledges and allows use of either procedure quoted in the MPD.

iii.	The NPRM allows for using AMM and Boeing task cards that have more recent issue dates than 05 May 2007.