SPILL  PREVENTION,  CONTROL,  AND  COUNTERMEASURES

BEST  MANAGEMENT  PLAN

N O A A

NATIONAL WEATHER SERVICE

Goodland Weather Forecast Office

920 Armory Road

Goodland, Kansas  67735

Designated Person Responsible for Spill Prevention (DRO):

Printed Name:			Scott Mentzer

Signature:

Date:

Telephone:			(785) 899-2360

The Regional Environmental Compliance Officer (RECO)  has reviewed the facility and determined that an SPCC Plan is not required per 40 CFR 112.  This Plan is developed strictly as a Best Management Plan.  The determination is based on:

X   	The facility does not exceed capacity.

The facility meets capacity requirements but, a discharge will not reach navigable waterways.

RECO Printed Name:		Sherilyn Villegas

RECO Signature:

Date:

PART I - GENERAL INFORMATION

A.	GENERAL

This section of the Best Management Plan provides general information about the facility.

  - Name:

National Weather Service (NWS) Goodland Weather Forecast Office (WFO)

  - Date of Initial Operation:

February 20, 1991

  - Location:

Street: 			920 Armory Road

City: 			Goodland

State/Zip Code: 	Kansas / 67735

Latitude:

Longitude:

4.	Name and phone number of owner (POC)

Scott Mentzer, Environmental Focal Point (785) 899-2360

5. 	Facility Contacts

Name             		Title/EC Role    			Telephone Number

Scott Mentzer		Environmental Focal Point		(785) 899-2360

B. 	SITE DESCRIPTION AND OPERATIONS

The facility is located in Sherman County, Kansas, just north of the outskirts of Goodland.  The facility’s aboveground storage tanks (AST) are used to store diesel fuel for emergency backup generators that provide emergency power to the WFO.  The Goodland WFO contains a total of four ASTs, including a 500-gallon AST, two 225-gallon ASTs, and a 25-gallon day tank.

Fuel usage for the weather station is estimated at 80 gallons per month, based on fuel records for a 6-month period.  The WFO generator is tested for 30 minutes per week.  Fuel consumption would increase based on the frequency and duration of any power outages.

In addition to the diesel fuel used for emergency power generation, this facility also stores small amounts of other chemicals (e.g., paint, solvents, antifreeze, and pesticides) for maintenance activities in a dedicated flammable locker located within a WFO building storage room.

Appendix A includes a Tank Ullage and Fueling Log (Appendix A-1) that should be used when fuel is delivered.  Appendix A-2 includes a Fuel Unloading Procedure Checklist that should be completed when fuel is delivered.

PART II - SPILL COUNTERMEASURES AND REPORTING

- SPILL COUNTERMEASURES

This section presents countermeasures to contain, clean up, and mitigate the effects of an oil spill that impacts navigable waters or adjacent shorelines.

A spill containment and cleanup activity will never take precedence over the safety of personnel.  No countermeasures will be undertaken until conditions are safe for workers.  The SWIMS procedure should be implemented as countermeasures:

S   -	Stop the leak and eliminate ignition sources.

a. 	Attempt to seal or some how stop leak if it can be done safely.

b. 	Attempt to divert flow away from the drainage ditch with a spill barrier or the contents of spill kit. The spill kit is located near the day tank in the generator room.

c. 	Eliminate all ignition sources in the immediate area.

W  -	Warn others.

a.  	Yell out “SPILL.”  Inform the person in-charge at your facility.

b. 	Account for all personnel and ensure their safety.

c. 	Notify contacts and emergency response contractor as described in the following section for assistance in control and cleanup.

I    -	Isolate the area.

a. 	Rope off the area.

M  -	Minimize your exposure.  Stay upwind.

S    -	Stand by to assist the emergency response contractor, if necessary.

B. 	SPILL REPORTING

1.  General Notification Procedures for All Spills

Within 24 hours, the responsible person or designee (DRO on this plan title page) is directly charged with reporting all oil spills that result from facility operations as follows

    - In the event of an emergency (for example, fire or injury), call 9-1-1

b.	Notify the appropriate persons within your region and line office.

National Weather Service:

Mike Jacob, NWS Environmental Compliance Officer

Phone number: (301) 713-1838 Ext. 165, Jmichael.Jacob@NOAA.GOV

Olga Kebis, NWS Safety Officer

Phone number: (301) 713-1838 Ext. 173, Olga.Kebis@NOAA.GOV

Kirt Grahl, NWS Midwest Regional Environmental/Safety Coordinator

Phone number: (816) 426-3226 Ext. 470, Kirt.Grahl@NOAA.GOV

c.	Notify the appropriate Regional Environmental Compliance Officer (RECO) at the NOAA Environmental Compliance and Safety Office Program.

Sherilyn Villegas, Central Regional Environmental Compliance Officer

Phone number: (816) 426-3925 Ext. 263, Sherilyn.S.Villegas@NOAA.GOV

- RECO must determine if Federal or State notification is required and follow up accordingly.

2.  Cleanup Contractor Notification

An emergency response contractor should also be notified to assist with the clean up if necessary.  NWS  has identified and contacted the following contractors that are available for an emergency response:

Contractor					Phone Number

D J Environmental				(888) 564-5550

Philip Environmental Services			(800) 567-7455

Hertel Tank Services Inc.			(785) 628-6061

3.  Spill Report

Complete a spill report using the format provided in Appendix B.  Send this to the RECO.

C.  Training

The Environmental/Safety Focal Point and an alternate should be trained in spill countermeasures.  The alternate should be designated in case the primary person is off site at the time of a spill.

# Comments

Bottom of Form