| Radiocommunication Study Groups |  |
| --- | --- |
| Source: Document 5-6/TEMP/27 Subject: WRC-11 Agenda item 1.17, Resolution 749 (WRC-07), Circular Letter CA/171 | Annex 8 to Document 5-6/53-E |
|  | 19 November 2008 |
|  | English only |
| Annex 8 to Joint Task Group 5-6 Chairman’s Report |
| Note from Chairman JTG 5-6 to chairman of Working Party 3K |
| Propagation models needed for use in sharing studies at UHF frequencies |

At its second meeting held in Geneva 4-10 November 2008, JTG 5-6 discussed various aspects related to the sharing of mobile services with other services allocated on a primary basis in the band 790-862 MHz.

Joint Task Group 5-6 has developed preliminary draft methodologies (including interference objectives) for sharing studies between the mobile service, on the one hand, and the terrestrial broadcasting, fixed and aeronautical radionavigation services, on the other hand, in the band 790-862 MHz.

Input contributions to JTG 5-6 suggested a propagation model based on elements of the ITU-R Recommendation P.1546-3 and the Okumura-Hata model (Report ITU-R SM.2028) to address sharing studies between the broadcasting and the mobile services (see Appendix A of Annex 1 of Document 5-6/53, Annex 7).

Joint Task Group 5-6 kindly requests the advice of WP 3K on the appropriate propagation models to be used in sharing and compatibility studies between systems in the mobile service and systems of other services in the band 790-862 MHz.

JTG 5-6 also kindly requests that WP 3K provides details on the most appropriate building penetration loss figures applicable to the band 790-862 MHz to allow the best unified approach to these sharing studies (see Tables 4.1 – 4.3 and 4.6 – 4.7 of Annex 1 of Document 5-6/53, Annex 7).

Joint Task Group 5-6 would appreciate any comments WP 3K (or the WP 3K Chairman) can provide on these issues as soon as possible noting that JTG 5-6 must commence its sharing and compatibility studies in the near future so that preliminary results can be available at its next meeting to be held in Geneva, Switzerland, 11-15 May 2009.

Joint Task Group 5-6 thanks WP 3K for its consideration of these matters.

# Status:		For action

# Contact:	Roland Beutler (JTG 5-6 SWG2 Chairman)

# Attachment:	Document 5-6/53, Annex 7 (http://www.itu.int/md/R07-JTG5.6-C-0053/en)