Specification for a 805 MHz Fast Phase Shifter

Specification for Shorted Stub Tuner:

Frequency = 805 MHz +/-2.5 MHz

Fast Phase Shift = +/- 45 Degrees without attenuation

Fast attenuation Change = 3 dB with 90 Degree phase Shift

Forward RF power = 320 kW at Duty Cycle of 1.5 %

Reverse RF power = 320 kW at Duty Cycle of 1.5 %

Typical Pulse lengths = 1.5 ms, 2.5 ms, 3.5 ms and 4.5 ms

Tuning Time response  = 100 μs , Vendor is responsible

For eddy current compensation

Circuit, magnetic circuit, magnets

And transformer network circuit

requited to meet the fast response

specification. Power supply

specification also requited from

Vendor to meet this specification.

Power Supply to be supplied by

Fermilab.

Insertion Loss  = less than 0.15 dB, 805. +/- 2.5 MHz

Response time requested for phase changes of +/- 22.5 Degrees

Response time requested for attenuation delta of 3 dB and

1.5.dB.

Design could be wav guide or Coax Hardline.