# UNITED STATES ENVIRONMENTAL PROTECTION AGENCY

# WASHINGTON D.C., 20460

# MEMORANDUM	Date:  September 12, 2006

SUBJECT:	Environmental Fate and Ecological Risk Assessment Chapter (DP Barcode D310733) in Support of Phase I of the Reregistration Eligibility Decision on Antimycin A (PC Code 006314)

# FROM:	Dirk Young, Ph.D., Environmental Engineer

# Thomas Steeger, Ph.D., Senior Biologist

# Environmental Risk Branch IV

# Environmental Fate and Effects Division (7507C)

# Office of Pesticide Programs

# THROUGH:	Elizabeth Behl, Branch Chief

Environmental Risk Branch IV

Environmental Fate and Effects Division (7507C)

Office of Pesticide Programs

TO:		Lance Wormell, Chemical Review Manager

# Dirk Helder, Risk Manager

# Special Review and Reregistration Division (7508C)

# Office of Pesticide Programs

The Environmental Fate and Effects Division (EFED) has completed the draft environmental fate and ecological risk assessment chapter (DP Barcode D310733) in support of Phase I of the reregistration eligibility decision on antimycin A (PC Code 006314).  Conclusions regarding the environmental fate, ecological effects and ecological risks associated with the current uses of antimycin A can be found in the executive summary of the attached document.  EFED recommends that application of antimycin directly to water only be made through close adherence to established standard operating procedures intended to limit the extent to which antimycin can move outside of treatment areas.

The risk assessment relies on a treatment rate of 25 µg/L.  This is a rough approximation of the maximum rate since the label was not specific.  This rate is based on the use closure memo dated October 26, 2005.

Data Gaps

Table A1 identifies the status of environmental fate and transport study requirements and Table A2 identifies the status of ecological effects study requirements.  In a memo (DP Barcode D276036) dated July 20, 2001, aqueous photolysis (Guideline §161-2), leaching-adsorption-desorption (Guideline §163-1), and anaerobic aquatic metabolism (Guideline §162-3) studies were waived assuming that antimycin is inactivated after the desired kill is achieved.  The only guideline studies that were required are hydrolysis (Guideline §161-1) and aerobic aquatic metabolism (Guideline §162-4) focusing on parent compound alone and not its degradates.  Although hydrolysis data are available on antimycin, there is considerable variability in the data and degradation half-lives range from 30 minutes to 47 days.  Additionally, while there are anecdotal data suggesting that antimycin A is inactivated through the use of an oxidant, e.g. potassium permanganate, there are no data to identify the reaction products.    Although environmental fate data gaps have been identified, efforts are underway by the U. S. Geological Survey, the EPA Office of Research and Development and the Office of Pesticide Programs’ Biologic and Economic Assessment Division laboratories to address some of the uncertainties regarding analytical method development and potential routes of degradation.

Most of the ecological effects data gaps result from uncertainties surrounding potential ecological risks associated with the chronic effects of antimycin in aquatic animals (Guideline §72-4) and terrestrial animals (avian Guideline §71-4 and mammalian Guideline §83-4).  Additionally, there are no data to evaluate the toxicity of antimycin to aquatic (Guideline §123-2) or terrestrial plants (Guideline §123-1).  These data are important in assessing direct and indirect risks to Federally-listed endangered and/or threatened species.

# Labeling Recommendations

According to the Label Review Manual, the following label statements are recommended:

Non-Target Organism Statements

The following statement is required because the pesticide is intended for outdoor use and contains an active ingredient which has a mammalian acute oral LD50 ≤100 mg/kg:

"This pesticide is toxic to mammals."

The following statement is required because the pesticide is intended for outdoor use and contains an active ingredient with a fish acute LC50 and an aquatic invertebrate EC50 ≤1 ppm:

"This pesticide is toxic to fish, aquatic invertebrates, oysters and shrimp.”

| Table A1. Environmental Fate and Transport Data Requirements for Antimycin A |
| --- |
| Guideline # | Data Requirement | MRID / ACC # | Study Classification | Are Data Adequate for Risk Assessment? |
| 161-1 | 835.2120 | Hydrolysis | MRID 46023101 | Supplemental | YES |
| 161-2 | 835.2240 | Photodegradation in Water | Waived |
| 161-3 | 835.2410 | Photodegradation on Soil | Waived |
| 161-4 | 835.2370 | Photodegradation in Air | Waived |
| 162-1 | 835.4100 | Aerobic Soil Metabolism | Waived |
| 162-2 | 835.4200 | Anaerobic Soil Metabolism | Waived |
| 162-3 | 835.4400 | Anaerobic Aquatic Metabolism |  |  |  |
| 162-4 | 835.4300 | Aerobic Aquatic Metabolism | 458959-01 | Supplemental | YES |
| 163-1 | 835.1240 835.1230 | Leaching-Adsorption/Desorption | Waived |
| 163-2 | 835.1410 | Laboratory Volatility | Waived |
| 163-3 | 835.8100 | Field Volatility | Waived |
| 164-1 | 835.6100 | Terrestrial Field Dissipation | Waived |
| 164-2 | 835.6200 | Aquatic Field Dissipation | No data submitted |
| 164-3 | 835.6300 | Forestry Dissipation | No data submitted |
| 165-4 | 850.1730 | Accumulation in Fish | In Reserve |
| 165-5 | None | Accumulation-Aquatic, Non-Target | Waived |
| 166-1 | 835.71 | Small Scale Prospective Groundwater | Waived |
| 166-2 | None | Small Scale Retrospective Ground Water | Waived |
| 166-3 | None | Large Scale Retrospective Ground Water | Waived |

| Table A2. Ecological Effects Data Requirements for Antimycin A. |
| --- |
| Guideline # and Data Requirement | Species | Test Materiala (% a.i.) | MRID/ACC# | Study Classification | Are Data Adequate for Risk Assessment? |
| Avian and Mammalian Studies: |
| 71-1, Acute Avian Oral, Quail/Duck | Mallard duck | NS | 135924 | Supplemental | YES |
|  | Bobwhite quail | NS | 135924 | Supplemental | YES |
| 71-2, Acute Avian Diet, Quail/Duck |  | No Data Submitted |  |
| 71-4, Avian Reproduction, Quail/Duck |  | No Data Submitted |  |
| 81-1, Acute Mammalian Oral LD50 | Rat |  |  |  |  |
| 83-1, Chronic Tox Rodent | Rat | No Data Submitted |  |
| Freshwater Fish Studies: |
| 72-1, Acute Freshwater Fish Toxicity | Bluegill sunfish Green sunfish Rainbow trout Cutthroat trout Coho salmon Lake trout Goldfish Fathead minnow Black bullhead Channel catfish Mosquito fish Largemouth bass Yellow perch White crappie Paddlefish | 95.5% | 400980-01 | Supplemental | YES |
| 72-4(a), Early Life-Stage Fish |  | No Data Submitted |  |
| 72-5 Life Cycle Fish |  | No Data Submitted |  |
| Freshwater Invertebrate Studies: |
| 72-2(a), Acute Freshwater Invertebrate Toxicity | Waterflea Scud Isopod | 95.5% | 400980-01 | Supplemental | YES |
| 72-4(b), Life Cycle Aquatic Invertebrate |  | No Data Submitted |  |
| Estuarine/Marine Fish Studies: |
| 72-3, Acute Estuarine/Marine Tox Fish LC50 | Spot | 95.5% | 400980-01 | Supplemental | YES |
| 72-3, Acute Estuarine/Marine Tox Invertebrate LC50 |  |  |  |  |  |
| 72-4, Chronic Estuarine/Marine Tox Fish NOAEC |  | No Data Submitted |  |
| Estuarine/Marine Aquatic Invertebrates: |
| 72-3(b), Acute Estuarine/Marine Mollusk |  | No data submitted | NO |
| 72-3(c), Acute Estuarine/Marine Shrimp | Pink Shrimp | 95.5% | 400980-01 | Supplemental | YES |
| 72-4, Chronic Estuarine/Marine Shrimp |  | No data submitted | NO |
| Terrestrial and Aquatic Plants: |
| 122-1, Seedling Emergence and Vegetative Vigor |  | No Data Submitted | NO |
| 122-2, Aquatic Plant Growth (Tier I) |  | No Data Submitted | NO |
| 123-1, Seed Germ, Seedling Emergence, Vegetative Vigor (Tier II) |  | No Data Submitted | NO |
| 123-2 Aquatic Plant Growth (Tier II) |  | No Data Submitted | NO |
| Terrestrial Insect Testing: |
| 141-2, Honey Bee Residue on Foliage |  | No Data Submitted | NO |
| 144-1, Honey Bee Acute Contact |  | No Data Submitted | NO |

a TGAI = technical grade active ingredient; TEP = typical end-use product; ND = not determined, because purity was not reported or original study was unavailable.

b Study was classified as supplemental pending upgrade to acceptable.  The upgrade was denied, but for piscicidal uses EPA did not require a repeat of the study due to the preponderance of data available.

# Comments

BR: Again, use of 25 ppb Fintrol per application seems very high, and needs to be documented.  Throughout the document, it needs to be clear if the discussion is about ppb/mg/l of Fintrol or antimycin A.

BR: I would think the data is better than “ancecdotal” that Fintrol is neutralized by potassium permanganate.  This is the same process used to neutralize rotenone.  The Assessment does reference the publication by Moore.