WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A10942 | In-Flight Anomaly Number -- | Contractor Report Number P-059-1 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title PROPULSION LINE PD4800175-030 X-RAY REVIEW INTERPRETATIONS (L02 FEEDLINE, FWD ELBOW) |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT 1 | Sys_Lvl N | Misc Codes A (4) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE ET | PART# 80901000000 | SER/LOT# NOTED | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE LO2 PROP FEED | PART# 80971028465 | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE PROPULSION LINE | PART# PD4800175-030 | SER/LOT# 171 | MANUFACTURER ARROWHEAD |
| Test/Operation L - FLD | Prevailing Condtion N - INSPECTION | F / U F | Fail Mode UC - UNSAT | Cause MAW - MFG-ASY-WORK |
| System PROPULSION | Defect DC - BROKEN | Material M - LINK-G | Work Contact J. FINCHER | Fail Date 07/17/1987 |
| Received at MSFC 08/14/1987 | Date Isolated -- | FMEA Reference 2.1.7.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MMC | Symptom UC - UNSAT | Time Cycle -- |
| Effectivity Text LWT 16 AND UP |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 11/04/1991 | CN RSLV SBMT 05/17/1988 | Defer Date -- | Add Date -- | R/C Codes 5 - TRNG -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR P. BRIDWELL |
| Approval |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR P. BRIDWELL |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 06/03/1988 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description DURING A SECOND REREVIEW ON X-RAYS ON LWTS 21 AND 16, PROPULSION LINES, INTERPRETATIONS WERE IN- CONSISTENT WITH PREVIOUS REVIEWS. X-RAYS INDICATIONS WERE DOCUMENTED WHICH HAD NOT BEEN PREVIOUSLY REPORTED REF. CAPS P-053 AND MARS T-93899 |
| Contractor Investigation/Resolution R/C: 1- A COMPLETE RE-REVIEW OF EXISTING X-RAYS UNDER TD808 2- ENHANCEMENT OF THE X-RAY TESTING PROGRAM THIS IS A LAUNCH CONSTRAINTS FOR LWTS 21 AND 16. THE CONSTRAINTS RATIONALE AS FOLLOWS: LINE RUP- TURE WOULD BE CATASTROPHIC. THIS STATEMENT HAS BEEN COORDINATED WITH: ____________________________________________ MR. G. P. BRIDWELL, ET PROJECT MANAGER, ___________________________________________ MR. J NICHOLS, ET CHIEF ENGINEER 12/17/87 FAILURE MODE: WELD FAILURE ON PROPULSION LINES CAUSE: EMPLOYEE/VENDOR ERROR 5/3/88 PRB UPDATE: SENIOR MRB HAS DISPOSITIONED THIS ITEM AS "USE AS IS" WHICH CLEARS LWT 21 FOR FLIGHT THIS REPORT HAS BEEN DEFERRED FOR STS-26, PER NSTS 07700, VOLUME XI AND NSTS 08126 PARAGRAPH 3.4.1, ITEM C WHICH STATES "PROBLEM CONDITION DOES NOT EXIST IN THE FLIGHT HARDWARE AND IS CLEARLY SCREENED BY ACCEPTANCE TEST, PREFLIGHT CHECKOUT, OR SPECIAL TEST." THE DEFERRAL STATUS HAS BEEN APPROVED BY THE ET PROJECT MANAGER, MR. G.P. BRIDWELL _______G.P. BRIDWELL (SIGNED) 5/13/88______ 5/17/88 - GENERAL: THESE INDICATIONS HAVE BEEN DOCUMENTED ON MARS AND FINAL DISPOSITIONS ARE FORTHCOMING TASK I FAILURE/PROBLEM INVESTIGATION AS A RESULT OF STS 51L, TD808 WAS INITIATED TO REREVIEW ALL MAF/VENDOR ET WELD X-RAYS. THIS ACTIVITY WAS CONDUCTED BY PERSONNEL WHICH HAD PERFORMED THE ORIGINAL ACCEPTANCE REVIEW. THERE WAS NO FINDINGS DOCUMENTED AS A RESULT OF THIS ACTIVITY. ANOTHER REVIEW WAS CONDUCTED BY PERSONNEL UNASSOCIATED WITH THE TWO PRIOR X-RAY REVIEWS. THIS INDEPENDENT REVIEW REVEALED SEVERAL ANOMALOUS CONDITIONS IN PROPULSION LINES THE REVIEW ACTIVITY WAS COORDINATED TO COMPLETE X-RAYS BY EFFECTIVITY, LWTS 16 AND 21 BEING THE FIRST VEHICLES REVIEWED. SUBSEQUENT REVIEW ACTIVITY WILL EXAMINE WELDS ON ALL EXISTING HARDWARE TASK II CORRECTIVE ACTION IT HAS BEEN DETERMINED THAT THE FOLLOWING ACTIONS ARE REQUIRED TO PRECLUDE A RECURRENCE OF X-RAY MISINTERPRETATION A. DISCIPLINARY ACTION FOR THE MMC PERSONNEL ASSOCIATED WITH X-RAY MISINTERPRETATION CLOSURE STATEMENT THIS ACTION HAS BEEN COMPLETED. REFERENCE DEPARTMENT 3700 MEMORAN- DUM DATED JULY 27, 1987 X-RAY CERTIFICATION WAS REVOKED FOR THE EMPLOYEES INVOLVED B. IMPLEMENT REAL TIME INSPECTION OF WELD X-RAYS BY PROCUREMENT QUALITY AT THE VENDOR'S FACILITY CLOSURE STATEMENT ACTION IS COMPLETE. PER MEMO 3761-87-193, REAL TIME X-RAY INSPECTION IMPLEMENTED AS OF 8/31/87 C. ENHANCE TRACEABILITY OF VENDOR DOCUMENTATION TO SPECIFIC COMPONENTS CLOSURE STATEMENT ACTION IS COMPLETE. REFERENCE ATTACHED MEMO 3761-87-193 WHICH DESCRIBES IMPROVED TRACEABILITY PROCEDURES D. PREPARE AND RELEASE A PLAN TO CREATE WORKMANSHIP STANDARDS FOR UNIQUE CONDITIONS AT VENDORS AND MAF CLOSURE STATEMENT REFERENCE MEMO 3770-88-028. ACTION IS COMPLETE. REFERENCE TASK II-P E. REVIEW X-RAY CERTIFICATION PROGRAM AT VENDORS AND MAF CLOSURE STATEMENT ACTION IS COMPLETE. REFERENCE ATTACHED MEMO 3720-87-070. PROGRAM WAS FOUND TO BE ACCEPTABLE F. EVALUATE PERSONNEL AWARENESS AS IT RELATES TO LESSONS LEARNED AT THE VENDOR AND MAF CLOSURE STATEMENT ACTION IS COMPLETE. REFERENCE MEMO 3760-87-331. PERSONNEL ARE COGNIZANT OF RECENT X-RAY MISINTERPRETATIONS G. ESTABLISH A SEMIANNUAL AUDIT OF X-RAY INTERPRETER PROFICIENCY AT THE VENDORS AND MAF CLOSURE STATEMENT ACTION IS COMPLETE. REFERENCE MEMO 3770-87-235 H. PREPARE A PLAN TO REVIEW X-RAY CONTROL DRAWING/TECHNIQUES SHEETS BY VENDOR SOURCE REPRESENTATIVE AND MAF NDE AT VENDOR CLOSURE STATEMENT PLAN HAS BEEN SUBMITTED. ACTION IS COMPLETE. REFERENCE TASK II-P I. ESTABLISH REQUIREMENT TO INITIATE REVIEW OF X-RAYS BY MAF PERSONNEL WITHIN ONE WEEK OF FILM RECEIPT CLOSURE STATEMENT ACTION COMPLETED (REFERENCE QLI N-009) J. GENERATE RFF ON ADDITIONAL X-RAY REVIEW FACILITIES AND EQUIPMENT CLOSURE STATEMENT RFFS C02-0439, C02-0447, AND C02-0472 HAVE BEEN GENERATED TO OBTAIN ADDITIONAL EQUIPMENT. INSTALLATION OF NEW EQUIPMENT IS SCHEDULED TO BE COMPLETED THE SECOND QUARTER OF 1991 K. INVESTIGATE THE FEASIBILITY OF USING CAD/CAM MODELS OF PROPULSION HARDWARE FOR REFERENCE DURING REVIEW OF X-RAYS CLOSURE STATEMENT ACTION IS COMPLETE. REFERENCE ATTACHED MEMO 3742-87-173. USE OF CAD FOR THIS APPLICATION IS NOT RECOMMENDED L. EVALUATE FILM PACKAGING, HANDLING, AND STORAGE FOR ADEQUACY CLOSURE STATEMENT ACTION IS COMPLETE. REFERENCE ATTACHED MEMO 3742-87-157 M. REVIEW ALL RADIOGRAPHIC PROCEDURES FOR ADEQUACY CLOSURE STATEMENT ACTION IS COMPLETE. REFERENCE ATTACHED MEMO 3743-87-157 N. A COMPLETE REVIEW OF VENDOR X-RAYS WILL BE ACCOMPLISHED ON ALL EXISTING HARDWARE (TD808) CLOSURE STATEMENT REVIEW OF VENDOR AND MAF X-RAYS WILL BE TRACKED BY DC&R P-88-001 UPON COMPLETION OF AN EFFECTIVITY MAF CONTRACTS WILL BE NOTIFIED O. SENIOR MRB REVIEW AND ACCEPTANCE OF BSTRA WELD INDICATIONS CLOSURE STATEMENT ALL BSTRA X-RAY INDICATIONS ON LWT-21 HAVE BEEN DISPOSITIONED "USE-AS-IS" BY SENIOR MATERIAL REVIEW BOARD ACTION (REFERENCE SMRB T-97953). A WORKMANSHIP STANDARD WAS GENERATED TO ESTABLISH ACCEPTANCE CRITERIA ON FUTURE INDICATIONS (REFERENCE WORKMANSHIP STANDARD 9.1) P. EVALUATE PROPOSED PLANS DEVELOPED UNDER TASKS II.D. AND H FOR IMPLEMENTATION |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A10942 | IFA# -- | Contractor RPT# P-059-1 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD4800175-030 | Asmnt Part Name PROPULSION LINE | Asmnt Serial/Lot# 171 |
| HCRIT CD -- | FCRIT CD 1 | CAUSE CD MAW - MFG-ASY-WORK | FAIL MODE UC - UNSAT |
| Asmnt FMEA 2.1.7.1 | Asmnt FM 1 | FMEA CSE A | FMEA SCSE 2 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES NONE |
| ASSESSMENT TEXT |