# B.2.5  ELV DATA SERVICES FSA (OPTION 2)

This FSA defines the ELV data services to be provided by the CSOC contractor.

The ELV Telemetry Station is located in NASA facilities at the CCAS and VAFB. The principal function is to provide telemetry, real-time software operations, and communication support for ELV launches and NASA-sponsored spacecraft for ground processing and launch through loss of vehicle telemetry. This support includes system engineering for telemetry, data processing, audio communications, data transmission, and closed-circuit television systems. Also included are operational planning and real-time support for data acquisition and communication support.

The ELV Telemetry Station includes a telemetry/real-time software lab and a communications support area located in Hanger AE at CCAS and in Building 836 at VAFB. There is also an MDC and LVDC at CCAS and VAFB. Operations of the MDC and LVDC are directed by NASA with technical support provided by the contractor. The MDC and LVDC are launch and testing support rooms for upper level management. During operations, NASA and customer representatives from the Air Force, Vehicle, Spacecraft, and Public Affairs monitor operations from the MDC and LVDC.

Major customers include NASA ELV launches and NASA-sponsored spacecraft. Other customers include USAF (Delta and Atlas), Lockheed Martin (Atlas), McDonnell Douglas (Delta), and Orbital Sciences Corporation (Pegasus).

## 1.  Readiness Requirements

The contractor shall provide ELV Telemetry Station readiness reports to critical activity review boards that are responsible for ELV Telemetry Station readiness. The readiness status will include testing results, training, certification, hardware/software status, and procedures. DRD B.2.5 contains the readiness data requirements.

## 2.  Data Services Requirements

The contractor shall provide data services in accordance with requirements documents contained in the integrated tables B.2.5-3.0-A and B.2.5-3.0-B and the ELV Launch requirements table B.2.5-3.1.

Required Service:	Provide data services for KSC ELV telemetry station.

Std of Excellence:	99.9% reliability measured over the period of an ELV launch countdown (L–3 hours through T–0) and other major support periods (Wet Dress Rehearsal (WDR) for Atlas and Flight Program Verification (FPV) for Delta) and in no case impact safety, mission success or major program schedule milestones.

Expectation:	98% reliability measured over the period of an ELV launch countdown (L–3 hours through T–0) and other major support periods wet dress rehearsal for Atlas and flight program verification for Delta) and in no case impact safety, mission success, or major program schedule milestones.

## 2.1  Data Acquisition

The contractor provides data acquisition services in accordance with requirements defined in the integrated tables B.2.5-3.0-A and B.2.5-3.0-B.

## 2.2  Data Formatting and Transfer

The contractor provides data formatting and transfer services in accordance with requirements contained in the integrated tables B.2.5-3.0-A and B.2.5-3.0-B.

## 2.3  Command Handling

Command handling  services are not required.

## 2.4  Command Transmission

Command transmission services are not required.

## 2.5  Tracking Data Generation

Tracking data generation services are not required.

## 2.6  Data Distribution

The contractor provides data distribution services in accordance with requirements contained in the integrated tables B.2.5-3.0-A and B.2.5-3.0-B.

## 2.7  Network Management

The contractor provides network management services in accordance with requirements contained in the integrated tables B.2.5-3.0-A and B.2.5-3.0-B.

## 2.8  Reserved

## 2.9  Data Services Development

The contractor provides development services in accordance with requirements documents as specified in the integrated tables B.2.5-3.0-A and B.2.5-3.0-B.

1.	Transferred Development – None.

2.	Integration and Installation – The contractor shall provide integration and installation services to support ELV Telemetry Station development in accordance with requirements documents.

3.	New or Transferred Development by CSOC and M&O by a Non-CSOC Organization – None.

4.	New Development and M&O by the CSOC Contractor – None.

5.	Cost Estimates – None.

## 2.10  Supporting Services

Refer to integrated tables B.2.5-3.0-A and B.2.5-3.0-B.

## 3.  Integrated Tables

| Table B.2.5-3.0-A ELV Data Services Descriptions of Service Elements |
| --- |
| New Service Element | SEID | Service Element Description | Address/Location | Ownership | Security Level | Operating Hours | Notes |
| CS010 | N/A | CSOC Integration Center | Lockheed Martin Space Operations Center, Houston, TX | CL | 3 | 8x5 except CSOC Online and special support 24x7 | New in FY99 |
| CS020 | N/A | CSOC Integrated Operations Center | Lockheed Martin Space Operations Center, Houston, TX | CL | 2 | 8x5 except CSOC Online and special support 24x7 | New in FY99 |
| CS030 | N/A | CSOC Integrated Product Support Center | Lockheed Martin Space Operations Center, Houston, TX | CL | 2 | 8x5 except CSOC Online and special support 24x7 | New in FY99 |
| KP030 | A5002 | A.5.2 Hanger AE Telemetry Lab and Real-Time Software Support | CCAS: Bldg. 60680 (Hanger AE), Room 125 | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | Consolidated into KP030 during FY02 |
| KP030 | A5003 | A.5.3 Hanger AE Communications Support | CCAS: Bldg. 60680 (Hanger AE) | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | Consolidated into KP030 during FY02 |
| KP030 | A5004 | A.5.4 Hanger AE Mission Director’s Center | CCAS: Bldg. 60680 (Hanger AE), Room 109A | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | Consolidated into KP030 during FY02 |
| KP030 | A5005 | A.5.5 Hanger AE Launch Vehicle Data Center and E&O Control Center | CCAS: Bldg. 60680 (Hanger AE), and Bldg. E&O | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | Consolidated into KP030 during FY02 |
| KP030 | N/A | Hangar AE Launch Operations Facilities | CCAS: Bldg. 60680 (Hanger AE) Room 125 | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | New in FY02 |
| KV030 | A5006 | A.5.6 VAFB Telemetry Lab and Real-Time Software Support | VAFB: Bldg. 836, Telemetry Laboratory (Room 12) | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | Consolidated into KV030 during FY01 |
| KV030 | A5007 | A.5.7 VAFB Communications Support | VAFB: Bldg. 836, Room 20A | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | Consolidated into KV030 during FY01 |

| Table B.2.5-3.0-A (Cont’d) |
| --- |
| New Service Element | SEID | Service Element Description | Address/Location | Ownership | Security Level | Operating Hours | Notes |
| KV030 | A5008 | A.5.8 VAFB Mission Director’s Center | VAFB: Bldg. 840, Room B207 | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | Consolidated into KV030 during FY01 |
| KV030 | A5009 | A.5.9 VAFB Launch Vehicle Data Center | VAFB: Bldg. 836, Room 20 | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | Consolidated into KV030 during FY01 |
| KV030 | N/A | VAFB ELV Launch Operations Facilities | VAFB: Bldg. 836, Telemetry Laboratory (Room 12) | GO | 2 | 8x5; 24x7 during test, wet dress, and launch | New in FY01 |
| Note: Operating hours are not necessarily reflective of staffing requirements. |

| Table B.2.5-3.0-B ELV Data Services Customers and Services |
| --- |
| New |  |  | CWBS No. (Refer to DRD 2.1.1-b) |
| Service | Customer | Requirement | 2.4.2._ |
| Element |  |  | 1 | 2 | 6. | 6.b | 6.c | 6.d | 6.e | 7.a | 7.b | 7.c | 7.d |
| KP030 | Atlas | NASA/Atlas Subagreement for ETR (KCA-007) | X | X | X | X | X | X | X | X | X | X | X |
| KP030 | Delta | NASA/Delta Subagreement for ETR (KCA-008) | X | X | X | X | X | X | X | X | X | X | X |
| KP030 | Delta | NASA/Delta Subagreement for VAFB (KCA-008 Amendment A) | X | X | X | X | X | X | X | X | X | X | X |
| KP030 | ELV | MOA Between NASA and USAF on Launch Services and Range Support to Government ELV Programs | X | X | X | X | X | X | X | X | X | X | X |
| KP030 | ELV | NASA/Spaceport Florida MOU | X | X | X | X | X | X | X | X | X | X | X |
| KP030 | Space Shuttle Program | Space Shuttle Program Requirements Documents PRD/OR/PSP/OD 20000 | X | X | X | X | X | X | X | X | X | X | X |
| KV030 | Atlas | NASA/Atlas Subagreement for VAFB | X | X | X | X | X | X | X | X | X | X | X |
| KV030 | Delta | NASA/Delta Subagreement for VAFB (KCA-008 Amendment A) | X | X | X | X | X | X | X | X | X | X | X |
| KV030 | ELV | MOA Between NASA and USAF on Launch Services and Range Support to Government ELV Programs | X | X | X | X | X | X | X | X | X | X | X |
| KV030 | OSC | Agreement Between NASA and Orbital Sciences Corp. (OSC) for Support to OSC Commercial Launch Vehicle Program (1566-001) | X | X | X | X | X | X | X | X | X | X | X |

Table B.2.5-3.1 depicts the number of ELV launches that require ELV Telemetry Station support for each year.

| Table B.2.5-3.1 ELV Launch Requirements |
| --- |
|  |  | Eastern Test Range (CCAS) | Western Test Range (VAFB) |
| Year | Vehicle | NASA | Commercial | DOD | NASA | Commercial | DOD |
| CY1998 | Small Class |  | 1 |  | 1 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 3 |  |  |  | 3 |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class |  | 6 | 4 | 2 | 2 |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class |  | 8 |  | 1 |  | 1 |
|  | Atlas |  |  |  |  |  |  |
| CY1999 | Small Class | 1 |  |  | 4 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 2 | 1 |  | 1 | 1 |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class |  |  | 4 | 1 |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class | 2 | 5 |  |  |  | 1 |
|  | Atlas |  |  |  |  |  |  |
| CY2000 | Small Class |  |  |  | 4 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 2 |  |  | 1 |  |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class |  |  |  | 3 |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class |  | 8 |  |  |  |  |
|  | Atlas |  |  |  |  |  |  |
| CY2001 | Small Class | 2 |  |  | 3 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 4 |  |  | 3 |  |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class | 1 |  |  | 1 |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class | 2 | 8 |  |  |  |  |
|  | Atlas |  |  |  |  |  |  |
| * Not part of SOMO mission set, but expected to become part of the mission set in the future. |

| Table B.2.5-3.1 (Cont’d) |
| --- |
|  |  | Eastern Test Range (CCAS) | Western Test Range (VAFB) |
| Year | Vehicle | NASA | Commercial | DOD | NASA | Commercial | DOD |
| CY2002 | Small Class | 2 |  |  | 3 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 2 |  |  |  |  |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class |  |  |  | 1 |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class | 2 | 8 |  |  |  |  |
|  | Atlas |  |  |  |  |  |  |
| CY2003 | Small Class | 2 |  |  | 2 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 4 |  |  | 2 |  |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class | 1 |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class | 2 | 8 |  |  |  |  |
|  | Atlas |  |  |  |  |  |  |
| CY2004 | Small Class | 2 |  |  | 4 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 3 |  |  | 3 |  |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class | 2 |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class |  | 8 |  |  |  |  |
|  | Atlas |  |  |  |  |  |  |
| CY2005 | Small Class | 1 |  |  | 4 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 5 |  |  | 1 |  |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class | 1 |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class | 1 | 8 |  |  |  |  |
|  | Atlas |  |  |  |  |  |  |
| * Not part of SOMO mission set, but expected to become part of the mission set in the future. |

| Table B.2.5-3.1 (Cont’d) |
| --- |
|  |  | Eastern Test Range (CCAS) | Western Test Range (VAFB) |
| Year | Vehicle | NASA | Commercial | DOD | NASA | Commercial | DOD |
| CY2006 | Small Class | 2 |  |  | 3 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 3 |  |  | 1 |  |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class | 1 |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class | 1 | 8 |  |  |  |  |
|  | Atlas |  |  |  |  |  |  |
| CY2007 | Small Class | 1 |  |  | 3 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 1 |  |  | 3 |  |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class | 1 | 8 |  |  |  |  |
|  | Atlas |  |  |  |  |  |  |
| CY2008 | Small Class | 2 |  |  | 3 |  |  |
|  | Pegusus |  |  |  |  |  |  |
|  | UELV* |  |  |  |  |  |  |
|  | SELV* |  |  |  |  |  |  |
|  | Low-Cost Booster* |  |  |  |  |  |  |
|  | Med-Lite | 3 |  |  | 2 |  |  |
|  | Taurus |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Medium Class |  |  |  |  |  |  |
|  | Delta |  |  |  |  |  |  |
|  | Titan II |  |  |  |  |  |  |
|  | Intermediate Class | 1 | 8 |  |  |  |  |
|  | Atlas |  |  |  |  |  |  |
| * Not part of SOMO mission set, but expected to become part of the mission set in the future. |

## 4.  CSOC Interfaces

## 4.1  PGOC and CSOC Interrelationship

The government will transition services involved in the management and operations of the ELV Telemetry Station at CCAS from the PGOC contractor at the end of PGOC.

## 4.2  OSSC and CSOC Interrelationship

The government will transition services involved in the management and operations of the ELV Telemetry Station at VAFB from the OSSC contractor at the end of OSSC. This transition shall encompass all ELV Telemetry Station ground systems operations areas.

## 4.3  CSOC and NASA

Refer to Table B.2.5-4.0 for a roles and responsibilities breakdown between CSOC and NASA.

| Table B.2.5-4.0 Roles and Responsibilities for the ELV Telemetry Station |
| --- |
| Area | NASA Responsibility | CSOC Responsibility |
| ELV Telemetry Lab and Real-Time Software Support | Coordinates all customer requirements; perform sustaining engineering on the real-time software; provide postlaunch commentary when requested; perform research and development on the telemetry lab and real-time computer. | Provide integration and installation of COTS and NASA-provided software tools supporting user interfaces; operate and maintain telemetry lab equipment and real-time computer systems; perform initialization and configuration of real-time system software. |
| ELV Communications Support | Coordinate all requirements with the customer; interface with customer, other government agencies, and commercial communications groups to coordinate all requirements. | Provide data services. |
| Mission Director’s Center (MDC) | Coordinate all requirements with the customer; act as the MDC Operations Director during simulations and launch countdown; is the launch countdown point of contact for all equipment problems in the MDC; is the approving authority for changes and upgrades to the MDC. | Implement simulation and launch countdown requirements; provide operation support to the MDC Operations Director and maintenance of video, audio, data, and other equipment in the MDC; provide an F-1 day verification of all MDC equipment; provide engineering and technical support for changes and upgrades to the MDC. |
| Launch Vehicle Data Center (LVDC) | Coordinate all requirements with the customer; is the launch countdown point of contact for all equipment problems in the LVDC; is the approving authority for changes and upgrades to the LVDC. | Implement simulation and launch countdown requirements; provide operation support to the LVDC Operations Director and maintenance of video, audio, data, and other equipment in the LVDC; provide an F-1 day verification of all LVDC equipment; provide engineering and technical support for changes and upgrades to the LVDC. |

## 4.4  CSOC and ELV Telemetry Station Users

ELV Telemetry Station services shall be provided to the users as negotiated in their respective agreements. These users include commercial launch vehicle providers. Requirements for services to McDonnell Douglas for commercial Delta ELV support are included in the NASA/Delta Subagreement for ETR (KCA-008) and the NASA/Delta Subagreement for VAFB (KCA-008 Amendment A). Requirements for services to Lockheed/Martin for commercial Atlas ELV support are included in the NASA/Atlas Subagreement for ETR (KCA-007). Requirements for services to OSC for commercial Pegasus ELV support are included in the Agreement Between NASA and Orbital Sciences Corporation (OSC) for Support to OSC Commercial Launch Vehicle Program (1566-001).

Agreements between NASA and the USAF are documented in the Memorandum of Agreement Between NASA and USAF on Launch Services and Range Support to Government ELV Programs.

## 4.5  CSOC and CCAS Base Support Contractor

The CCAS base support contractor is responsible for facility maintenance and operations.

## 4.6  CSOC and CCAS Technical Services Contractor

The CCAS technical services contractor is responsible for interfacility communications infrastructure on CCAS except for Hangar AE. CSOC is responsible for communication services within Hangar AE (refer to Service Element A.5.3).

## 4.7  CSOC and KSC JBOSC CONTRACTOR

The JBOSC contractor provides facility sustaining engineering functions for all NASA facilities located on CCAS.

## 4.8  Plant Engineering and Operations

NASA is responsible for providing building utilities (i.e., power, water, administrative computer networks and telephones), building maintenance (i.e., lighting, painting, custodial services, bulletin board installation, cooling, heating, floor tile replacements, elevator maintenance, etc.), external building maintenance, landscape services, and onsite office equipment (i.e., furniture, copiers, and FAX machines).

NASA is responsible for providing telephones and administrative computer network service prior to the exercise of Options 3A and 3B of this contract. Upon the exercise of Options 3A and 3B, CSOC shall be responsible for provision of these services. If Options 3A and 3B are not exercised, NASA will provide telephone and administrative computer network services throughout the contract term.

## 4.9 INTERDEPENDENCE WITH NASA INITIATIVES

Implementation of our integrated architecture relies on completion of a number of NASA initiatives. These interrelationships are depicted in Table B.2.5-4.1.0. CSOC IOA development work for data services is performed as a 2.4.1.9.d space operations service.

| Table B.2.5-4.1.0 CSOC IOA Interdependencies |
| --- |
| Development Requirement | DP1 | NASA Development Initiative | Technical Performance | NASA Initiative Complete |
| Consolidate the logistics management at the CLF warehouse facility to a lower cost region of Baltimore’s industrial area. Implement a full bar-coding capability. | N/A | N/A | N/A | N/A |
| Implement the consolidation of the DSN Logistics Facility and the Goldstone Logistics Depot into a single DSN Logistics Facility located at Barstow. | N/A | N/A | N/A | N/A |
| Provide a central facility that directly supports the central CSOC Engineering organization. It provides the computerized environment to perform SVEL engineering, IOA Systems Engineering, Operations Integration and Test, Technology Assessment. | 1/99 | N/A | N/A | N/A |

## 5.  Supporting Information

ACAs will be required with the CCAS base support, CCAS technical services, and KSC JBOSC contractors.