Table of Contents

ACRONYMS AS USED THROUGHOUT THIS CONTRACT ARE AS FOLLOWS:	2

SCHEDULE OF SUPPLIES/SERVICES	3

A1.	ITEM REQUIREMENT	3

A2.  DELIVERY DATE	4

SECTION B – TECHNICAL SPECIFICATIONS	5

GENERAL REQUIREMENTS	5

B1   Scope of Contract	5

B2   Certifications	5

B3   Order of Precedence (Specifications)	5

EQUIPMENT REQUIREMENTS	5

B4   Condition of Equipment	5

B5   Aircraft Minimum (Mandatory) Equipment Requirements	5

B6   Aircraft Target Equipment	5

B7  Minimum (Mandatory) Avionics Requirements	7

AIRCRAFT MAINTENANCE REQUIREMENTS	9

B8 Maintenance and Record Keeping Requirements	9

B9  Airworthiness Directives (AD’s) and Service Bulletins	9

B10  Weight and Balance	10

B11 Exhibits	10

SECTION C – CONTRACT TERMS AND CONDITIONS	14

CONTRACT CLAUSES	14

CONTRACT CLAUSES	14

C1  Contract Terms and Conditions – Commercial Items (52.212-4 OCT 2008) [Tailored SEPT 2005]	14

C2  Contract Terms and Conditions Required to Implement Statutes or Executive Orders-Commercial Items (52.212-5 JAN 2009)	16

C3. AUTHORITY OF GOVERNMENT REPRESENTATIVES	19

C4. WARRANTY	19

C5. PROOF OF OWNERSHIP	19

C6. INSPECTION/ACCEPTANCE	19

C7. Payment Terms	19

C8  Availability of Funds (52.232-18 APR 1984)	19

D1.  INTRODUCTION	20

D2.  INSTRUCTIONS TO OFFERORS--COMMERCIAL ITEMS (52.212-1 SEPT 2006) [Tailored SEPT 2005]	20

D2.1 North American Industry Classification System (NAICS) Code and Small Business Size Standard	20

D2.2  Send proposals to:	20

D2.3  Period for accepting Quotes	20

D2.4   Submission of Quote.  Quote should include:	20

D2.5  Late Submissions, Modifications, Revisions, and Withdrawals of Quotes	20

D2.6 Data Universal Numbering System (DUNS) Number)	20

D2.7  Special Notice	20

D3.  EVALUATION OF QUOTES	21

D3.1  Acceptability	21

D3.2  Evaluated Price	21

D3.3  Capability	21

D3.4 Aircraft Capabilities and Condition.	21

D3.5  Tradeoff Analysis and Contractor Selection	21

D3.6  Notice of Award	21

# ACRONYMS AS USED THROUGHOUT THIS CONTRACT ARE AS FOLLOWS:

AM	Aviation Management

CFR	Code of Federal Regulations

CO 	Contracting Officer

COTR	Contracting Officer’s Technical Representative

FAA	Federal Aviation Administration

FAR	Federal Acquisition Regulations

NBC	National Business Center

RFP	Request for Proposals

# SCHEDULE OF SUPPLIES/SERVICES

## A1.	ITEM REQUIREMENT

Aircraft Requirement:	Purchase of one rotor wing aircraft meeting the minimum helicopter requirements specified below.

Delivery:	F.O.B. origin

Delivery Date:	May 1, 2009 – It is desired that the aircraft be capable of being delivered with the aircraft minimum requirements below and as specified in Section B by no later than this date. However, quotes with delivery dates beyond this date will be considered.

Minimum Helicopter Requirements:

Seating:					Five (5) passenger seats not including pilot, but including copilot seat in an aircraft, normally single-pilot operated.

Landing gear:	Skid-Type

Powerplant:	Single Engine Turbine engine

Airspeed:	120 knots

Section B:	The aircraft must also meet the minimum requirements as specified in Section B of this solicitation

Airframe Life:	The airframe shall be a 1990 airframe or newer.

Maintenance:	The aircraft must be capable of a maintenance cycle of at least 50 hours between maintenance events performed by an A&P mechanic.

Performance:	Rotorcraft certified in accordance with 14 CFR 27.143 paragraph (c):  which states: A wind velocity of not less than 17 knots must be established in which the rotorcraft can be operated without loss of control on or near the ground  in any maneuver appropriate to the type (such as crosswind takeoffs, sideward flight, and rearward flight), with (1) Critical weight; (2) Critical center of gravity; (3) Critical rotor r.p.m.; and (4) Altitude from standard sea level conditions to the maximum altitude capability of the rotorcraft or 7,000 feet, whichever is less.

Payload*:	Non-jettisonable internal payload (HIGE) of 800 pounds at 25 degrees C at 7,000 feet pressure altitude using a pilot weight of 240 pounds, a 25-pound survival kit, and fuel for 1.9 hours.

Target Helicopter Requirements:

Fixed Float Capable:

It is desired that the helicopter be capable of being on fixed floats, however the Government will evaluate this ability against other factors as identified in Section D.

Payload*:  	Jettisonable payload (HOGE-J) of 1100 pounds at 25 degrees C at 7,000 feet pressure altitude using a pilot weight of 240 pounds, a 25 pound survival kit, and fuel for 1.9 hours.

*Payload amounts shall be computed by using the Government’s Standard Interagency Load Calculation Method and Form and the Helicopter Fuel Consumption and Weight Reduction Chart included under the exhibits along with the offered aircraft’s applicable Hover Ceiling Charts, weight and balance report and equipment list that you provide.

An AS350B2, BH206L4, or BH 407 series aircraft may fulfill the above minimum and/or target requirements.

PRICING (QUOTE)

| ITEM | DESCRIPTION | QUANTITY | UNIT | TOTAL AMOUNT |
| --- | --- | --- | --- | --- |
| 1. | Purchase of one rotor wing meeting the minimum requirements of the solicitation. | 1 | EACH | $ |

# A2.  DELIVERY DATE

Delivery is desired on or before May 1, 2009 however, it is not required.  (See Paragraph D3.4)

Proposed Delivery Date      ______________________

Offeror elects to waive the adjustment in accordance with 52.219.4, Notice of Price Evaluation Preference for HUBZone Small Business Concerns (Jan 1999). Mark this box if you elect to waive the adjustment.

SECTION B – TECHNICAL SPECIFICATIONS

# GENERAL REQUIREMENTS

## B1   Scope of Contract

B1.1  Purchase of one light helicopter equipped as specified in Section B.

## B2   Certifications

B2.1 The aircraft must have a current Federal Aviation Administration (FAA) Standard Airworthiness certificate.   The aircraft must be equipped in accordance with 14 CFR Parts 91.205 for visual flight rules (VFR) day and night operation. Installation of any equipment required by this contract must be FAA approved.  Aircraft built from spare and surplus parts in accordance with FAA Advisory Circular 31-13 (4-5-73) and certified in accordance with 14 CFR 21.183(d)(1) are not acceptable.

## B3   Order of Precedence (Specifications)

In the event of inconsistencies within the technical specification, the following order will be used in such resolution:  (1) typed provisions of these specifications;   (2) DOI NBC-Aviation Management supplements and/or exhibits incorporated by reference; (3) 14 CFR incorporated by reference; (4) aircraft manufacturer's specifications; (5) other documents incorporated by reference.

# EQUIPMENT REQUIREMENTS

## B4   Condition of Equipment

The aircraft and all other required equipment must be operable, free of damage, and in good repair.  Aircraft systems and components must be free of leaks, except where specified by the manufacturer.

B4.1  Temporary repairs to windows and windshields are unacceptable.

B4.2  The aircraft interior must be clean and neat with no unrepaired tears, rips, or other damage.  The exterior finish, including the paint, must be clean, neat, and in good condition.  Any corrosion must be within manufacturer or FAA acceptable limits.

B4.3   See the Unacceptable Lap Belt and Shoulder Harness Conditions Exhibit for lap belt and shoulder harness conditions that are not acceptable.

## B5   Aircraft Minimum (Mandatory) Equipment Requirements

The aircraft must be equipped as shown below:

B5.1   Flight Instruments for low visibility flight conditions, including directional gyro, gyroscopic bank and pitch indicator, rate of turn indicator, and vertical speed indicator.

B5.2   Free air temperature gauge.

B5.3   One set of individual lap belts for each installed seat.

B5.4   Double strap shoulder harness with automatic or manual locking inertia reel for each front seat occupant.  Shoulder straps and lap belts must fasten with one single-point metal-to-metal, quick-release mechanism. Heavy-duty (military-style) harnesses with fabric loop connecting the shoulder harness to the male portion of the lap belt buckle are acceptable.

B5.5  Shoulder harnesses (either single-strap or double-strap) for each aft cabin occupant.  Shoulder harness straps and lap belts must fasten with a single-point, metal-to-metal, quick-release mechanism.

B5.6  Fire extinguisher(s), as required by 14 CFR Part 135, must be a handheld bottle, minimum 2-B:C rating, mounted and accessible to the flight crew while seated.  (See the fire extinguisher maintenance instructions in Section B29.)

B5.7 Dual controls for initial pilot performance evaluation.

B5.8   Aircraft lighting for night operation in accordance with 14 CFR Part 91.205(c), including instrument lights.

B5.9   High-skid-type landing gear, if manufactured for make and model.

B5.10  A minimum of 15-cubic-feet of baggage space within the aircraft fuselage specifically designed to carry cargo separate from the cabin.  This compartment must be capable of accommodating 58-inch long shovels, rakes, and other tools (requiring rear bulkhead modification of baggage compartment of some models).

B5.11   Ground-handling wheels.

## B6   Aircraft Target Equipment

The following equipment is a target and is what is ultimately desired by the agency. Your aircraft do not have to be equipped with this equipment; however, the evaluated price of your quote will be adjusted with the cost for the Government to add the equipment to the aircraft.

B6.1   Locking cap(s) on all fuel inlet ports

B6.2 High visibility, pulsating, forward-facing conspicuity lighting.

B6.3   High visibility markings on main rotor blades as specified by the Acceptable Paint Schemes Exhibit.

B6.4  Cockpit-mounted external load indicator with readout of weight carried on the cargo hook.

B6.5  An accessory power source consisting of an MS 3112E-12-3S three-pin connector, accessible in the cabin. Pin B must be airframe ground; pin A must be +28VDC (for 28-volt aircraft); and pin C must be +14VDC (for 14-volt aircraft).  The circuit must be protected by a 5-amp circuit protection.

B6.6	One  collapsible, variable capacity water/retardant bucket.  See the Water Bucket Use Procedures Exhibit.  The bucket must have a manufacturer's capacity adjustment commensurate with the maximum lifting capability of the aircraft.  The bucket must be capable of being operated with all increments of the longline; i.e., 50, 100, 150 feet.

B6.7    A water/retardant bucket operating switch clearly marked for "open" and "closed," and mounted on the collective control to avoid confusion with the cargo hook release.  The switch must be of a different design and must be mounted so as to  not easily be confused with the RPM Control [Beep] switch.

B6.8  Part number MS 3101E-24-11S, nine-pin connector, for use as the power source for a helitorch or remote cargo hook.  Pin D must be airframe ground.  Pin E must be switched 28VDC, protected by a manually operable, 50-amp circuit breaker.  The water bucket/tank open switch must also activate this circuit.

B6.8.1   A lanyard to support the connector and mounted within 12 inches of the cargo hook.

B6.8.2   This connector must have multiple circuit capacity sufficient to provide power and control for Contractor-furnished equipment.  The longline remote hook, fixed tank, or water bucket must be wired through this connector.  A list of water buckets with required pin wiring can be found in the FS/AMD Drawing A-16 Exhibit.  Wiring diagrams for various equipment configurations are available from the U.S. Department of the Interior, National Business Center, Aviation Management, 300 E. Mallard Drive, Suite 200, Boise, ID  83706, or USDA Forest Service, 3833 S. Development Avenue, Boise, ID 83705-5354.

B6.9    Fixed float landing gear in addition to standard skid landing gear.

B6.10    Emergency popout float landing gear in addition to standard skid landing gear.

B6.11   Agricultural spray system used for the delivery of liquid chemicals.

B6.12  Engine intake barrier filtering device capable of filtering sand and dust particles.

B6.13   One digital hour meter installed in a location visible by the pilot and front seat observer while seated.  The meter must be wired in series with a switch on the collective control, and a switch activated by engine or transmission oil pressure or by equivalent means, to record flight time only.

B6.14   A strobe light, with either a white, or half-white and half-red lens, mounted on top of the aircraft, or otherwise visible from above.  If the aircraft certification requires the anti-collision light to be aviation red, then a white strobe light with an independent activating switch must be provided in addition to the red strobe.

B6.15   Personnel access steps for aircraft with a floor height greater than 18 inches, to ensure safe entrance and exit from each door.

B6.16    Cabin heater and window defogger.

B6.17  Cargo restraint system for aircraft manufactured with a parcel/storage area behind the rear passenger seats.

B6.18   A convex mirror for the pilot to observe the sling load.

B6.19   One cargo hook that may be loaded and locked in a single motion with one hand and is rated at the maximum lifting capacity of the aircraft.

B6.20  Wire strike protection system (mechanical).  (Note: If manufactured for make and model of helicopter.)

B6.21  (BH-206L-4 only) High Altitude Tail Rotor System 206-704-722.

B6.22   Main rotor brake.

B6.23  Acceptable high visibility paint scheme and condition of paint job.

B6.24  Air-conditioning system.

## B7  Minimum (Mandatory) Avionics Requirements

B7.1  General.

B7.1. The Contractor must provide, install, and maintain the following systems in accordance with the manufacturer's specifications and the installation and maintenance standards of Section B7.   Detailed avionics systems performance requirements are listed in Avionics Operational Test Standards (copies available upon request from NBC AMD Avionics, or at

http://amd.nbc.gov/library/handbooks/aots.pdf

B7.2  Avionics Installation and Maintenance Standards.

B7.2.1  Strict adherence to the recommendations in the following FAA Advisory Circulars is required:  AC 43.13-1B Chapter 11, "Aircraft Electrical Systems," and Chapter 12, "Aircraft Avionics Systems”; AC 43.13-2A Chapter 1, "Structural Data," Chapter 2, "Radio Installation," and Chapter 3, "Antenna  Installation."

B7.2.2  All avionics systems requiring an antenna must be installed with a properly matched, aircraft-certified antenna, unless otherwise specified.  Antennas must be polarized as required by the avionics system and must have a voltage standing wave radio (VSWR) of 2.5 to 1 or better.

B7.2.3  The aircraft's static pressure system, altimeter instrument system, and automatic pressure altitude reporting system must meet the IFR requirements of 14 CFR Part 91.411 and inspected and tested within 24 calendar months, as specified by 14 CFR Part 43, appendices E and F.

B7.3   Communications  Systems.

B7.3.1 One panel-mounted VHF-AM (VHF-1) aeronautical transceiver with a minimum of 760 channels covering 118.000 to 136.975 MHz.  It must have channels selectable in no greater than 25 kHz increments and a minimum of 5 watts carrier output power.  The transceiver's operational controls must be mounted so they are readily visible and accessible to the pilot.

B7.3.2  One air traffic control (ATC) transponder and altitude reporting system meeting the requirements of 14 CFR Part 91.215 (a) and (b).

B7.4 Target Avionics Components

The following avionics systems are targets which are ultimately desired by the Government.  Any aircraft offered do not have to be so equipped.  However, the evaluated price of your quote will be adjusted with any costs required for the Government to bring the aircraft up to the targeted specifications.

B7.4.1 One automatic-portable/automatic-fixed or automatic-fixed Emergency Locator Transmitter (ELT), certified to either Technical Standard Order (TSO)-C91a or TSO-C126, utilizing an external antenna and meeting the same requirements as those detailed for airplanes in 14 CFR Part 91.207 (excluding section f.). It must be installed in a conspicuous or marked location.

B7.4.2 One VHF-FM multi-mode aeronautical transceiver (FM-1, which provides selection of  narrowband (12.5 kHz) analog, wideband (25.0 kHz) analog, or “P-25” narrowband digital bandwidth operation on each channel.    The transceiver’s operational controls must be located and arranged so that the pilot and observer/copilot, when seated, have full and unrestricted movement of each control without interference from their clothing, the cockpit structure, or the flight controls.

B7.4.2.1  The transceiver’s operational frequency range must include the band of 150 to 174 MHz. The operator(s) must be able to program any usable channels within that band while in flight.  Unless instructed by the Government for use on a specific project, all frequencies programmed for use under this Contract must be in the narrowband analog mode.

B7.4.2.2  Carrier output power for the transceiver must be 10 watts nominal value (original design specification).  The transceiver must be capable of displaying receiver and transmitter operating frequency, and must provide both receiver and transmitter activation indicators for main and Guard.  Simultaneous monitoring of both main (150-174 MHz) and Guard (168.625 MHz) receivers is required.   Scanning of the Guard frequency is not acceptable.

B7.4.2.3  The transceiver must incorporate one Continuous Tone-Controlled Squelch System (CTCSS) sub-audible tone encoder, with the lowest 32 TIA/EIA-603 standard tone frequencies (from 67.0 to 203.5 Hz, less 69.3 Hz) being selectable for use on any channel.

B7.4.2.4  Prior to acceptance under this contract, the transceiver must be programmed with the narrowband analog Guard transmit and receive frequencies of 168.625 MHz, and a 110.9 Hz CTCSS tone on transmit only.

B7.4.2.5  The following VHF-FM aeronautical transceivers are known to meet the above requirements:

Technisonics TDFM-136

NAT (Northern Airborne Technology) NPX-136D

B7.4.3. Provisions for auxiliary VHF-FM (AUX-FM)  portable radio:

B7.4.3.1  Interface for installing and properly operating an auxiliary VHF-FM portable radio through the aircraft's audio control system(s).  The interface must consist of the appropriate wiring from the audio control system, terminated in an ITT/Cannon type MS3112E12-10S 10-pin connector conveniently located for use by the observer/copilot, and utilizing the contact assignments as specified by drawing FS/AMD-17 in the exhibits.

B7.4.3.2  One weatherproof, external, broadband antenna covering the 150-174 MHz band, with associated RG-58A/U (or equivalent) coaxial cable and connector, terminated in a bulkhead-mounted, female BNC connector (type UG-290A), conveniently located for use by the observer/copilot adjacent to the above 10-pin connector (Comant model CI-177 or equal).

B7.4.3.3 Mounting facilities for securely installing the auxiliary VHF-FM portable radio in the cockpit in accordance with the FAA AC 43.13-2A specifications. Locate and arrange the mounting facilities so that a seated observer/copilot has full and unrestricted movement of the radio's controls, without interference from the 18-inch adapter cable, clothing, cockpit structure, or flight controls.

B7.4.3.4. Positive-polarity microphone excitation voltage provided to the AUX-FM system from the aircraft DC power system through a suitable resistor network.  A blocking capacitor must be provided to prevent the portable radio microphone excitation voltage from entering the system.  Sidetone for the AUX-FM must also be provided (NAT model AA34-300, Premier model PA-34, or equivalent).

B7.4.3.5  In lieu of the above AUX-FM requirements, the Contractor may substitute one VHF-FM aeronautical transceiver (FM-2) which meets the requirements (less guard) for the VHF-FM aeronautical transceiver (FM-1), as detailed above.

B7.4.4  One Automated Flight Following (AFF) system compatible with the governments AFF tracking network (Webtracker) is required.  Not all available AFF systems are compatible with Webtracker nor meet Webtracker’s requirements.  The contractor must ensure that the AFF system offered is compatible with Webtracker.  To view Webtracker’s current compatibility requirements refer to https://www.aff.gov.

B7.4.4.1  The AFF system must be powered by the aircraft’s electrical system, installed per the manufacturer’s installation manual, and operational in all phases of flight.  AFF equipment must utilize as a minimum:  Satellite communications, provide data to the Government’s Webtracker software, use aircraft power via a dedicated circuit breaker for power protection, and be mounted so as to not endanger any occupant from AFF equipment during periods of turbulence.  Any AFF manufacturer-required pilot display(s) or control(s) must be visible/selectable by the pilot(s).  Remote equipment having visual indicators should be mounted in such a manner as to allow visual indicators to be easily visible.

B7.4.4.2 This clause incorporates Specification Section Supplement available at:https://www.aff.gov/contractspecs with the same force and effect as if they were presented as full text herein.

B7.4 5  Navigational Systems

B7.4.5.1  One permanently installed, panel-mounted global positioning system (GPS). The GPS must utilize the WGS-84 datum, reference latitude and longitude coordinates in the degrees/minutes/decimal minutes (DM)  mode for aircraft positioning; utilize an approved, fixed, external aircraft antenna; and be powered by the aircraft electrical system. The GPS installation must be FAA approved (or approval pending). Handheld and/or marine-type equipment is not acceptable.

B7.4.6  Audio Systems

B7.4.6.1  Two separate audio control systems (which may be combined in a single unit) for the pilot and observer/co-pilot to select receiver audio outputs and transmitter microphone/push to talk (PTT) audio inputs for all installed radios and public address (PA) systems.  Each system must also allow the pilot and observer/copilot to independently adjust both the intercommunications system (ICS) and the receiver audio output levels (NAT AMS-42F or equivalent).

B7.4.6.1.1  Transmitter selection and operation.  Separate transmitter selection controls for both the pilot’s and observer/copilot’s microphone/PTT inputs.  Configure the system so the pilot and observer/copilot may each simultaneously select and utilize a different transmitter (or PA system when installed) via their respective microphone/PTT.  Whenever a transmitter is selected, the companion receiver audio must automatically be selected for the corresponding earphone.  Transmitter sidetone audio must be provided for the user as well as for cross-monitoring via the corresponding receiver selection switch on the other audio control system.

B7.4.6.1.2    Receiver selection and operation.   Separate controls for both pilot and observer/copilot to select audio from one or any combination of available receivers.  The ICS-equipped aft passenger positions must monitor the receiver(s) as selected by the observer/copilot. The receiver audio output must be free of excessive distortion, hum, noise, and crosstalk, and must be amplified sufficiently to facilitate ease of use in a noisy cockpit/cabin environment.

B7.4.6.1.3  The audio system(s) controls must be located and arranged so that both the pilot and observer/copilot, when seated, have full movement of their respective controls without interference from their clothing, the cockpit structure, or the flight controls. Labeling and marking of controls must be clear, understandable, legible, and permanent. Electronic label maker marking is acceptable.

B7.4.6.2   An ICS for the pilot, observer/copilot, and the two aft cabin exit positions.  ICS audio must mix with, but not mute, selected receiver audio.  An ICS audio level control must be provided for each position above. Adjustment of the ICS audio level at any position must not affect the level at any other position.  A "hot mic" capability, controlled via an activation switch or voice activation (VOX), must be provided for the pilot and observer/copilot positions.   ICS sidetone audio must be provided for the earphones corresponding with the microphone in use.  The ICS audio output must be free of excessive distortion, hum, noise, and crosstalk and must be amplified sufficiently to facilitate ease of use in a noisy cockpit/cabin environment.

B7.4.6.3  Earphones, microphones, PTT’s, and jacks designed for operation with  600-ohm earphones and carbon-equivalent, noise-canceling boom type microphones (Gentex electret type model 5060-2, military dynamic type M-87/AIC with type CE-100 TR preamplifier, or equivalent) with U-174/U (single/male) type connector plug.  The pilot position only may be configured for low impedance (dynamic) operation.

B7.4.6.1  All earphone/microphone jacks in the aircraft (except the pilot's) must be U-92A/U (single/female) type, which will accept U-174/U type plugs.

B7.4.6.2   Separate PTT switches for radio transmitter and ICS microphone operation at the pilot, observer/copilot, and the two aft exit passenger positions.  The pilot's PTT switches must be mounted on the cyclic control.  The observer/copilot's and aft exit passengers' PTT switches must be mounted on the cord to the earphone/microphone connector. In lieu of the observer/copilot's cord-mounted PTT switches, a footswitch-operated PTT system may be utilized.  ICS PTT switches for the other required positions must be mounted on the cord to the earphone/ microphone connector.

# AIRCRAFT MAINTENANCE REQUIREMENTS

## B8 Maintenance and Record Keeping Requirements

B8.1  Manuals/Records.

The Contractor must ensure that all maintenance performed on the aircraft before delivery to the Government is recorded in the affected aircraft maintenance record in accordance with 14 CFR (reference 14 CFR 43.9, 43.11, and 91.417).

B8.1.1  The airframe and engine logbooks must be provided, complete, and contain all maintenance records since date of manufacture, including the manufacturer’s approval for return to service and must be in English. A complete airworthiness limitations schedule and inspections and component overhaul schedule shall be provided. This schedule must indicate aircraft total time, aircraft total time at installation/compliance, life limit of component/inspection, and time remaining.

B8.1.2  Maintenance, operating, and parts manuals for the helicopter, engine, and equipment must be furnished to the Government at time of delivery. All flight manual supplements applicable to the aircraft as delivered and optional configurations must be provided. The information provided must include instructions for continued airworthiness for all equipment and alterations accomplished to comply with this agreement.

B8.1.3 All installations must be FAA approved and documented in accordance with 14 CFR.

B8.1.4  Installation drawings and any equipment warranty information must be supplied covering the installation of avionics and all other installed equipment.

## B9  Airworthiness Directives (AD’s) and Service Bulletins

B9.1  All applicable manufacturers' service bulletins and Federal Aviation Administration Airworthiness Directives must be complied with prior to delivery date. A list of FAA ADs and manufacturers' mandatory service bulletins on the make and model of aircraft will be provided. The list must record whether applicable or not and, if applicable, the date and airframe total time at compliance, method of compliance, next compliance due date if recurring, and authorized signature of maintenance personnel with their certificate number. The list will be similar to that shown in Advisory Circular AC 43-9C.

## B10  Weight and Balance

B10.1  The aircraft must have a current equipment list and weight and balance (within the preceding 24 months) for all installed equipment.

## B11 Exhibits

B11.1 	Unacceptable Lap Belt and Should Harness Conditions.

B11.2	FS/AMD Drawing A-16: Accessory Connector Pin Assignment.

B11.3	FS/AMD Drawing A-17: Wiring Diagram for AUX-FM Connector.

EXHIBIT B11.1

UNACCEPTABLE AIRCRAFT LAP BELT AND SHOULDER HARNESS CONDITIONS

| Item | Unacceptable Conditions |
| --- | --- |
| Webbing | Frayed: 5 percent or more Torn Crushed Swelling: twice the thickness of original web or if difficult to operate through hardware Creased: no structural damage allowed Sun deterioration: severe fading, brittleness, discoloration, and stiffness |
| Hardware | Inoperable buckle or other hardware Nylon bushing at shoulder-harness-to-lap-belt connection missing or damaged Fabricated bushings or tie wraps used as bushings Rust/corrosion: only minor surface rust/corrosion allowed Wear: wear beyond normal use |
| Stitches | Broken or missing Severe fading or discoloring Inconsistent pattern |
| TSO Tags (see 14 CFR 21.607) | Missing Illegible |
| Age | Belts/fabric over 10 years from date of manufacture will be closely inspected for possible damage from exposure to the elements, but do not have to be replaced if they can be determined to be in serviceable condition. |

EXHIBIT E11.2

DRAWING FS/AMD A-16

Accessory Connector Pin Assignments

Griffith Bucket (7 wire)

MS 3101E-24-11S (Helicopter)	MS 3107B-24-11P (Bucket)

Pin	Function	Function

A	Up limit relay coil	Up limit switch	(Green)

B	Up switch	Up limit switch	(White #16)

F	28VDC/Ground (up)	28VDC/Ground (up)	(White #12)

G	Down limit relay coil	Down limit switch	(Red #16)

H	Ground/28VDC (down)	Ground/28VDC (down)	(Black #12)

I	Down switch	Down limit switch	(Black #16)

Sims Bucket (3 wire)

MS 3101E-24-11S (Helicopter)	MS 3107B-24-11P (Bucket)

Pin	Function	Function

B	28VDC/Ground	28VDC/Ground 	(Green)

G	Ground (close)	Ground (close)	(White)

I	28VDC (open)	28VDC (open) 	(Black)

Sims Bucket (8 wire)

MS 3101E-24-11S (Helicopter)	MS 3107B-24-11P (Bucket)

Pin	Function	Function

A	28VDC (open)	28VDC (open) 	(White/Black)

D	Ground	System Ground 	(Blue/Green)

F	28VDC 	System Power	(White, Red, Black)

H	Indicator light	Indicator light return	(Red/Black)

I	28VDC (close)	28VDC (close)	(Orange)

Chadwick Bucket (2 wire)

MS 3101E-24-11S (Helicopter)		MS 3107B-24-11P (Bucket)

Pin		Function		Function

B		28VDC/Ground (open)		28VDC/Ground (open)

H		Ground/28VDC (close)		Ground/28VDC (close)

Brackett Carousel/Chadwick Bucket (3 wire)

MS 3101E-24-11S (Helicopter)		MS 3107B-24-11P (Bucket)

Pin		Function		Function

C		28VDC Reset/bucket close		28VDC Reset/bucket close

D		Airframe Ground		System Ground

E		28VDC Hook/bucket open		28VDC Hook/bucket open

Simplex Helitorch, Bambi Bucket, Remote Hook, And Seeders (2 wire)

MS 3101E-24-11S (Helicopter)		MS 3107B-24-11P (Bucket)

Pin		Function		Function

D		Airframe Ground		System Ground

E	28VDC (bucket open)				28VDC Bucket/Hook Open-Torch/Seeder

EXHIBIT E11.3

Drawing FS/AMD A-17

Auxiliary FM Radio Interface

# SECTION C – CONTRACT TERMS AND CONDITIONS

# CONTRACT CLAUSES

# CONTRACT CLAUSES

## C1  Contract Terms and Conditions – Commercial Items (52.212-4 OCT 2008) [Tailored SEPT 2005]

(SEE ADDENDA WHICH FOLLOWS IMMEDIATELY AFTER CLAUSE 52.212-5)

(a) Inspection/Acceptance. The Contractor shall only tender for acceptance those items that conform to the requirements of this contract. The Government reserves the right to inspect or test any supplies or services that have been tendered for acceptance. The Government may require repair or replacement of nonconforming supplies or reperformance of nonconforming services at no increase in contract price.   If repair/replacement or reperformance will not correct the defects or is not possible, the Government may seek an equitable price reduction or adequate consideration for acceptance of nonconforming supplies or services. The Government must exercise its post-acceptance rights (1) within a reasonable time after the defect was discovered or should have been discovered; and (2) before any substantial change occurs in the condition of the item, unless the change is due to the defect in the item.

(b) Assignment. The Contractor or its assignee's may assign its rights to receive payment due as a result of performance of this contract to a bank, trust company, or other financing institution, including any Federal lending agency in accordance with the Assignment of Claims Act (31 U.S.C. 3727).  However, when a third party makes payment (e.g., use of the Governmentwide commercial purchase card), the Contractor may not assign its rights to receive payment under this contract.

(c) Changes. Changes in the terms and conditions of this contract may be made only by written agreement of the parties.

(d) Disputes. This contract is subject to the Contract Disputes Act of 1978, as amended (41 U.S.C. 601-613). Failure of the parties to this contract to reach agreement on any request for equitable adjustment, claim, appeal or action arising under or relating to this contract shall be a dispute to be resolved in accordance with the clause at FAR 52.233-1, Disputes, which is incorporated herein by reference. The Contractor shall proceed diligently with performance of this contract, pending final resolution of any dispute arising under the contract.

(e) Definitions. The clause at FAR 52.202-1, Definitions, is incorporated herein by reference.

(f) Excusable delays. The Contractor shall be liable for default unless nonperformance is caused by an occurrence beyond the reasonable control of the Contractor and without its fault or negligence such as, acts of God or the public enemy, acts of the Government in either its sovereign or contractual capacity, fires, floods, epidemics, quarantine restrictions, strikes, unusually severe weather, and delays of common carriers. The Contractor shall notify the CO in writing as soon as it is reasonably possible after the commencement of any excusable delay, setting forth the full particulars in connection therewith, shall remedy such occurrence with all reasonable dispatch, and shall promptly give written notice to the CO of the cessation of such occurrence.

(g) Invoice.

(1) The Contractor shall submit an original invoice and three copies (or electronic invoice, if authorized,) to the address designated in the contract to receive invoices. An invoice must include--

(i) Name and address of the Contractor;

(ii) Invoice date and number;

(iii) Contract number, contract line item number and, if applicable, the order number;

(iv) Description, quantity, unit of measure, unit price and extended price of the items delivered;

(v) Shipping number and date of shipment, including the bill of lading number and weight of shipment if shipped on Government bill of lading;

(vi) Terms of any discount for prompt payment offered;

(vii) Name and address of official to whom payment is to be sent;

(viii) Name, title, and phone number of person to notify in event of defective invoice; and

(ix) Taxpayer Identification Number (TIN).  The Contractor shall include its TIN on the invoice only if required elsewhere in this contract.

(x) Electronic funds transfer (EFT) banking information.

(A)  The Contractor shall include EFT banking information on the invoice only if required elsewhere in this contract

(B) If EFT banking information is not required to be on the invoice, in order for the invoice to be a proper invoice, the Contractor shall have submitted correct EFT banking information in accordance with the applicable solicitation provision, contract clause (e.g., 52.232-33, Payment by Electronic Funds Transfer -Central Contractor Registration, or 52.232-34, Payment by Electronic Funds Transfer-Other Than Central Contractor Registration), or applicable agency procedures

(C)  EFT banking information is not required if the Government waived the requirement to pay by EFT.

(2) Invoices will be handled in accordance with the Prompt Payment Act (31 U.S.C. 3903) and Office of Management and Budget (OMB) prompt payment regulations at 5 CFR part 1315.

(h) Patent indemnity. The Contractor shall indemnify the Government and its officers, employees and agents against liability, including costs, for actual or alleged direct or contributory infringement of, or inducement to infringe, any United States or foreign patent, trademark or copyright, arising out of the performance of this contract, provided the Contractor is reasonably notified of such claims and proceedings.

- Payment. –

- Items accepted. Payment shall be made for items accepted by the Government that have been delivered to the delivery destinations set forth in this contract.

- Prompt Payment. The Government will make payment in accordance with the Prompt Payment Act (31 U.S.C. 3903) and prompt payment regulations at 5 CFR part 1315.

- Electronic funds transfer (EFT). If the Government makes payment by EFT, see 52.212-5(b) for the appropriate EFT clause.

- Discount. In connection with any discount offered for early payment, time shall be computed from the date of the invoice. For the purpose of computing the discount earned, payment shall be considered to have been made on the date which appears on the payment check or the specified payment date if an electronic funds transfer payment is made.

- Overpayments. If the Contractor becomes aware of a duplicate contract financing or invoice payment or that the Government has otherwise overpaid on a contract financing or invoice payment, the Contractor shall --

(i) Remit the overpayment amount to the payment office cited in the contract along with a description of the overpayment including the-

(A) Circumstances of the overpayment (e.g., duplicate payment, erroneous payment, liquidation errors, date(s) of overpayment);

(B)  Affected contract number and delivery order number, if applicable;

(C) Affected contract line item or subline item, if applicable; and

(D) Contractor point of contact.

(ii) Provide a copy of the remittance and supporting documentation to the Contracting Officer.

(6) Interest. (i)  All amounts that become payable by the Contractor to the Government under this contract shall bear simple interest from the date due until paid unless paid within 30 days of becoming due.  The interest rate shall be the interest rate established by the Secretary of the Treasury as provided in Section 611 of the Contract Disputes Act of 1978 (Public Law 95-563), which is applicable to the period in which the amount becomes due, as provided in (i)(6)(V) of this clause, and then at the rate applicable for each six-month period as fixed by the Secretary until the amount is paid.

(ii) The Government may issue a demand for payment to the Contractor upon finding a debt is due under the contract.

(iii) Final decisions.  The Contracting Officer will issue a final decision as required by 33.211 if –

(A) The Contracting Officer and the Contractor are unable to reach agreement on the existence or amount of a debt within 30 days;

(B) The Contractor fails to liquidate a debt previously specified in the demand for payment unless the amounts were not repaid because the Contractor has requested an installment payment agreement; or

(C) The Contractor requests a deferment of collection on a debt previously demanded by the Contracting Officer (see 32.607-2).

(iv) If a demand for payment was previously issued for the debt, the demand for payment included in the final decision shall identify the same due date as the original demand for payment.

(v) Amounts shall be due at the earliest of the following dates:

(A) The date fixed under this contract.

(B) The date of the first written demand for payment, including any demand for payment resulting from a default termination.

(vi) The interest charge shall be computed for the actual number of calendar days involved beginning on the due date and ending on—

(A)The date on which the designated office receives payment from the Contractor;

(B) The date of issuance of a Government check to the Contractor from which an amount otherwise payable has been withheld as a credit against the contract debt; or

(C) The date on which an amount withheld and applied to the contract debt would otherwise have become payable to the Contractor.

(vii) The interest charge made under this clause may be reduced under the procedures prescribed in 32.608-2 of the Federal Acquisition Regulation in effect on the date of this contract.

(j) Risk of loss.  Unless the contract specifically provides otherwise, risk of loss or damage to the supplies provided under this contract shall remain with the Contractor until, and shall pass to the Government upon:

- Delivery of the supplies to a carrier, if transportation is f.o.b. origin; or

- Delivery of the supplies to the Government at the destination specified in the contract, if transportation is f.o.b. destination.

(k) Taxes. The contract price includes all applicable Federal, State, and local taxes and duties.

(l) Termination for the Government's convenience. The Government reserves the right to terminate this contract, or any part hereof, for its sole convenience. In the event of such termination, the Contractor shall immediately stop all work hereunder and shall immediately cause any and all of its suppliers and subcontractors to cease work. Subject to the terms of this contract, the Contractor shall be paid a percentage of the contract price reflecting the percentage of the work performed prior to the notice of termination, plus reasonable charges the Contractor can demonstrate to the satisfaction of the Government using its standard record keeping system, have resulted from the termination. The Contractor shall not be required to comply with the cost accounting standards or contract cost principles for this purpose. This paragraph does not give the Government any right to audit the Contractor's records. The Contractor shall not be paid for any work performed or costs incurred which reasonably could have been avoided.

(m) Termination for cause. The Government may terminate this contract, or any part hereof, for cause in the event of any default by the Contractor, or if the Contractor fails to comply with any contract terms and conditions, or fails to provide the Government, upon request, with adequate assurances of future performance. In the event of termination for cause, the Government shall not be liable to the Contractor for any amount for supplies or services not accepted, and the Contractor shall be liable to the Government for any and all rights and remedies provided by law.  If it is determined that the Government improperly terminated this contract for default, such termination shall be deemed a termination for convenience.

(n) Title.  Unless specified elsewhere in this contract, title to items furnished under this contract shall pass to the Government upon acceptance, regardless of when or where the Government takes physical possession.

(o)  Warranty.  The Contractor warrants and implies that the items delivered hereunder are merchantable and fit for use for the particular purpose described in this contract.

(p) Limitation of liability. Except as otherwise provided by an express warranty, the Contractor will not be liable to the Government for consequential damages resulting from any defect or deficiencies in accepted items.

(q) Other compliances. The Contractor shall comply with all applicable Federal, State and local laws, executive orders, rules and regulations applicable to its performance under this contract.

(r) Compliance with laws unique to Government contracts. The Contractor agrees to comply with 31 U.S.C. 1352 relating to limitations on the use of appropriated funds to influence certain Federal contracts; 18 U.S.C. 431 relating to officials not to benefit; 40 U.S.C 3701, et seq., Contract Work Hours and Safety Standards Act; 41 U.S.C. 51-58, Anti-Kickback Act of 1986; 41 U.S.C. 265 and 10 U.S.C. 2409 relating to whistleblower protections; 49 U.S.C 40118, Fly American; and 41 U.S.C. 423 relating to procurement integrity.

(s) Order of precedence. Any inconsistencies in this

solicitation or contract shall be resolved by giving precedence in the following order: (1) the schedule of supplies/services; (2) the Assignments, Disputes, Payments, Invoice, Other Compliances, and Compliance with Laws Unique to Government Contracts paragraphs of this clause; (3) the clause at 52.212-5; (4) addenda to this solicitation or contract, including any license agreements for computer software; (5) solicitation provisions if this is a solicitation; (6) other paragraphs of this clause; (7) the Standard Form 1449; (8) other documents, exhibits, and attachments; and (9) the specification.

(t) Central Contractor Registration (CCR).

(1) Unless exempted by an addendum to this contract, the Contractor is responsible during performance and through final payment of any contract for the accuracy and completeness of the data within the CCR database, and for any liability resulting from the Government's reliance on inaccurate or incomplete data. To remain registered in the CCR database after the initial registration, the Contractor is required to review and update on an annual basis from the date of initial registration or subsequent updates its information in the CCR database to ensure it is current, accurate and complete. Updating information in the CCR does not alter the terms and conditions of this contract and is not a substitute for a properly executed contractual document.

(2)(i) If a Contractor has legally changed its business name, "doing business as" name, or division name (whichever is shown on the contract), or has transferred the assets used in performing the contract, but has not completed the necessary requirements regarding novation and change-of-name agreements in FAR Subpart 42.12, the Contractor shall provide the responsible Contracting Officer a minimum of one business day's written notification of its intention to (A) change the name in the CCR database; (B) comply with the requirements of Subpart 42.12; and (C) agree in writing to the timeline and procedures specified by the responsible Contracting Officer. The Contractor must provide with the notification sufficient documentation to support the legally changed name.

(ii) If the Contractor fails to comply with the requirements of paragraph (q)(2)(i) of this clause, or fails to perform the agreement at paragraph (q)(2)(i)(C) of this clause, and, in the absence of a properly executed novation or change-of-name agreement, the CCR information that shows the Contractor to be other than the Contractor indicated in the contract will be considered to be incorrect information within the meaning of the "Suspension of Payment" paragraph of the electronic funds transfer (EFT) clause of this contract.

(3) The Contractor shall not change the name or address for EFT payments or manual payments, as appropriate, in the CCR record to reflect an assignee for the purpose of assignment of claims (see Subpart 32.8, Assignment of Claims). Assignees shall be separately registered in the CCR database. Information provided to the Contractor's CCR record that indicates payments, including those made by EFT, to an ultimate recipient other than that Contractor will be considered to be incorrect information within the meaning of the "Suspension of payment" paragraph of the EFT clause of this contract.

(4) Offerors and Contractors may obtain information on registration and annual confirmation requirements via the internet at http://www.ccr.gov or by calling 1-888-227-2423 or 269-961-5757.

## C2  Contract Terms and Conditions Required to Implement Statutes or Executive Orders-Commercial Items (52.212-5 JAN 2009)

(a) The Contractor shall comply with the following Federal Acquisition Regulations (FAR) clauses, which are incorporated in this contract by reference, to implement provisions of law or Executive orders applicable to acquisitions of commercial items:

(1)   52.233-3, Protest after Award (AUG 1996) (31 U.S.C. 3553).

(2)  52.233-4, Applicable Law for Breach of Contract Claim (OCT 2004) Public L. 108-77, 108-78)

(b) The Contractor shall comply with the FAR clauses in this paragraph (b) that the Contracting Officer has indicated as being incorporated in this contract by reference to implement provisions of law or Executive orders applicable to acquisitions of commercial items:

(1) 52.203-6, Restrictions on Subcontractor Sales to the Government (SEPT 2006), with Alternate I (SEPT 2006) (41 U.S.C. 253g and 10 U.S.C. 2402).

(2) 52.203-13, Contractor Code of Business Ethics and Conduct (DEC 2008) (Pub. L. 110-252, Title VI, Chapter 1 (41 U.S.C. 251 note)).

(3) 52.219-3, Notice of Total HUBZone Small Business Set-Aside (JAN 1999) (15 U.S.C 657a).

(4) 52.219-4, Notice of Price Evaluation Preference for HUBZone Small Business Concerns (JULY 2005) (if the offeror elects to waive the preference, it shall so indicate in its offer) (15 U.S.C. 657a).

(5) [Reserved]

(6) (i)52.219-6, Notice of Total Small Business Set-Aside (JUNE 2003)(15 U.S.C. 644).

(ii) Alternate I (OCT 1995) of 52.219-6.

(iii) Alternate II (MAR 2004) of 52.219-6.

(7)(i) 52.219-7, Notice of Partial Small Business Set-Aside (JUNE 2003)(15 U.S.C. 644).

(ii) Alternate I (OCT 1995) of 52.219-7.

(iii) Alternate II (MAR 2004 of 52.219-7.

(8) 52.219-8, Utilization of Small Business Concerns (MAY 2004)(15 U.S.C. 637 (d)(2) and (3)).

(9)(i) 52.219-9, Small Business Subcontracting Plan (NOV 2007)(15 U.S.C. 637(d)(4).

(ii)Alternate I (OCT 2001) of 52.219-9.

(iii) Alternate II (OCT 2001) of 52.219-9.

(10) 52.219-14, Limitations on Subcontracting (DEC 1996) (15 U.S.C. 637(a)(14).

(11)(i) 52.219-16, Liquidated Damages – Subcontracting Plan (JAN 1999) (15U.S.C. 637(d)(4)(F)(i).

(12)(i) 52.219-23, Notice of Price Evaluation Adjustment for Small Disadvantaged Business Concerns (OCT 2008)(10 U.S.C. 2323) (if the offeror elects to waive the adjustment, it shall so indicate in its offer).

(ii) Alternate I (JUNE 2003)of 52.219-23.

(13) 52.219-25, Small Disadvantaged Business Participation Program-Disadvantaged Status and Reporting (OCT 1999)(Pub. L. 103-355, section 7102, and 10 U.S.C. 2323).

(14) 52.219-26, Small Disadvantaged Business Participation Program-Incentive Subcontracting (OCT 2000) (Pub. L. 103-355, section 7102, and 10 U.S.C. 2323).

(15) 52.219-27, Notice of Total Service-Disabled Veteran-Owned Small Business Set-Aside (MAY 2004) (15 U.S.C. 657f).

(16) 52.219-28, Post Award Small Business Program Representation (JUNE 2007) (15 U.S.C. 632(a)(2).

(17) 52.222-3, Convict Labor (JUNE 2003)(E.O. 11755).

(18) 52.222-19, Child Labor-Cooperation with Authorities and Remedies (FEB 2008)(E.O. 13126).

(19) 52.222-21, Prohibition of Segregated Facilities (Feb 1999).

(20) 52.222-26, Equal Opportunity (MAR 2007)(E.O. 11246).

(21) 52.222-35, Equal Opportunity for Special Disabled Veterans, Veterans of the Vietnam Era, and Other Eligible Veterans (SEPT 2006)(38 U.S.C. 4212).

(22) 52.222-36, Affirmative Action for Workers with Disabilities (JUN 1998) (29 U.S.C. 793).

(23) 52.222-37, Employment Reports on Special Disabled Veterans, Veterans of the Vietnam Era, and Other Eligible Veterans (SEPT 2006)(38 U.S.C. 4212).

(24) 52.222-39, Notification of Employee Rights Concerning Payment of Union Dues or Fees (DEC 2004)(E.O. 13201).

(25)(i) 52.222-50, Combating Trafficking in Persons (AUG 2007) (Applies to all contracts).

(ii) Alternate I (AUG 2007) of 52.222-50

(26) 52.222-54, Employment Eligibility Verification (JAN 2009). (Not applicable to the acquisition of commercially available off-the-shelf items or certain other types of commercial items as prescribed in 22.1803.)

(27)(i) 52.223-9, Estimate of Percentage of Recovered Material Content for EPA-Designated Products (AUG 2000)(42 U.S.C. 6962(c)(3)(A)(ii)).

(ii) Alternate I (AUG 2000) of 52.223-9 (42 U.S.C. 6962(i)(2)(C)).

(28) 52.223-15, Energy Efficiency in Energy-Consuming Products (DEC 2007)(42 U.S.C. 8259b).

(29) 52.223-16, IEEE 1680 Standard for the Evironmental Assessment of Personal Computer Products (DEC 2007)(E.O. 13423).

(30) 52.225-1, Buy American Act-Supplies (JUNE 2003)(41 U.S.C. 10a - 10d).

(31)(i) 52.225-3, Buy American Act - Free Trade Agreements-Israeli Trade Act (AUG 2007) (41U.S.C. 10a - 10d, 19U.S.C. 3301 note, 19U.S.C. 2112 note, Pub. L. 108-77, 108-78, 108-286,  109-53 and 109-169).

(ii) Alternate I (JAN 2004) of 52.225-3.

(iii) Alternate II (JAN 2004) of 52.225-3.

(32) 52.225-5, Trade Agreements (NOV 2007)(19 U.S.C. 2501, et seq., 19 U.S.C. 3301 note).

(33) 52.225-13, Restriction on Certain Foreign Purchases (JUNE 2008) (E.O’s, proclamations and statutes administered by the Office of Foreign Assets Control of the Department of the Treasury).

(34)  52.226-4, Notice of Disaster or Emergency Area Set-Aside (NOV 2007) (42 U.S.C. 5150).

(35) 52.226-5, Restrictions on Subcontracting Outside Disaster or Emergency Area (NOV 2007) (42.U.S.C. 5150)

(36) 52.232-29, Terms for Financing of Purchases of Commercial Items (FEB 2002)(41 U.S.C. 255(f), 10 U.S.C. 2307(f)).

(37) 52.232-30, Installment Payments for Commercial Items (OCT 1995)(41 U.S.C. 255(f), 10 U.S.C. 2307(f)).

(38) 52.232-33, Payment by Electronic Funds Transfer-Central Contractor Registration (OCT 2003)(31 U.S.C. 3332).

(39) 52.232-34, Payment by Electronic Funds Transfer-Other than Central Contractor Registration (MAY 1999)(31 U.S.C. 3332).

(40) 52.232-36, Payment by Third Party (MAY 1999)(31 U.S.C. 3332).

(41) 52.239-1, Privacy or Security Safeguards (AUG 1996)(5 U.S.C. 552a).

(42)(i) 52.247-64, Preference for Privately Owned U.S.-Flag Commercial Vessels (FEB 2006)(46 U.S.C. Appx 1241 and 10 U.S.C. 2631).

(ii) Alternate I (APR 2003) of 52.247-64.

(c) The Contractor shall comply with the FAR clauses in this paragraph (c), applicable to commercial services, which the Contracting Officer has indicated as being incorporated in this contract by reference to implement provisions of law or Executive orders applicable to acquisitions of commercial items:

(1) 52.222-41, Service Contract Act of 1965 (NOV 2007)(41 U.S.C. 351, et seq.).

(2) 52.222-42, Statement of Equivalent Rates for Federal Hires (MAY 1989)(29 U.S.C. 206 and 41 U.S.C. 351, et seq.).  (See Exhibits)

(3) 52.222-43, Fair Labor Standards Act and Service Contract Act-Price Adjustment (Multiple Year and Option Contracts) (NOV 2006) (29 U.S.C. 206 and 41 U.S.C. 351, et seq.).

(4) 52.222-44, Fair Labor Standards Act and Service Contract Act-Price Adjustment (FEB 2002)(29 U.S.C. 206 and 41 U.S.C. 351, et seq.).

(5) 52.222-51, Exemption from Application of the Service Contract Act to Contracts for Maintenance, Calibration, or Repair of Certain Equipment – Requirements (NOV 2007) (41 U.S.C. 351, et seq.).

(6) 52.222-53, Exemption from Application of the Service Contract Act to Contracts for Certain Services – Requirements (NOV 2007) (41U.S.C. 351, et seq.).

(7) 52.237-11, Accepting and Dispensing of $1 Coin (SEPT 2008) (31U.S.C. 5112(p)(1)).

(d) Comptroller General Examination of Record. The Contractor shall comply with the provisions of this paragraph (d) if this contract was awarded using other than sealed bid, is in excess of the simplified acquisition threshold, and does not contain the clause at 52.215-2, Audit and Records-Negotiation.

(1) The Comptroller General of the United States, or an authorized representative of the Comptroller General, shall have access to and right to examine any of the Contractor's directly pertinent records involving transactions related to this contract.

(2) The Contractor shall make available at its offices at all reasonable times the records, materials, and other evidence for examination, audit, or reproduction, until 3 years after final payment under this contract or for any shorter period specified in FAR Subpart 4.7, Contractor Records Retention, of the other clauses of this contract. If this contract is completely or partially terminated, the records relating to the work terminated shall be made available for 3 years after any resulting final termination settlement. Records relating to appeals under the disputes clause or to litigation or the settlement of claims arising under or relating to this contract shall be made available until such appeals, litigation, or claims are finally resolved.

(3) As used in this clause, records include books, documents, accounting procedures and practices, and other data, regardless of type and regardless of form. This does not require the Contractor to create or maintain any record that the Contractor does not maintain in the ordinary course of business or pursuant to a provision of law.

(e)(1) Notwithstanding the requirements of the clauses in paragraphs (a), (b), (c) and (d) of this clause, the Contractor is not required to flow down any FAR clause, other than those listed in paragraphs(e)(1)(i) through (xi) of this paragraph in a subcontract for commercial items. Unless otherwise indicated below, the extent of the flow down shall be as required by the clause –

(i) 52.203-13, Contractor Code of Business Ethics and Conduct (DEC 2008) (Pub. L. 110-252, Title VI, Chapter 1 (41 U.S.C. 251 note)).

(ii) 52.219-8, Utilization of Small Business Concerns (MAY 2004)(15 U.S.C. 637 (d)(2) and (3)), in all subcontracts that offer further subcontracting opportunities. If the subcontract (except subcontracts to small business concerns) exceeds $550,000 ($1,000,000 for construction of any public facility), the subcontractor must include 52.219-8 in lower tier subcontracts that offer subcontracting opportunities.

(iii) 52.222-26, Equal Opportunity (MAR 2007)(E.O. 11246);

(iv) 52.222-35, Equal Opportunity for Special Disabled Veterans, Veterans of the Vietnam Era, and Other Eligible Veterans (SEPT 2006)(38 U.S.C. 4212);

(v) 52.222-36, Affirmative Action for Workers with Disabilities (JUNE 1998)(29 U.S.C. 793);

(vi) 52.222-39, Notification of Employees Rights Concerning the Payment of Union Dues or Fees (DEC 2004)(E.O. 13201);

(vii) 52.222-41, Service Contract Act of 1965 (NOV 2007) (41 U.S.C. 351, et seq.).

(viii) 52.222-50, Combating Trafficking in Persons (AUG 2007) (22 U.S.C. 7104(g)).  Flow down required in accordance with paragraph (f) of FAR clause 52.222-50.

(ix) 52.222-51, Exemption from Application of the Service Contract Act to Contracts for Maintenance, Calibration, or Repair of Certain Equipment – Requirements (NOV 2007) (41U.S.C. 351, et seq.).

(x) 52.222-53, Exemption from Application of the Service Contract Act to Contracts for Certain Services – Requirements (NOV 2007) (41U.S.C. 351, et seq.).

(xi) 52.222-54, Employment Eligibility Verification (JAN 2009).

(xii) 52.247-64, Preference for Privately Owned U.S.- Flag Commercial Vessels (FEB 2006)(46 U.S.C. Appx 1241 and 10 U.S.C. 2631). Flow down required in accordance with paragraph (d) of FAR clause 52.247-64).

(2) While not required, the contractor may include in its subcontracts for commercial items a minimal number of additional clauses necessary to satisfy its contractual obligations.

# C3. AUTHORITY OF GOVERNMENT REPRESENTATIVES

C3.1  Contracting Officer (CO)

The CO is the appointed Government official with authority to enter into, administer and terminate this contract.  No one but the CO is authorized under any circumstances to:

C3.1.1  Award, agree to, or execute any contract, contract modification, or notice of intent.

C3.1.2  Obligate, in any way, the payment of money by the Government.

C3.1.3  Make a final decision on any contract matter that is subject to the Disputes clause of this contract.

C3.1.4  Terminate, for any cause, the Contractor's right to proceed.

C3.2  Contracting Officer's Technical Representative (COTR)

The COTR will be identified at the time of contract award.  The COTR is authorized to take any or all actions necessary to assure compliance with the technical portions of the contract.  The COTR’s authorized representative will conduct all requested or required inspections.

# C4. WARRANTY

Contractor shall provide their/a standard commercial warranty on both workmanship and materials furnished in the aircraft.  The terms and conditions of the warranties available shall be part of the offer and shall address both parts and labor. The location of warranty adjustments shall also be addressed.  Assignment of third party suppliers (parts suppliers) shall also be included in warranty provisions.

# C5. PROOF OF OWNERSHIP

The Contractor shall furnish documentation of aircraft title search to show certification of clear title to the aircraft and proof of ownership before payment for the aircraft will be processed.

# C6. INSPECTION/ACCEPTANCE

C6.1 Inspection/acceptance of the aircraft by Government personnel will be at the location identified at award in accordance with the contractor's delivery schedule and as approved by the Government. The Government reserves the right to perform a peruse inspection and take a test flight prior to acceptance of the aircraft.

# C7. Payment Terms

C7.1 The Government will make payment via electronic funds transfer prior to physically taking possession of the aircraft.

# C8  Availability of Funds (52.232-18 APR 1984)

Funds are not presently available for this contract.  The Government’s obligation under this contract is contingent upon the availability of appropriated funds from which payment for contract purposes can be made.  No legal liability on the part of the Government for any payment may arise until funds are made available to the Contracting Officer for this contract and until the Contractor receives notice of such availability, to be confirmed in writing by the Contracting Officer.

# D1.  INTRODUCTION

D1.1  The supplies of this Request for Quotes (RFQ) are being acquired under the authority of Federal Acquisition Regulations (FAR), Part 12, Acquisition of Commercial Items and FAR Subpart 13.5, Test Program for Certain Commercial Items.

D1.2  If you want to compete for the contract described in Sections A through C of this RFQ, submit a Quote to include a signed and dated offer and other requested information by the time and date shown on the SF1449.

# D2.  INSTRUCTIONS TO OFFERORS--COMMERCIAL ITEMS (52.212-1 SEPT 2006) [Tailored SEPT 2005]

## D2.1 North American Industry Classification System (NAICS) Code and Small Business Size Standard

The NAICS code and small business size standard for this acquisition is 441229 and $8.5 million annual receipts.

## D2.2  Send Quotes to:

By mail, hand carried or express delivery service:

Department of the Interior

Aviation Management

300 E. Mallard Drive, Suite 200

Boise, Idaho 83706-3991

SOLICITATION 8008-09

Email: Michael_mcfarlane@nbc.gov

## D2.3  Period for accepting Quotes

The company agrees to hold the prices in its offer for 60 calendar days from the date specified for receipt of quotes however, the contractor is not bound to hold the aircraft for that time period.

## D2.4   Submission of Quote.  Quote should include:

D2.4.1  A price quote for the aircraft.

D2.4.2  A detailed Specifications Sheet with sufficient detail to determine time life components and equipment that will come with the aircraft. This shall include empty weight, max gross weight, useful load, and any charts that may be helpful in determining the capability of the aircraft.

D2.4.3  Pictures of the aircraft to determine basic condition.

D2.4.4  Acknowledgment of Solicitation Amendments (if any).

D2.4.5  A list of all damage history of the aircraft.

D2.4.6 Estimated timeline of where (city and country) the aircraft has been operated over the aircraft’s operational life.

## D2.5  Late Submissions, Modifications, Revisions, and Withdrawals of Quotes

Late Submissions, Modifications, Revisions and Withdrawals of Quotes are subject to the terms of Federal Acquisition Regulation (FAR) clause 52.212-1(f), which is incorporated by reference, except that quotes may be withdrawn at any time before performance or agreement of the contractor.

## D2.6 Data Universal Numbering System (DUNS) Number)

Data Universal Numbering System (DUNS) Number. (Applies to all offers exceeding $25,000, and offers of $25,000 or less if the solicitation requires the Contractor to be registered in the Central Contractor Registration (CCR) database. The offeror shall enter, in the block with its name and address on the cover page of its offer, the annotation "DUNS" or "DUNS+4" followed by the DUNS or DUNS+4 number that identifies the offeror's name and address. The DUNS+4 is the DUNS number plus a 4-character suffix that may be assigned at the discretion of the offeror to establish additional CCR records for identifying alternative Electronic Funds Transfer (EFT) accounts (see FAR Subpart 32.11) for the same parent concern. If the offeror does not have a DUNS number, it should contact Dun and Bradstreet directly to obtain one. An offeror within the United States may contact Dun and Bradstreet by calling 1-866-705-5711 or via the internet at http://www.dnb.com. An offeror located outside the United States must contact the local Dun and Bradstreet office for a DUNS number.

## D2.7  Special Notice

D2.7.1 Central Contractor Registration

Unless exempted by an addendum to this solicitation, by submission of a quote, the company acknowledges the requirement that a prospective awardee shall be registered in the CCR database prior to award, during performance and through final payment of any contract resulting from this solicitation.  Failure to register in the CCR database prior to award may affect your ability to be awarded a contract and the Contracting Officer may proceed to award to the next otherwise successful registered company. Companies may obtain information on registration and annual confirmation requirements via the internet at http://www.ccr.gov or by calling 1-888-227-2423 or 269-961-5757.

Prior to contract award, the company will be required to complete Representations and Certifications at FAR 52.212-3 (JUNE 2008).

# D3.  EVALUATION OF QUOTES

The Government intends on awarding a contract resulting from this solicitation to the responsible company whose quote conforms to the solicitation and is the most advantageous to the Government, price and other factors considered.  We will evaluate quotes and select the Contractor based on (1) evaluated price (2) capability to include proposed delivery date, as explained below, and (3) aircraft capabilities and condition.

## D3.1  Acceptability

Your quote in response to this solicitation must be acceptable. We will eliminate unacceptable quotes without considering price. We will determine the acceptability of your offer based on the subfactors identified below.  Failure to meet any one subfactor would be grounds for an unacceptable offer.

D3.1.1  Assent to Solicitation Terms. We will consider your quote to be unacceptable if you take exception to any terms of this solicitation. Your offer must assent to all required terms of this request for quote and you must provide all information requested (See D2.4).

D3.1.2  Aircraft Requirements. We will consider your quote to be unacceptable if you propose an aircraft that fails to meet the minimum capabilities in Section B.

## D3.2  Evaluated Price

The offered total unit price will be adjusted by the factors identified below to determine the evaluated total price.

D3.2.1.  The price of all aircraft will be adjusted for time control components in accordance with the aircraft blue book.

D3.2.2  The evaluated price of all aircraft that do not include the target requirement listed in B6 and B7.6 will be adjusted to add  the estimated cost to the Government to add the equipment to the aircraft.

D3.2.3   Any other probable costs to the government.

D3.2.4 The Government has $1,500,000.00 available for the purchase of a basic helicopter. Basic helicopter is defined as one meeting all of the required capabilities but not the target capabilities.

## D3.3  Capability

Delivery Date. Delivery is desired on or before May 1, 2009.  Quotes will be evaluated on the proposed delivery date based on their ability to meet the May 1, 2009 delivery date. Companies with the ability to meet the delivery date will be evaluated higher than those not capable of meeting the delivery date. The further from the May 1, 2009 delivery date you propose, the lower of an evaluation you will receive.

## D3.4 Aircraft Capabilities and Condition.

D3.4.1 Aircraft Capability. We will consider the capability of the aircraft to include additional equipment above and beyond what is required or targeted. Aircraft offering additional capabilities or equipment that the Government considers to be beneficial will receive a more favorable rating. Additionally, aircraft equipped with the target equipment will receive a more favorable evaluation than a comparably equipped aircraft.

D3.4.2 Condition. We will evaluate the overall condition of your aircraft based upon all data provided to include a possible pre-buy inspection. The better condition your offered aircraft is in, the better evaluation you will receive. The Government reserves the right to reject offers for aircraft that have what we consider to be significant accident histories or those that include aircraft that are not in what we feel is acceptable condition.

## D3.5  Tradeoff Analysis and Contractor Selection

We will select the Contractor by comparing the acceptable quotes with reasonable evaluated prices.  We will compare them on the basis of evaluated price, offeror capability to include delivery, and aircraft capability and condition.  If one offer is best on all the factors, then we will select that quote as the best value. If no quote is best on all the factors, then we will consider the differences among offers and make tradeoffs in order to determine which offer is the better value. We will award the contract to the company that has the best combination of aircraft capability and condition, capability, evaluated price, and delivery.

## D3.6  Notice of Award

We will provide the successful Contractor with a written offer either by mail or other means after we have made our selection.  This written offer will comprise a contract and shall result in a binding contract upon initiation of performance or acceptance of the order. Once agreed to, the contractor will be bound to the contract.

# Text boxes

AUXILIARY VHF-FM RADIO INTERFACE

DRAWING FS/OAS A-17