Before the

Federal Communications Commission

Washington, D.C. 20554

In the Matter of 					)

)

Petition of Celtronix Telemetry, Inc. for		)		Call Sign KIVD0054

Waiver of Sections 95.855(a) and 95.863 of	)

The Commission’s Rules to Provide a Vehicle	)

Tracking Service in the Norfolk/Virginia Beach	)

Metropolitan Statistical Area			)

ORDER

Adopted:  November 17, 1999	Released:  November 17, 1999

By the Chief, Public Safety and Private Wireless Division, Wireless Telecommunications Bureau:

I.  INTRODUCTION

1.	 Celtronix Telemetry, Inc. (Celtronix), a licensee in the 218-219 MHz Service, requests a waiver of the Commission’s Rules as part of its planned operation of a vehicle tracking service in its license area.  For the reasons set forth below, we grant the petition.

II. BACKGROUND

2.	Celtronix is licensee of Station KIVD0054 in the 218-219 MHz Service for the Norfolk-Virginia Beach Metropolitan Statistical Area (MSA).  In its Waiver Request, Celtronix describes its plans to provide a vehicle tracking service by using a series of Cell Transceiver Stations (CTSs) as base stations and Remote Transmitter Units (RTUs) deployed in vehicles.  Specifically, Celtronix seeks to operate mobile RTUs at up to one watt with no duty cycle.  To build this system, Celtronix seeks waiver of two technical rules for the 218-219 MHz Service, namely, Sections 95.955(a) and 95.863 of the Commission’s Rules, 47 C.F.R. §§ 95.955(a) and 95.863.  Section 95.955(a) of the Commission’s Rules limits the effective radiated power (ERP) of mobile RTUs to 100 milliwatts.  Section 95.863 of the Commission’s Rules prescribes a maximum five-second-per-hour duty cycle for each RTU.

3.	At the time Celtronix filed the Waiver Request, the Commission was in the process of revising its rules for the 218-219 MHz band.  Originally allocated as the Interactive Video and Data Service, the 218-219 MHz Service was designed as a short-distance communications service in which licensees could provide information or services to individual subscribers and those subscribers could provide interactive responses.  The technical rules for the 218-219 MHz band were designed to support a specific service model – a television set-top unit.  On September 7, 1999, the Commission adopted changes to the 218-219 MHz Service rules that were designed to “allow 218-219 MHz Service providers to fully utilize the spectrum,” with the expectation that the “rule changes will foster full and effective development and deployment of the 218-219 MHz Service.”  In recognition of the variety of systems that could now develop in the 218-219 MHz Service, the Commission largely replaced specific technical rules with a general requirement that systems not interfere with television reception within a TV Channel 13 station’s Grade B predicted contour.  In this connection, we note that Section 95.855 of the Commission’s Rules was modified to limit mobile RTU transmissions to four watts, and Section 95.863 – the duty cycle limitation – was removed.

III.  DISCUSSION

4.	Section 1.3 of the Commission’s Rules allows the waiver of a rule provision “if special circumstances warrant a deviation from the general rule and such deviation will serve the public interest.”   Celtronix claims that a special circumstance exists because the underlying purpose of the rules will not be served.  While we recognize that the technical rules at issue are designed to protect TV Channel 13 reception from 218-219 MHz Service systems, we nonetheless note that Celtronix indicates that it has performed tests, in conjunction with the Technology Applications Center of Norfolk and the Engineering Department of Old Dominion University, demonstrating that mobile RTUs operating in excess of 100 milliwatts with no duty cycle in Celtronix’s service area do not present an interference concern for TV Channel 13 operations.  Moreover, Celtronix describes how it has operated mobile RTUs under an experimental license since the fall of 1998 without interference complaints from TV Channel 13 licensees or viewers.  We further note that in the 218-219 MHz Service R&O, the Commission concluded that the “general rules” of which Celtronix seeks a waiver are no longer necessary.  We believe that grant of the requested waiver would be consistent with the Commission’s determination that certain technical rules “provide a measure of interference protection that may not be necessary in all cases.” We further believe that grant of a waiver in this instance would allow Celtronix to deploy a system that will be permissible without waiver once the newly adopted rules take effect.  We conclude that these factors, taken together, constitute “special circumstances” within the meaning of Section 1.3 of the Commission’s Rules.

5.	Moreover, we are convinced that the public interest will be served by the grant of the instant waiver.  An important goal of the Commission’s 218-219 MHz Service proceeding was to “encourage competition and provide services to the largest feasible number of users within the 218-219 MHz band.”  Celtronix has identified a service it believes will be commercially viable and responsive to public need – vehicle tracking services.  It also notes that the Commission has previously recognized that the provision of vehicle tracking services is beneficial to the public.  For these reasons, we conclude that it would not serve the public interest to delay the deployment of Celtronix’s service.  Moreover, because Celtronix proposes operations that are consistent with the newly adopted rules, we do not believe that the public interest would be furthered by requiring Celtronix to wait until the effective date of the rules to commence operations.

6.	Although we grant the instant waiver request, we reiterate that our action here does not relieve Celtronix from its obligations to comply with the interference protection requirements of Section 95.861 of the Commission’s Rules.  We require Celtronix to take appropriate measures under that rule to identify and mitigate any interference its 218-219 MHz Service system may cause, regardless of the power or duty cycles it uses.  In addition, on our own motion, we grant Celtronix a waiver to operate its mobile RTUs with up to four watts ERP.  Although Celtronix proposed a maximum one-watt output, a four-watt limit is consistent with our recently adopted but not-yet-effective rules.

III.  CONCLUSION

7.	We conclude that Celtronix has demonstrated good cause exists for the grant of its waiver request, and we will allow operation of mobile RTUs within its licensed service area at up to four watts and with no duty cycle.  This waiver will continue until the rules adopted in WT Docket No. 98-169 on September 7, 1999, become effective.

IV.  ORDERING CLAUSES

8.	Accordingly, IT IS ORDERED pursuant to Sections 4(i) and of the Communications Act of 1934, as amended, 47 U.S.C. §§ 154(i), and Sections 1.3 and 90.305 of the Commission’s Rules, 47 C.F.R. §§ 1.3, 90.305, the request by Celtronix Telemetry, Inc. to operate RTUs in its licensed service area in excess of 100 milliwatts and with no duty cycle, filed June 22, 1998, IS GRANTED to the extent described above.

9.	This action is taken under delegated authority pursuant to Sections 0.131 and 0.331 of the Commission’s Rules, 47 C.F.R. §§ 0.131, 0.331.

FEDERAL COMMUNICATIONS COMMISSION

D'wana R. Terry									Chief, Public Safety and Private Wireless Division

Wireless Telecommunications Bureau

# Footnotes

Celtronix Telemetry, Inc., Petition for Waiver (April 27, 1999) (Waiver Request).

Together, the components of a 218-219 MHz Service system are the administrative apparatus, the RTUs, and one or more CTS.  47 C.F.R. § 95.803(b).  In the original service model for this band, the CTS was envisioned as a base site that would communicate with multiple RTUs placed in subscribers’ homes.  See generally Amendment of Part 95 of the Commission’s Rules to Provide Regulatory Flexibility in the 218-219 MHz Service, Report and Order and Memorandum Opinion and Order, WT Docket No. 98-169, FCC 99-239, ¶ 6 (218-219 MHz Service R&O).

Waiver Request at 1-2.

Id. at 1.

47 C.F.R. § 95.955(a).

47 C.F.R. § 95.863.

Amendment of Part 95 of the Commission’s Rules to Provide Regulatory Flexibility in the 218-219 MHz Service, Order, Memorandum Opinion and Order, and Notice of Proposed Rulemaking, 13 FCC Rcd 19064, 19065 ¶ 1.

See generally 218-219 MHz Service R&O, ¶¶ 13 and 99.

Id., ¶ 14.

Id., ¶ 112.

56 Fed. Reg. 69,656 (1999).  The final rules are scheduled to take effect 60 days after their Nov. 3, 1999, publication in the Federal Register.

47 C.F.R. § 1.3.  Celtronix cites Section 1.925 of our Rules, 47 C.F.R. § 1.925, as the basis under which we consider waiver requests in the Wireless Radio Services.  We note, however, that these waiver rules were not yet in effect at the time of Celtronix’s filing, and that we have previously used a Section 1.3 analysis when evaluating waiver requests in the 218-219 MHz Service.  Request of Licensees in the 218-219 MHz Service for Waiver of the Five-Year Construction Deadline, Order, 14 FCC Rcd 5190 (1999).

218-219 MHz Service R&O, ¶ 96.

Waiver Request at 4 and Attachment A.

Id. at 4.

218-219 MHz Service R&O, ¶ 99.

Id., ¶ 1.

Celtronix Waiver Request at 6 (citing Amendment of Part 90 of the Commission’s Rules to Adopt Regulations for Automatic Vehicle Monitoring Systems, PR Docket No. 93-61, Report and Order, 10 FCC Rcd 4695).  These public interest functions include, inter alia, allowing the efficient use of fleet vehicles, encouraging efficient energy use, reducing harmful automobile emissions, and increasing national productivity.  Id.

See 218-219 MHz Service R&O at para. 12 for a discussion of the difficulties licensees have had in developing services for the 218-219 MHz Service under the prior service rules.

47 C.F.R. § 95.861.  The Commission revised these provisions in the 218-219 MHz Service R&O.