|  | Fermilab |
| --- | --- |

Particle Physics Division

Mechanical Department Engineering Note

# Number:	MD-ENG- 088	         Date:  Sep. xx, 2005

Project Internal Reference:

Project:  ILC

Title:	Vacuum Vessel Engineering Note for 3.9 GHz, 3rd Harmonic

Author(s): Edward Chi

Reviewer(s):

Key Words:

Crymodule, Vacuum, Pressure, FEA, Vessel Shell, Stiffening Rib,

Reinforcement, Flange, Weldment, Up & Downstream,

Abstract Summary:

The vacuum vessel of 3.9 GHz, 3rd harmonic has 42.87” O. D, ~ 82.64”

Length with multiple openings for different connections and

instrumentation. This engineering note is presented extensive

discussion,  FEA analysis and calculations for the vessel and nozzle

shells, stiffening rings, multiple openings and reinforcements, different

flanges, welds and others per Fermilab, ASME and other applicable

codes.

Applicable Codes:

ES&H Manual Chapter 5033, Fermilab.

“Boiler & Pressure Vessel Code” ASME VIII, Div.1

2004 Edition

“Allowable Stress Design”, AISC, 9th edition

“Structural Welding Code-Steel”, AWS D1.1-90

EXHIBIT A-1

Vacuum Vessel Engineering Note

(per Fermilab ES&H Manual Chapter 5033)

| Prepared by | Edward Chi | Date | 08-26-2005 | Div/Sec | PPD/MD/ME |
| --- | --- | --- | --- | --- | --- |
| Reviewed by |  | Date |  | Div/Sec |  |
| Div/Sec Head |  | Date |  | Div/Sec |  |

1.	Identification and Verification of Compliance

Fill in the Fermilab Engineering Conformance Label information below:

This vessel conforms to Fermilab ES&H Manual Chapter 5033

| Vessel Title | 3.9 GHz, 3rd Harmonic Vacuum Vessel |
| --- | --- |
| Vessel Number |  |
| Vessel Drawing Number | 5520 – ME - 439317 |
| Internal MAWP | 1 psig |
| External MAWP | 14.7 psi |
| Working Temperature Range | 20 oF 100 oF |
| Design/Manufacturer | DESY |
| Date of Manufacture |  |
| Acceptance Date |  |

Director's signature (or designee) if vessel is for manned area and requires an exception to the provisions of this chapter.

| Amendment No. | Reviewed by: | Date: |
| --- | --- | --- |

| Laboratory location code |  |
| --- | --- |
| Laboratory property number |  |
| Purpose of vessel |  |

List all pertinent drawings

| Drawing No. | Location of Original |
| --- | --- |
| 5520 – ME – 439317 -1 |  |
| 5520 – ME – 439317 -2 |  |
| 5520 – ME - 439262 |  |

2.	Design Verification

Provide design calculations in the Note Appendix.

See the attached vacuum vessel engineering note #MD-Eng-088

3.	System Venting Verification

Can this vessel be pressurized either internally or externally?    [   ] Yes

[X] No

If “Yes”, to what pressure? _____________

List all reliefs and settings. Provide a schematic of the relief system components and appropriate calculations or test results to prove that the vessel will not be subjected to pressures greater than 110% beyond the maximum allowable internal or external pressure.

| Manufacturer | Relief | Pressure Setting | Flow Rate | Size |
| --- | --- | --- | --- | --- |

4.	Operating Procedure Section

Is an operating procedure necessary for the safe operation of this vessel?

[  ] Yes      [ X] No        (If "Yes", it must be appended)

Is a testing procedure necessary for the safe acceptance testing (acceptance

testing) of this vessel?

[  ] Yes      [ X] No

If “Yes”, the written procedure must be approved by the division head prior to testing and supplied with this Engineering Note.

5.	Welding Information

Has the vessel been fabricated in a Fermilab shop?     [  ] Yes      [ X] No

If "Yes," append a copy of the welding shop statement of welder qualification.

The fabrication will be performed by using qualified welder of an

outside contractor.

6.	Exceptional, Existing, Used and Non-Manned Area Vessels

Is this vessel or any part thereof in the above categories?  [   ]  Yes

[ X]  No

If "Yes" follow the Engineering Note requirements for documentation and append to note.

CONTENTS

Section                                             Descriptions                                                        Pages

i.        Exhibit A-1, Fermilab ES&H Manual Chapter 5033                                          2

1.       Calculation for the Vacuum Vessel Cylindrical Shell Thickness                         7

2.       The Permissible Out of Roundness of the Vessel Cylindrical Shell                     9

3.       Analysis and Calculations for the Stiffening Rings

3.1  To Define the Downstream End Flange as the Stiffening Ring for the                10

Vessel Shell Under the External Pressure

3.2  To Define the Upstream End Flange as the Stiffening Ring for the                     13

Vessel Shell Under the External Pressure

4.       Calculations and Analysis for the Vessel Shell Openings

4.1.  Calculations for the Opening of Port Coldmass for the Reinforcement               14

and Weld Size

4.2.   Calculations for the Opening of  MC Port (#9) for the Reinforcement and        19

Weld Size

4.3    Calculations for the Opening of Electronic Port for the                                      23

Reinforcement and Weld Size

5.        Calculations and Analysis for the Flanges, Bolts and Welds

5.1    Downstream End Flange, and the Bellow Flange                                                26

5.2    Upstream End Flange, Slide Flange and the Bellow Flange                                36

5.3    Calculations for Flanges #8, #10, #2 and #3                                                        40

6.        Finite Element Analysis (FEA) for the Vessel Weldment, Bottom

Supports and Top Lifting Fixtures                                                       42

7.        Appendix                                                                                                              47

Figure i.1, An overall view of the vacuum vessel weldment of 3.9 MHz,

3rd Harmonic

Reference drawing: ME – 439317- 1(2)

Overall length = 82.64 in

Wws ≈ 2,264 lbs. the weight of the vessel shell weldment.

Assuming the vessel shell is operating under the room temperature.

Vessel shell material:  SA 516-60

Materials for flanges, ports and nozzles: see respective notes and drawings.

1.  Calculation for the Vacuum Vessel Cylindrical Shell Thickness

The Vacuum Vessel Cylindrical Shell:

Given:

P:   14.7 psi, the external design pressure,

Do:  38.00 in, outside diameter of the vessel shell

Di:   37.25 in, inside diameter of the vessel shell

tn:   The nominal vessel shell thickness.

Fa: 20,000 psi, the max. allowable stress of the shell material under the operating

temp, -20o F to 100o F, also know as Sv. for vessel shell material SA 516-70,

carbon steel, see dwg.  #ME-439747 (per Table 1A, part D, section II, ASME

VIII, 2004 edition)

Lv: Design length of the vessel between lines of the support.

M.A: Material corrosion and other misc. allowance, ~ 1/16”

Assuming:

Lv ≈ 82.64 in (per drawing #ME-439317-01)

Find out the required vessel shell thickness tn:

- Try tn = 0.31”

Lv/Do = 82.64” / 42.87” = 1.93

Do/tn = 42.87” / 0.31” = 138.29

Per section UG-28, also Fig. G and Fig. CS-2 in Subpart 3 of Section II, part D,

ASME VIII, Div. 1:

It is found out that:

A = 0.00043

B = 6000

Then:

Pa = (4B) / (3Do/tn)

= (4 x 6000) ÷ (3 x 138.29)

= 57.85 psi

where:

Pa : The max. allowable external working pressure, psi

A:  Factor determined from Fig. G

B:  Factor determined from the applicable material chert in Fig. CS-2.

- Try tr2 = 0.2

Lv/Do = 1.93

Do/tr2 = 42.87”/0.20” = 214

Find:

A ≈ 0.00023

B = 3300

Then:

Pa2 = (4B) / (3Do/tn)

= (4 x 3300) ÷ (3 x 214)

≈ 19.64 psi

- Try tr3 = 0.175

Lv/Do = 1.93

Do/tr3 = 42.87”/0.175 = 245

Find:

A ≈ 0.00019

B = 2800

Then:

Pa3 = (4B) / (3Do/tn)

= (4 x 2800) ÷ (3 x 245)

≈ 15.23 psi

So, tr = 0.175”

So the vessel shell thickness is required 0.175”, using 0.31” as vessel shell thickness is above the shell thickness required and it is satisfactory.

2.  The Permissible Out of Roundness of the Vessel Cylindrical Shell

Given:

P:   14.7 psi, the external design pressure,

Do:  42.87 in, outside diameter of the vessel shell

Di:  42.24 in, inside diameter of the vessel shell

tn:   0.31”, the nominal vessel shell thickness.

Fa: 15,000 psi, the max. allowable stress of the shell material at the operating temp,

also know as Sv.

Vessel shell material: SA 516-60, carbon steel, see dwg. #ME-439317

Lv: ~82.64”, design length of the vessel between lines of the support.

The difference between the max. dia and the mini. dia. of the vessel shell at any cross

section shall not exceed:

  - x 42.87 in = 0.428 in

(per section UG-80 (b)(1) of ASME VIII, Div.1)

Per section UG-80(b)(2) and figure UG-80 of ASME VIII, Div.1,  it is found out that

the maximum plus or minus deviation from the true circular form, measured radially on

the outside or inside of the cylindrical vessel shall not exceed the maximum permissible

deviation e:

e ≈ 0.65t

= 0.65 x 0.31 in

= 0.202 in

where:

Do / t = 138

Lv / Do = 1.93

Per Figure UG-29.2, section UG-29 of ASME VIII, Div.1, it is found out that:

Arc length ≈ 0.20 Do

= 0.20 x 42.87 in

= 8.574 in

Chord length = 2 x Arc length

= 2 x 8.574 in

= 17.15 in

So, in a chord length of 17.15 in, the maximum plus or minus deviation from the true

circle form shall not exceed 0.202 in.

3.    Analysis and Calculation for the Stffening Rings

  - To Define the Downstream End Flange as the Stiffening Ring for the Vessel

Shell Under the External Pressure

Reference drawings: ME-439317, MD-439240

Givien:

E = 28 x 106 psi, Modules of elasticity of the flange materials

le = 1.1 (Dot)0.5 = 1.1 (42.87” x 0.31”)0.5

= 4.01”, the effective regional length of the vessel shell

Fy: 25 ksi, min. yield stress of the stiffening material A182-F304L under the

operating temperature.

Figure 3.2,  The cross-section view of the end flange with the vessel shell, also refer to

detail L of drawing ME-439317, and drawing MD-439240..

To find the required moment of inertia of the combined end flange – shell cross section about the neutral axis parallel to the axia of the shell, in4, Is’:

Is’ = [Do2Ls(t + As/Ls)A] / 10.9                     (eq. 3-2)

(per UG-29, ASME VIII, Div.1)

Where:

Asd:  Cross-sectional area of the downstream end flange stiffening area, in2

≈ (1.57 x 3.74) – (0.79 X 1.57) in2 = 4.6315 in2,  see figure 3.2 and MD-439240

Lsd:  Distance between the stiffening ring and downstream end flange,  ~82.64 in

( See drawing ME-439317)

B:  Factor determined from the applicable chart,

= 0.75 [PDo ÷ (t + As/Ls)]

= 0.75 [14.7 psi x 42.87 in ÷ (0.31 in + 4.6315 in2/82.64 in)]

= 1291

Per figure CS-2 in Subpart 3 of section II, Part D,  where B = 1084 falling below the left end of the material/temperature curve, so:

A = 2B/E

= 2 x 1291 / (28 x 106)

= 0.0000922

(per step 5 of UG-29, ASME VIII, Div. 1)

Then the Eq. 3-2 becomes:

Is’ = {[42.872 x 82.64 x (0.31 + 4.6315/82.64) x 0.0000922] / 10.9}in4

= ((151,879 x 0.366 x 0.0000922) /10.9) in4

=  0.4702 in4

To find the combined moment of inertia of the cross section area of the stiffening ring and shell

It is found that from the figure 3.2:

A1 = 2.79 in x 0.31 in = 0.8649 in2

A2 ≈ (1.57 x 3.74) – (0.79 X 1.57) in2 = 4.6315 in2

y1 = 0.155 in

y2 = 2.18 in

y = (A1y1 + A2y2) ÷ (A1 + A2)

= 1.8613 in

dy12 = (y – y1)2 = 2.9115 in2

dy22 = (y – y2)2 = 0.1016 in2

I1 = 0.0069 in4

I2 = 6.8444 in4

I = ∑Ii + ∑Aidyi2

= (6.8513 + 2.9887) in4

= 9.84 in4 > I’= 0.4702 in4

Since the requirement moment of inertia I’ is less than the value of I provided by the combined moment inertia of the end flange(downstream) and vessel shell, so the downstream end flange is satisfactory and it can be treated as a support of the vessel.

  - To Define the Upstream End Flange as the Stiffening Ring for the Vessel Shell Under the External Pressure

Reference drawings: Detail K of drawing ME-439317-2,

MD- 439240

Lsu:  Distance between the stiffening ring and upstream end flange,  ~ 82.64 in = Lsd

Asu: ≈ (1.57 x 3.74) – (0.79 X 1.57) in2 = 4.6315 in2 = Asd

Since using the same flange at the upstream end and the downstream end,  also, Lsu = Lsd;  Asu = Asd, Dou = Dod, tu = td, from the calculation steps of section 3.2, we can conclude that the requirement moment of inertia Iu’ = Id’, the available combined moment inertia Iu = Id, that leads to the conclusion:

Iu = Id = 9.84 in4 > Iu’ = Id’= 0.4702 in4

So the upstream end flange is satisfactory and it can be treated as a support of the vessel.

4.         Calculations and Analysis for the Vessel Shell Openings

  - Calculations for the Opening of Coldmass Port (#3) for the Reinforcement and

Weld Size

The main vessel shell:

(ref. drawings: ME-439317, ME-4392620, MD-439252)

P:   14.7 psi, external design pressure

Do: 42.87 in, outside dia. Of the vessel shell.

Di: 42.24, inside dia. of the vessel shell.

t:   0.31 in, the nominal pipe wall thickness.

Fa: 15,000 psi, the max. allowable stress of the shell material at the operating temp,

also know as Sv. at the operating temp.,  -200  F to 1000 F (per Table 1A, part D,

Section II, ASME Boiler & Pressure Vessel Code 1995 edition).

Vessel shell material: SA 516, grade 60, carbon steel (see ME-439262)

Lv: Design length of the vessel section between lines of support (see Page UG-28(b)),

≈ 82.64”

Find out the required vessel shell thickness tr:

1.   Try tn = 0.31”

Lv/Do = 82.64” / 42.87” = 1.93

Do/tn = 42.87” / 0.31” = 138.29

Per section UG-28, also Fig. G and Fig. CS-2 in Subpart 3 of Section II, part D,

ASME VIII, Div. 1:

It is found out that:

A = 0.00043

B = 6000

Then:

Pa = (4B) / (3Do/tn)

= (4 x 6000) ÷ (3 x 138.29)

= 57.85 psi

where:

Pa : The max. allowable external working pressure, psi

A:  Factor determined from Fig. G

B:  Factor determined from the applicable material chert in Fig. CS-2.

- Try tr2 = 0.2

Lv/Do = 1.93

Do/tr2 = 42.87”/0.20” = 214

Find:

A ≈ 0.00023

B = 3300

Then:

Pa2 = (4B) / (3Do/tn)

= (4 x 3300) ÷ (3 x 214)

≈ 19.64 psi

- Try tr3 = 0.175

Lv/Do = 1.93

Do/tr3 = 42.87”/0.175 = 245

Find:

A ≈ 0.00019

B = 2800

Then:

Pa3 = (4B) / (3Do/tn)

= (4 x 2800) ÷ (3 x 245)

≈ 15.23 psi

So, tr = 0.175”

The coldmass port:

do: 25.197”, outside dia. of the port.

Di:  15.512”, inside dia . of the port.

tn:  4.842”, wall thickness  of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  28 x 106 psi, modulus of elasticity of the material at the operating temp.

Material: SA 182- 304L stainless steel pipe, Fa = Sn = 16,700 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: ME-439317, MD-439251, MD-439252, and also as shown from

figure 4.1.

Figure 4.1, 3D view of the coldmass port #3 and the vessel shell

Find out the thickness required:

- Assuming  L1 = 5.49 in, tr1 = 0.375 in, then:

L1/do = 5.49/25.197 = 0.2179

do/tr1 = 25.197/0.375 = 67

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.0165

B = 13800

Pa = (4B)/(3(do/tr1)) = (4 x 13800)/(3 x 67) = 275 psi > P

- Try: L2 = 5.49 in, tr2 = 0.0625 in

L2/do = 0.2179

do/tr2 = 403

get:

A = 0.00083

B = 8250

Pa = (4B)/(3(do/tr2)) = (4 x 8250)/(3 x 403) = 27.30 psi > P

- Try: L3 = 6.64 in, tr3 = 0.0425 in

L3/do = 0.2179

do/tr3 = 25.197/0.0425 = 593

get:

A = 0.000475

B = 6750

Pa = (4B)/(3(do/tr2)) = (4 x 6750)/(3 x 593) = 15.18 psi ≈ P

So: trn = tr3 = 0.0425 in

Size of the weld required:

Per UG-37, UW-16 and Fig. UW-16.1(p) of ASME VIII, Div.1.

to:  the throat dimension of the outer attachment weld,  ≥ 0.5 tmin.

ti:   the throat dimension of the inside of the shell cutout,  ≥ 0.7tmin

to = 0.5 tmin = 0.5 x 0.31” = 0.155”, so the fillet leg size is 0.22”

ti  = 0.7 tmin = 0.7 x 0.31” =0.217”, so the fillet leg size is 0.31”

(See details J & K of dwg. ME-439317-1 as the references)

So the sizes of the weld are satisfactory.

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1)

= 0.5 x (16.299” x 0.175” x 1.0 +2 x 4.842” x 0.25” x 1.0 x 0)

= 1.4262 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

D = 16.299 in (per drawing ME-439262)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 =1.0 for nozzle wall abutting the vessel wall as shown in figure UG-40(j),

(k), (n), (o) and (p).

fr2 = Sn / Sv = 16.7 / 15 = 1.113

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 16.299” x  (1 x 0.31” – 1.0 x 0.175”) – 0

= 2.2004 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.31” + 4.842”) x (1.0 x 0.31” – 1.0 x 0.175”) – 0

= 1.391 in2

So pick A1 = 2.2004 in2

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (4.842 in – 0.0425 in) x 0.31 in x 1.0

= 7.4392 in2

or     = 5 (tn-trn) fr2tn

= 5 x (4.842 in – 0.0425 in) x 1.113 x 4.842 in

= 129.33 in2

So pick A2 = 7.4392 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.222 in2 x 1.0

=0.0484 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.312 in2 x 1.0

= 0.0961 in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (2.2004 + 7.4392 + 0 + 0.0484 + 0.0961) in2

= 9.784 in2 > Ar = 1.4262 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the current designated boundary conditions.

The analysis and conclusion should be also true for coldmass port opening #2 (see drawing MD-439251), this is because: all basic data such as: do, Di, L, to, ti, Sn of coldmass #2 are the same as coldmass #3. So, per section UG-37 of ASME VIII, Div.1, the #3 opening is adequately reinforced under current design.

  - Calculations for the Opening of  MC (main coupler) Port (#9) for the

Reinforcement and Weld Size

The main vessel shell:

From section 4.1, it is found that  tr = 0.175”

The MC port:

do: 11.339”, outside dia. of the port.

Di:  10.945”, inside dia . of the port.

tn:  0.197”, wall thickness  of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  28 x 106 psi, modulus of elasticity of the material at the operating temp.

Material: SA 249-TP304L stainless steel pipe, Fa = Sn = 14,200 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: ME-439317-2, and also as shown from figure 4.2.

Figure 4.2, The partial 2D and 3D views of the MC port from ME-439317

Find out the wall thickness required:

- Assuming  L1 = 8.57 in, tr1 = 0.125 in, then:

L1/do = 8.57/11.339 =0.7558

do/tr1 = 11.339/0.125 = 91

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.00225

B = 10500

Pa = (4B)/(3(do/tr1)) = (4 x 10500)/(3 x 91) = 153 psi > P

- Try: L2 = 8.54 in, tr2 = 0.0625 in

L2/do = 0.7558

do/tr2 = 181

get:

A = 0.00075

B = 8050

Pa = (4B)/(3(do/tr2)) = (4 x 8050)/(3 x 181) = 59.3 psi > P

Try: L3 = 8.54 in, tr3 = 0.033 in

L2/do = 0.7558

do/tr3 = 344

get:

A = 0.000280

B = 3950

Pa = (4B)/(3(do/tr2)) = (4 x 3950)/(3 x 344) = 15.31 psi ≈ P

So: trn = tr3 = 0.033 in

Size of the weld required:

Per UG-37, UW-16 and Fig. UW-16.1© of ASME VIII, Div.1.

tmin:   0.197”

tc:     ≥ 0.7tmin = 0.138”, so the fillet leg size is 0.195”

Full penetration weld (bevel groove) plus the fillet weld tc.

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1)

= 0.5 x (11.339” x 0.175” x 1.0 +2 x 0.197” x 0.175” x 1.0 x 0.053)

= 0.994 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

D = 11.339 in (per drawing ME-439317)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 = Sn / Sv  for nozzle wall inserted through the vessel wall

fr2 = Sn / Sv = 14.2 / 15 =0.947

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 11.339” x  (1 x 0.31” – 1.0 x 0.175”) – 2 x 0.197 (1.0 x 0.31 – 1.0 x 0.175) x

0.053

= (1.5308 – 0.0028) in2

= 1.528 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.31” + 0.197”) x (1.0 x 0.31” – 1.0 x 0.175”) – 2 x 0.197 (1.0 x 0.31 – 1.0 x

0.175) x 0.053

= (0.1825 – 0.0028) in2

= 0.1341 in2

So pick A1 = 1.528 in2

A2: Smaller of the following:

= 5 (tn-trn)tfr2

= 5 x (0.197 in – 0.033 in) x 0.31 in x 0.947

=  0.2407 in2

or     = 5 (tn-trn) fr2tn

= 5 x (0.197 in – 0.033 in) x 0.947 x 0.197 in

= 0.153 in2

So pick A2 = 0.153 in2

A3:   Area available in inward nozzle, use the smallest value:

Since there is no inward nozzle

So pick A3 = 0.0 in2

A41: Outward nozzle weld

= leg2 fr2

= 0.1952 in2 x 0.947

=0.036 in2

A43: Inward nozzle weld

= leg2 fr2

= 0.02 in2 x 1.0

= 0.0 in2

Then:

Aa = A1 + A2 + A3 + A41 + A43

= (1.528 + 0.153 + 0 + 0.036 + 0.0) in2

= 1.717 in2 > Ar = 0.994 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the current designated boundary conditions.

The analysis and conclusion should be true for all 2 openings (#9 openings, see drawings ME-439317 & ME-439262)

4.3      Calculations for the Opening of  Electronic Port (#11 opening)

for the Reinforcement and Weld Size

The main shell (Tube #9)

From section 4.2, it is found that:  tr = 0.033 in

The instrumentation port:

do: 3.50”, outside dia. of the port.

Di:  3.334”, inside dia . of the port.

tn:  0.083”, wall thickness of the port.

trn: required thickness of the port.

L:  length of projection defining the thickness portion of integral reinforcement of the

port beyond the outside surface of the vessel wall.

E:  28 x 106 psi, modulus of elasticity of the material at the opening temp.

Material: SA 249-TP304L stainless steel pipe, Fa = Sn = 14,200 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Reference drawings: section D-D, ME-439317, and also as shown from figure 4.2.

Find out the wall thickness requires:

Assuming  L1 = 2.0075 in, tr1 = 0.083 in, then:

where: L1 = 7.48 – (11.339/2 – 0.197) = 2.0075”

L1/do = 2.0075/3.50 =0.5736

do/tr1 = 3.50/0.083 = 42

From Fig. G and Fig. HA-3 of subpart 3 of Sect. II, part D:

A = 0.009

B = 13200

Pa = (4B)/(3(do/tr1)) = (4 x 13200)/(3 x 42) = 419 psi > P

Try: L2 = 2.0075 in, tr2 = 0.015625 in

L2/do = 0.5736

do/tr2 = 224

get:

A = 0.0007

B = 8000

Pa = (4B)/(3(do/tr2)) = (4 x 8000)/(3 x 224) = 47.62 psi > P

Try: L3 = 2.0075 in, tr3 = 0.0094 in

L3/do = 0.5732

do/tr3 = 372

get:

A = 0.0003

B = 4250

Pa = (4B)/(3(do/tr2)) = (4 x 4250)/(3 x 372) = 15.23 psi ≈ P

So: trn = tr3 = 0.0094 in

Size of the weld required:

Per UG-37, UW-16 and Fig. UW-16.1(c) of ASME VIII, Div.1.

tmin:   0.083”

tc:       ≥ 0.7tmin = 0.056”, so the fillet leg size is 0.08”

Full penetration weld (bevel groove) plus the fillet weld tc.

Area of the reinforcement required Ar:

Per section UG-37(d)(1):

Ar = 0.5(dtrF + 2tntrF(1-fr1)

= 0.5 x (3.5” x 0.033” x 1.0 + 2 x 0.083” x 0.033” x 1.0 x 0)

= 0.0578 in2

Where:

d:  Finished diameter of circle opening, see Fig. UG-37.1 of UG-37.

D = 11.339 in (per drawing ME-439262)

F: Correction factor

fr : Strength reduction factor, not greater than 1.0

fr1 = Sn / Sv  for nozzle wall inserted through the vessel wall

fr2 = Sn / Sv = 14.2 / 14.2 = 1.0

Area of reinforcement available Aa:

A1: Larger of the following calculated value: (area available in shell):

= d(E1t – Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 3.50” x  (1 x 0.197” – 1.0 x 0.033”) – 2 x 0.083 (1.0 x 0.197 – 1.0 x 0.033) x 0

= 0.574 in2

or      = 2(t + tn)(E1t –Ftr)-2tn(E1t – Ftr) x (1-fr1)

= 2 (0.197” + 0.083”) x (1.0 x 0.197” – 1.0 x 0.033”) – 2 x 0.197 (1.0 x 0.375 – 1.0

x 0.25) x 0.0

=  (2 x 0.28 x 0.164) in2

= 0.0918 in2

So pick A1 = 0.574 in2

Since A1 = 0.574 in2

Also: Aa = A1 + A2 + A3 + A41 + A43

That leads to:

Aa > Ar = 0.0578 in2

# Per Fig. UG-37.1, section UG-37, the opening is adequately reinforced under the current designated boundary conditions.

The analysis and conclusion should be true for all 2 electronic ports (#11 openings, see section D-D, drawing ME-439317 and Figure 4.2 of Page 19).

5.  Analysis and Calculations for the Flanges,Their Bolts and Welds

5.1  Downstream End Flange and the Bellow Flange

References: ME-439317-2, MD-439240

Endcap (module 2-3), #0988348/0, DESY – MKS1

and Figure 5.1

Figure 5.1, Downstream end flanges with the below flange

Figure 5.1 is the assembly configuration of the downstream flange connecting with the below flange per DESY’s layout “Endcap (module 2-3)”

It was found that:

A = 50.35” (dia.)

B1 = 47.34” (dia.)

B2 = 42.24” (dia.)

C = 49.21” (dia.)

G = 47.889” (dia.)

T1 = 1.575”

T2 = 1.575”

P = 14.7 psi

n = 24

E1 = E2 = 2.8 x 107 psi

Material: SA 182-F304L stainless steel, Fa = Sf= 16,700 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

assuming bolt spec: ½ - 13 UNC

Ab = 24 x  0.1257 in2 = 3.0168 in2

The cross-sectional area of the bolts using the root  dia. (0.4001”) of the

thread in sq. in.

Per section Y-5.1, Y-5.2, figure Y-5.1.2 of Appendix Y,

Section 2-4, figure 2-4 of Appendix 2 of ASME VIII:

B2 > ½ C,

So it is defined as: Class 2, Category 3 flange

Flange Analysis:

The moment due to the pressure M’p:

M’p = HD’hD’ + HT’hT’ (per Y-6.2(3), Appendix Y, ASME VIII)

HD’= 0.785 B22 P

= 0.785 x 42.242 in2 x 14.7 psi

= 20,589 lbs.

HT’= 0.785P (B12 –B22)

= 0.785 x 14.7 psi (47.342 – 42.242) in2

=  5,272 lbs.

hD’ = (B1 – B2) ÷ 2

= (47.34 – 42.24) in ÷ 2

= 2.55 in

hT’ = (B1 – B2) ÷ 4

= (47.34 – 42.24) in ÷ 4

= 1.275 in

So:    M’p = (20,589 x 2.55) lbs-in + (5,272 x 1.275) lbs-in

= 59,224 lbs-in

= C5

(per section Y-6.2(4)(a), Appendix Y, ASME VIII, Div.1)

Let:    C6 = 0.829 / log(B1/B2)

= 0.829 ÷ 0.0495

= 16.747

(per section Y-6.2(4)(b), Appendix Y, ASME VIII, Div.1)

C1 = [1 – 2.095Js log(A/B1)] ÷ (- C6 – 1.738 Js)

(per section Y-6.2(4)(c), Appendix Y, ASME VIII, Div.1)

Where:

Js = (1/B1) [2hD/β + hC/α] + π ґB

hD = (C – B) / 2

=  (49.21 – 47.34) / 2 in

= 0.935 in

hC =  (A – C) / 2

= (50.35 – 49.21) / 2 in

= 0.57 in

β = ( C + B)/ 2B

= (49.21 + 47.34) / (2 x 47.34)

= 1.02

α = ( A + C)/ 2B

= (50.35 + 49.21) / (2 x 47.34)

= 1.052

ґB = (1/n)[4/(1 – ()2)1/2tan-1((1+ )/(1 - ))1/2 – π -2]

where:

= nD/ πC

= (24 x 0.551”) / π 49.21”

= 0.0855

D: the bolt hole diameter

ґB = (1/24)[4/(1 – (0.0855)2)1/2tan-1((1+ 0.0855)/(1 – 0.0855))1/2 – π –

2 x 0.0855]

= 0.041667 x (4.0147 x 0.8282- π – 0.171)

= 0.0005159

Js = (1/47.34”) [2 x 0.935/1.02 + 0.57/1.052] + π x 0.0005159

= 0.0211 x (1.8333 + 0.5418) + 0.0016

= 0.0517

So:

C1 = [1 – 2.095 x 0.0517 x log(50.35/47.34)] ÷ ( - 16.747 – 1.738 x 0.0517)

= ( 1 – 0.0029 ) ÷ (-16.8369)

= -0.0592

C2 = (1.738JpMp – C5C6) ÷ (- C6 – 1.738 Js)

(per section Y-6.2(4)(d), Appendix Y, ASME VIII, Div.1)

where:

Jp = (1/B1) [hD/β + hC/α] + π ґB

= (1/47.34”) [0.935/1.02 + 0.57/1.052] + π x 0.0005159

= 0.0211 x (0.9167 + 0.5418) + 0.0016

= 0.0324

Mp = HDhD + HThT + HGhG (per sectionY-3, Appendix Y, ASME VIII)

HD = 0.785 B12 P

= 0.785 x 47.342 in2 x 14.7 psi

= 25,861 lbs.

H   = 0.785G2P

= 0.785 x 47.8892 in2 x 14.7 psi

= 26,464 lbs.

HT = H - HD

= 26,464 – 25,861

= 603 lbs.

hG  = (C – G)/2

= (49.21 – 47.889) in / 2

= 0.6605 in

hD = 0.935 in

hT = (hD  + hG) / 2

= 0.7978 in

HG = W – H, gasket load

(per section 2-3, appendix 2, ASME VIII)

W = H + Hp,

flange design load for the operating condition

(per section 2-5(c)(1), appendix 2, ASME VIII)

which leads to:

HG = W – H

=  H + Hp – H

=  Hp

= 2b x 3.14GmP

= 2 x 0.281 in x 3.14 x 47.889 in x 3.5 x 14.7 psi

=  4,348 lbs.

Mp = HDhD + HThT + HGhG

= (25,861 x  0.935 + 603 x 0.7978 + 4,348 x 0.6605)  lbs-in

= (24,180 + 481 + 2,872) lbs-in

= 27,533 lbs-in

C2 = (1.738JpMp – C5C6) ÷ (- C6 – 1.738 Js)

= (1.738 x 0.0324 x 27,533 – 16.747 x 59,244) lbs-in ÷ (-16.747 – 1.738 x

0.0517)

= 990,609 lbs-in / (- 16.8369)

=  -58,836 lbs-in

For the rigid body rotation of the flange times E*:

E1* θrbi = X(C4 – C2) ÷ (1.206 log(A/B1) –XC3 – (1 – X)C1)

where:

C3 = - (0.575 – 1.206 Js log(A/B1)) ÷ (Js + t13/F1’)

= 0

C4 = - (JpMp) ÷ (Js + t13/F1’)

= 0

F1’= 0 (per section Y-3(6c), Appendix Y, ASME VIII, Div.1)

X = E1* / (E1* + E2*)

E1* = E1 t13

E2* = E2 t23

E1 = E2

X = E1 t13 / (E1 t13  + E2 t23 )

= t13 / (t13 + t23 )

= 3.907 / (3.907 + 3.907)

= 0.50

E1* θrbi = 0.50( 0 + 58,836) ÷ [(1.206 x 0.0268) –(0.50 x 0.0) – (1 –

0.50) x -0.0592)]

= 0.50 x (+58,836) lbs-in ÷ (0.0323 – 0.0 + 0.0296)

=  29,418 lbs-in ÷ 0.0619

=  475,250 lbs-in

E2* θrbii = - E1* θrbi (E2* / (E1*)

= - (475,250 x 1.0) lbs-in

=  - 475,250 lbs-in

Total Flange Moment at Diameter B1:

Ms1 = C3 (E1* θrbi) + C4

= 0.0

Ms2 = C1 (E2* θrbii) + C2

= - 0.0592 x - 475,250 lbs-in - 58,836 lbs-in

= - 30,701 lbs-in

Unbalanced Flange Moment at Diameter B1:

Mu1 = 1.206 (E1* θrbi) log(A/B1)

= 1.206 x  475,250 lbs-in x 0.0268

=  15,360 lbs-in

Mu2 = 1.206 (E2* θrbii) log(A/B1)

= 1.206 x (- 475,250 lbs-in) x 0.0268

=  -15,360 lbs-in

Balanced Flange Moment at Diameter B1:

Mb1 =  Ms1 - Mu1

= 0.0 lbs-in - (15,360 lbs-in)

= -15,360 lbs-in

Mb2 =  Ms2 - Mu2

= -30,701 lbs-in + 15,360 lbs-in

= -15,341 lbs-in

Slope of Flange at Diameter B1 times E:

E1 θBi = (5.46/π t13) (JsMb1 + JpMp) + E1* θrbi / t13

= 0.4448 in-3 x (0.0517 x (– 15,360 lbs-in) + 0.0324 x 27,533 lbs-in) +

475,250 lbs-in / 3.907 in3)

= (44 + 121,641) psi

= 121,685 psi

E2 θBii = (5.46/π t23) (JsMb2 + JpMp) + E2* θrbii / t23

(per section Y-6.2(e), Appendix Y, ASME VIII, Div.1)

= [0.4448 x (0.0517 x (-15,341) + 0.0324 x 27,533) - 475,250 / 3.907] psi

= (44 – 121,641) psi

= -121,597 psi

Contact Force between Flange at hc:

Hc = (Mp + Mb1) / hc

= (27,533 - 15,360) lbs-in / 0.57 in

= 12,173 lbs.

Bolt Load at Operating Conditions:

Wm1 = H + HG  + HC

= (26,464 + 4,348 + 12,173) lbs

= 42,985 lbs.

Operating Bolt Stress fb:

fb  = Wm1 /Ab1

= 42,985 lbs / 3.0168 in2 (See page 52, section 5.1 of the note)

= 14,249 psi

Design Pre-stress in Bolts:

Si = fb – 1.159 hc2 (Mp + Mb1) / (2(1 – X)a t13 l re1B1)

where:

re1: ≈ 1.0, elasticity factor, the ratio between Eflange and Ebolt

a = (A + C) / 2B1

= (50.35 + 49.21) in / 2 x 47.34 in

= 1.052  (shape factor)

l: = t1 + t2 + 0.5db (calculated strain length of the bolt)

= (1.575 + 1.575 + 0.25) in

= 3.40 in

Si = 14,249 psi– 1.159 x 0.572 in2 x (27,533 – 15,360)lbs-in / (2(1 – 0.50) x

1.052 x 1.5753 in3  x 3.40 in x 1.0 x 47.34 in)

= 14,249 psi – 4,584 lbs-in3 / 662 in5

= 14,242 psi

Redial Stress in Flange I @ Bolt Circle:

SR1 = 6(Mp + MS1) / t12(πC –nD)

= 6 x ( 27,533 -0) lbs-in / 1.5752 in2  x (π 49.21 in – 24 x 0.551 in)

= 165,198 lbs-in / 350.7 in3

= 471 psi < Sn = 16,700 psi

Tangential Stress in Flange I @ Inside Diameter:

St1 =  t1 E1 θBi / B1 + (2Ft1 Z/(ho + Ft1) -1.8)(Ms1/(πB1t12)

= 1.575 in x 121,685 psi / 47.34 in

= 4,048 psi < Sn = 16,700 psi

Tangential Flange Stress Adjacent to Central Nozzle:

St2n = Y(M’p + MS2) / t22 B2

where:

Y = (1/(K-1))[0.66845 + 5.71690 K2log10K/(K2 -1)]

(per figure 2-7.1, Appendix 2, ASME VIII, Div. 1)

K = A/B

= 50.35 / 42.24

= 1.192

Y = (1/(1.192-1))[0.66845 + 5.71690 x 1.4209 x log10K/(K2 -1)]

= 5.2083 x (0.6685 + 5.7169 x 0.2575)

= 11.1489

St2n = 11.1489 x (59,224 – 30,701) lbs-in / (1.5752 x 42.24) in3

= 3,035 psi < Sn = 16,700 psi

Longitudinal Hub Stress in Flange 1:

Sh1 = 0

(per equation (34c), section Y-6.3, appendix Y, ASME VIII, Div.1)

Radial Stress in Flange 2 @ bolt circle:

Sr2b =  0

Radial Stress in Flange 2 @ Diameter B1:

Sr2B1 =  0

Tangential Stress at Center of Flange 2:

St2B2 = (0.3094 PB12 / t22) – (6 MS2 / πB1 t22)

= (0.3094 x 14.7 psi x 47.342 in2 / 1.5752 in2 )

- ( 6 x (-30,701 lbs-in) / π 47.34 in x 1.5752 in2 )

= 4,109 psi + 499 psi

= 4,608 psi < Sn = 16,700 psi

Welds Analysis and Calculations:

See UW-13 (e)(2), Fig. UW-13.2, section 2-3 and  Fig. 2-4(4a), Appendix 2 of

ASME VIII, Div.1. for the related codes and the physical representation of the

nomenclatures.

Per above codes, it is required that the throat of the fillet  c = 0.7tmin. = 0.7 x 0.31”

= 0.22”,

So the fillet leg size is ~ 0.31” as shown in figure 5.1.

It is found that:

tp= 0.53” > 0.25”

where is the smallest of tn, tx and 0.25” is 0.25”

c = tn = 0.31” = leg of the fillet

b = 0.16” + 2 x tan 15o x 0.38”

= 0.36”

a = 0.38” + 0.31”- 0.06”

= 0.63”

a + b = 0.99” ≥ 3tn = 0.93”

The weld size design for the end flange is satisfactory.

Also run a weld strength calculation for the noted location as the 2nd analysis

approach:

Radial pressure load Frp:

Frp = P Lsd

= 14.7 psi x 82.84 in

= 1,215 lbs/in

Shear flow due to radial shear load Fsr:

Fsr = VQ/I

where:

Radial shear load V:

V = 0.01 P Lsd Do

= 0.01 x 14.7 psi x 82.64 in x 42.87 in

= 521 lbs.

The 1st moment of area Q:

Q = 2.79 in x 0.31 in x (1.8613 – 0.155) in

= 1.4758 in3

I = 9.84 in4

Fsr = VQ/I

= 521 lbs. x 1.4758 in3 / 9.84 in4

=  78 lbs/in

The required resultant weld load Frw:

Frw = ( 1,2152 + 782)1/2 lbs/in

=  1,218 lbs/in

The welds for connecting the flange and the vessel shell is single groove weld inside

and intermittent fillet outside, the lowest allowable weld stress Faw:

Faw = 0.60 Sn = 0.60 x 16.7 ksi

= 10.02 ksi

The requires calculated minimum weld size Cm:

Cm  =  Frw / Faw

= 1,218 / 10,020 (in)

= 0.122 in < 0.38 in (designated single groove weld)

If adding the value of the outside intermittent fillet weld (0.31”), the weld

size even can go further smaller size.

So, the design of the weld for the upstream end flange is satisfactory.

Per the above calculations and analysis, the downstream end flange and the bellow flange have met the codes of ASME VIII, Div.1.

5.2.        Upstream End Flange, Slide Flange and Bellow Flange

References: ME-439317-2, MD-439240

Endcap (module 2-3), #0988348/0, DESY – MKS1

and Figure 5.2

Figure 5.2. Upstream flange with the below flange

Since there some information are missing at this moment, so it is to make the best assumption as followings:

1. The upstream end flange connect to the downstream stream end flange of the

bellow (see drawing Endcap (module 2-3), #0988348/0, DESY – MKS1).

2. The above two flanges are connected by a slide flange.

3.  A = 50.35”, G = 47.889”, T1 = 1.57”, T2 = 1.57”, B1 = 47.34”, B2 = 42.24”,

C = 49.21”

4.  n = 24,  D = 0.551”

E = 28 x 106 psi, Modules of elasticity of the flange materials

Material: SA 182-F304L stainless steel, Fa = Sf = 16,700 psi at the operating

temp.,  -200  F to 1000 F (per Table 1A, part D, Section II, ASME Boiler &

Pressure Vessel Code 1995 edition).

Sb = 25 ksi for bolt material: SA-193, S304 for operating

temperature, -200  F to 1000 F (per Table 3, part D, Section II, ASME

Boiler &  Pressure Vessel Code 1995 edition).

Per section Y-5.1, Y-5.2, figure Y-5.1.2 of Appendix Y,

Section 2-4, figure 2-4 of Appendix 2 of ASME VIII:

B2 > ½ C,

So it is defined as: Class 2, Category 3 flange

In order to reduce the amount of work required as shown on section 5.1, per section Y-9, of Appendix Y, ASME VIII, Div.1, we apply the method of estimating flange thickness and bolting for the downstream flanges.

ta = 2.45 [Mp / ((πC –nD)Sf)]1/2

(per eq. 39 of Y-9, appendix Y, ASME VIII, Div.1)

where:

Mp = HDhD + HThT + HGhG (per sectionY-3, Appendix Y, ASME VIII)

HD = 0.785 B12 P

= 0.785 x 47.342 in2 x 14.7 psi

= 25,861 lbs.

H   = 0.785G2P

= 0.785 x 47.8892 in2 x 14.7 psi

= 26,484 lbs.

HT = H - HD

= (26,464 – 25,861) lbs.

=  603 lbs.

hG  = (C – G)/2

= (49.21 – 47.889)in / 2

= 0.6605 in

hD = (C – B) / 2

= ( 49.21 – 47.34) / 2

= 0.935 in

hT = (hD  + hG) / 2

= 0.7978 in

HG = W – H, gasket load

(per section 2-3, appendix 2, ASME VIII)

W = H + Hp,

flange design load for the operating condition

(per section 2-5(c)(1), appendix 2, ASME VIII)

which leads to:

HG = W – H

=  H + Hp – H

=  Hp

= 2b x 3.14GmP

= 2 x 0.281 in x 3.14 x 47.889 in x 3.50 x 14.7 psi

=  4,348 lbs.

Mp = HDhD + HThT + HGhG

= (25,861 x  0.935 + 603 x 0.7978 + 4,348 x 0.6605)  lbs-in

= (24,180 + 481 + 2,872) lbs-in

= 27,533 lbs-in

ta = 2.45 [Mp / ((πC –nD)Sf)]1/2

= 2.45 x [ 27,533 lbs-in / ((π 49.21 in – 24 x 0.551 in) x 16,700 psi)]1/2

= 2.45 x 0.1078 in

= 0.264 in

tb = 0.56 B1 (P/Sf)1/2

= 0.56 x 47.34 in x (14.7 psi / 16,700 psi)1/2

= 0.56 x 47.34 in x 0.0297

= 0.788 in

Since tc is the greater of ta or tb, so:

tc = tb = 0.788”

Per equation 42 of A-7, Appendix Y, ASME VIII, Div. 1:

A’b = (H + 2 Mp / (A – C)) ÷ Sb

= (26,464 lbs + 2 x 27,533 lbs-in / (50.35 – 49.21) in ) ÷ 25,000 psi

= (26,464 lbs + 48,304 lbs) / 25,000 psi

= 2.9907 in2

Per Table Y-9.1, Appendix Y, ASME VIII, Div.1, it is found:

t1 = 1.1ta = 0.29” < T1 = 1.57”

t2 = 1.1tc = 0.867” < T2 = 1.57”

So the thickness of the flanges are ok for the upstream end flanges.

Welds Analysis and Calculations:

The weld configurations are the same as the upstream flange, it designed per section UW-13 (e)(2), Fig. UW-13.2, section 2-3 and Fig. 2-4(4a), Appendix 2 of ASME VIII, Div.1

Also, since the valus of Lsd for upstream end flange is the same as for the downstream end flange), “I” value for upstream end flange is similar as the downstream flange, all these lead to a similar values of Frw and Cm for the upstream end and downstream end flanges, so the same sizes and types of the weld design of the upstream end flange are satisfactory.

Per the above calculations, the upstream end flange and the bellow flange have met the codes of ASME VIII, Div.1.

5.3.            Flanges #8, #10, #2 and #3

In order to reduce the amount of work required as shown on section 5.1, per section Y-9, of Appendix Y, ASME VIII, Div.1, we apply the method of estimating flange thickness and bolting for the above flanges.

Since the information of the most mating flanges are not available at this moment, I made some engineering judgments per the best of my logic knowledge.

Table 5.3,  Estimated Calculated Flange thickness and bolting VS. the designated data

|  |  | Flanges (see drawing ME-439317) |
| --- | --- | --- |
| nomenclature | unit | #8 | #10 | #2 | #3 |
|  |  | MC-439243 | MC-439246 | MC-439251 | MC-439252 |
| P | psi | 14.7 | 14.7 | 14.7 | 14.7 |
| Sf | psi | 18,800 | 18,800 | 18,800 | 18,800 |
| A | in | 10.945 | 5.512 | 25.2 | 25.2 |
| B1 | in | 8.386 | 3.334 | 21.65 | 21.65 |
| B2 | in | 3.75 | 3.334 | 0 | 0 |
| C | in | 9.646 | 4.882 | 23.622 | 23.622 |
| G | in | 8.793 | 4.012 | 22.636 | 22.636 |
| Classification | 3 | 1 | 3 | 3 |
| Categorization | 3 | 3 | 3 | 3 |
| n |  | 24 | 4 | 16 | 16 |
| D | in | 0.3125 | 0.394 | 0.394 | 0.394 |
| m |  | 3.5 | 3.5 | 3.5 | 3.5 |
| b |  | 0.21 | 0.21 | 0.21 | 0.21 |
| HD | lbs | 812 | 128 | 5409 | 5409 |
| H | lbs | 892 | 186 | 5913 | 5913 |
| HT | lbs | 81 | 57 | 504 | 504 |
| hG | in | 0.4265 | 0.435 | 0.493 | 0.493 |
| hD | in | 0.63 | 0.774 | 0.986 | 0.986 |
| hT | in | 0.5283 | 0.6045 | 0.7395 | 0.7395 |
| HG | lbs | 597 | 272 | 1536 | 1536 |
| MP | lbs-in | 808 | 252 | 6463 | 6463 |
| ta | in | 0.1064 | 0.0766 | 0.1744 | 0.1744 |
| tb | in | 0.1313 | 0.0522 | 0.3390 | 0.3390 |
| tc | in | 0.1313 | 0.0766 | 0.3390 | 0.3390 |
| A'b | in^2 | 0.1137 | 0.0525 | 0.7502 | 0.7502 |
| t1 | in | 0.1171 | 0.0766 | 0.1918 | 0.1918 |
| t2 | in | 0.1444 | 0.0766 | 0.3729 | 0.3729 |
| Ab | in^2 | 0.1193 | 0.0525 | 0.7877 | 0.7877 |
| t1d | in | 0.787 | 0.512 | 1.393 | 0.79 |
| t2d | in | N/A | 0.512 | N/A | N/A |
| Abd | in^2 | 1.088 | 0.271 | 1.085 | 1.085 |

The most nomenclatures of the Table can be found from section 5.1 of this note, also from the appendix 2 and appendix Y of ASME VIII, Div.1, except:

t1,  Estimated calculated flange 1 thickness

t2,  Estimated calculated flange 2 thickness

Ab, Estimated calculated root diameter area of the bolts.

t1d,  Designated flange 1 thickness

t2d,  Dersignated flange 2 thickness

Abd, Designated root diameter area of the bolts.

Per table 5.3, it is found that all t1 > t1d; t2 > t2d and Ab > Abd for all respective flanges, so the flange design are satisfactory.

Per figure UW-13.2, section UW-13, appendix 2 of ASME VIII, Div. 1 and drawing ME-439317, it is found that all flange welds are designed per the related codes.

- Finite Element Analysis (FEA) For the Vessel Weldment, Bottom

Supports, and Top Lifting Fixtures

Reference drawing:     ME-439317-1 (2)

Figure: i.1.

Per drawing ME-439317, it is found that there are 4 lifting points which are symmetrical in both in xy and yz planes, it is also found that the 4 bottom supports only mirrored about y axis rotation (assuming that the center of the vessel is the rotational point).

It is found that:

Wws = 2,264 lbs. the weight of the vessel shell weldment

Wother ≈ 3,005 lbs.,

The weight of coldmass shields, support posts, support tubes weldment,

other attachments and mice. accessories.

Wtot  ≈ Wws + Wother  = 5,269 lbs

Figures 6.1 & 6.2 are the calculated stresses from the FEA simulating model, which is based on the 3.9 MHZ vessel weldment with the following boundary conditions:

Wws = 2,264 lbs applied to the model based the vessel physical properties;

Wother ≈ 3,005 lbs external additional force applied to the model through the 2 top

surfaces of coldmass port;

All (4) bottom saddle supports are assumed as simple support.

Figure 6.1, Stress Values in X, Y & Z directions

Figure 6.2, The Von Mises Stress & the Deform.Display of the Vessel w/4 Bottom Supts.

Figure 6.3, The Von Mises Stress & the Deform.Display of the Vessel w/4 Top Lift Pts.

Figure 6.4, The Von Mises Stress & the Deform.Display of the Vessel w/vacuum Cond.

It is found that the maximum Von Mises stress is about fvm = 3.58 ksi < Fa=15 ksi,

The higher stress areas are: bottom pad base support areas and port opening area, however, all are far below the allowable stress Fa.

Figure 6.3  is the Von Mises stress and deformation display of the vessel weldment model, which is simulating the vessel under the same boundary condition except to lift the vessel from 4 top pick points (instead of supporting by 4 bottom locations).  It is found that the maximum Vom Mises stress is about 2.08 ksi, and the max. displacement is about 0.0024”.

The simulating results of the vessel under the vacuum working environment can be found from Figure 6.4, the following are the lists of boundary condition:

- All open flanges and ports are connected with blind flanges with the matching

thickness.

- All outside surfaces of the sealed vessel experienced pressure of 14.7 psi.

(Assuming all internal surfaces under pressure of zero)

3.  Wws = 4,429 lbs. the weight of the vessel shell weldment and the blind flanges.

Wother ≈ 3,000 lbs.,

The weight of coldmass shields, support posts, support tubes weldment,

other attachments and mice. accessories.

Wtot  ≈ Wws + Wother  = 7,429 lbs

- All 4 bottom saddle supports are assumed as simple support.

It is found from Figure 6.4 that the maximum Von Mises is about  fvm = 7.18 ksi,  and the most stress area is located around the top corner area of the pad base plate of the bottom support which is next to the upstream or downstream flange. The transition areas from the end flange to the vessel shell, and the main coupler port opening areas are also the relatively higher stress area, however, all calculated stress values are less than the allowable stress Fa under the current boundary condition. It is also found that the max. displacement (~0.01”) is around the center of the end blind flange, that is due to the vacuum pressure. All the results from FEA data confirm that the design of  the bottom supports, top lifting fixtures and the vessel weldment assembly are satisfactory per the applicable codes.

- Appendix

  - The Lists of the Design Drawings of 3.9 MHz, 3rd harmonic Vacuum

Vessel (Fermilab)

1.  Vacuum Vessel Weldment Assy.                  ME – 439317 – 1 (2)

2.  Vessel Shell                                                   ME – 439262

3.  Port Fixed Coldmass                                     MD – 439251

4.  Port Sliding Coldmass                                   MD – 439252

5.  Pick Point Weldment                                     MC – 439257

6.  Pad Weld Upper                                            MC – 439242

7.  Vessel Support Weldment                             MC – 439254

8.  Pad Base Support                                           MC – 439241

9.  Flange MC Support                                        MD – 439243

10. Flange Vessel Electronics                              MD – 439246

11. Bracket, Weldment MC LH                           MC - 439238

12. Bracket, Weldment MC LH                           MC – 439239

13. Flange, Cryostat End                                      MD - 439240

14. Rib, Stiffening                                                MC – 439253

15. Gusset, Outrigger                                           MC – 439247

16. Plate, Outrigger                                              MC – 439248