PAGE III-4

Note:  The following agencies require the operator to wear an approved secondary restraint during doors-off PSD operations: USDA Forest Service, Bureau of Land Management, National Park Service, U.S. Fish and Wildlife Service, and Bureau of Indian Affairs.  If your agency is not identified, refer to the approving agency official for agency/bureau-specific direction.  Seat belts must be worn AT ALL TIMES.

Approved secondary restraints consist of either:

- A full body harness meeting 29 CFR 1910.66, 29 CFR 1926.502, or ANSI Z 359.1.  In conjunction with:

  - A carabiner that complies with ANZI Z359.1 per 3.2.

  - A Harness Tether manufactured in accordance with drawing #MTDC 1062 or 990.

  - A Harness Tether Attachment manufactured in accordance with drawing #MTDC 946.

- A Rappeller Gunner Strap manufactured in accordance with drawing #MTDC-984. In conjunction with:

  - A carabiner that complies with ANZI Z359.1 per 3.2.

  - A Harness Tether Attachment manufactured in accordance with drawing #MTDC 946.

Procurement Source: Full body harnesses and carabiners are available commercially.  The Rappeller Gunner Strap, Harness Tether and Harness Tether Attachment are obtained from:

John Day Air Base
730 Airport Rd
John Day, OR 97845
(541) 575-1322

PAGE III-6

# VIII.	Preparation for Aerial Ignition

#### A.	Preparation of Helicopter

##### 1.	Remove appropriate door/doors.

##### 2.	Remove all loose cushions and other loose materials.

##### 3.	Locate and assure proper electrical connections.

##### 4.    Install Harness Tether Attachment to hard points or seat belt hardware per instructions on MTDC drawing #- 943 (reference Appendix G).

##### 5.	Hook Harness Tether or Gunner Strap tether to Harness Tether Attachment using approved carabiner, and adjust tether length.  A properly adjusted tether shall insure that the operator is restrained inside the aircraft if the seat belt should become unbuckled during flight.

PAGE III-6

# XV.	Required PSD Kit Items

#### A.	Required PSD Support Kit, Tools, Supplies, and Spare Parts

- Approved Secondary Restraint (reference Chapter III.VI)

  - Full Body Harness (29 CFR 1910.66, 29 CFR 1926.502 or ANZI Z359.1) and Harness Tether  (MTDC 1062), OR Rappel Gunner Strap (MTDC 984)

  - Harness Tether Attachment (MTDC 946)

  - Carabiner (ANZI Z359.1 per 3.2)

- Seatbelt cutter (NFES 1093), or approved Rappel knife

- Sphere bags (refer to Tech Tip 91571305 Dec 1991)

- Interagency Aerial Ignition Guide

- One Gallon canteen