WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A11016 | In-Flight Anomaly Number -- | Contractor Report Number E-100-2 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title LO2 LEVEL SENSOR FAILED ISOLATION TEST |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 1 |
| HCRIT 1 | Sys_Lvl Y | Misc Codes A B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE L02 LEVEL SENSOR | PART# 74L4-1 | SER/LOT# 948 | MANUFACTURER SIMMONDS |
| HARDWARE LRU | NOMENCLATURE L02 TANK | PART# 80911000000 | SER/LOT# N/A | MANUFACTURER MMC |
| HARDWARE NCA | NOMENCLATURE L02 LEVEL SENSOR | PART# 74L4-1 | SER/LOT# 948 | MANUFACTURER SIMMONDS |
| Test/Operation A - ATP | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EE - RANDOM | Cause ETP - EI-TEST-INST |
| System ELECTRICAL | Defect EM - ELADJ | Material C - EEE | Work Contact J. ADAMS | Fail Date 11/21/1986 |
| Received at MSFC 09/28/1987 | Date Isolated -- | FMEA Reference 3.1.2.1 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location MAF | Symptom EVM - CON/MEG FAIL | Time Cycle -- |
| Effectivity Text LWTS 16, 20, 21, 22, 24/SUBS |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 02/10/1995 | CN RSLV SBMT 09/28/1987 | Defer Date -- | Add Date -- | R/C Codes 4 - TEST -- -- |
| Assignee |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| Approval |
| Design P. MULLER | Chief Engineer J. NICHOLS | S & MA R. JACKSON | Project M. PESSIN | Project MGR -- |
| PAC Assignee J.EL-IBRAHIM | PAC Review Complete JE | MSFC Closure Date 12/17/1987 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description A LIQUID OXYGEN LEVEL SENSOR, P/N 74L4-1, FAILED TO MEET THE ISOLATION RESISTANCE REQUIREMENT OF AN ET, WORK-IN-PROGRESS, CONFIDENCE TEST PROCEDURE. THE MINIMUM ALLOWABLE RESISTANCE AT 50 VOLTS DC IS 5 MEGOHMS. THE ACTUAL VALUE OBTAINED WAS 2.5 MEGOHMS. REFERENCE MARS T-62787. REF: CAPS E-081, E-093, MARS T62787, AND A10102. THIS PROBLEM WAS OPENED DUE TO MULTI-FAILURES AS REPORTED ON CAPS E-100B |
| Contractor Investigation/Resolution R/C: THE TEST REQUIREMENTS FOR THE SENSORS ARE NOT CONSISTENT AMONG THE VENDOR, MAF, AND THE LAUNCH SITES. TEST REQUIREMENTS HAVE BEEN REVISED TO BE CONSISTENT WITH THE VENDOR'S. 10/6/87 - TASK I FAILURE INVESTIGATION THE RESULTS OF FAILURE ANALYSIS T-62787/T-62792/T-92260, AS PERFORMED BY MMC, ARE LISTED BELOW. THE ANALYSIS INCLUDED THE ORIGINAL FAILURE AS WELL AS SEVERAL OTHER SENSORS, FROM THE SAME LEVEL SENSOR MAST ASSEMBLY, WHICH HAD LOWER THAN EXPECTED ISOLATION RESISTANCE. 1. THE CAUSE OF THE ORIGINAL SENSOR FAILURE, SERIAL NUMBER 948, WAS ARCING BETWEEN THE CIRCUIT PATH ON THE SENSOR ELEMENT SUBSTRATE AND THE METAL CASE OF THE SENSOR. 2. THE PROBABLE CAUSE OF THE LOW ISOLATION RESISTANCE ON THE TWO ADDITIONAL SENSORS, SERIAL NUM- BERS 949 AND 950, WAS A THIN OR POROUS TEFLON PAINT ON THE TRANSDUCER CASE COMBINED WITH THE CIRCUIT PATH ON THE SENSOR ELEMENT SUBSTRATE PRESSING AGAINST THE TEFLON PAINT. 3. THE VENDOR ACCEPTANCE TESTS DOES NOT CONTROL HUMIDITY DURING THE ELECTRICAL TEST. HUMIDITY AGGRAVATES THE PROBLEMS ASSOCIATED WITH THIN OR POROUS TEFLON PAINT. 4. THE VENDOR ACCEPTANCE TEST REQUIRES AN ISOLATION RESISTANCE OF GREATER THAN 2 MEGOHMS AT 500 VDC. THE MAF REQUIREMENT IS 5 MEGOHMS AT 50 VDC. THIS RESULTED IN SENSOR SERIAL NUMBER 948 FAILING THE MAF REQUIREMENT WHILE STILL PASSING THE VENDOR REQUIREMENTS. TASK II CORRECTIVE ACTION A. THE VENDOR DEVELOPED AN ASSEMBLY AID TO MORE ACCURATELY CENTER THE SUBSTRATE IN THE CASE. THIS SHOULD REDUCE THE OCCURRENCES OF THE CIRCUIT PATH TOUCHING THE INTERNAL SURFACE OF THE CASE (REFERENCE MARS T-53578). HOWEVER, THE DESIGN OF THE SENSOR PROVIDES NO POSITIVE MECHANICAL SEPARATION AND THE PARTS COULD SHIFT INTO CONTACT AT A LATER TIME. B. ELECTRICAL ENGINEERING HAS SUBMITTED PRCN-MMC-XL TO REVISE OMRSD FILE 4 TO INCLUDE AN ISOLATION RESISTANCE TEST OF THE LH2 DEPLETION SENSORS AND TO TEST ALL VEHICLES THAT HAVE ALREADY COM- PLETED FILE 4 TESTING. CLOSURE STATEMENT: THE RCN WAS APPROVED AND ASSIGNED NUMBER MT-7484. C. ELECTRICAL ENGINEERING HAS INITIATED CHANGE SUMMARY B01806 TO REVISE THE SENSOR ISOLATION RESISTANCE REQUIREMENTS AND TEST METHODS AT THE VENDOR AND AT MAF. CLOSURE STATEMENT: CHANGE SUMMARY B01806 WAS APPROVED ON SEPTEMBER 16, 1987. THE VENDOR ATP REQUIREMENTS WERE REVISED TO INCLUDE HUMIDITY AND TEMPERATURE CONTROLS DURING THE ISOLATION RESISTANCE TESTS. THE MAF FLIGHT ACCEPTANCE REQUIREMENTS, MMC-ET-TM04K-B, WERE REVISED TO REQUIRE THE SAME ISOLATION RESISTANCE VALUE AS USED DURING THE VENDOR ATP. TASK III CLEARANCE OF EFFECTIVITIES THERE ARE NO CONSTRAINTS. ALL ETS ARE TO BE RETESTED FOR ISOLATION RESISTANCE OF THE LH2 DEPLETION CIRCUITS, PER RCN MT-7484. TASK CLOSED TASK IV CAPS CLOSURE SUMMARY THE SENSOR EXPERIENCED ISOLATION RESISTANCE FAILURES WHICH RESULTED FROM BOTH THE SENSITIVITY OF THE SENSOR TO HIGH HUMIDITY AND THE ISOLATION RESISTANCE REQUIREMENTS BEING MORE STRINGENT AT MAF THAN AT THE VENDOR HISTORICALLY, THERE HAVE BEEN NO LEVEL MEASUREMENT CIRCUIT FAILURES AT KSC WHICH WERE ATTRIBUTED TO LOW ISOLATION RESISTANCE ON ANY OF THE APPROXIMATELY 20 SENSORS ON EACH ET. THE SENSOR DESIGN IS CONSIDERED TO BE ADEQUATE. THE ISOLATION RESISTANCE REQUIREMENTS WERE REVISED AT THE VENDOR, MAF, AND THE LAUNCH SITE. THE CHANGES WILL INCREASE THE LIKELIHOOD OF DETECTING SENSOR FAILURES DURING VENDOR ACCEPTANCE TESTING, RATHER THAN AFTER INSTALLATION ON AN ET. THE TEST REQUIREMENTS AT THE LAUNCH SITE FOR THE SENSORS IN THE LH2 DEPLETION CIRCUITS WERE REVISED TO INCLUDE AN ISOLATION RESISTANCE TEST TO THE SAME VALUE AS A NEW SENSOR. LOW ISOLATION RESISTANCE WILL CAUSE AN ORBITER LEVEL SENSOR SIGNAL CONDITIONER TO GIVE A FALSE "WET" INDICATION. SINCE THIS FAILURE MODE IS CRITICAL ONLY FOR THE LH2 DEPLETION CIRCUITS, ADDITIONAL TESTS FOR THE REMAINING SENSORS WERE NOT ADDED TO THE TESTING AT THE LAUNCH SITE. THE VENDOR ACCEPTANCE TEST REQUIREMENTS ARE NOW SUFFICIENTLY STRINGENT TO DETECT THE MAJORITY OF ALL SENSORS WHICH HAVE LOW ISOLATION RESISTANCE. THE LIMITED NUMBER OF ISOLATION RESISTANCE TEST FAILURES CAN BE EXPECTED TO OCCUR DURING VENDOR TESTING AS A NATURAL RESULT OF THE SENSOR DESIGN. THIS PROBLEM IS SUBMITTED TO MSFC FOR CLOSURE REVIEW AND APPROVAL 11/20/87 - THE SENSOR DESIGN HAS NOT BEEN CHANGED TO PROVIDE POSITIVE PHYSICAL SEPARATION BETWEEN THE ELECTRICAL CIRCUIT PATH OF THE SENSOR ELEMENT AND METAL CASE. THEREFORE, A RISK REMAINS THAT THE SENSOR ELEMENT MAY SHIFT IN THE CASE AT SOME TIME AFTER MANUFACTURING AND PRESS AGAINST THE TEFLON COVERED INTERIOR OF THE CASE |
| MSFC Response/Concurrence |

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A11016 | IFA# -- | Contractor RPT# E-100-2 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# 74L4-1 | Asmnt Part Name LOX LEVEL SENSOR | Asmnt Serial/Lot# 948 |
| HCRIT CD -- | FCRIT CD 1R | CAUSE CD ETP - EI-TEST-INST | FAIL MODE EM - ELECT LEAK |
| Asmnt FMEA 3.1.2.2 | Asmnt FM 2 | FMEA CSE A | FMEA SCSE 1 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |