| World Radiocommunication Conference (WRC-07) Geneva, 22 October - 16 November 2007 |  |
| --- | --- |
| PLENARY MEETING | Addendum 27 to Document 41-E |
|  | 22 August 2007 |
|  | Original: English |
| Asia-Pacific Telecommunity Administrations |
| common proposals for the work of the conference |
| Agenda item 7.1 |

7	in accordance with Article 7 of the Convention:

7.1	to consider and approve the Report of the Director of the Radiocommunication Bureau:

–	on the activities of the Radiocommunication Sector since WRC-03;

–	on any difficulties or inconsistencies encountered in the application of the Radio Regulations; and

–	on action in response to Resolution 80 (Rev.WRC-2000)

Introduction

The views of APT members and associated proposals on a number of issues being considered under Agenda item 7.1 are given below.

Issue A:	Resolution 951 (WRC-03)

Resolution 951 (WRC-03) – Options to improve the international spectrum regulatory framework

Study Group 1 has recently completed its report in response to Resolution 951 – Options to improve the international spectrum regulatory framework. The text was prepared by Working Party 1B (Revision 2 to Document 1/149) and approved by Study Group 1 at its June meeting.

In this report, four possible options have been identified so far for improving the effectiveness, appropriateness and impact of the RR with respect to the evolution of existing, emerging and future applications, systems and technologies. A combination of these options, as well as other options, may also be considered.

Option 1 is keeping the current practice as it is.

Option 2 is reviewing and possibly revising the current service definitions or adding a new service to the list of service definitions, which would encompass several of the existing ones.

Option 3 is the introduction of a new provision in the RR enabling substitution between assignments of specific services.

Option 4 is the introduction of composite services in the Table of Frequency Allocations.

The ITU-R studies in response to Resolution 951 (WRC-03) have shown that any change intended to improve the flexibility of administrations in accommodating converging services has to rely on a combination of service definitions, allocations and procedures. Improving flexibility of the RR and the timeliness of their implementation will therefore require continuation of the studies, with more focus on the allocation and sharing issues.

APT has identified the following three methods to progress work on this issue:

Method 1: Create a new agenda item for consideration at a future WRC. The item could be given priority at the conference by limiting the overall number of agenda items so that additional time and resources can be allocated to this issue.

Method 2: Hold a dedicated conference on this issue.

Method 3: Create a dedicated task group involving all relevant ITU-R Study Groups and associated working parties, outcome of which to be submitted to the subsequent WRC either through the Director’s Report or otherwise, as appropriate.

Method 1 is a realistic mechanism to consider options to improve the international spectrum regulatory framework. Following the work completed in Working Party 1B and Study Group 1, a further cycle of work prior to the WRC-11 should ensure that studies are sufficiently mature for consideration by all administrations.

Method 2 is a mechanism that can respond to what may be a very large workload. The disadvantage of this approach is that it is very expensive in terms of the conference itself and the preparation required by administrations. Currently, administrations are seeking to reduce both the length and number of meetings.

In relation to Method 3, a dedicated task group could potentially be used as a mechanism to complete the studies required as a basis to satisfy a future WRC agenda item, however this is not the only method for completion of the work. It should be noted that it will not be possible to determine work methodologies until the matter has been discussed at WRC-07.

ASP/41A27/360

APT Common View: APT countries concur with the Report of the Director of the Radiocommunication Bureau, where that report reflects the work completed by ITU-R.

Issue B:	Recommendation 723 (WRC-03)

Recommendation 723 (WRC-03) – Spectrum usage and operational characteristics of electronic news gathering systems

The use of portable and nomadic/transportable microwave radio equipment operating in appropriate fixed and mobile service bands commonly described as electronic news gathering (ENG) is now an important element in comprehensive news coverage by broadcasters.

ASP/41A27/361

APT Common View: APT countries support the conclusions reached at CPM-07 and contained in the Report namely that WRC-07 considers the approval of a Resolution [ENG] (WRC-07) calling for studies to establish whether it is feasible to, and to what extent, worldwide harmonization of user requirements and spectrum usage for electronic news gathering may be achievable in terms of the frequency bands used for such applications, including the identification of specific band(s).

The proposed example text of a draft Resolution [ASP/AI7.2/4-XX3] (WRC-07) is agreed to be dealt with as an APT proposal under WRC-07 Agenda item 7.2.

Issue C:	Resolution 74 (Rev.WRC-03)

Resolution 74 (Rev.WRC-03) – Process to keep the technical bases of Appendix 7 current

This issue is under consideration by Study Group 1, as appropriate.

Issue D:	Resolution 547 (WRC-03)

Resolution 547 (WRC-03) – Updating of the “Remarks” columns in the Tables of Article 9A of Appendix 30A and Article 11 of Appendix 30 of the Radio Regulations

This issue is under consideration by the Bureau and the Director’s Report will be submitted to WRC-07.

Issue E:	Consideration of the technical parameters for the possible planning of the broadcasting-satellite service in the band 21.4-22 GHz in Regions 1 and 3

Resolution 507 (Rev.WRC-03) – Establishment of agreements and associated plans for the broadcasting-satellite service

Resolution 525 (Rev.WRC-03) – Introduction of high-definition television systems of the broadcasting-satellite service in the band 21.4-22.0 GHz in Regions 1 and 3

Resolution 525 (Rev.WRC-03) identifies interim procedures for the introduction of HDTV BSS systems in the band 21.4-22 GHz in Regions 1 and 3, including procedures for systems introduced before 1 April 2007, and procedures for systems introduced before the next competent conference following the 2007 Conference.

WARC-92 reallocated the band 21.4-22.0 GHz in Regions 1 and 3 to the broadcasting-satellite service (BSS) to be implemented after 1 April 2007. It should be recognized that the two sets of interim procedures which are described in Resolution 525 (Rev.WRC-03) are no longer valid regarding the coordination between terrestrial services and BSS in the 21.4-22.0 GHz band.

Further, ITU-R has studied the technical issues associated with the possible planning of the BSS in the band 21.4-22.0 GHz in Regions 1 and 3, including mitigation techniques for rain attenuation, system parameters, power flux-density levels and intra-service sharing criteria. The results of these studies are included in the relevant recommendations as follows:

1)	Recommendation ITU-R BO.1659 – Mitigation techniques for rain attenuation for broadcasting-satellite service systems in frequency bands between 17.3 GHz and 42.5 GHz

2)	Recommendation ITU-R BO.1776 – Reference power flux-density for the broadcasting-satellite service in the band 21.4-22.0 GHz in Regions 1 and 3

3)	Recommendation ITU-R BO.1785 – Intra-service sharing criteria for GSO BSS systems in the band 21.4-22.0 GHz in Regions 1 and 3.

ITU-R is also developing the technical parameters beyond HDTV as in the area of extremely high resolution imagery (EHRI) that could be used as future satellite broadcasting. Those results are summarized in Recommendations ITU-R BT.1201, BT.1769 and Report ITU-R BT.2042.

To deal with the technical parameters for the possible planning of the broadcasting-satellite service in the band 21.4-22 GHz in Regions 1 and 3, two options have been identified:

1) 	request WRC-07 to include on the agenda of WRC-11 an item to consider RR No. 5.530, taking into account Resolutions 507 (Rev.WRC-03) and 525 (Rev.WRC-03), with a view to planning of the BSS band 21.4-22 GHz in Regions 1 and 3 at WRC-11;

2)	revise Resolution 525 (Rev.WRC-03).

APT countries concur with the ITU-R conclusions that Resolution 525 (Rev.WRC-03) should be revised taking into account the results of studies stated in § 7/7.1/5.2 of the CPM Report, and that further study is needed to consider the planning of the BSS band 21.4-22 GHz in Regions 1 and 3. APT proposes the following modifications to Resolution 525 (Rev.WRC-03).

MOD	ASP/41A27/362

RESOLUTION  525  (Rev.WRC-07)

Introduction of high-definition television systems
of the broadcasting-satellite service in the
band 21.4-22.0 GHz in Regions 1 and 3

The World Radiocommunication Conference (Geneva, 2007),

considering

a)	that WRC-92 has reallocated the band 21.4-22.0 GHz in Regions 1 and 3 to the broadcasting-satellite service (BSS) to be implemented after 1 April 2007;

b)	that until 1 April 2007 the existing services operating in the band 21.4-22.0 GHz in Regions 1 and 3 in accordance with the Table of Frequency Allocations are therefore entitled to continue operating without harmful interference from other services;

c)	that it also may be possible to introduce operational HDTV systems in this band before 1 April 2007 without affecting the continued operation of existing services;

d)	that after 1 April 2007 the introduction of HDTV systems in this band must be regulated in a flexible and equitable manner until such time as a future competent world radiocommunication conference has adopted definitive provisions for this purpose in accordance with Resolution 507 (Rev.WRC-03);

e)	that procedures are required for the circumstances envisaged in considering e) above,

further considering

a)	that mitigation techniques for rain attenuation for the BSS have been developed and given in Recommendation ITU-R BO.1659;

b)	that in the band 21.4-22.0 GHz in Regions 1 and 3, reference power flux-density for the BSS have been developed and given in Recommendation ITU-R BO.1776;

c)	that in the band 21.4-22.0 GHz in Regions 1 and 3, intra-service sharing criteria for GSO BSS systems have been developed and given in Recommendation ITU-R BO.1785;

d)	that in the band 21.4-22.0 GHz in Regions 1 and 3, system parameters of BSS between 17.3 GHz and 42.5 GHz and associated feeder links have been developed and given in Report ITU-R BO.2071,

noting

a)	that Recommendation ITU-R BT.1201 contains extremely high resolution imagery (EHRI);

b)	that Recommendation ITU-R BT.1769 contains parameter values for an expanded hierarchy of large screen digital imagery (LSDI) image formats for production and international programme exchange;

c)	that in future BSS systems in the band 21.4-22.0 GHz, HDTV applications may include such EHRI applications as shown in Report ITU-R BT.2042,

resolves

to adopt the interim procedures contained in the Annex hereto,

invites all administrations

to comply with the above procedures,

instructs the Radiocommunication Bureau

to apply the above procedures.

MOD	ASP/41A27/363

ANNEX  TO  RESOLUTION  525  (Rev.WRC-07)

Interim procedures for the introduction of BSS (HDTV) systems in
the band 21.4-22.0 GHz in Regions 1 and 3

Section I  –  General provisions

1	It shall be understood that prior to 1 April 2007 all existing services in the band 21.4-22.0 GHz in Regions 1 and 3 operating in accordance with the Table of Frequency Allocations shall be entitled to continue to operate. After that date they may continue to operate, but they shall neither cause harmful interference to BSS (HDTV) systems nor be entitled to claim protection from such systems. It shall be understood that the introduction of an operational BSS (HDTV) system in the band 21.4-22.0 GHz in Regions 1 and 3 should be regulated by an interim procedure in a flexible and equitable manner until the date to be decided by a future competent conference.

Section II   –  Interim procedure relating to BSS (HDTV) systems
introduced after 1 April 2007

2	For the purpose of introducing and operating BSS (HDTV) systems in the band 21.4-22.0 GHz in Regions 1 and 3 after 1 April 2007, and before a future conference has taken decisions on definitive procedures, all relevant provisions of Articles 9 to 14 except No. 9.11 shall be applied.

3	Administrations shall, to the maximum extent possible, seek to ensure that operational BSS (HDTV) systems introduced in the band 21.4-22.0 GHz in Regions 1 and 3 have characteristics which take into account the studies of the ITU-R for the preparation of a future competent world radiocommunication conference.

Issue F:	Technical aspects of use of terrestrial optical free-space telecommunications

Resolution 118 (Marrakesh, 2002) – Use of spectrum at frequencies above 3 000 GHz

CPM06-1 identified Issue F “Technical aspects of use of terrestrial optical free-space telecommunications (see PP Resolution 118 (Marrakesh, 2002))” as an item requiring urgent study by the ITU-R study groups. Moreover, PP Resolution 118 (Marrakesh, 2002) instructs the Director, BR, to Report to WRC-07 on the progress of studies concerning the use of frequencies above 3 000 GHz.

The current status of ITU-R studies on this issue is reflected in the development of recommendation and reports based on approved relevant ITU-R Questions.

ASP/41A27/364

APT Common View: APT countries concur with the status of the current studies of the ITU-R on this issue as reflected in the CPM Report.

Issue G:	Definition of HDFSS

ITU-R considered the need for a definition of HDFSS from the regulatory/procedural perspective, and also from the technical/operational perspective.

Since the acronym HDFSS is intended to refer to high-density applications within the fixed-satellite service and not to a separate service in the regulatory/procedural sense, and since the only bands identified for such applications in RR Article 5 are permitted also to be used for other FSS applications, the ITU-R study concludes that there is no need for a definition of HDFSS in RR Article 1.

ASP/41A27/365

APT Common View: APT countries support the conclusion reached at the CPM that there is no need for a definition of HDFSS in RR Article 1.

Issue H:	Definition of HEO

The term “HEO” has been used in several ITU-R Recommendations for different services during the last years. In these Recommendations, HEO has been used either as an undefined term or as an acronym for any of several different types of non-geostationary satellite orbit. The term HEO has not been formally defined in ITU-R.

ASP/41A27/366

APT Common View: APT countries concur with the conclusions reached at the CPM with regard to HEOs as follows:

–	a reconfirmation of the CPM Report to WRC-03, § 3.7.1, “HEO systems are a subcategory of non-GSO systems”;

–	it is not possible to briefly define HEO for all space radio services;

–	a description of HEO specific to a radiocommunication service other than the FSS could, and for FSS must, include both orbital and operational characteristics;

–	a description which includes such characteristics is neither suitable for inclusion nor required to be included in RR Article 1 or Recommendation ITU-R S.673;

–	within the FSS, HEO is not an acronym but refers to a type of FSS satellites and systems as characterized in Recommendation ITU-R S.1758 for use in sharing studies.

Issue I:	Review of RR No. 23.3 by WRC-07

No. 23.3 of the RR stipulates that: “In principle, except in the frequency band 3 900-4 000 kHz, broadcasting stations using frequencies below 5 060 kHz or above 41 MHz shall not employ power exceeding that necessary to maintain economically an effective national service of good quality within the frontiers of the country concerned.”

After discussion at various meetings the Radio Regulations Board has concluded that it could not provide regulatory interpretation of RR No. 23.3.

In reviewing the issue at its December 2006 meeting, the Special Committee for regulatory/procedural matters concluded that it was not in a position to provide clarification of RR No. 23.3 for the Bureau.

ASP/41A27/367

APT Common View: APT countries concur with the conclusions reached at the CPM acknowledging the importance of this issue and the need for a review of RR No. 23.3 by WRC-07 with possible actions. There are possible ways to address this issue namely to include part of the text as currently contained in No. 23.13 of the Radio Regulations in the provisions of RR 23.3 to alleviate the situation and resolve the difficulties that administrations and the Bureau are encountering.

Issue J:	Incorporation of GE06 coordination and notification data in RR Appendix 4

The Regional Radiocommunication Conference (RRC-06) met in Geneva, 15 May - 16 June 2006 and adopted the Regional Agreement relating to the planning of digital terrestrial broadcasting in parts of Regions 1 and 3, in the frequency bands 174-230 MHz and 470-862 MHz. RRC-06 also adopted Resolution 2 inviting WRC-07 to review, as appropriate, RR Appendix 4 with a view to incorporating the characteristics in Annex 3 of the Agreement that are to be submitted to the Bureau for the coordination and notification of assignments within the planning area.

APT countries prefer Method C as contained in the CPM Report under which there will be no change to RR Appendix 4 (Annex 1A and Annex 1B). In this case an additional footnote needs to be added to Annex 1A.

APPENDIX 4 (Rev.WRC-03)

Consolidated list and tables of characteristics for use in the
application of the procedures of Chapter III

MOD	ASP/41A27/368

ANNEX 1A

List of characteristics of stations in the terrestrial services1, ADD 2

_______________

1	The Radiocommunication Bureau shall develop and keep up-to-date forms of notice to meet fully the statutory provisions of this Appendix and related decisions of future conferences. Additional information on the items listed in this Annex together with an explanation of the symbols is to be found in the Preface to the International Frequency List.

ADD	ASP/41A27/369

2	For the application of the procedures governed by the GE06 Agreement by the Member States that are parties to that Agreement, within the planning areas and the frequency bands specified in that Agreement, the electronic formats for submission of the required data elements are included in the Preface to the BR IFIC and to the International Frequency List.

Issue K: 	Cancellation of the notifications in non-payment of the cost recovery

WRC-2000 adopted several footnotes relating to the consequences of non-payment of the cost recovery fees in Article 9 of the RR, Article 4 of Appendices 30/30A to the RR and Article 6 of 30B to the RR. Those footnotes provide that if the payments are not received in accordance with the provisions of Council Decision 482, as amended, on the implementation of cost recovery for satellite network filings, the Bureau shall cancel the publication, after informing the administration concerned.

Council-05 extended the scope of the application of the cost recovery fees to satellite network filings concerning the notification for recording of frequency assignments in the Master International Frequency Register (Article 11 of the RR, Article 5 of Appendices 30/30A to the RR and Article 8 of Appendix 30B to the RR).

In view of the above, similar footnotes are needed to address the consequences of the non-payment of cost recovery fees for the notifications. Therefore, APT countries propose that the following modifications be made to the Radio Regulations.

MOD	ASP/41A27/370

ARTICLE  11

Notification and recording of frequency
            assignments1,2,3,4,5, 6, ADD 6A     (WRC-07)

Section I  –  Notification

ADD	ASP/41A27/371

_______________

6A		If the payments are not received in accordance with the provisions of Council Decision 482, as amended, on the implementation of cost recovery for satellite network filings, the Bureau shall cancel the publication, after informing the administration concerned. The Bureau shall inform all administrations of such action, and that the network specified in the publication in question no longer has to be taken into consideration by the Bureau and other administrations. The Bureau shall send a reminder to the notifying administration not later than two months prior to the deadline for the payment in accordance with Council Decision 482 unless the payment has already been received. See also Resolution 87 (WRC-03).

APPENDIX  30 (Rev.WRC-03)*

Provisions for all services and associated Plans and List1 for
the broadcasting-satellite service in the frequency bands
11.7-12.2 GHz (in Region 3), 11.7-12.5 GHz (in Region 1)
             and 12.2-12.7 GHz (in Region 2)     (WRC-03)

(See Articles 9 and 11)     (WRC-03)

MOD	ASP/41A27/372

Article 5   (Rev.WRC-07)

Notification, examination and recording in the Master International
Frequency Register of frequency assignments to space stations
 in the broadcasting-satellite serviceADD 17A

ADD	ASP/41A27/373

_______________

17A	If the payments are not received in accordance with the provisions of Council Decision 482, as amended, on the implementation of cost recovery for satellite network filings, the Bureau shall cancel the publication, after informing the administration concerned. The Bureau shall inform all administrations of such action, and that the network specified in the publication in question no longer has to be taken into consideration by the Bureau and other administrations. The Bureau shall send a reminder to the notifying administration not later than two months prior to the deadline for the payment in accordance with Council Decision 482 unless the payment has already been received. See also Resolution 87 (WRC-03).

APPENDIX  30A  (Rev.WRC-03)*

Provisions and associated Plans and List1 for feeder links for the
broadcasting-satellite service (11.7-12.5 GHz in Region 1, 12.2-12.7 GHz
in Region 2 and 11.7-12.2 GHz in Region 3) in the frequency bands
14.5-14.8 GHz2 and 17.3-18.1 GHz in Regions 1 and 3,
and 17.3-17.8 GHz in Region 2     (WRC-03)

(See Articles 9 and 11)     (WRC-03)

MOD	ASP/41A27/374

ARTICLE  5     (rev.WRC-07)

Coordination, notification, examination and recording in the Master 
International Frequency Register of frequency assignments to
feeder-link transmitting earth stations and receiving
space stations in the fixed-satellite service21, ADD 21A

ADD	ASP/41A27/375

_______________

21A	If the payments are not received in accordance with the provisions of Council Decision 482, as amended, on the implementation of cost recovery for satellite network filings, the Bureau shall cancel the publication, after informing the administration concerned. The Bureau shall inform all administrations of such action, and that the network specified in the publication in question no longer has to be taken into consideration by the Bureau and other administrations. The Bureau shall send a reminder to the notifying administration not later than two months prior to the deadline for the payment in accordance with Council Decision 482 unless the payment has already been received. See also Resolution 87 (WRC-03).

APPENDIX  30B  (Rev. WRC-2000)

Provisions and associated Plan for the fixed-satellite service
in the frequency bands 4 500-4 800 MHz, 6 725-7 025 MHz,
10.70-10.95 GHz, 11.20-11.45 GHz and 12.75-13.25 GHz

MOD	ASP/41A27/376

ARTICLE  8     (rev.WRC-07)

Procedure for notification and recording in the Master Register of
assignments in the planned bands for the fixed-satellite serviceADD 3A

ADD	ASP/41A27/377

_______________

3A	If the payments are not received in accordance with the provisions of Council Decision 482, as amended, on the implementation of cost recovery for satellite network filings, the Bureau shall cancel the publication, after informing the administration concerned. The Bureau shall inform all administrations of such action, and that the network specified in the publication in question no longer has to be taken into consideration by the Bureau and other administrations. The Bureau shall send a reminder to the notifying administration not later than two months prior to the deadline for the payment in accordance with Council Decision 482 unless the payment has already been received. See also Resolution 87 (WRC-03).

Reasons:	Council-05 extended the scope of the application of the cost recovery fees to satellite network filings concerning the notification for recording of frequency assignments in the Master International Frequency Register.

Issue L:	Outdated provisions

The applicability of No. 5.203 passed on 1 January 2002 and therefore it is proposed to be suppressed.

ARTICLE  5

Frequency allocations

Section IV  –  Table of Frequency Allocations
(See No. 2.1)

SUP	ASP/41A27/378

5.203

Issue M:	Typographical error in the 2004 edition of RR

The Report from the Director of BR lists the typographical and other apparent errors discovered in the 2004 edition of the RR.  It is also proposed to fix the following typographical errors:

ARTICLE  9

Procedure for effecting coordination with or 
            obtaining agreement of other administrations1, 2, 3, 4, 5, 6, 7, 8    (WRC-03)

Section I  –  Advance publication of information on satellite
networks or satellite systems

General

(MOD)	ASP/41A27/379

9.2B		On receipt of the complete information sent under Nos. 9.1 and 9.2, the Bureau shall publish10 it in a Special Section of its BR IFIC within three months. When the Bureau is not in a position to comply with the time limit referred to above, it shall periodically so inform the administrations, giving the reasons therefor.     (WRC-2000)

Reasons:	Correction of typographical error by replacing the word “therefore” with “therefor”, thus the text would be similar to the text in No. 9.38 and No. 8.5 of Article 8 of Appendix 30B.

ARTICLE  11

Notification and recording of frequency
            assignments1, 2, 3, 4, 5, 6     (WRC-03)

Section II  –  Examination of notices and recording of frequency assignments
in the Master Register

(MOD)	ASP/41A27/380

11.28		Complete notices shall be marked by the Bureau with their date of receipt and shall be examined in the date order of their receipt. On receipt of a complete notice the Bureau shall, within no more than two months, publish its contents, with any diagrams and maps and the date of receipt, in the BR IFIC which shall constitute the acknowledgement to the notifying administration of receipt of its notice. When the Bureau is not in a position to comply with the time limit referred to above, it shall periodically so inform the administrations, giving the reasons therefor.

Reasons:	Correction of typographical error by replacing the word “therefore” with “therefor”, thus the text would be similar to the text in No. 9.38 and No. 8.5 of Article 8 of Appendix 30B.

__________________

# Footnotes

This term needs to be clarified and defined properly.