# IEEE P1451.3 Proposal

| Proposal Title: | PSD mask changes |
| --- | --- |
| Proposal Number: | 2002-24 |
| Revision Number: | C |
| Date: | 10/12/02 |
| Name: | Lee Eccles/Steve Smith |
| Company: | Boeing Commercial Airplanes/ORNL |
| Phone Number: | (206) 655-2824/ 865 576-2184 |
| Fax Number: | (206) 655-7724/ 865 576-2813 |
| Email Address: | Lee.h.eccles@boeing.com / smithsf@ornl.gov |
| Proposal Status: | Initial Draft Revised Draft Ready for Vote |
| Impacts: | __ __ |
| Action: | _A Approved __ Approved with changes __ Rejected __ Returned for revision |

Background:

Catlin-38

Figure 22 – Figure is difficult to understand. What is the meaning of the dotted line, what are the levels of the plateaus & frequencies on the X-axis, why does the Y-axis use dBm/Hz instead of dBm?

The comment here can be satisfied by duplicating the figure and table from G989.1 in the standard for systems without synchronization. Then for systems that use synchronization the information can be duplicated and modified to include the sync signal.

I changed the equation between 3.5 and 4 MHz.

Proposal:

### 9.4.7	Power spectrum density (PSD) mask

The power spectral density mask limiting the output of the transmitter in either a TBC or TBIM is specified in ITU Recommendation G.989.1 for systems that do not use the synchronization signal. This information is duplicated in subclause 9.4.7.1. For systems that use the synchronization signal this standard has modified the mask as shown in subclause 9.4.7.2.

#### 9.4.7.1	Power spectrum density (PSD) mask for TBIMs

The acceptable power spectral density mask for a TBIM is specified in Paragraph 5 of ITU Recommendation G.989.2 and duplicated here in Figure 1. Table 70 gives the PSD mask in table form.

Figure 1—PSD of TBIM transmitter output

Table 70—PSD Mask from G.989.1

| Frequency (MHz) | PSD limit (dBm/Hz) |
| --- | --- |
| 0.015 < f < 1.7 | -140 |
| 1.7 < f ( 3.5 | -140 + (f-1.7)*50.0/1.8 |
| 3.5 < f ( 4.0 | -90 + (f-3.5)*8.5/0.5 |
| 4.0 < f < 7.0 | -71.5 |
| 7.0 ( f ( 7.3 | -81.5 |
| 7.3 < f < 10.0 | -71.5 |
| 10.0 ( f < 13.0 | -81.5 – (f-10)*43.5/3.0 |
| 13.0 ( f < 25.0 | -125 |
| 25.0 ( f < 30.0 | -140 |

#### 9.4.7.2	Power spectrum density (PSD) mask for TBCs

This subclause gives the power spectral density mask for TBCs. Figure 2 shows the mask in graphical form and Table 71 duplicates the information in table format.

Figure 2—PSD Mask for TBC Transmitters

Table 71—PSD Mask from G.989.1 Modified for the synchronization signal

| Frequency (MHz) | PSD limit (dBm/Hz) |
| --- | --- |
| 0.015 < f < 1.0 | -140 |
| 1.0 < f ( 1.9 | -140 + (f-1.0)*68.5/0.9 |
| 1.9 < f ( 2.1 | -71.5 |
| 2.1 < f ( 2.6 | -71.5 – (f-2.1)*38.5/0.5 |
| 2.6 < f ( 3.5 | -110 + (f-2.6)*20.0/0.9 |
| 3.5 < f ( 4.0 | -90 + (f-3.5)* 8.5/0.5 |
| 4.0 < f < 7.0 | -71.5 |
| 7.0 ( f ( 7.3 | -81.5 |
| 7.3 < f < 10.0 | -71.5 |
| 10.0 ( f < 13.0 | -81.5 – (f-10)*43.5/3.0 |
| 13.0 ( f < 25.0 | -125 |
| 25.0 ( f < 30.0 | -140 |