POLAR Spacecraft Status As of: Thurs 21 Nov, 12:00 EST

(Changes from last week in bold border)

| Subsystem/ Component | NOAA-15K AM: 17:49=AN GAC data only | NOAA-16L PM: 15:04=AN GAC data | NOAA-17M AM: 22:23=AN GAC&LAC data | NOAA-18N PM 13:49=AN GAC & LAC data |
| --- | --- | --- | --- | --- |
| LAUNCHED | 05/13/98 | 09/21/00 | 6/24/02 | 5/20/05 |
| CNTL OBP | OBP2 | OBP2 | OBP2 | OBP2 |
| BUS | B-BUS XSU-1 | B-BUS XSU-2: TOAR472 | B-BUS XSU-1 | B-BUS XSU-1 |
| BUS VETO | NO | NO | NO | NO |
| ADACS | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/26/00 Gyro chans=AAB N2 Low PSI invalid | RGYRO Mode Estimate Y-ROLL Rgmode=PASSIVE Gyros-1 & 3 Inop/Off Gyro chans XA-ZB Pitch wheel bias 2400 Gyro2 safe macro | Nominal Mode Rgmode=Monitor Gyro-3 Off 6/10/04 Gyro chans=AAB GAS Enabled Dec 05 | Nominal Mode Gyro-A MIMU-2 Z-wheel -Pitch TOAR 447 Z-momentum transition complete Pitch Torquer again active |
| RXO | PRI daily bias -8 mS -500 mS 12/31/05 | PRI Daily Bias –5.5 mS -1500 mS 31Dec05 | PRI Daily Bias –3 mS -1500 mS 31Dec05 | PRI No daily bias -1500 mS 31Dec05 |
| CLOCK DIV | 2 | 2 | 2 | 2 |
| MIRP | External Synch Rephase 0730 daily | External Sync Rephase each orbit | External Sync Rephase Enabled | External Synch Rephase Enabled |
| TIP SIDE | 2 (since 4/3/03) 3 channels inop | 2 since 4/18/05 (analog drifting?) | 2 Swapped 9/20/06 | 1 Analog telem drifting |
| Recorders (DTR, SSR) | DTRs 1, 2, 3, 4 Safestate 1B EOT | DTRs 1, 2, 3, 4A Safestate 3A 4B STIP only | DTR 1,3,4 / SSR 2 Safestate=SSR 2B 4A Pressure leak | SSRs 1,2,3,4,5 Safestate=5B Current spikes |
| VTX (APT data) | #1 ON As of 19 June 07 | OFF / INOP since 11/15/00 | #2 ON 137.62 MHZ | #1 ON 137.1 MHZ As of 16 Aug 07 |
| BTX | #1 137.35 MHZ | #2 137.77 MHZ | #2 137.77 MHZ | #1 137.35 MHZ |
| STX 1 = rcp 1698.0 mhz 2 = lcp 1702.5 mhz 3= rcp 1707.0 mhz 4= rcp 2247.5 mhz | 2-Omni HRPT 2 Omni=rcp Power TOAR 446 4-Playback 1,2,3-Degraded | 2 – HRPT 1– Playback 4 Restored -11 Oct 2007 3 low power INOP -10 Aug 2007 | 3 – HRPT TOAR424 low power 2 & 1 Playback STX-1 Power drop STX-4 no modulation | 1 - HRPT 3 - Playback 2-Playback 4-Test & Standby |
| POWER (Array offset and CANT angle, eclipse states and sun angle) | Array Off -45 Since 1/25/01 Full Sun Sun Angle 13 Uptrend to 18 early Jan 07 SA CANT=37 degs | Array Off -20 Since 9/13/07 Eclipse all year Sun Angle 34 Steady trend SA CANT=22 degs Full sun S/C in Sept 07 BVR Phase Control auton swap 7/19/07 | Array Off. –40 Since 1/29/04 Eclipse all year Sun Angle at 66 Steady trend SA CANT=37 degs BVR Phase Control auton swap 9/17/07 Swap back 9/18/07 | Array Off. -40 Since 6/6/05 Eclipse all year Sun Angle 63 uptrend to 65 on 1 Jan 07 Batts 1-3=LRC BVR Phase Control auton swap 3/29/06 & 1/4/07 |
| AVHRR | Nominal Channel 3B only Occasional minor scan motor instabilities | Nominal Recent SM current increases TCE24 OFF 4/14/04 Channel 3B only | Nominal 3A-B switch enabled Previous scan motor current mini surges | Nominal Channel 3B only Scan motor current drop 29 Aug 06 |
| AMSU-A1 | Operational Ch14 inoperative Ch11 inoperative | Operational Primary PLLO chans 9-14 bias shift. Backup PLLO inop. Channel 9-14 noise | OFF/INOP Since 10/30/03 Survival heat on. | Nominal Full Scan mode |
| `AMSU-A2 | Nominal | Nominal | Nominal | Nominal |
| AMSU-B | Operational Bias in All Chans. Degraded Chan-3 | Operational Space Position-3 Chan-8 degradation | Nominal | Replaced by MHS |
| HIRS | NOMINAL FW Abrupt return to nominal 7/12/05 After years of minor and major current surges FW mode=Hi Powr | NOMINAL New all time high filter motor current reached 9/17/06. Imagery occasionally exhibits high levels of radiometric noise | NOMINAL 1 Pixel cross-track misalignment. | Operational Filter Heat OFF. LW channel 1-12 noise TOAR 448 Loose LWIR lens. LW imagery erratic. |
| MHS/MIU |  |  |  | Nominal Fly Wheel Motor Current Spiking but not alarming since 27 Dec 06 Entered Motor Spin State on 27 March 07 H4 gain increased 2 Oct 07 H3 gain increased 31Oct 07 |
| DCS RFI investigation | Nominal | Nominal Pseudo message turned on 1/5/06 | Nominal | Nominal DRU’s 1-7 On DRU8 inop/off |
| SARR | Operational A-Side, AGC Mode Intermittent failures for 243MHz A&B | Operational Mode =AA A-side, AGC Mode (B-side in FG mode) 243 MHz = INOP. | Nominal A-side All AGC Mode | Nominal A-Side All AGC Mode Since 15 Aug 05 |
| SARP | Nominal RCVR B/W = 2 | Nominal RCVR B/W = 2 | Nominal | Nominal A-side 23 May05 |
| SEM | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=0 | Nominal E-CDEM-HVPS=6 P-CDEM-HVPS=5 27 Jun 0615:30z | Nominal E-CDEM-HVPS=2 P-CDEM-HVPS=4 27 June 06 16:00z | Nominal Elec-CH-HVPS=1 27 June 06 17:00z Prot-CH-HVPS=0 |
| SBUV |  | Operational Degraded Ozone data Backup Diffuser inop Primary Diffuser deployment problem TOAR 426 AMSU EMI causing erratic Behavior in PMT cathod, range 3 | Nominal Anode Mode Plan sweep mode Standard Ops TOAR 463 sun glint IBSL test performed 12 Sept 06 Grating motor investigation | Nominal Anode mode since 6 July 05 13:30z Electronics turnoff taken out of STESM safestate table TOAR 462 sun glint |
| SADPOS |  | ON Enabled MFactor50% Timer = 12 mins | ON ENABLED Timer = 12mins | ON Enabled Timer =12 mins |
| THERMAL Heaters, louvers TCE’s | TCE26 & 15H Telem valid TOAR 432 closed TCE24L&25L (HIRS & AVHRR) failed 5/13/98 RCE thermostat failed 5/13/98 Spacecraft in thermal uptrend | Nominal TCE24 OFF 4/14/05 (AVHRR H&L) HIRS Filter heater turned OFF 1/18/05 | TCE3H Batt 2A heater failed ON, turned off 8/26/03 AMSU-A1 survival heaters on 10/29/03 | All TCE’s active HIRS filter heater turned OFF 9/28/06 |

COMMENTS/CHANGES:

MISC:	SIMPACT Board on the DEV Rail is now operational. More testing of the OPS Rail SIMPACT boards are TBD.

NOAA-15:	There were relatively no changes to the NOAA-15 payload health situation during the past week.

No significant change in the IMU performance. Yaw gyro is as quiet as it has been in four months.

NOAA-16: 	There was relatively no change in the performance of the NOAA-16 payload or bus subsystems during the past week.

NOAA-17: 	There was relatively no change in the performance of the NOAA-17 payload or bus subsystems during the past week.

NOAA-18:	There were relatively no changes to the NOAA-18 health situation during the past week.

After the quick 6 degree rise in temperature at the end of September of the N18 AMSU-A2 DC Converter; the component temperature has been trending on track with the curves of the past two years. It should reach a local maximum of approximately 310.5 K at the end of December (over 10 degrees below the recommended maximum limit of this component).  Figure 2 shows the long term trend of this point. No other component of the instrument shows any sign of problems related to this as of yet unexplained change in component performance. A TOAR has been submitted.

The "popcorn" noise that appeared last week on 14-15 Nov 2007 (2007/318-319) on the N18 AMSU-A1 has not manifested itself since the final small occurrence observed on 16 Nov 2007 (2007/320). Figure 3 highlights the largest magnitudes and durations of noisy data observed on 14-15 Nov 2007 (2007/318-319).  A TOAR has been submitted. Two software patches were loaded to NOAA-18 on 20 Nov 2007.  Forced GYE won’t use pitch data if it is available and SCPs will not update MIMU ID form telemetry if L7 interrupts are disabled.

MetOp-A:      Trend Observations (NOAA Instruments)

·         The A-DCS, SARR, SARP and SEM temperatures all dropped on 18 Nov 2007 as IASI experienced another SEU/SET anomaly that triggered an autonomous transition to STANDBY/REFUSE at 01:31 UTC.  The SEM DPU saw the largest temperature drop of approximately 5 deg C (the other instruments saw a drop of 0.5 – 1.0 deg C).  The temperatures are not fully recovered yet, as IASI is still only in HEATER2 mode.

·         The AVHRR and HIRS cooler efficiencies (i.e. Patch Power) and science data have not been affected by the IASI anomaly or the recovery procedures to date.  It is important to note, however, that the HEATER2 mode is not the same mode that is used for IASI Decontamination (HEATER1 mode).

·         All other housekeeping telemetry and science data were stable during this reporting period.  All performance data is well within specification (NEDT, NEDN).

·         HIRS Filter Wheel re-sync period continued its slight increasing trend, averaging about 97 seconds this week.  This correlates with the SVM CCU oscillator temperature, which is also still showing a slight increasing trend.

Anomalies

·         AR8360, “HIRS Scan Mirror Temperature Out-of-Limits”:  Two recurrences of this anomaly were observed on Wednesday, 14 Nov 2007.   ITT is investigating this and has developed a fault tree for identifying a likely cause.  Currently waiting on EUMETSAT PA to call the next ARB.

·       AR8154, “HRPT SSPA Failure”:  No change in status.  SSST states that the most likely cause is due to a failed CLY38 transistor, failing in short-circuit on one of the two parallel output stages.  An MSG-based design change is expected for MetOp-B and C, but the final report and recommendation from SSST is still outstanding (due by Dec/Jan timeframe).

·         AR8310, “HIRS Filter Wheel Resynch Rate”:  No change in status.  Originally submitted on August 8 in response to an SIOV action item.  This AR is intended to get confirmation from Astrium that the more frequent FW resynchs observed now in orbit compared to the rate observed during ground testing can be attributed to temperature effects on the 1 Hz and 1.248 MHz oscillators.

·         AR8877, “PMC Time Stamp Wrap Around Anomaly”:   The PMC wrap around occurred on Sunday, Nov. 11, and affected the files produced by the CAL/VAL facility in the so called NOAA EGSE FORMAT. A certain number of files for day 316 (SEM, AMSU, HIRS, AVHRR files) have packets with incorrect time stamps (UTC plus UNIX time in the header).

·         AR8903, “IASI Autonomous Transition to STANDBY/REFUSE”:  IASI had another autonomous transition to STANDBY/REFUSE this past week (Sunday, 18 Nov 2007 @ 01:31 UTC), apparently due to another SEU/SET.  The anomaly occurred over the SAA.

Operations Performed

·         EUMETSAT and CNES have worked the recovery of IASI from STANDBY/REFUSE.  As of Wednesday, 21 Nov 2007, the instrument was still in HEATER2 mode awaiting the CBS 3rd stage stabilization before proceeding to the next step in returning to nominal operations.

·         The SEM IFCs were run on their regular schedule.  On Tuesday, 20 Nov 2007 the TED IFC started at 09:20:46 UTC and the MEPED IFC started at 09:22:06 UTC.

Operations Planned

·         SEM IFCs are planned for 27 Nov 2007.

NOTES: Figure 1 has been omitted for web listing

Figure 2 NOAA-18 AMSU-A2 (2005/070-2007/330)

Figure 3 NOAA-18 AMSU-A1 (2007/317-320)