APPENDIX D-7

Aggregate Lead and Copper 90th Percentile Data

This Page is intentionally left blank

D-7.	Aggregate Lead and Copper 90th Percentile Data (Section 3.6.8)

Check-Point Restart Issues: This process will be driven by changes to the SSMPA table triggered by New or Changed Lead (1030) and Copper (1022) SARs.

Calculate Aggregates for New or Changed Lead (1030) and Copper (1022) Copper SARs.

The driver for this subprocess is the SSMPA table.

The record key for this subprocess is the composite of CDS trigger timestamp and the TMNSASCH_IS_NUMBER and TMNMPRD_IS_NUMBER columns.

The sort order for this subprocess will be CDS trigger timestamp ascending and  TMNMPRD_IS_NUMBER ascending.

Use these detailed specifications to determine whether and how to calculate lead 90th percentile values for those Sample Schedule Monitoring Period Assignments that are related to Lead Tap Water Sample Schedules.

1.  	Create a log in the CDS Execution Log indicating the process start time.

2. 	Read each SSMPA where

  - its CDS trigger timestamp is greater than the last run date & time for the CDS Setup process (note that the CDS trigger timestamp for an SSMPA record gets updated when a new result is added or an existing result is modified) AND

  - SSMPA is associated to a Sample Schedule where:

    - the Analyte Code referenced by the referenced Monitoring Requirement is equal to “1030" AND

    - the Sample Type Code for the referenced Monitoring Requirement's Violation Type is not equal to 03 or 56 or that the Monitoring Requirement does not reference a Violation Type and

- For each unique SSMPA identified,

Determine whether a lead 90th percentile sample summary already exists for the same water system facility and monitoring period as referenced by the SSMPA.

If one is found,

If USERID <> CDSSETUP (it is user-entered), do not calculate 90th percentile values ( go on to next SSMPA.

Else modify existing lead 90th percentile sample summary.

If one is not found, then create lead 90th percentile sample summary.

(Developer Note: The detailed logic follows.)

  - Select WSF where it belongs to the Sample Schedule referenced in the current SSMPA.  Select Monitoring Period referenced in the current SSMPA.  If Sample Summary exists where:

    - Water System Facility referenced by the Sample Summary is equal to selected Water System Facility [JSB/KF/SRP on 10/3/01] AND

    - Monitoring Period referenced by the Sample Summary is equal to selected Monitoring Period AND

    - The Code for the Analyte referenced by the Sample Summary is equal to “PB90” AND

    - The TYPE_CODE for the Sample Summary Result referenced by the Sample Summary is equal to “90.”

When found

If Sample Summary User ID is NOT equal to CDSSETUP,

Then skip SSMPA and go to next SSMPA.

Else go to the “Lead 90th Percentile Values Routine to modify.”

When not found, go to the “Lead 90th Percentile Values Routine to add.”

Lead 90th Percentile Values Routine

- Read and temporarily store each result where:

  - result references the current SSMPA AND

  - analyte code referenced by the result is equal to 1030 (lead).

- Count the number of results and store as 90_Count (this will be the value for sample_summary_result count_qty).

- Determine the earliest Collection_End_Date of Samples for SARs and store it as Collection_Begin_Date for the Summary (this will be the value for sample_summary sample_collection_start_date).

- Determine the latest Collection_End_Date of Samples for SARs and store it as Collection_End_Date for the Sample Summary (this will be the value for sample_summary sample_collection_end_date).

- If all results analyzed by same Lab, store Lab IS Number as Lab_IS_Number and Lab_ST_Code as Lab_St_Code.

- Convert all results to milligrams per liter:

  - If UOM is UG/L(divide concentration by 1,000.

  - If UOM is NG/L(divide by 1,000,000.

  - If UOM is MG/L(leave as is.

  - If UOM is null and Less_Than_IND is equal to Y, no conversion needed, treat result as a zero.

  - If UOM is any other, the process will create an advisory referencing Message Number 15 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility State Asgn ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analyte code.

  - Sort order the results (concentration) from least to greatest and sequentially number the sorted results starting with the lowest results (maximum 500).

  - Multiply the total number of lead results (90_Count) times 0.9 and store product (called 90th_Sample here).

  - If 90th_Sample is an integer, locate numbered result that is equal to 90th_Sample and store it as the lead 90th percentile value (90_Value).

  - If 90th_Sample is not an integer, store result of sample that is same as integer portion of 90th_Sample as 90_Lower and store result of sample that is 1+ the integer portion of 90th_Sample and call it 90_Upper; then calculate the difference between the two results (90_Upper minus 90_Lower); then multiply the difference times the decimal portion of 90th_Sample; then add this sum to 90_Lower and save as 90_Value.  Round 90_Value to the same number of significant digits as the Lead Action Level. (A.D-7.a)

- The matrix below contains the values that will be used to either modify an existing Lead 90th Percentile Summary or to create a new one.

- To Modify ( only values for fields in italics will be modified

- To Add - all values in matrix will be used

| Source of Data or Value | Destination |
| --- | --- |
|  | Entity | Attribute |
| Set to “Y” | SAMPLE_SUMMARY | COMPL_PURP_IND_CD |
| Set to “CDSSETUP” | SAMPLE_SUMMARY | D_USERID_CODE |
| IS_Number for TSAANLYT whose Code = PB90 | SAMPLE_SUMMARY | TSAANLYT_IS_NUMBER |
| ST_Code for TSAANLYT whose Code = PB90 | SAMPLE_SUMMARY | TSAANLYT_ST_CODE |
| Monitoring Period being evaluated | SAMPLE_SUMMARY | TMNMPRD_IS_NUMBER |
| Monitoring Period being evaluated | SAMPLE_SUMMARY | TMNMPRD_ST_CODE |
| Water System being evaluated | SAMPLE_SUMMARY | TINWSYS_IS_NUMBER |
| Water System being evaluated | SAMPLE_SUMMARY | TINWSYS_ST_CODE |
| Water System Facility being evaluated | SAMPLE_SUMMARY | TINWSF_IS_NUMBER |
| Water System Facility being evaluated | SAMPLE_SUMMARY | TINWSF_ST_CODE |
| Collection_Begin_Date variable | SAMPLE_SUMMARY | COLLECTION_STRT_DT |
| Collection_End_Date variable | SAMPLE_SUMMARY | COLLECTION_END_DT |
| Current date and time | SAMPLE_SUMMARY | D_LAST_UPDT_TS |
| Lab_IS_Number variable | SAMPLE_SUMMARY | TSALAB_IS_NUMBER |
| Lab_ST_Code variable | SAMPLE_SUMMARY | TSALAB_ST_CODE |
| To reference record created in SAMPLE_SUMMARY | SAMPLE_SUMMARY_RESULT | TSASMPSM_IS_NUMBER |
| To reference record created in SAMPLE_SUMMARY | SAMPLE_SUMMARY_RESULT | TSASMPSM_ST_CODE |
| Set to IS_Number of SSMPA to which current summary is associated | SAMPLE_SUMMARY | SSMPA_SASCH_IS_NO SSMPA_MPRD_IS_NO |
| Set to ST_Code of SSMPA to which current summary is associated | SAMPLE_SUMMARY | SSMPA_SASCH_ST_CO SSMPA_MPRD_ST_CO |
| Set to “90" | SAMPLE_SUMMARY_RESULT | TYPE_CODE |
| Set to “CDSSETUP” | SAMPLE_SUMMARY_RESULT | D_USERID_CD |
| Set to “A” | SAMPLE_SUMMARY_RESULT | DATA_QUALITY_CODE |
| Set to “MG/L” | SAMPLE_SUMMARY_RESULT | UOM_CODE |
| 90_Count variable | SAMPLE_SUMMARY_RESULT | COUNT_QTY |
| 90_Value variable | SAMPLE_SUMMARY_RESULT | MEASURE |
| Current date and time | SAMPLE_SUMMARY_RESULT | D_LAST_UPDT_TS |

End of (Lead 90th Percentile Values Routine(

B. Use these detailed specifications to determine whether and how to calculate copper 90th percentile values for those Sample Schedule Monitoring Period Assignments that are related to Copper Tap Water Sample Schedules.

- Read each Sample SSMPA where:

  - its CDS trigger timestamp is greater than the last run date & time for the CDS Setup process (note that the CDS trigger timestamp for an SSMPA record gets updated when a new result is added or an existing result is modified) AND

  - SSMPA is associated to a Sample Schedule where:

    - the Analyte Code referenced by the referenced Monitoring Requirement is equal to “1022" AND

    - the Sample Type Code for the referenced Monitoring Requirement's Violation Type is not equal to 03 or 56 or that the Monitoring Requirement does not reference a Violation Type.

- For each unique Sample Schedule Monitoring Period Assignment record identified,

Determine whether a copper 90th percentile sample summary already exists for the same water system facility and monitoring period as referenced by the SSMPA.

If one is found,

If USERID <> CDSSETUP (it is user-entered) do not calculate 90th percentile values ( go on to the next SSMPA.

Else modify existing copper 90th percentile sample summary.

If one is not found, then create copper 90th percentile sample summary.

(Developer Note: The detailed logic follows.)

  - Select WSF where it belongs to the Sample Schedule referenced in the current SSMPA.  Select Monitoring Period referenced in the current SSMPA.  If Sample Summary exists where:

Water System Facility referenced by the Sample Summary is equal to selected Water System Facility AND

Monitoring Period referenced by the Sample Summary is equal to selected Monitoring Period AND

The Code for the Analyte referenced by the Sample Summary is equal to (CU90" AND

The TYPE_CODE for the Sample Summary Result referenced by the Sample Summary is equal to “90.”

When found

If Sample Summary User ID is NOT equal to CDSSETUP,

Then skip SSMPA and go to next SSMPA.

Else go to the “Copper 90th Percentile Values Routine to modify”

When not found, go to the “Copper 90th Percentile Values Routine to add”

Copper 90th Percentile Values Routine

- Read and temporarily store each result where:

  - result references the current SSMPA AND

  - analyte code referenced by the result is equal to 1022 (copper).

- Count the number of results and store as 90_Count (this will be the value for sample_summary_result count_qty).

- Determine the earliest Collection_End_Date of Samples for SARs and store it as Collection_Begin_Date for the Summary (this will be the value for sample_summary sample_collection_start_date).

- Determine the latest Collection_End_Date of Samples for SARs and store it as Collection_End_Date for the Sample Summary (this will be the value for sample_summary sample_collection_end_date).

- If all results analyzed by same Lab, store Lab IS Number as Lab_IS_Number and Lab_ST_Code as Lab_St_Code.

- Convert all results to milligrams per liter:

If UOM is UG/L(divide concentration by 1,000.

If UOM is NG/L(divide by 1,000,000.

If UOM is MG/L(leave as is.

If UOM is spaces and Sample Result Less Than Indicator is Y(leave as is.

If UOM is any other, the process will create an advisory referencing Message Number 16 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility State Asgn ID and name; the Sampling Point ID and description; the sample(s lab sample number and collection date; and the result(s analyte code.

Sort order the results (concentration) from least to greatest and sequentially number the sorted results starting with the lowest results (maximum 500).

Multiply the total number of copper results (90_Count) times 0.9 and store product (called (90th_Sample( here).

If 90th_Sample is an integer, locate numbered result that is equal to 90th_Sample and store it as the copper 90th percentile value (90_Value).

If 90th_Sample is not an integer, store result of sample that is same as integer portion of 90th_Sample as 90_Lower and store result of sample that is 1+ the integer portion of 90th_Sample and call it 90_Upper, then calculate the difference between the two results (90_Upper minus 90_Lower), then multiply the difference times the decimal portion of 90th_Sample; then add this sum to 90_Lower and save as 90_Value.  Round 90_Value to the same number of significant digits as the Copper Action Level. (A.D-7.b)

The matrix below contains the values that will be used to either modify an existing Copper 90th Percentile Summary or to create a new one.

- To Modify ( only values for fields in italics will be modified

- To Add - all values in matrix will be used

| Source of Data or Value | Destination |
| --- | --- |
|  | Entity | Attribute |
| Set to “Y” | SAMPLE_SUMMARY | COMPL_PURP_IND_CD |
| Set to “CDSSETUP” | SAMPLE_SUMMARY | D_USERID_CODE |
| IS_Number for CU90 | SAMPLE_SUMMARY | TSAANLYT_IS_NUMBER |
| ST_Code for CU90 | SAMPLE_SUMMARY | TSAANLYT_ST_CODE |
| Monitoring Period being evaluated | SAMPLE_SUMMARY | TMNMPRD_IS_NUMBER |
| Monitoring Period being evaluated | SAMPLE_SUMMARY | TMNMPRD_ST_CODE |
| Water System being evaluated | SAMPLE_SUMMARY | TINWSYS_IS_NUMBER |
| Water System being evaluated | SAMPLE_SUMMARY | TINWSYS_ST_CODE |
| Water System Facility being evaluated | SAMPLE_SUMMARY | TINWSF_IS_NUMBER |
| Water System Facility being evaluated | SAMPLE_SUMMARY | TINWSF_ST_CODE |
| Current date and time | SAMPLE_SUMMARY | D_LAST_UPDT_TS |
| Collection_Begin_Date variable | SAMPLE_SUMMARY | COLLECTION_STRT_DT |
| Collection_End_Date variable | SAMPLE_SUMMARY | COLLECTION_END_DT |
| Lab_IS_Number variable | SAMPLE_SUMMARY | TSALAB_IS_NUMBER |
| Lab_ST_Code variable | SAMPLE_SUMMARY | TSALAB_ST_CODE |
| Set to “90" | SAMPLE_SUMMARY_RESULT | TYPE_CODE |
| 90_Count variable | SAMPLE_SUMMARY_RESULT | COUNT_QTY |
| 90_Value variable | SAMPLE_SUMMARY_RESULT | MEASURE |
| Set to “MG/L” | SAMPLE_SUMMARY_RESULT | UOM_CODE |
| Set to ST_Code of SSMPA to which current summary is associated | SAMPLE_SUMMARY | SSMPA_SASCH_ST_CO SSMPA_MPRD_ST_CO |
| Set to (CDSSETUP( | SAMPLE_SUMMARY_RESULT | D_USERID_CD |
| To reference record created in SAMPLE_SUMMARY | SAMPLE_SUMMARY_RESULT | TSASMPSM_IS_NUMBER |
| To reference record created in SAMPLE_SUMMARY | SAMPLE_SUMMARY_RESULT | TSASMPSM_ST_CODE |
| Set to “A” | SAMPLE_SUMMARY_RESULT | DATA_QUALITY_CODE |
| Set to IS_Number of SSMPA to which current summary is associated | SAMPLE_SUMMARY | SSMPA_SASCH_IS_NO SSMPA_MPRD_IS_NO |
| Current date and time | SAMPLE_SUMMARY_RESULT | D_LAST_UPDT_TS |
| 90_Count variable | SAMPLE_SUMMARY_RESULT | COUNT_QTY |
| 90_Value variable | SAMPLE_SUMMARY_RESULT | MEASURE |

End of (Copper 90th Percentile Values Routine(