MSFC Problem Reporting and Corrective Action (PRACA) System

WHOLE RECORD REPORT( + ADDENDUM)

| MSFC Record # A08476 | In-Flight Anomaly Number -- | Contractor Report Number E-083 | JSC# -- | KSC# -- |
| --- | --- | --- | --- | --- |
| Problem Title TEMP MEASUREMENT WAS HIGH |
| EICN# -- | ELEMENT ET | Contractor MMMSS | FSCM# -- | FCRIT 3 |
| HCRIT -- | Sys_Lvl N | Misc Codes A (4) B C D E F G H I J K L M N O |
| HARDWARE EIM | NOMENCLATURE EXTERNAL TANK | PART# 82601000000 | SER/LOT# LWT-6 | MANUFACTURER MMC |
| HARDWARE LRU | NOMENCLATURE N/A | PART# N/A | SER/LOT# N/A | MANUFACTURER N/A |
| HARDWARE NCA | NOMENCLATURE TEMPERATURE SENSOR | PART# PD7400095-149 | SER/LOT# 1022 | MANUFACTURER HYCAL |
| Test/Operation F - FLT | Prevailing Condtion F - FUNCTIONAL | F / U F | Fail Mode EN - OPEN | Cause U - UNKNOWN |
| System ELECTRICAL | Defect DC - BROKEN | Material T - S-STRT | Work Contact D. WESTPHAL | Fail Date 07/09/1984 |
| Received at MSFC 08/01/1984 | Date Isolated -- | FMEA Reference 3.3 | IFA: Mission Phase -- | Mission Elapsed Time -- |
| Location KSC | Symptom ET - MEAS ANOMALY | Time Cycle -- |
| Effectivity Text NONE |
| Vehicle Effectivity Codes |
| Vehicle 1 -- | Vehicle 2 -- | Vehicle 3 -- | Vehicle 4 -- | Vehicle 5 -- |
| Mission Effectivity Codes |
| Mssn 1 -- | Mssn 2 -- | Mssn 3 -- | Mssn 4 -- | Mssn 5 -- |
| Estimated Completion Dates |
| MSFC Approved Defer Until Date -- | Contractor Req Defer Until Date -- | LVL 3 Close -- | Remark / Action -- |
| Investigation / Resolution Summary |
| Last MSFC Update 01/03/1992 | CN RSLV SBMT 07/25/1985 | Defer Date -- | Add Date -- | R/C Codes 0 - EXPL -- -- |
| Assignee |
| Design W. COBB | Chief Engineer -- | S & MA D. NEWMAN | Project J. BREWER | Project MGR -- |
| Approval |
| Design W. COBB | Chief Engineer -- | S & MA D. NEWMAN | Project J. BREWER | Project MGR -- |
| PAC Assignee G. MILLER | PAC Review Complete GM | MSFC Closure Date 08/07/1985 | Status C - CLOSED | F/A Completion -- |
| Problem Type -- | SEV -- | Program Name -- | REVL -- | OPRINC -- |
| FUNC MOD -- | Software Effectivity -- -- -- -- -- | Software Fail CD -- | SUBTYPE -- | Software Closure CD -- |
| RES PERSON L2 -- | Approval Signature L3 -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Related Document Type -- | Related Document ID -- |
| Related Document Title -- |
| Contractor Status Summary |
| Reliability/Quality Assurance Concerns, Recommendations: |
| Problem Description REF: BOTH NOSE CONE PURGE TEMP MSRMNTS FAILED HIGH DURING THE 1ST LAUNCH ATTEMPT OF STS-41D (LWT-6) WHILE IN STABLE REPLENISH MODE. TEMP SENSORS, 327A9 & 327A10, WERE LATER DETERMINED TO BE OPEN CIRCUITED WHEN TESTED FROM THE GSE SIGNAL CONDITIONER CONNECTOR |
| Contractor Investigation/Resolution CAUSE - UNDER INVESTIGATION. 3/6/85 STATUSED AT PRB MTG 2-25-85 AS FOLLOWS - AWAITING FRF OR TANKING TEST TO GET MORE ACCURATE ACOUSTICAL DATA TO PERFORM ANALYSIS. 3/13/85 ET CLEARANCES - NO CONSTRAINTS TRANSDUCERS USED ONLY FOR GROUND OPERATIONS. NOSE CONE PURGE CAN BE CONTROLLED USING HEATER OUTLET TEMPS AS PREVIOUSLY DONE ON STS-9 & 41D LAUNCH ATTEMPTS.6/3/85 - INVESTIGATION A. THE NOSE CONE TEMPERATURE SENSORS ON LWT-6 WERE INSPECTED USING A FIBER-OPTIC BOROSCOPE INSERTED THROUGH THE NOSE CONE AERO VENT. THE SENSORS ARE POSITIONED SUCH THAT ONLY THE 327A10 SENSOR COULD BE SEEN. THE CERAMIC TIP OF THE SENSOR WAS FOUND TO BE FRACTURED IN TWO PLACES. A VIDEO- TAPE OF THE SENSOR WAS MADE USING THE BOROSCOPE. B. A REVIEW OF PREVIOUS LAUNCH DATA FOUND THAT A SIMILAR FAILURE OF BOTH NOSE CONE TEMPERATURE SENSORS OCCURRED ON LWT-4. EFFECTIVE WITH LWT-4 AND SUBSEQUENT, THE NOSE CONE NITROGEN PURGE RATE WAS INCREASED FROM 11 POUNDS PER MINUTE TO 14 POUNDS PER MINUTE. NO INSPECTION OF THE SENSORS ON LWT-4 WAS POSSIBLE AS THE FAILURE OCCURRED DURING THE LOADING OF THE TANK PRIOR TO A SUCCESSFUL LAUNCH ATTEMPT. C. IN ORDER TO ATTEMPT TO DUPLICATE THE TEMPERATURE SENSOR FAILURE SEEN ON LWT-6, A TEST WAS PER- FORMED AT WYLE LABORATORIES IN HUNTSVILLE, ALABAMA. ELECTRICAL ENGINEERING, DEPARTMENT 3513, AND DYNAMICS AND LOAD, DEPARTMENT 3524, DEVELOPED AN ACOUSTIC ENVIRONMENT SIMULATION THAT GENERATED IN THE NOSE CONE DURING THE PROPELLANT LOADING CYCLE ON THE LAUNCH PAD. THE TRANS- DUCERS FUNCTIONED PROPERLY THROUGHOUT THE TEST. D. TANK MPTA HAS BEEN INSTRUMENTED TO RECORD THE ACOUSTIC AND VIBRATION ENVIRONMENT IN THE NOSE CONE. DURING THE TANKING FOR THE PLANNED CLUSTER FIRING TO CERTIFY THE SHUTTLE MAIN ENGINES FOR 109 PERCENT, THE PREDICTED NOSE CONE ENVIRONMENT WILL BE VERIFIED. THIS WILL INCLUDE ALL PRELAUNCH CONDITIONS. 6/6/85 PRB STATUS 4-16-85 MTG - AWAITING FRF OR TANKING TEST TO GET MORE ACCURATE ACOUSTICAL DATA TO PERFORM ANALYSIS. NO ADDITIONAL DATA AVAILABLE AT THIS TIME. ECD IS NOW THE END OF JUNE 1985. 6/6/85 PRB STATUS 5-16-85 MTG - AWAITING MPT AT NSTL TO GET DATA TO VERIFY ACOUSTICAL ENVIRONMENT. 7/2/85 STATUSED AT PRB MTG 6-20-85 AS FOLLOWS - MR. H. JACOB/MMC IS TO PREPARE PRESENTATION TO EXPLAIN THE CAUSES OF THE OPEN CIRCUITS IN TEMP TRANSDUCERS & PLAN OF ACTION FOR R/C. HE EXPECTS TO PRESENT THIS INFO TO MR. NICHOLS/MSFC UPON HIS VISIT TO MMC 6-21-85. ALSO NO ENG TEST IS SCHEDULED TO GET ACOUSTICAL DATA MMC PROPOSES CLOSING THIS CAPS SINCE TRANSDUCER PASSED THE WYLE LAB TESTS. ALSO HAVE A WORKAROUND. MSFC CONCURS WITH CLOSING THIS CAPS WILL STILL NEED CHECK AT NEXT TANK TEST AT NSTL. 7/25/85 RESOLUTION - NO C/A IS POSSIBLE AT THIS TIME. THE TRANSDUCERS HAVE BEEN SHOWN TO BE ABLE TO WITHSTAND THE NOSE CONE ENVIRONMENT DURING TESTS AT WYLE LABS THE FAILED HARDWARE ON LWT-6 WAS NOT REMOVED PRIOR TO FLT &, THEREFORE, COULD NOT BE ANALYZED. TANK MPTA HAS BEEN INSTRUMENTED TO ENABLE THE NOSE CONE ENVIRONMENT TO BE MEASURED DURING THE NEXT TANKING FOR AN ENG TEST RUN AT NSTL. SHOULD THE MEASURED ENVIRONMENT BE FOUND TO BE MORE SEVERE THAN THE CURRENT DESIGN VIBRATION DATA, AN ENGR'G CHANGE PROPOSAL (ECP) WILL BE GENERATED TO EFFECT THE NECESSARY DESIGN CHANGES. NO FURTHER RCA CAN BE ACCOMPLISHED AT THIS TIME. RECOMMEND THAT THIS PROBLEM REPORT BE CLOSED |
| MSFC Response/Concurrence |

MSFC Problem Reporting and Corrective Action (PRACA) System

ASSESSMENT ADDENDUM REPORT

| MSFC Report# A08476 | IFA# -- | Contractor RPT# E-083 | JSC# -- | KSC# -- | EICN# -- |
| --- | --- | --- | --- | --- | --- |
| Asmnt Part# PD7400095-149 | Asmnt Part Name TEMPERATURE SENSOR | Asmnt Serial/Lot# 1022 |
| HCRIT CD -- | FCRIT CD 3 | CAUSE CD U - UNKNOWN | FAIL MODE EN - OPEN |
| Asmnt FMEA 3.9.10.1 | Asmnt FM 1 | FMEA CSE A | FMEA SCSE 2 |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Asmnt FMEA -- | Asmnt FM -- | FMEA CSE -- | FMEA SCSE -- |
| Correlated Part# -- | Correlated Part# -- | Correlated Part# -- |
| Associated LRU# -- | Associated LRU# -- | Associated LRU# -- |
| MAJOR DESIGN CHANGES |
| APRV DATE -- | DESCRIPTION OF CHANGES -- |
| ASSESSMENT TEXT |