PDM4 MODELING OF DIDECYL DIMETHYL AMMONIUM CHLORIDE (DDAC) IN ONCE-THROUGH

INDUSTRIAL WATER SYSTEMS

David C. Bays, Microbiologist

Kathryn V. Montague, Biologist

Rick Petrie, Team Leader

Risk Assessment and Science Support Branch

Antimicrobials Division

Office of Pesticide Programs

U.S. EPA

INTRODUCTION

This document provides estimated environmental concentrations (EECs) in the receiving body of water from the use of didecyl dimethyl ammonium chloride (DDAC) in industrial cooling water systems.  DDAC has been shown to be hydrolytically stable under abiotic and buffered conditions.  Metabolic transformation is unlikely to occur; therefore, degradation products of DDAC are not expected.  The Probabilistic Distribution Model version 4 (PDM4) was used to evaluate the DDAC concentration in stream water resulting from the use of DDAC products in once-through cooling water systems.  An average sized plant was modeled as being located on small, average, and large rivers.  The chances of exceedance on any given day were determined, as well as percent chances of exceedance over extended durations.

Overview of PDM4

PDM4 calculates downstream chemical concentrations from a chemical discharge using the probabilistic distribution model.  The algorithm used is taken from DiToro (1984).  A simple mass balance approach forms the basis of PDM.  However, the input variables are not single point estimates, because, in reality, these variables are not constant.  Streams follow a highly variable seasonal flow pattern and numerous variables in a manufacturing process can affect the chemical concentration and flow rate of the effluent. PDM4 models the stream flow as constantly changing and calculates the probability that the concentration in a given target stream will exceed some target value. Specifically, it calculates the percent of days per year that the concentration of concern is exceeded.  PDM4 uses probability distributions as inputs and calculates the resulting probability distribution of the concentration in the stream.

ONCE-THROUGH COOLING WATER

Inputs

Application Rate

The dose rates for DDAC from product labels ranged from 32 to 63 ppm a.i. (i.e., 1 part DDAC per million parts of water flowing through the system) for continuous feed and from 1000 to1800 ppm a.i. for intermittent treatment.  For this assessment, four rates were modeled: 32 ppm a.i. (low dose – continuous feed), 63 ppm a.i. (high dose – continuous feed), 1000 ppm a.i. (low dose – intermittent treatment) and 1800 ppm a.i. (high dose – intermittent treatment).

Power Plant Information

In modeling the fate of DDAC in the receiving body of water, it was assumed that the 7Q10 flow rate (a flow rate that, once every ten years, a stream is expected to be below for seven consecutive days) was assumed to be the normal cooling water flow rate.  This value was chosen because it is assumed that electric plants would need to have a steady supply of cooling water, and the 7Q10 flow reflects a rate that could be maintained continuously by the power plant.  This is not a conservative assumption, since electric plants may use more cooling water under normal conditions, though at a greater risk of running out of usable water.  For lack of better data, however, these values were used.

PDM4 Model Inputs

A summary of the input parameters is described below.

- Release Days - It has been assumed that the product is released 365 days per year.

- Pretreatment Release – The following equations were used to calculate the loading (kg/site/day):

Continuous Feed Scenario-Calculation for Loading (kg/site/day):

System Flow (MLD) * 106 (Conversion factor for million liters/day to liters/day) 	(Equation #1)

* 1 (kg water/liter of water) * dose rate (kg/kg)

where,

Dose rate (kg of chemical/ kg of water) = dose rate (ppm) * 10-6  			(Equation #2)

The cooling system flow rate was assumed to be identical to the 7Q10 flow rate (a flow rate that, once every ten years, a stream is expected to be below for seven consecutive days).

Intermittent Feed Scenario-Calculation for Loading (kg/site/day): As no information was provided regarding the application time associated with intermittent treatment, it was assumed that one application is made per day for 15 minutes:

System Flow (MLD) * 106 (Conversion factor for million liters/day to liters/day)  	(Equation #3)

* 1 (kg water/liter of water) * dose rate (kg/kg) * (0.25/24 (hrs/day))

where,

Dose rate (kg of chemical/ kg of water) = dose rate (ppm) * 10-6 			(Equation #4)

- Concentration of Concern - PDM4 is designed to report the number of days that the concentration in the water body exceeds a concentration of concern that has been specified by the user.  For this study, the model was run multiple times using different COCs to determine a curve.  The COCs considered for each flow regime are as follows: 14, 18, 69, 73, 95, 320, 1000 ppb a.i.  These COC values were derived from studies of the sensitivity of various species to DDAC.

The input parameters are summarized in Table 1 below.

| Table 1. PDM4 Model Inputs |
| --- |
| Parameter | Value | Rationale |
| Industry Type | Steam Electric Power Plants (SIC #4911) Various NPDES | EPA assumption as being the representative facility for once-through industrial water systems using DDAC. |
| Release Days | 365 | EPA assumption. |
| Pretreatment Release | Determined for each site using Eq. 1-4 | See discussion regarding Eq. 1-4. |
| Concentration of Concern | 14, 18, 69, 73, 95, 320, 1000 ppb a.i | A range was used to determine a curve. The range is based on the sensitivity of different species to DDAC. |

The three different flow regimes consisted of power plants with stream flow rates of 100 ± 10 MGD (million gallons per day), 500 ± 50 MGD, and 1000 ± 50 MGD.  The low, medium, and high stream flow rates correspond to 378.5 ± 37.85, 1982.5 ± 189.25, and 3785 ± 189.25 million liters per day.  These plants were pulled from a database of NPDES plant codes based on the above criterion.  Tables 2, 3, and 4 below show details regarding the power plants and their cooling streams.

| Table 2. Low Flow (100 MGD1) Stream Specifications |
| --- |
| NPDES | Mean Stream Flow (MLD2) | Mean7Q103 Stream Flow (MLD) |
| IA0033235 | 401 | 2.84 |
| PA0002062 | 391 | 4.09 |
| LA0003042 | 384 | 44.6 |
| MI0038172 | 379 | 14.0 |
| OK0002682 | 363 | 3.37 |
| WV0005525 | 359 | 14.6 |
| IL0036919 | 356 | 3.89 |
| LA0036145 | 354 | 13.6 |
| UT0000116 | 352 | 32.4 |
| TX0054500 | 352 | 26.8 |
| PA0008443 | 337 | 12.6 |
| IL0048321 | 336 | 97.0 |

1.	MGD = million gallons per day

2.	MLD = million liters per day

3.	Mean 7Q10 = Seven consecutive days of lowest stream flows over a ten year period

| Table 3. Medium Flow (500 MGD1) Stream Specifications |
| --- |
| NPDES | Mean Stream Flow (MLD2) | Mean7Q103 Stream Flow (MLD) |
| MA0004367 | 2,030 | 227 |
| IA0000108 | 1,970 | 61.3 |
| NM0000108 | 1,970 | 5.92 |
| FL0025526 | 1,960 | 653 |
| IN0032948 | 1,950 | 153 |
| TX0001163 | 1,870 | 11.4 |
| OH0010421 | 1,840 | 59.8 |
| IN0041246 | 1,820 | 167 |
| PA0002054 | 1,790 | 115 |
| MN0000906 | 1,750 | 28.9 |
| NH0001431 | 1,730 | 75.7 |
| IN0038806 | 1,720 | 58.2 |

1.	MGD = million gallons per day

2.	MLD = million liters per day

3.	Mean 7Q10 = Seven consecutive days of lowest stream flows over a ten year period

| Table 4. High Flow (1000 MGD1) Stream Specifications |
| --- |
| NPDES | Mean Stream Flow (MLD2) | Mean7Q103 Stream Flow (MLD) |
| GA0004341 | 3,960 | 838 |
| WA0003280 | 3,830 | 592 |
| KS0079057 | 3,760 | 20.4 |
| NC0005088 | 3,690 | 812 |
| SC0001104 | 3,650 | 50.3 |
| IL0002186 | 3,640 | 1,170 |

1.	MGD = million gallons per day

2.	MLD = million liters per day

3.	Mean 7Q10 = Seven consecutive days of lowest stream flows over a ten year period

Twelve different sites throughout the United States were tested in the model from the low and medium stream regimes, and six were tested from the high flow regime.

RESULTS

For each reach, PDM4 calculates the percent of days per year that a reach would have concentrations above a particular COC.  These values were averaged by Versar within each of the three different flow regimes (i.e., low, medium, and high), giving average percentages of exceedance. Versar also looked at the worst-case scenarios for the low, medium, and high stream flows considered.  These calculations were performed for four dose rates: intermittent low- and high-end doses, and the continuous low- and high-end doses.  Versar also calculated the chance of exceeding a particular COC over time periods of 48 hours (2 days) and 96 hours (4 days).  Average results for each of the three flow regimes are presented in Tables 5, 6, and 7.

| Table 5. Average Percent of Days per Year COC Exceeded (Dose = 32 ppm a.i.-Continuous Low-End Dose) |
| --- |
| COC1 (ppb) | LF2 Percent Days COC Exceeded (%) | LF-Standard Deviation (%) | MF3-Percent Days COC Exceeded (%) | MF-Standard Deviation (%) | HF4-Percent Days COC Exceeded (%) | HF-Standard Deviation (%) |
| 14 | 96.4 | 9.59 | 99.4 | 1.34 | 100 | 0.0744 |
| 18 | 94.6 | 13.4 | 99.2 | 1.95 | 99.9 | 0.177 |
| 69 | 80.1 | 32.8 | 94.9 | 10.3 | 95.9 | 7.82 |
| 73 | 79.4 | 33.4 | 94.6 | 10.9 | 95.5 | 8.69 |
| 95 | 76.3 | 35.9 | 92.9 | 14.1 | 93 | 13.4 |
| 320 | 62.7 | 40.4 | 81.2 | 27.1 | 80 | 35.7 |
| 1000 | 47 | 37.7 | 63.3 | 27.9 | 70.6 | 41.6 |

1. COC = Concentration of Concern

2. LF = Low Flow Regime (100 MGD)

3. MF = Medium Flow Regime (500 MGD)

4. HF = High Flow Regime (1000 MGD)

| Table 6. Average Percent of Days per Year COC Exceeded (Dose = 63 ppm a.i.- Continuous High-End Dose) |
| --- |
| COC1 (ppb) | LF2 Percent Days COC Exceeded (%) | LF-Standard Deviation (%) | MF3-Percent Days COC Exceeded (%) | MF-Standard Deviation (%) | HF4-Percent Days COC Exceeded (%) | HF-Standard Deviation (%) |
| 14 | 99.1 | 2.59 | 99.8 | 0.439 | 100 | 0.00802 |
| 18 | 98.4 | 4.53 | 99.7 | 0.671 | 100 | 0.0184 |
| 69 | 88.2 | 24.1 | 97.8 | 4.72 | 99.1 | 1.55 |
| 73 | 87.6 | 25 | 97.6 | 5.05 | 99 | 1.82 |
| 95 | 84.5 | 28.6 | 96.7 | 6.91 | 98.1 | 3.62 |
| 320 | 70.2 | 39.3 | 88.3 | 21.1 | 87 | 24.7 |
| 1000 | 56.9 | 39.9 | 75.2 | 28.5 | 76.2 | 39.4 |

1. COC = Concentration of Concern

2. LF = Low Flow Regime (100 MGD)

3. MF = Medium Flow Regime (500 MGD)

4. HF = High Flow Regime (1000 MGD)

| Table 7. Average Percent of Days per Year COC Exceeded (Dose = 1000 ppm a.i.-Intermittent Low-End Dose) |
| --- |
| COC1 (ppb) | LF2 Percent Days COC Exceeded (%) | LF-Standard Deviation (%) | MF3-Percent Days COC Exceeded (%) | MF-Standard Deviation (%) | HF4-Percent Days COC Exceeded (%) | HF-Standard Deviation (%) |
| 14 | 85.8 | 27.1 | 97.1 | 6.04 | 98.5 | 2.71 |
| 18 | 82.8 | 30.3 | 96.1 | 8.08 | 97.4 | 4.96 |
| 69 | 67.4 | 40.1 | 85.7 | 24 | 84 | 29.8 |
| 73 | 66.7 | 40.2 | 85.1 | 24.5 | 83.4 | 30.8 |
| 95 | 63.8 | 40.5 | 82.3 | 26.6 | 80.8 | 34.7 |
| 320 | 47.2 | 37.7 | 63.7 | 28 | 70.8 | 41.5 |
| 1000 | 28.2 | 29.3 | 37.4 | 24.5 | 54.3 | 37.6 |

1. COC = Concentration of Concern

2. LF = Low Flow Regime (100 MGD)

3. MF = Medium Flow Regime (500 MGD)

4. HF = High Flow Regime (1000 MGD)

| Table 8. Average Percent of Days per Year COC Exceeded (Dose = 1800 ppm a.i.-Intermittent High-End Dose) |
| --- |
| COC1 (ppb) | LF2 Percent Days COC Exceeded (%) | LF-Standard Deviation (%) | MF3-Percent Days COC Exceeded (%) | MF-Standard Deviation (%) | HF4-Percent Days COC Exceeded (%) | HF-Standard Deviation (%) |
| 14 | 92.2 | 18 | 98.7 | 2.89 | 99.7 | 0.469 |
| 18 | 89.6 | 22.1 | 98.2 | 4.01 | 99.4 | 1.05 |
| 69 | 73.8 | 37.5 | 91.2 | 17 | 90.7 | 17.8 |
| 73 | 73.2 | 37.9 | 90.7 | 17.7 | 90.1 | 19 |
| 95 | 70.3 | 39.3 | 88.4 | 21.1 | 87 | 24.6 |
| 320 | 55.9 | 39.8 | 74.1 | 28.6 | 75.7 | 39.8 |
| 1000 | 38.2 | 34.4 | 51.4 | 26.6 | 64.4 | 41.2 |

1. COC = Concentration of Concern

2. LF = Low Flow Regime (100 MGD)

3. MF = Medium Flow Regime (500 MGD)

4. HF = High Flow Regime (1000 MGD)

Tables 9, 10, 11, and 12 list the calculations for those power plants with the highest exceedance rates for each of the three stream flow sizes considered.

| Table 9. Worst Case Scenarios: Percent of Days per Year COC Exceeded (Dose = 32 ppm a.i.-Continuous Low-End Dose) |
| --- |
| COC1 (ppb) | LF2-Percent Days COC Exceeded (%) | MF3-Percent Days COC Exceeded (%) | HF4-Percent Days COC Exceeded (%) |
| 14 | 100 | 100 | 100 |
| 18 | 100 | 100 | 100 |
| 69 | 100 | 100 | 100 |
| 73 | 100 | 100 | 100 |
| 95 | 100 | 100 | 100 |
| 320 | 100 | 100 | 100 |
| 1000 | 98.8 | 99.2 | 99.6 |

1. COC = Concentration of Concern

2. LF = Low Flow Regime (100 MGD)

3. MF = Medium Flow Regime (500 MGD)

4. HF = High Flow Regime (1000 MGD)

| Table 10. Worst Case Scenarios: Percent of Days per Year COC Exceeded (Dose = 63 ppm a.i.- Continuous High-End Dose) |
| --- |
| COC1 (ppb) | LF2-Percent Days COC Exceeded (%) | MF3-Percent Days COC Exceeded (%) | HF4-Percent Days COC Exceeded (%) |
| 14 | 100 | 100 | 100 |
| 18 | 100 | 100 | 100 |
| 69 | 100 | 100 | 100 |
| 73 | 100 | 100 | 100 |
| 95 | 100 | 100 | 100 |
| 320 | 100 | 100 | 100 |
| 1000 | 99.9 | 99.9 | 100 |

1. COC = Concentration of Concern

2. LF = Low Flow Regime (100 MGD)

3. MF = Medium Flow Regime (500 MGD)

4. HF = High Flow Regime (1000 MGD)

| Table 11. Worst Case Scenarios: Percent of Days per Year COC Exceeded (Dose = 1000 ppm a.i.-Intermittent Low-End Dose) |
| --- |
| COC1 (ppb) | LF2-Percent Days COC Exceeded (%) | MF3-Percent Days COC Exceeded (%) | HF4-Percent Days COC Exceeded (%) |
| 14 | 100 | 100 | 100 |
| 18 | 100 | 100 | 100 |
| 69 | 100 | 100 | 100 |
| 73 | 100 | 100 | 100 |
| 95 | 100 | 100 | 100 |
| 320 | 98.8 | 99.2 | 99.6 |
| 1000 | 84.8 | 88.5 | 88.6 |

1. COC = Concentration of Concern

2. LF = Low Flow Regime (100 MGD)

3. MF = Medium Flow Regime (500 MGD)

4. HF = High Flow Regime (1000 MGD)

| Table 12. Worst Case Scenarios: Percent of Days per Year COC Exceeded (Dose = 1800 ppm a.i.-Intermittent High-End Dose) |
| --- |
| COC1 (ppb) | LF2-Percent Days COC Exceeded (%) | MF3-Percent Days COC Exceeded (%) | HF4-Percent Days COC Exceeded (%) |
| 14 | 100 | 100 | 100 |
| 18 | 100 | 100 | 100 |
| 69 | 100 | 100 | 100 |
| 73 | 100 | 100 | 100 |
| 95 | 100 | 100 | 100 |
| 320 | 99.8 | 99.9 | 100 |
| 1000 | 95.2 | 96.7 | 97.5 |

1. COC = Concentration of Concern

2. LF = Low Flow Regime (100 MGD)

3. MF = Medium Flow Regime (500 MGD)

4. HF = High Flow Regime (1000 MGD)

Tables 13, 14, 15, and 16 show the average of all power plants modeled, and compares these values to the average of the three worst-case scenarios that were presented in Tables 9, 10, 11, and 12, respectively.

| Table 13. Total Average Exceedance Rates vs. Worst-Case Exceedance Rates (Dose = 32 ppm a.i.-Continuous Low-End Dose) |
| --- |
| COC1 (ppb) | Percent of Days COC Exceeded (%) |
|  | Total Average | Average of the Three Worst Case Scenarios (Table 9) |
| 14 | 98.3 | 100 |
| 18 | 97.5 | 100 |
| 69 | 89.2 | 100 |
| 73 | 88.7 | 100 |
| 95 | 86.3 | 100 |
| 320 | 73.6 | 100 |
| 1000 | 58.2 | 99.2 |

1. COC = Concentration of Concern

| Table 14. Total Average Exceedance Rates vs. Worst-Case Exceedance Rates (Dose = 63 ppm a.i.-Continuous High-End Dose) |
| --- |
| COC1 (ppb) | Percent of Days COC Exceeded (%) |
|  | Total Average | Average of the Three Worst Case Scenarios (Table 10) |
| 14 | 99.6 | 100 |
| 18 | 99.3 | 100 |
| 69 | 94.2 | 100 |
| 73 | 93.9 | 100 |
| 95 | 92.1 | 100 |
| 320 | 80.8 | 100 |
| 1000 | 68.1 | 99.9 |

1. COC = Concentration of Concern

| Table 15. Total Average Exceedance Rates vs. Worst-Case Exceedance Rates (Dose = 1000 ppm a.i.-Intermittent Low-End Dose) |
| --- |
| COC1 (ppb) | Percent of Days COC Exceeded (%) |
|  | Total Average | Average of the Three Worst Case Scenarios (Table 11) |
| 14 | 92.9 | 100 |
| 18 | 91 | 100 |
| 69 | 78 | 100 |
| 73 | 77.4 | 100 |
| 95 | 74.6 | 100 |
| 320 | 58.5 | 99.2 |
| 1000 | 37.1 | 87.3 |

1. COC = Concentration of Concern

| Table 16. Total Average Exceedance Rates vs. Worst-Case Exceedance Rates (Dose = 1800 ppm a.i.-Intermittent High-End Dose) |
| --- |
| COC1 (ppb) | Percent of Days COC Exceeded (%) |
|  | Total Average | Average of the Three Worst Case Scenarios (Table 12) |
| 14 | 96.3 | 100 |
| 18 | 95 | 100 |
| 69 | 84.1 | 100 |
| 73 | 83.6 | 100 |
| 95 | 80.9 | 100 |
| 320 | 67.1 | 99.9 |
| 1000 | 48.7 | 96.5 |

1. COC = Concentration of Concern

To calculate the chance of exceedance of a concentration of concern over a consecutive number of days, the following assumptions were made:

- The chance of exceedance on any given day at a site is independent of whether exceedance occurred on previous days.

- Although the percentages calculated by PDM express the chance of exceedance during at least part of a day, it is assumed for this calculation that the percentages calculated by PDM imply exceedance over the total day.

Based on these assumptions, the following formula can be used to express the probability of exceedance over N consecutive days:

% probability = (Average Probability of Exceedance per Day/100%)N * 100%

Tables 17, 18, 19, and 20 show the calculation for these probabilities.  These tables can be used to determine an appropriate COC, based on the level of risk that is deemed acceptable.  The choice will depend on how conservative a value is deemed necessary.

| Table 17. Percent Probability of Exceedance Over Consecutive Days (Dose = 32 ppm a.i.-Continuous Low-End Dose) |
| --- |
| COC1 (ppb) | Number of Consecutive Days |
|  | Low Flow (100 MGD2) | Mid Flow (500 MGD2) | High Flow (1000 MGD2) |
|  | 2 day | 4 day | 2 day | 4 day | 2 day | 4 day |
| 14 | 92.9 | 86.4 | 98.8 | 97.6 | 100 | 100 |
| 18 | 89.5 | 80.1 | 98.4 | 96.8 | 99.8 | 99.6 |
| 69 | 64.2 | 41.2 | 90.1 | 81.1 | 92 | 84.6 |
| 73 | 63 | 39.7 | 89.5 | 80.1 | 91.2 | 83.2 |
| 95 | 58.2 | 33.9 | 86.3 | 74.5 | 86.5 | 74.8 |
| 320 | 39.3 | 15.5 | 65.9 | 43.5 | 64 | 41 |
| 1000 | 22.1 | 4.88 | 40.1 | 16.1 | 49.8 | 24.8 |

1. COC = Concentration of Concern

2. MGD = million gallons per day

| Table 18. Percent Probability of Exceedance Over Consecutive Days (Dose = 63 ppm a.i.-Continuous High-End Dose) |
| --- |
| COC1 (ppb) | Number of Consecutive Days |
|  | Low Flow (100 MGD2) | Mid Flow (500 MGD2) | High Flow (1000 MGD2) |
|  | 2 day | 4 day | 2 day | 4 day | 2 day | 4 day |
| 14 | 98.2 | 96.4 | 99.6 | 99.2 | 100 | 100 |
| 18 | 96.8 | 93.8 | 99.4 | 98.8 | 100 | 100 |
| 69 | 77.8 | 60.5 | 95.6 | 91.5 | 98.2 | 96.4 |
| 73 | 76.7 | 58.9 | 95.3 | 90.7 | 98 | 96.1 |
| 95 | 71.4 | 51 | 93.5 | 87.4 | 96.2 | 92.6 |
| 320 | 49.3 | 24.3 | 78 | 60.8 | 75.7 | 57.3 |
| 1000 | 32.4 | 10.5 | 56.6 | 32 | 58.1 | 33.7 |

1. COC = Concentration of Concern

2. MGD = million gallons per day

| Table 19. Percent Probability of Exceedance Over Consecutive Days (Dose = 1000 ppm a.i.-Intermittent Low-End Dose) |
| --- |
| COC1 (ppb) | Number of Consecutive Days |
|  | Low Flow (100 MGD2) | Mid Flow (500 MGD2) | High Flow (1000 MGD2) |
|  | 2 day | 4 day | 2 day | 4 day | 2 day | 4 day |
| 14 | 73.6 | 54.2 | 94.3 | 88.9 | 97 | 94.1 |
| 18 | 68.6 | 47 | 92.4 | 85.3 | 94.9 | 90 |
| 69 | 45.4 | 20.6 | 73.4 | 53.9 | 70.6 | 49.8 |
| 73 | 44.5 | 19.8 | 72.4 | 52.4 | 69.6 | 48.4 |
| 95 | 40.7 | 16.6 | 67.7 | 45.9 | 65.3 | 42.6 |
| 320 | 22.3 | 4.96 | 40.6 | 16.5 | 50.1 | 25.1 |
| 1000 | 7.95 | 0.632 | 14 | 1.96 | 29.5 | 8.69 |

1. COC = Concentration of Concern

2. MGD = million gallons per day

| Table 20. Percent Probability of Exceedance Over Consecutive Days (Dose = 1800 ppm a.i.-Intermittent High-End Dose) |
| --- |
| COC1 (ppb) | Number of Consecutive Days |
|  | Low Flow (100 MGD2) | Mid Flow (500 MGD2) | High Flow (1000 MGD2) |
|  | 2 day | 4 day | 2 day | 4 day | 2 day | 4 day |
| 14 | 85 | 72.3 | 97.4 | 94.9 | 99.4 | 98.8 |
| 18 | 80.3 | 64.5 | 96.4 | 93 | 98.8 | 97.6 |
| 69 | 54.5 | 29.7 | 83.2 | 69.2 | 82.3 | 67.7 |
| 73 | 53.6 | 28.7 | 82.3 | 67.7 | 81.2 | 65.9 |
| 95 | 49.4 | 24.4 | 78.1 | 61.1 | 75.7 | 57.3 |
| 320 | 31.2 | 9.76 | 54.9 | 30.1 | 57.3 | 32.8 |
| 1000 | 14.6 | 2.13 | 26.4 | 6.98 | 41.5 | 17.2 |

1. COC = Concentration of Concern

2. MGD = million gallons per day

UNCERTAINTIES/LIMITATIONS

The following limitations apply to the results of this model:

- The PDM4 database contains data on steam electric power plants in the United States.  In the database, no differentiation was made between those power plants that used a recirculating cooling water system and those that did not.  In the absence of better data, it was assumed that all power plants in the database used a once-through cooling water system, and that the amount of cooling water used in normal conditions was equal to the 7Q10 flow.  These assumptions may not be conservative.

- It is possible in all cases that more than one facility is located on a given reach.  For the purposes of modeling, however, it is assumed that only one facility is located at each reach.

- PDM4 is a screening-level model.  Screening-level models are rarely if ever used as the sole justification for regulatory decision-making at EPA.  Additional data and more rigorous tools are used to improve the estimates of exposures and risks for such decisions.  Results may not accurately reflect all of the information and data used by EPA to make a regulatory decision on a chemical.

- It has been assumed that a maintenance dose of the chemical is required daily, and that intermittent doses are applied for 15 minutes a day.

REFERENCES

Cloete TE, Smith Z, Saayman G.  1999. A Cooling Water System as a Biofilm Reactor for the Treatment of Municipal Wastewater.  Water SA Vol. 25 No. 3 July 1999.  Available on website

DiToro, D. M.  1984.  Probability Model of Stream Quality Due to Runoff.  ASCE.  Journal of Environmental Engineering.  110(3):607-628.

EFAST Help, beta version, 2004.

Genest, Dan, Dominion Power. Telephone interview.  June 14, 2004.

Versar, 2005.  Memorandum. Draft Environmental Fate Science Chapter for DDAC RED.  From Adria Diaz and Patricia Wood, Versar, Inc. to Srinivas Gowda, USEPA. Date: August 30, 2005.

Appendix: Input/Output Files