# Intrabeam Scattering in the VLHC

#### Valeri Lebedev

### Fermilab

VLHC mini-workshop

SLAC, March 21-23, 2001.

##### Content

- Machine Parameters

- IBS theory

- IBS estimate

- Conclusions

VLHC Parameters

|  |  | Stage 1 | Stage 2 |
| --- | --- | --- | --- |
| Beam energy | Ep | 20 TeV | 87.5 TeV |
| Luminosity | L | 1034 cm-2s-1 | 2(1034 cm-2s-1 |
| Magnetic field | B0 | 1.96 T | 10 T |
| Injection energy | Einj | 0.9 TeV | 10 TeV |
| Bunch spacing | b | 18.9 ns |
| Circumference | C=2R | 232 km |
| Revolution frequency | f0 | 1294 Hz |
| Number of bunches | Nb | 36943 |
| RF frequency | fRF | 477.9 MHz |
| Betatron tunes | ( | ~214 |
| Momentum compaction |  | 2.1(10-5 |
| Beta-function at IP |  | 30 cm | 50 cm |
| Head-on beam-beam tune shift per IP |  | 1.8(10-2 | 1.8(10-2 |
| Number of particles per bunch | N | 2.5(1010 |
| Beam current | Ib | 0.190 A | 0.175 A |
| RF voltage per turn, top/injection energy | V0 | 50/50 MeV | 50/50 MeV |
| Synchrotron frequency, top/injection energy | fs | 2.32/10.9 Hz | 1.1/3.28 Hz |
| Rms momentum spread, top/injection energy | p | 1.5/14.9(10-4 | 0.5/2.4(10-4 |
| Rms bunch length, top/injection energy | s | 6.6/14.2 cm | 4.5/7.8 cm |

- Intrabeam scattering theory

If in the beam frame the longitudinal momentum spread is much less than the transverse one

IBS calculations can be significantly simplified

##### The IBS growth rate for longitudinal degree of freedom

- IBS transfers the energy from the transverse degrees of freedom to the longitudinal one and the growth rate can be approximated by the following formula

,

where averaging is performed along the beam orbit,

,

, , and

-	are the beam sizes and angular spreads along the ring, and

- 	Lc - is the Coulomb logarithm.

- In the smooth focusing approximation,

- for equal horizontal and vertical emittances, ,

- equal betatron tunes, , and

- small contribution of energy spread into the beam size,,

( The momentum spread growth rate can be written in the following form

.

##### The IBS growth rate for transverse degree of freedom

- The heating of the longitudinal degree of freedom causes cooling for both transverse degrees of freedom;

- Additional mechanism heats the horizontal degree of freedom

  - At regions with non-zero dispersion, changes in longitudinal momentum change the particles reference orbits, which additionally excites the horizontal betatron motion,

,

where

Finally, one can write for the emittance growth rates

where

.

- In the smooth focusing approximation,

- for equal horizontal and vertical emittances, ,

- equal betatron tunes, , and

- small contribution of energy spread into the beam size,,

( The emittance growth rate can be written in the following form

- Intrabeam Scattering Estimate for the First Stage

- Intrabeam Scattering Estimate for the Second Stage

- SR damping decreases beam sizes to the level where it will be stabilized by IBS or other heating mechanism

  - SR damping time is ~ 2 hour

- We need to prevent decrease of horizontal and longitudinal emittances to avoid stronger IBS and TMCI.

    - Vertical beam size decrease is limited by increase in IBS for horizontal degree of freedom. That happens at the size aspect ratio,yx , of about 0.15.

      - Vertical emittance needs to be kept at this level to prevent growth of horizontal emittance.

- Conclusions

## IBS does not contribute into emittance growth for the first stage

## IBS is one of limiting factors for the second stage after the SR damping will cause significant cooling of beam emittances

# Text boxes

Growth rates for the longitudinal momentum spread (red solid line) and horizontal beam size (blue dashed line) as function of beam size aspect ratio, yx ; p/p = 5(10-5,

s = 2.6 cm, nx = 0.2 mm mrad