Proposed Joint Concept

C Neumeyer 3/6/3

Beryllium copper (BeCu) backing plate, 1/2” dia x 2” long BeCu shear pins, and 3/8” BeCu studs. Non-split flag

Coolant tube 0.25” OD, 0.186”ID…

Options for shear pin and bolt locations…

Assuming 5000# max load per bolt, and full vertical load on shear pins….

| Force per Bolt | 5000 | lbs |
| --- | --- | --- |
| Bolt Mat'l Tensile Yield | 100000 | psi |
| Bolt dia | 0.375 | in |
| Bolt Stress | 45270.7 | psi |
| SF | 2.21 |  |
| Shear Pin Dia | 0.5 | in |
| Shear Pin Depth | 1 | in |
| Shear Pin Yield | 100000 | psi |
| Copper Yield | 30000 | psi |
| Shear Load | 9234.25 | lbs |
| Number of Shear Pins | 2 |  |
| Load per Pin | 4617.12 | lbs |
| Shear Area in Pin | 0.20 | in |
| Stress in Pin | 23514.82 | lbs |
| SF in Pin | 4.25 |  |
| Bearing Stress Concentration Factor | 3 |  |
| Bearing Stress in Copper | 27702.75 | lbs |
| SF in Copper | 1.08 |  |