APPENDIX D-5

Calculate Total Trihalomethane, Total Haloacetic Acid,

Combined Nitrate = Nitrite, IndividualNitrate, Individual Nitrite,

Combined Radium, and Adjusted Gross Alpha Results

This Page is intentionally left blank

D-5.	Calculate Total Trihalomethane, Total Haloacetic Acid, Combined Nitrate = Nitrite, Individual Nitrate, Individual Nitrite, and Combined Radium, and Gross Alpha Excluding Uranium Results (Section 9.2.5)

Check-Point Restart Issues: This process will be driven by changes to the TSASAR table.

Calculate Totals for New or Changed SARs.

The driver for this subprocess is the TSASAR table.

The record key for this subprocess is the composite of D_Last_Update_Timestamp and the TSASAR_IS_NUMBER columns.

The sort order for this subprocess will be D_Last_Update_Timestamp ascending and TSASAR_IS_NUMBER ascending.

The following logic is used to create a total trihalomethanes result:

- Create a log in the CDS Execution Log indicating the process start time.

- Read each sample where:

  - the Last Update Timestamp or related result(s Last Update Timestamp is greater than the last time the CDS Setup program was run; AND

  - Collection End Date is greater than or equal to the CDS History Date; AND

  - related Water System Facility Type Code is equal to “DS”; AND

  - Rejection Reason Code is blank; AND

  - Compliance Purpose Indicator Code is equal to “Y” AND

  - Sample Type is equal to routine (RT) or maximum residence time (MR); AND

  - it does not have a result where

    - the referenced analyte code is equal to “2950" AND

    - the User ID is not equal to “CDSSETUP” AND

  - at least one result where:

    - the referenced analyte code is equal to any one of the four trihalomethane analytes (2941, 2942, 2943, or 2944); AND

    - the Data Quality Code is equal to accepted (A) or validated (V).

For each sample selected above:

- Read the Concentration, and UOM Code, Less Than Ind, and Detection Lim UOM Code for each result where:

  - the analyte code referenced is 2941 or 2942 or 2943 or 2944; AND

  - Data Quality Code is equal to accepted (A) or validated (V).

- If the Less Than Ind is “Y” for all, user-entered results:

  - If the Detection Lim UOM Code is not the same for all results,

    - Convert the Detection Limit Num of the other results to the same Detection Lim UOM Code unit for the first result as follows:

| Detectn Lim UOM Code of Other Results | Detectn Lim UOM Code of 1st Result | Multiplier |
| --- | --- | --- |
| MG/L | UG/L | 1000 |
| MG/L | NG/L | 1000000 |
| UG/L | MG/L | 0.001 |
| UG/L | NG/L | 1000 |
| NG/L | MG/L | 0.000001 |
| NG/L | UG/L | 0.001 |

    - Create a (or revise the existing) result for total trihalomethanes as indicated in Table TTHM1 and associate it to the current sample.

    - If conversion cannot be accomplished because one or more Detectn Lim UOM Codes do not correlate to the table, an advisory will be created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code.  write the following message to the CDS Setup Processing Report and then go to the next sample:

“Could not calculate a needed result for the following sample: Lab Sample No. [sbs sample.lab assigned id number], collected on [collection-end_date] from water system [water system.number] - [water system.name], water system facility [water system facility.state asgn identification code], and sampling point [sampling point.identification code] because encountered improper unit of measure for the result.”

  - If the Detection Lim UOM Code is the same for all results, create (or revise the existing) result for total trihalomethanes as indicated in Table TTHM1 and associate it to the current sample.

- If the Less Than Ind is not “Y” for all, user-entered results:

- If the UOM Code for all results where Less Than Ind does not equal “Y”  are not equal, then convert to the same UOM Code as the UOM Code for the first individual result where Less Than Ind does not equal “Y” as follows (note that, for a less than detect result, the UOM Code is often left blank which is the reason for adding the clause (where Less Than Ind does not equal (Y(():

| UOM Code of Other Results | UOM Code of 1st Result | Multiplier |
| --- | --- | --- |
| MG/L | UG/L | 1000 |
| MG/L | NG/L | 1000000 |
| UG/L | MG/L | 0.001 |
| UG/L | NG/L | 1000 |
| NG/L | MG/L | 0.000001 |
| NG/L | UG/L | 0.001 |

If conversion cannot be accomplished because one or more UOM Codes do not correlate to the table, an advisory will be created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code.

- Otherwise, create (or replace existing) result for Total Trihalomethanes (code 2950) as follows (only populate the fields indicated):

| Table TTHM1 |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If every individual trihalomethane result for sample has “MRL,” then set to ‘MRL”; if every one has ‘MDL,” then set to “MDL”; otherwise set to spaces. |
| LESS_THAN_IND | If every individual trihalomethane result for the sample has “Y,” then set to “Y.” Otherwise set to “N”. |
| DATA_QUALITY_CODE | Set to “A.” |
| REPORTED_MSR | Convert Concentration as calculated below to text |
| CONCENTRATION_MSR | Sum of the Concentration Measures for the individual trihalomethane . If a result is marked as less than detect, use zero for that result regardless of the value entered into concentration_msr. Round to the least number of significant figures used in the calculation (excluding the significant figures indicated by a result of zero). (Note, the SSWr1 design did include these rounding specifications but, apparently, they were not implemented in SSWr1.) (A.D-5.a) |
| UOM_CODE | If LESS_THAN_IND of created record is Y, do not value. Else, set to UOM_CODE of first individual trihalomethane with a UOM Code. |
| DETECTN_LIMIT_NUM | If LESS_THAN_IND is set to “Y” for the created record, Then add the DETECTN_LIMIT_NUM from each of the constituent results (after conversion and (A.D-5.b) rounding). Else (if LESS_THAN_IND is set to “N” for the created record), Do not value |
| DETECTN_LIM_UOM_CD | If LESS_THAN_IND is set to “Y” for the created record, Then set in accordance with specification above. Else (if LESS_THAN_IND is set to “N” for the created record), Do not value |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TSAANLYT_IS_NUMBER | 351 |
| TSAANLYT_ST_CODE | HQ |
| TSASMN_IS_NUMBER | If every individual trihalomethane result for sample references same Method Number, then set to same Method Number. Otherwise set to null. |
| TSASMN_ST_CODE |  |
| TSASAMPL_IS_NUMBER | Same Sample referenced by individual trihalomethane result. |
| TSASAMPL_ST_CODE |  |
| TMNMPRD_IS_NUMBER | If all the individual trihalomethane results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

The following logic is used to create a total haloacetic acid result:

Read each sample where:

  - the Last Update Timestamp or related result(s Last Update Timestamp is greater than the last time the CDS Setup program was run; AND

  - Collection End Date is greater than or equal to the CDS History Date; AND

  - Rejection Reason Code is blank; AND

  - Compliance Purpose Indicator Code is equal to “Y” AND

  - Sample Type is equal to routine (RT) or maximum residence time (MR); AND

  - it does not have a result where

    - the referenced analyte code is equal to “2456" AND

    - the User ID is not equal to “CDSSETUP”

AND

  - at least one result where:

    - the referenced analyte code is equal to any one of the five haloacetic acid analytes (2450, 2451, 2452, 2453, or 2454); AND

    - the Data Quality Code is equal to accepted (A) or validated (V).

For each sample selected above:

Read the Concentration and UOM Code for each result where:

  - the analyte code referenced is 2450 or 2451 or 2452 or 2453 or 2454

  - the Data Quality Code is equal to accepted (A) or validated (V).

- If the Less Than Ind is “Y” for all, user-entered results:

  - If the Detection Lim UOM Code is not the same for all results,

    - Convert the Detection Limit Num of the other results to the same Detection Lim UOM Code unit for the first result as follows:

| Detectn Lim UOM Code of Other Results | Detectn Lim UOM Code of 1st Result | Multiplier |
| --- | --- | --- |
| MG/L | UG/L | 1000 |
| MG/L | NG/L | 1000000 |
| UG/L | MG/L | 0.001 |
| UG/L | NG/L | 1000 |
| NG/L | MG/L | 0.000001 |
| NG/L | UG/L | 0.001 |

ii.	Create a (or revise the existing) result for total haloacetic acid as indicated in Table HAA1 and associate it to the current sample.

iii.	If conversion cannot be accomplished because one or more Detectn Lim UOM Codes do not correlate to the table an advisory will be created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code.

b.	If the Detection Lim UOM Code is the same for all results, create (or revise the existing) result for total haloacetic acids as indicated in Table HAA1 and associate it to the current sample.

4.	If the Less Than Ind is not “Y” for all, user-entered results:

  - If the UOM Code for all results where Less Than Ind does not equal “Y”  are not equal, then convert to the same UOM Code as the UOM Code for the first individual result where Less Than Ind does not equal “Y” as follows:

| UOM Code of Other Results | UOM Code of 1st Result | Multiplier |
| --- | --- | --- |
| MG/L | UG/L | 1000 |
| MG/L | NG/L | 1000000 |
| UG/L | MG/L | 0.001 |
| UG/L | NG/L | 1000 |
| NG/L | MG/L | 0.000001 |
| NG/L | UG/L | 0.001 |

If conversion cannot be accomplished because one or more UOM Codes do not correlate to the table an advisory will be created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code.

  - Otherwise, create (or replace existing) result for Total Haloacetic Acids (code 2456) as follows (only populate the fields indicated):

| Table HAA1 |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If every individual haloacetic acid result for sample has “MRL,” then set to “MRL”; if every one has “MDL,” then set to “MDL”; otherwise set to spaces. |
| LESS_THAN_IND | If every individual haloacetic acid result for the sample has “Y,” then set to “Y.” Otherwise set to “N.” |
| DATA_QUALITY_CODE | Set to “A” |
| REPORTED_MSR | Convert Concentration as calculated below to text. |
| CONCENTRATION_MSR | Sum of the Concentration Measures for the individual haloacetic acids. If a result is marked as less than detect, use zero for that result regardless of the value entered into concentration_msr. Round to the least number of significant figures used in the calculation (excluding the significant figures indicated by a result of zero). (Note, the SSWr1 design did include these rounding specifications but, apparently, they were not implemented in SSWr1.) (A.D-5.c) |
| UOM_CODE | Set to UOM_CODE of first individual haloacetic acid with a UOM Code. |
| DETECTN_LIMIT_NUM | If LESS_THAN_IND is set to “Y” for the created record, Then add the DETECTN_LIMIT_NUM from each of the constituent results (after conversion and (A.D-5.d) rounding). Else (if LESS_THAN_IND is set to “N” for the created record), Do not value |
| DETECTN_LIM_UOM_CD | If LESS_THAN_IND is set to “Y” for the created record, Then set in accordance with specification above. Else (if LESS_THAN_IND is set to “N” for the created record), Do not value |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TSAANLYT_IS_NUMBER | 812 |
| TSAANLYT_ST_CODE | HQ |
| TSASMN_IS_NUMBER | Set to null. |
| TSASMN_ST_CODE |  |
| TSASAMPL_IS_NUMBER | Same Sample referenced by individual haloacetic acid result. |
| TSASAMPL_ST_CODE |  |
| TMNMPRD_IS_NUMBER | If all the individual haloacetic acid results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

The following logic is used to create a combine nitrate + nitrite result:

1.	Read each sample where:

  - the Last Update Timestamp or related result(s Last Update Timestamp is greater than the last time the CDS Setup program was run; AND

  - Collection End Date is greater than or equal to the CDS History Date; AND

  - Rejection Reason Code is blank; AND

  - Compliance Purpose Indicator Code is equal to “Y” AND

  - Sample Type is equal to routine (RT) or confirmation (CO); AND

  - A result for both analyte code 1041 and 1040 where the Data Quality Code is equal to accepted (A) or validated (V) for both; AND

  - Either:

    - it does not have a result for analyte code “1038” or

    - it does have a result for analyte code “1038” where the User ID is equal to “CDSSETUP.”

For each sample selected above:

2.	Read the Concentration, UOM Code, Less Than Ind, Detection Limit Num, Detection Lim UOM Code for each result where:

the analyte code referenced is 1041 or 1040

the Data Quality Code is equal to accepted (A) or validated (V).

If the Less Than Ind is “Y” for both results:

If the Detection Lim UOM Code is not the same for both results,

Convert the Detection Limit Num of the second result to the same Detection Lim UOM Code unit for the first result as follows:

| Detectn Lim UOM Code of 2nd Result | Detectn Lim UOM Code of 1st Result | Multiplier |
| --- | --- | --- |
| MG/L | UG/L | 1000 |
| MG/L | NG/L | 1000000 |
| UG/L | MG/L | 0.001 |
| UG/L | NG/L | 1000 |
| NG/L | MG/L | 0.000001 |
| NG/L | UG/L | 0.001 |

ii.	Create a (or revise the existing) result for 1038 as indicated in Table N1 and associate it to the current sample.

iii.	If conversion cannot be accomplished because one or both Detectn Lim UOM Codes do not correlate to the table an advisory will be created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code.

b.	If the Detection Lim UOM Code is the same for both results, create (or revise the existing) result for 1038 as indicated in Table N1 and associate it to the current sample.

If the Less Than Ind is “Y” for one of the results and not “Y” for the other, create (or revise the existing) result for 1038 as indicated in Table N2 and associate it to the current sample.

If the LESS_THAN_IND is not “Y” for either 1041 or 1040.

If the UOM Code is not the same for both results,

Convert the Concentration_Msr of the second result to the same units as the first as follows:

| UOM Code of 2nd Result | UOM Code of 1st Result | Multiplier |
| --- | --- | --- |
| MG/L | UG/L | 1000 |
| MG/L | NG/L | 1000000 |
| UG/L | MG/L | 0.001 |
| UG/L | NG/L | 1000 |
| NG/L | MG/L | 0.000001 |
| NG/L | UG/L | 0.001 |

ii.	Create a (or revise the existing) result for 1038 as indicated in Table N3 and associate it to the current sample.

    - If conversion cannot be accomplished because one or both UOM Codes do not correlate to the table an advisory will be created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code.

If the UOM Code is the same for both units, create a (or revise the existing) result for 1038 as indicated in Table N3 and associate it to the current sample.

Use the same general logic as described above to create a result for nitrate (1040) except replace references to 1040 with 1038 references to 1038 with 1040.

Use the same general logic as described above to create a result for nitrite (1041) except replace references to 1041 with 1038 and references to 1038 with 1041.

| Table N1 (Less Than Ind is “Y” for both results) |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If the results for the two, user-entered results have “MRL,” then set to “MRL”; if both have “MDL,” then set to “MDL”; otherwise set to “MDL” |
| LESS_THAN_IND | Set to “Y” |
| DETECTN_LIMIT_NUM | Set to the larger of the DETECTN_LIMIT_NUM for the two user-entered results |
| DETECTN_LIM_UOM_CD | Set to DETECTN_LIM_UOM_CD of first, user-entered result. |
| DATA_QUALITY_CODE | Set to “A” |
| REPORTED_MSR | Set to “0” |
| CONCENTRATION_MSR | Set to 0 |
| UOM_CODE | Set to UOM_CODE of the first, user-entered, result |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TMNMPRD_IS_NUMBER | If both user-entered results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

| Table N2 (Less Than Ind is “Y” for one of the results and not “Y” for the other) |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If the results for the two, user-entered, results have “MRL,” then set to “MRL”; if both have “MDL,” then set to “MDL”; otherwise set to null |
| LESS_THAN_IND | Set to null |
| DETECTN_LIMIT_NUM | Set to 0 |
| DETECTN_LIM_UOM_CD | Set to null |
| DATA_QUALITY_CODE | Set to “A” |
| REPORTED_MSR |  |
| CONCENTRATION_MSR | Use zero for concentration msr for the result that is less than detection. If calculating a result for 1038, then = sum of the Concentration Msr for 1040 and 1041 If calculating a result for 1040, then = Concentration Msr for 1038 - Concentration Msr for 1041 If calculating a result for 1041, then = Concentration Msr for 1038 - Concentration Msr for 1040 Round to the least number of significant figures used in the calculation (excluding the significant figures indicated by a result of zero). (Note, the SSWr1 design did include these rounding specifications but, apparently, they were not implemented in SSWr1.) (A.D-5.e) |
| UOM_CODE | Set to UOM_CODE of the user-entered result where its LESS_THAN_IND is NOT equal to Y. |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TMNMPRD_IS_NUMBER | If both user-entered results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

| Table N3 (LESS_THAN_IND is not “Y” for either result) |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If the results for the two, user-entered, results have “MRL,” then set to “MRL”; if both have “MDL,” then set to “MDL”; otherwise set to null |
| LESS_THAN_IND | Set to null |
| DETECTN_LIMIT_NUM | Set to 0 |
| DETECTN_LIM_UOM_CD | Set to null |
| DATA_QUALITY_CODE | Set to “A” |
| REPORTED_MSR | Convert Concentration as calculated below to text |
| CONCENTRATION_MSR | If calculating a result for 1038, then = sum of the Concentration Msr for 1040 and 1041 If calculating a result for 1040, then = Concentration Msr for 1038 - Concentration Msr for 1041 If calculating a result for 1041, then = Concentration Msr for 1038 - Concentration Msr for 1040 Round to the least number of significant figures used in the calculation (excluding the significant figures indicated by a result of zero). (Note, the SSWr1 design did include these rounding specifications but, apparently, they were not implemented in SSWr1.) (A.D-5.f) |
| UOM_CODE | Set to UOM_CODE of the user-entered result |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TMNMPRD_IS_NUMBER | If both results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

The following logic is used to create a combined radium result (i.e., analyte code 4010):

1.	Read each sample where:

  - the Last Update Timestamp or related result(s Last Update Timestamp is greater than the last time the CDS Setup program was run; AND

  - Collection End Date is greater than or equal to the CDS History Date; AND

  - Rejection Reason Code is blank; AND

  - Compliance Purpose Indicator Code is equal to “Y” AND

  - Sample Type is equal to routine (RT) or confirmation (CO); AND

  - There are results for both analyte code 4020 (radium 226) and 4030 (radium 228) where the Data Quality Code is equal to accepted (A) or validated (V) for both; AND

  - Either:

    - There is not a result for analyte code 4010 (combined radium) or

    - There is a result for analyte code 4010 where the User ID is equal to “CDSSETUP.”

For each sample selected above:

2.	Read the Concentration, UOM Code, Less Than Ind, Detection Limit Num, Detection Lim UOM Code for each result where:

the analyte code referenced is 4020 or 4030

the Data Quality Code is equal to accepted (A) or validated (V).

If the Less Than Ind is “Y” for both results:

If the Detection Lim UOM Code is not the same for both results, write the following message to the CDS Setup Processing Report and then go to the next sample:

“Could not calculate a needed result for the following sample: Lab Sample No. [sbs sample.lab assigned id number], collected on [collection-end_date] from water system [water system.number] - [water system.name], water system facility [water system facility.state asgn identification code], and sampling point [sampling point.identification code] because encountered improper unit of measure for the result.”

b.	If the Detection Lim UOM Code is the same for both results, create (or revise the existing) result for 4010 as indicated in Table RA1 and associate it to the current sample.

If the Less Than Ind is “Y” for one of the results and not “Y” for the other, create (or revise the existing) result for 4010 as indicated in Table RA2 and associate it to the current sample.

If the LESS_THAN_IND is not “Y” for either result.

If the UOM Code is not the same for both results an advisory will be created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code.

If the UOM Code is the same for both units, create a (or revise the existing) result for 4010 as indicated in Table RA3 and associate it to the current sample.

| Table RA1 (Less Than Ind is “Y” for both results) |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If the results for the two, user-entered results have “MRL,” then set to “MRL”; if both have “MDL,” then set to “MDL”; otherwise set to “MDL” |
| LESS_THAN_IND | Set to “Y” |
| DETECTN_LIMIT_NUM | Set to the larger of the DETECTN_LIMIT_NUM for the two user-entered results |
| DETECTN_LIM_UOM_CD | Set to DETECTN_LIM_UOM_CD of first, user-entered result. |
| DATA_QUALITY_CODE | Set to “A” |
| REPORTED_MSR | Set to “0” |
| CONCENTRATION_MSR | Set to 0 |
| UOM_CODE | Set to UOM_CODE of the first, user-entered, result |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TMNMPRD_IS_NUMBER | If both user-entered results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

| Table RA2 (Less Than Ind is “Y” for one of the results and not the other) |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If the results for the two, user-entered, results have “MRL,” then set to “MRL”; if both have “MDL,” then set to “MDL”; otherwise set to null |
| LESS_THAN_IND | Set to null |
| DETECTN_LIMIT_NUM | Set to 0 |
| DETECTN_LIM_UOM_CD | Set to null |
| DATA_QUALITY_CODE | Set to “A” |
| REPORTED_MSR | Set to the REPORTED_MSR of the user-entered result where its LESS_THAN_IND is NOT equal to Y. |
| CONCENTRATION_MSR | Set to the CONCENTRATION_MSR of the user-entered result where its LESS_THAN_IND is NOT equal to Y. |
| UOM_CODE | Set to UOM_CODE of the user-entered result where its LESS_THAN_IND is NOT equal to Y. |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TMNMPRD_IS_NUMBER | If both user-entered results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

| Table RA3 (LESS_THAN_IND is not “Y” for either result) |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If the results for the two, user-entered, results have “MRL,” then set to “MRL”; if both have “MDL,” then set to “MDL”; otherwise set to null |
| LESS_THAN_IND | Set to null |
| DETECTN_LIMIT_NUM | Set to 0 |
| DETECTN_LIM_UOM_CD | Set to null |
| DATA_QUALITY_CODE | Set to “A” |
| REPORTED_MSR | Convert Concentration as calculated below to text |
| CONCENTRATION_MSR | Equal to the sum of the Concentration Msr for 4020 and 4030. Round to the least number of significant figures used in the calculation (excluding the significant figures indicated by a result of zero). (Note, the SSWr1 design did include these rounding specifications but, apparently, they were not implemented in SSWr1.) (A.D-5.g) |
| UOM_CODE | Set to UOM_CODE of the first, user-entered result |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TMNMPRD_IS_NUMBER | If both results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

The following logic is used to create an adjusted gross alpha result (i.e., gross alpha excluding uranium - analyte code 4000):

1.	Read each sample where:

the Last Update Timestamp or related result(s Last Update Timestamp is greater than the last time the CDS Setup program was run; AND

Collection End Date is greater than or equal to the CDS History Date; AND

Rejection Reason Code is blank; AND

Compliance Purpose Indicator Code is equal to “Y” AND

Sample Type is equal to routine (RT) or confirmation (CO); AND

There are results for (analyte code 4002 (gross alpha including uranium) or analyte code 4109 (gross alpha, total)) and 4006 (combined uranium) where the Data Quality Code is equal to accepted (A) or validated (V) for both; AND

Either:

There is not a result for analyte code 4000 (gross alpha excluding uranium) or

There is a result for analyte code 4000 where the User ID is equal to “CDSSETUP.”

For each sample selected above:

2.	Read the Concentration, UOM Code, Less Than Ind, Detection Limit Num, Detection Lim UOM Code for each result where:

the analyte code referenced is 4002, 4109 or 4006.

the Data Quality Code is equal to accepted (A) or validated (V).

If the Less Than Ind is “Y” for both results, create (or revise the existing) result for 4000 as indicated in Table GA1 and associate it to the current sample.

If the Less Than Ind is “Y” for one of the results and not “Y” for the other, create (or revise the existing) result for 4000 as indicated in Table GA2 and associate it to the current sample.

If the LESS_THAN_IND is not “Y” for either result.

If the gross alpha result(s less_than_ind is not “Y” and its UOM is not pCi/L,  an advisory will be created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code.  The process will then move on to the next result.

If the uranium result(s less_than_ind is not “Y” and its UOM is not pCi/L or ug/L or mg/L, an advisory will be created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code.  The process will then move on to the next result.

Else (i.e., if the results are in the UOMs indicated above), create a (or revise the existing) result for 4000 as indicated in Table GA3 and associate it to the current sample.

| Table GA1 - If Created Result is Less Than Detect |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If the results for the two, user-entered results have “MRL,” then set to “MRL”; if both have “MDL,” then set to “MDL”; otherwise set to “MDL” |
| LESS_THAN_IND | Set to “Y” |
| DETECTN_LIMIT_NUM | Set to the larger of the DETECTN_LIMIT_NUM for the two user-entered results |
| DETECTN_LIM_UOM_CD | Set to DETECTN_LIM_UOM_CD of the result with the larger DETECTN_LIMIT_NUM. |
| DATA_QUALITY_CODE | Set to “A” |
| REPORTED_MSR | Set to “0” |
| CONCENTRATION_MSR | Set to 0 |
| UOM_CODE | Set to spaces. |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TMNMPRD_IS_NUMBER | If both user-entered results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

| Table GA2 - One is LTD the Other is Not |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If the results for the two, user-entered, results have “MRL,” then set to “MRL”; if both have “MDL,” then set to “MDL”; otherwise set to null |
| LESS_THAN_IND | If the 4002 or 4109 result(s LESS_THAN_IND is NOT equal to Y, Set to null. If the 4002 or 4109 result(s LESS_THAN_IND is equal to Y, set to Y. Note: there should only be a result for one or the other, not both. If there is a result for both, use the first selected. |
| DETECTN_LIMIT_NUM | If the 4002 or 4109 result(s LESS_THAN_IND is equal to Y, set to the DETECTN_LIMIT_NUM of the 4002 or 4109 result. Otherwise, set to the larger of the DETECTN_LIMIT_NUM for the two user-entered results. |
| DETECTN_LIM_UOM_CD | If the 4002 or 4109 result(s LESS_THAN_IND is equal to Y, set to the DETECTN_LIM_UOM_CD of the 4002 or 4109 result. Otherwise, set to DETECTN_LIM_UOM_CD of the result with the larger DETECTN_LIMIT_NUM. |
| DATA_QUALITY_CODE | Set to “A” |
| REPORTED_MSR | Set to Concentration Msr after calculation. |
| CONCENTRATION_MSR | If the 4002 or 4109 result(s LESS_THAN_IND is NOT equal to Y, set to the CONCENTRATION_MSR of the 4002 or 4109 result If the 4002 or 4109 result(s LESS_THAN_IND is equal to Y, set to zero. Note: there should only be a result for one or the other, not both. If there is a result for both, use the first selected. |
| UOM_CODE | Set to UOM_CODE of the gross alpha result. |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TMNMPRD_IS_NUMBER | If both user-entered results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| SSMPA_SASCH_IS_NO | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| SSMPA_SASCH_ST_CO |  |
| SSMPA_MPRD_IS_NO |  |
| SSMPA_MPRD_ST_CO |  |

| Table GA3 - Neither Result is LTD |
| --- |
| Field Name | Specification for Populating |
| LESS_THAN_CODE | If the results for the two, user-entered, results have “MRL,” then set to “MRL”; if both have “MDL,” then set to “MDL”; otherwise set to null |
| LESS_THAN_IND | Set to null |
| DETECTN_LIMIT_NUM | Set to null |
| DETECTN_LIM_UOM_CD | Set to null |
| DATA_QUALITY_CODE | Set to (A( |
| REPORTED_MSR | Convert Concentration as calculated below to text |
| CONCENTRATION_MSR | If the uranium result is in ug/L, it will be converted to pCi/L by multiplying it by 0.67 pCi/ug. If the uranium result is in mg/L, it will be converted to pCi/L by multiplying it by 670 pCi/mg. If the uranium result is in pCi/L, no conversion is necessary. If uranium is in any other UOM, an advisory will created referencing message number 14 and will record: the Water System No., name, tinwsys_is_number, and tinwsys_st_code; the water system facility state assigned ID and name; the sampling point ID and description; the sample(s lab sample number and collection date; and the result(s analtye code. Concentration_msr = gross alpha concentration - converted uranium concentration, rounded to significant figures. Round to the least number of significant figures used in the calculation (excluding the significant figures indicated by a result of zero). (Note, the SSWr1 design did include these rounding specifications but, apparently, they were not implemented in SSWr1.) (A.D-5.h) |
| UOM_CODE | Set to UOM_CODE of the gross alpha result. |
| D_LAST_UPDT_TS | Current Date and Time |
| D_USERID_CODE | CDSSETUP |
| TMNMPRD_IS_NUMBER | If both results reference the same Monitoring Period, then reference the same. Otherwise set to null. |
| TMNMPRD_ST_CODE |  |
| TMNSASCH_IS_NUMBER | Do not need to relate the new result to an SSMPA because, if appropriate, this will be done by a subsequent process. |
| TMNSASCH_ST_CODE |  |
| TMNMPRD0IS_NUMBER |  |
| TMNPRPD0ST_CODE |  |