*****************************************************************************

NOTICE OF PARAMETERS FOR

OPERATION UNDER PRE-SUNRISE AUTHORITY (PSRA)

NOVEMBER 15, 2004

(Post this letter with your current authorization )

*****************************************************************************

Pursuant to Section 73.99 of FCC Rules and Regulations, Pre-Sunrise operation

(PSRA) is permitted in accordance with the parameters listed below.  The

powers listed below are maximum values that may not be exceeded. However,

operation at any power not in excess of those listed is permissible.

*****************************************************************************

FACILITY ID: 29515                               CALCULATIONS BASED ON:

CALL: WECR   CITY: NEWLAND            STATE: NC  LICENSED FACILITY

ANTENNA: DAYTIME          FREQUENCY: 1130 KHZ    BL-19780720AA

MONTH   TIME  CONVERSION  POWER       TIME  CONVERSION  POWER    LIMITING

PERIOD   FACTOR    WATTS      PERIOD   FACTOR    WATTS    STATION(S)

JAN     6:00    0.1048     11.0       7:15    0.1702     29.0    KWKH  /KWKH

FEB     6:00    0.1048     11.0       6:45    0.1702     29.0    KWKH  /KWKH

MAR     6:00    0.1341     18.0       6:15    0.1702     29.0    KWKH  /KWKH

APR     6:00    0.1673     28.0                                     KWKH

--FOR APRIL, ALSO SEE SPECIAL NOTE REGARDING ADVANCED TIME--

MAY     6:00    0.1702     29.0                                     KWKH

JUNE    6:00    0.1702     29.0                                     KWKH

JULY    6:00    0.1702     29.0                                     KWKH

AUG     6:00    0.1048     11.0                                     KWKH

SEP     6:00    0.1048     11.0       6:30    0.1341     18.0    KWKH  /KWKH

OCT     6:00    0.1048     11.0       7:00    0.1341     18.0    KWKH  /KWKH

--FOR OCTOBER, ALSO SEE SPECIAL NOTE REGARDING ADVANCED TIME--

NOV     6:00    0.1048     11.0       6:45    0.2167     47.0    KWKH  /KWKH

DEC     6:00    0.1048     11.0       7:15    0.2280     52.0    KWKH  /KWKH

SPECIAL NOTE REGARDING ADVANCED TIME

------------------------------------

APRIL--Follow MARCH parameters until advanced time begins.

OCTOBER--Follow NOVEMBER parameters as soon as advanced time ends.

***************************************************************************

STATUS OF PREVIOUS PRE-SUNRISE AUTHORITY

----------------------------------------

This notice and its parameters supersede any previous Pre-Sunrise authority.

If these parameters are lower than those previously authorized, the power

must be reduced within 30 days of receipt of this letter or PSRA must be

terminated.  PSRA operation may be resumed on completion of the reduction.

Page 1 of 3

CALCULATION OF ANTENNA INPUT POWER

----------------------------------

The nominal power listed is not necessarily the same as the Antenna Input

Power. To determine the Antenna Input Power permitted during PSRA; multiply

the INPUT POWER listed on the station authorization by the SQUARE of the

ANTENNA CURRENT CONVERSION FACTOR. The Antenna Current or Common Point

Current permitted during PSRA is obtained by multiplying the ANTENNA CURRENT

CONVERSION FACTOR by the AUTHORIZED ANTENNA CURRENT or COMMON POINT CURRENT.

NATURE OF AUTHORITY GRANTED

---------------------------

PSRA is secondary to the basic instrument of authorization with which it is

to be associated. The PSRA may be suspended, modified, or withdrawn by the

FCC without prior notice or right to hearing, if necesary to resolve

interference conflicts, to implement agreements with foreign governments, or

in other circumstances warranting such action. Moreover, the PSRA does not

extend beyond the term of the basic authorization.

NOTIFICATION PROCEDURE

----------------------

PSRA operation under this authorization may commence immediately upon

submission of the following information:

1. Licensee name, station call sign and location

2. Indication that such PSRA operation is intended by the

station

3. A description of the method whereby any necessary power

reduction will be achieved.

Send to:

Federal Communications Commission

Audio Division, Media Bureau

Technical Processing Group, Mail Stop 1800-B3

445 12th Street, SW

Washington, D.C. 20554

FOR ADDITIONAL INFORMATION

--------------------------

If there are any questions concerning PSRA operation please call:

Audio Division, Media Bureau

(202) 418-2700

Page 2 of 3

*****************************************************************************

STATION PARAMETERS

*****************************************************************************

FACILITY ID: 29515                            CALCULATIONS BASED ON:

CALL: WECR   CITY: NEWLAND            STATE: NC  LICENSED FACILITY

ANTENNA: DAYTIME          FREQUENCY: 1130 KHZ    BL-19780720AA

POWER:   1.000 kW  RMS: 363.71 mV/m  Q FACTOR: ******

REGION2 CLASS: B  STATION CLASS: D  DOMESTIC STATUS: L

ANTENNA MODE: NDD  TOWERS:  1  AUGMENTATIONS:  0  DOMESTIC PATTERN: T

LATITUDE: N 36:04:39  LONGITUDE: W 81:54:59 TIME ZONE: EST

Tower   Field     Phase      Space      Orient  Tower Ref Height     TL

No.     Ratio     (Deg.)     (Deg.)     (Deg.)  Switch    (Deg.)   Switch

1     1.0000     0.0000     0.0000     0.0000     0    165.4000      0

Page 3 of 3

REVISED PARAMETERS FOR OPERATION UNDER POST-SUNSET AUTHORITY (PSSA)

NOVEMBER 15, 2004

(Post this letter with your current authorization )

THIS AUTHORIZATION SUPERSEDES ANY PREVIOUS POST-SUNSET AUTHORITY

******************************************************************************

Post-Sunset operation as set forth below is authorized. These values

may not be exceeded, but operation at lower power is permitted.

******************************************************************************

FACILITY ID: 29515                            CALCULATIONS BASED ON:

CALL: WECR   CITY: NEWLAND            STATE: NC  LICENSED FACILITY

ANTENNA: DAYTIME          FREQUENCY: 1130 KHZ    BL-19780720AA

------------------------------------------------------------------------------

| MONTH |    TIME   | POWER |  CONV. |  | MONTH |    TIME   | POWER |  CONV. |

|       |   PERIOD  | WATTS | FACTOR |  |       |   PERIOD  | WATTS | FACTOR |

|-------------------------------------  -------------------------------------|

| JAN   | 5:30- 6:30|  16.0 | 0.1264 |  | JULY  | 8:45- 9:30|  19.0 | 0.1378 |

|       | 6:30- 7:30|   8.0 | 0.0894 |  |       | 9:30-10:45|   8.0 | 0.0894 |

|-------------------------------------  -------------------------------------|

| FEB   | 6:15- 7:00|  16.0 | 0.1264 |  | AUG   | 8:15- 9:00|  19.0 | 0.1378 |

|       | 7:00- 8:15|   8.0 | 0.0894 |  |       | 9:00-10:15|   8.0 | 0.0894 |

|-------------------------------------  -------------------------------------|

| MAR   | 6:30- 7:15|  19.0 | 0.1378 |  | SEP   | 7:30- 8:15|  19.0 | 0.1378 |

|       | 7:15- 8:30|   8.0 | 0.0894 |  |       | 8:15- 9:30|   8.0 | 0.0894 |

|-------------------------------------  -------------------------------------|

| APR   | 7:00- 7:45|  19.0 | 0.1378 |  | OCT   | 7:00- 7:45|  16.0 | 0.1264 |

|(STD.) | 7:45- 9:00|   8.0 | 0.0894 |  |(ADV.) | 7:45- 9:00|   8.0 | 0.0894 |

|(TIME) |           |       |        |  |(TIME) |           |       |        |

|-------------------------------------  -------------------------------------|

| APR   | 8:00- 8:45|  19.0 | 0.1378 |  | OCT   | 6:00- 6:45|  16.0 | 0.1264 |

|(ADV.) | 8:45-10:00|   8.0 | 0.0894 |  |(STD.) | 6:45- 8:00|   8.0 | 0.0894 |

|(TIME) |           |       |        |  |(TIME) |           |       |        |

|-------------------------------------  -------------------------------------|

| MAY   | 8:30- 9:00|  26.0 | 0.1612 |  | NOV   | 5:15- 6:15|  16.0 | 0.1264 |

|       | 9:00-10:30|   8.0 | 0.0894 |  |       | 6:15- 7:15|   8.0 | 0.0894 |

|-------------------------------------  -------------------------------------|

| JUNE  | 8:45- 9:30|  19.0 | 0.1378 |  | DEC   | 5:15- 6:15|  16.0 | 0.1264 |

|       | 9:30-10:45|   8.0 | 0.0894 |  |       | 6:15- 7:15|   8.0 | 0.0894 |

|----------------------------------------------------------------------------|

(All times listed are PM local time)

Page 1 of 3

NATURE OF AUTHORITY GRANTED

---------------------------

PSSA is secondary to the basic instrument of authorization with which it is

to be associated. The PSSA may be suspended, modified, or withdrawn by the

FCC without prior notice or right to hearing, if necesary to resolve

interference conflicts, to implement agreements with foreign governments, or

in other circumstances warranting such action. Moreover, the PSSA does not

extend beyond the term of the basic authorization.

NOTIFICATION PROCEDURE

----------------------

PSSA operation under this authorization may commence immediately upon

submission of the following information:

1. Licensee name, station call sign and location

2. Indication that such PSSA operation is intended by the

station

3. A description of the method whereby any necessary power

reduction will be achieved.

Send to:

Federal Communications Commission

Audio Division, Media Bureau

Technical Processing Group, Mail Stop 1800-B3

445 12th Street, SW

Washington, D.C. 20554

FOR ADDITIONAL INFORMATION

--------------------------

If there are any questions concerning PSSA operation please call:

Audio Division, Media Bureau

(202) 418-2700

Page 2 of 3

*****************************************************************************

STATION PARAMETERS

*****************************************************************************

FACILITY ID: 29515                            CALCULATIONS BASED ON:

CALL: WECR   CITY: NEWLAND            STATE: NC  LICENSED FACILITY

ANTENNA: DAYTIME          FREQUENCY: 1130 KHZ    BL-19780720AA

POWER:   1.000 kW  RMS: 363.71 mV/m  Q FACTOR: ******

REGION2 CLASS: B  STATION CLASS: D  DOMESTIC STATUS: L

ANTENNA MODE: NDD  TOWERS:  1  AUGMENTATIONS:  0  DOMESTIC PATTERN: T

LATITUDE: N 36:04:39  LONGITUDE: W 81:54:59 TIME ZONE: EST

Tower   Field     Phase      Space      Orient  Tower Ref Height     TL

No.     Ratio     (Deg.)     (Deg.)     (Deg.)  Switch    (Deg.)   Switch

1     1.0000     0.0000     0.0000     0.0000     0    165.4000      0

Page 3 of 3