July 22, 1994

Contract # TW0592

SPECIAL SPECIFICATION

SECTION 15932

AIR OUTLETS AND INLETS

Page

PART 1 - GENERAL

1.01 Description...	2

1.02Related Work.	2

1.03Quality Assurance..	2

1.04References.	3

1.05Submittals.	3

1.06 Delivery, Storage, and Handling..	4

PART 2 - PRODUCTS

2.01Acceptable Manufacturers...	5

2.02 Ceiling Air Diffusers.	5

2.03 Grilles.	7

PART 3 - EXECUTION

3.01 Inspection..	9

3.02 Installation/Application/Erection..	9

3.03 Extra Parts..	9

SPECIAL SPECIFICATION

SECTION 15932

AIR OUTLETS AND INLETS

PART 1 - GENERAL

1.01	DESCRIPTION

A.  	This Section and the Drawings indicate the work for providing the air terminals.

B.  	Types of outlets and inlets required for project include the following:

1.  	Ceiling air diffusers.

2.  	Grilles.

1.02	RELATED WORK

A.  	Section 01300

B.  	Section 15010

C.  	Section 15901

1.03	QUALITY ASSURANCE

A.  	Manufacturer's Qualifications:  Firms regularly engaged in manufacture of air outlets and inlets of types and capacities required, whose products have been in satisfactory use in similar service for not less than 5 years.

B.  	Codes and Standards:

1.  	Test and rate air outlets and inlets in accordance with American Refrigeration Institute (ARI) 650 "Standard for Air Outlets and Inlets".

2.  	Test and rate air outlets and inlets in accordance with American Society of Heating, Refrigerating, and Air-Conditioning Engineers (ASHRAE) 70 "Method of Testing for Rating the Air Flow Performance of Outlets and Inlets".

3.  	Test and rate air outlets and inlets in certified laboratories under requirements of Air Diffusion Council (ADC) 1062 "Certification, Rating and Test Manual".

4.  	Provide air outlets and inlets bearing ADC Certified Rating Seal.

5.  	Install air outlets and inlets in accordance with National Fire Protection Association (NFPA) 90A "Standard for the Installation of Air Conditioning and Ventilating Systems".

1.04	REFERENCES

A.  	ADC 1062, Certification, Rating and Test Manual

B.  	AMCA 500, Test Method for Louvers, Dampers and Shutters

C.  	ARI 650, Standard for Air Outlets and Inlets

D.  	ASHRAE 70, Method of Testing for Rating the Air Flow Performance of Outlets and Inlets

E.  	American Society for Testing and Materials (ASTM) B 221

F.  	NFPA 90A, Standard for the Installation of Air Conditioning and Ventilating Systems

1.05	SUBMITTALS

A.  	Make submittals according to this Section, Section 15010, and Section 01300.

B.  	Submit manufacturer's technical product data for air outlets and inlets including the following:

1.  	Schedule of air outlets and inlets indicating drawing designation, room location, number furnished, model number, size, and accessories furnished.

2.  	Data sheet for each type of air outlet and inlet, and accessory furnished; indicating construction, finish, and mounting details.

C.  	Submit 3 samples of each type of finish furnished.

D.  	Submit maintenance data, including cleaning instructions for finishes, and spare parts lists.  Include this data, product data, and shop drawings in maintenance manuals.

1.06	DELIVERY, STORAGE, AND HANDLING

A.  	See Section 15010.

B.  	Deliver air outlets and inlets wrapped in factory-fabricated fiber-board type containers.  Identify on outside of container type of outlet or inlet and location to be installed.  Avoid crushing or bending and prevent dirt and debris from entering and settling in devices.

C.  	Store air outlets and inlets in original cartons and protect from weather and construction work traffic.  Where possible, store indoors; when necessary to store outdoors, store above grade and enclose with waterproof wrapping.

PART 2 - PRODUCTS

2.01	ACCEPTABLE MANUFACTURERS

A.  	Provide diffusers of one of the following:

1.  	Anemostat Products Div.; Dymanics Corp. of America.

2.  	Krueger Mfg. Co.

3.  	Titus Products Div.; Philips Industries, Inc.

B.  	Provide registers and grilles of one of the following:

1.  	Anemostat Products Div.; Dynamics Corp. of America.

2.  	Titus Products Div.; Philips Industries, Inc.

2.02	CEILING AIR DIFFUSERS

A.  	General:  Except as otherwise indicated, provide manufacturer's standard ceiling air diffusers where shown; of size, shape, capacity and type indicated; constructed of materials and components as indicated, and as required for complete installation.

B.  	Performance:  Provide ceiling air diffusers that have, as minimum, temperature and velocity traverses, throw and drop, and noise criteria ratings for each size device as listed in manufacturer's current data.

C.  	Ceiling Compatibility:  Provide diffusers with border styles that are compatible with adjacent ceiling systems, and that are specifically manufactured to fit into ceiling module with accurate fit and adequate support.  Refer to general construction drawings and specifications for types of ceiling systems which will contain each type of ceiling air diffuser.

D.  	Types:  Provide ceiling diffusers of type, capacity, and with accessories and finishes as listed on diffuser schedule.  The following requirements shall apply to nomenclature indicated on schedule.

1.  	Diffuser Faces:

a. 		Square:  Square housing, core of square concentric louvers, square or round duct connection.

b. 		Perforated:  Square or rectangular housing covered with removable perforated panel in frame and square or round duct connection.  Conceal air pattern devices above panel.

c. 		Linear Slot:  Extruded aluminum continuous slot, single or multiple.

d. 		Linear Bar:  Extruded aluminum with fixed deflection bars parallel to the long dimension.

2.  	Diffuser Mountings:

a. 		Flush:  Diffuser housing above ceiling surface with flush perimeter flange and gasket to seal against ceiling.

b. 		Lay-In:  Diffuser housing sized to fit between ceiling exposed suspension tee bars and rest on top surface of tee bar.

3.  	Diffuser Patterns:

a. 		Adjustable linear:  Manual adjustable core with concentric rings or louvers, fully adjustable for horizontal to vertical air flow and fully adjustable for 1- or 2-direction flow as indicated on drawings.

b. 		1 Way:  Fixed louver face for 1-direction air flow, direction indicated on drawings.

c. 		2 Way:  Fixed louver face for 2-direction air flow, directions indicated on drawings.

d. 		3 Way:  Fixed louver face for 3-direction air flow, directions indicated on drawings.

e. 		4 Way:  Fixed louver face for 4-direction air flow, directions indicated on drawings.

f. 		Adjustable perforated:  Manual fully adjustable discharge pattern for 1-, 2-, 3-, or 4-direction flow and fully adjustable for horizontal to vertical air flow as indicated on drawings.

4.  	Diffuser Dampers:

a. 		Opposed Blade:  Adjustable opposed blade damper assembly (rectangular or radial), key operated from face of diffuser.

b. 		Integral:  Combination volume control and pattern adjustment for linear diffusers.

5.  	Diffuser Accessories:

a. 		Operating Keys:  Tools designed to fit through diffuser face and operate volume control device and/or pattern adjustment.

6.  	Diffuser Finishes:

a. 		White Enamel:  Semi-gloss white enamel finish.

2.03	GRILLES

A.  	General:  Except as otherwise indicated, provide manufacturer's standard grilles where shown; of size, shape, capacity and type indicated; constructed of materials and components as indicated, and as required for complete installation.

B.  	Performance:  Provide grilles that have, as minimum, temperature and velocity traverses, throw and drop, and noise criteria ratings for each size device and listed in manufacturer's current data.

C.  	Provide grilles with border styles that are compatible with adjacent wall or ceiling systems, and that are specifically manufactured to fit into construction with accurate fit and adequate support.  Refer to general construction drawings and specifications for types of construction which will contain each type of grille.

D.  	Types:  Provide grilles of type, capacity, and with accessories and finishes as listed on air distribution schedule.  The following requirements shall apply to nomenclature indicated on schedule:

1.  	Materials:

a. 		Aluminum Construction:  Manufacturer's standard extruded aluminum frame and adjustable blades.

2.  	Grille Faces:

a. 		Horizontal Straight Blades:  Horizontal blades, individually adjustable or fixed, at manufacturer's standard spacing.  See drawings.

b. 		Vertically Straight Blades:  Vertical blades, individually adjustable or fixed, at manufacturer's standard spacing.  See Drawings.

c. 		Eggcrate Blades:  Eggcrates grilles at manufacturer's standard spacing.

3.  	Grille Dampers:

a. 		Opposed Blade:  Adjustable opposed blade damper assembly, key operated from face of register.

4.  	Grille Accessories:

a. 		Operating Keys:  Tools designed to fit through register or grille face and operate volume control device.

5.  	Grille Finishes:

a. 		White Enamel:  Semi-gloss white enamel finish.

PART 3 - EXECUTION

3.01	INSPECTION

A.  	Inspect areas and conditions under which air outlets and inlets are to be installed.  Do not proceed with work until unsatisfactory conditions have been corrected.

3.02	INSTALLATION/APPLICATION/ERECTION

A.  	General:  Install air outlets and inlets in accordance with manufacturer's written instructions and in accordance with recognized industry practices to insure that products serve intended function.

B.  	Coordinate with other work, including ductwork and duct accessories, as necessary to interface installation of air outlets and inlets with other work.

C.  	Locate ceiling air diffusers, registers, and grilles, as indicated on general construction "Reflected Ceiling Plans".  Locate units as shown on drawings.

3.03	EXTRA PARTS

A.  	Furnish to Sandia National Laboratory with receipt, 3 operating keys for each type of air outlet and inlet that require them.

END OF SECTION